## Slide 1: Technical Challenges and Breakthroughs for the FCC-hh (mostly valid for FCC-ee and FCC-he)
FCC Kick-Off 2014
Dr. José Miguel JIMENEZ CERN, Technology Department Department Head
Emails contacts:
FCC-technologies-hh for the FCC hh
FCC-technologies-ee for the FCC ee
FCC-technologies-he for the FCC he

## Slide 2: Main topics
Introduction
Items included in “Special Technologies”
Challenges and expected Breakthroughs
Setting Collaborations…
Many thanks to CERN Colleagues and to the Coordination Committee for the input.

## Slide 3: Introduction
Special technologies are fundamental for this study
  Need to identify the challenges, the showstoppers…
  …and the opportunities for technology breakthroughs.
  This last point will complement perfectly the Physic Cases to get an approval for the next step…
  …and these are the domains where we need your help.

## Slide 4: Items included in “Special Technologies” Using the preliminary WBS structure as guidelines…

## Slide 5: Items included in “Special Technologies” …with some more details… (1/3)
Technologies that require R&D
  Identify all the technologies that require specific R&D. Already identified the RF system (beam power, high gradient and klystron efficiency) and superconducting magnets.
  Special technologies could also require R&D when looking forward to breakthrough or identified as show-stopping.
Beam diagnostics
  Define the needs for the core beam instrumentation. Estimate the required number of components (for example BPMs) and their performance in terms of resolution and dynamic range. Consider including machine protection components like beam loss monitors.
Beam transfer elements
  Define the requirements and parameters for beam transfer elements (injection and dump kickers, electrostatic separators). Study the design of those elements.
Collimation requirements
  Define the number of components and the power loads for collimators. Explore potential materials for collimators. Define mechanical requirements for collimators.
Control system requirements
  Define the needs in terms of network, data transfer rates and logging volumes. Define requirements for synchronization.
Dump and stopper requirements
  Define the requirements in terms of energy/power deposition on the dumps and other beam stopper devices. Explore possible designs of dumps and absorbers.

## Slide 6: Items included in “Special Technologies” …with some more details… (2/3)
Element support and alignment requirements
  Define the requirements in terms of alignment for beam line elements and experiments. Define needs for active alignment and stabilization.
Machine detector integration
  Define technical requirements for elements that are required at the interface of machine and detector, like synchrotron radiation masks, vacuum pumping and maintenance safety aspects.
Machine protection
  Define requirements and explore the design of the machine protection elements.
Normal magnet requirements
  Define the requirements in terms of peak fields or peak gradients and length of the normal conducting magnets. Explore the design the main magnets, in particular for the arc section and long straight sections.
Power converter requirements
  Define requirements in terms of current, voltage and stability of the power converters for the collider and the booster ring.

## Slide 7: Items included in “Special Technologies” …with some more details… (3/3)
Quench protection
  Define the requirements for quench protection of the super-conducting magnets for the low-beta insertions.
Cryogenics
  Define the requirements on the cryogenic system for the RF, the low-beta quadrupoles and cryomagnets. Impact of beam screens operating temperature and required stability.
Vacuum system
  Define the requirements and explore the design of the vacuum system for the arcs and the straight sections. The design must take into account the large amount of synchrotron radiation and the possible shielding of the vacuum chamber as protection of tunnel equipment. It has also to mitigate beam-induced dynamic effects (pressure blow-up, electron and ion clouds).
Shielding
  Define and explore the design of static shielding for synchrotron radiation inside and outside of the vacuum chamber.

## Slide 8: Challenges and expected Breakthroughs Cryogenics
Challenges
  Study and development of larger cryoplants:
    New type of cycle compressors ? (centrifugal vs screw).
    New refrigeration cycle ? (higher HP pressure).
  Study and development of larger cold-compressor systems (10 kW range):
    Larger cold compressors development ?
    Operation with parallel cold compressor trains ?
  Management of He inventory and He losses, in particular helium release during magnet resistive transitions and cold buffering.
  Higher availability of cryo-systems.
Breakthroughs
  The beam screen cooling:
    High heat deposition: up to 44 W/m per aperture.
    Integration of the cooling circuits in a narrow space.
    Control of the 40-60 K temperature level with high dynamic range (up to 10) alternative cooling method (with neon…).
Please refer to the talk given by Laurent TAVIAN Friday morning Session

## Slide 9: Challenges and expected Breakthroughs Radioprotection and Radiation
Challenges
  Radioprotection has to be considered in early stages of the design due to implications of normative regulations:
    Limit number of access pits / Hard-wire cabling of safety signals / Radiation access veto / …
  Remote Handling and Telemanipulation: here we need a giant leap in both technology and culture:
    The machine should be designed such that most of the standard maintenance can be performed with cots robots. All machine components shall have to be designed to be maintained / repaired / removed remotely.
Breakthroughs
  Material developments to find low-activation alternatives
  Combine machine protection (BLM) with dose rate instrumentation…

## Slide 10: Challenges and expected Breakthroughs Resistive Magnets
Requirements
  Decide which operating mode is used since having huge implications on magnets (and power converters)
    Continuous, cycled, pulsed, fixed or variable energy
    Just dedicated to fill the FCC or also for other purposes…
Challenges
  Energy efficiency vs flexibility of the machine vs cost optimisation
Breakthroughs
  Increase the radiation hardness of the coil insulation:
    A gain of a factor 10 in radiation hardness (from 20 MGy to at least 200 MGy) appears on reach, for example by using mica + cyanate esther systems or other alternatives…
    Local shielding included at the design stage…
  Need a proper technological development in particular in the processing/manufacturing techniques and in the experimental validation of the radiation hardness.

## Slide 11: Challenges and expected Breakthroughs Beam Instrumentation
Challenges
  BPMs and BLMs
    Thousands (>16’000?) of them needed all along the ring with an order of magnitude to be gained in resolution, reliability and availability!
      Operational constraints…
Breakthroughs
  Non-invasive emittance measurements are already a challenge in the LHC it will be even more so for FCC:
    Synchrotron light: will have to go for X-ray imaging (diffraction already limited in the visible at 7TeV).
    Gas targets: being investigated in the LHC (ionisation profile monitors and the beam gas vertex detector) but concerns with vacuum compatibility (radiation).
  Maintenance, electromagnetic compatibility (EMI), radiation hardness:
    Minimal tunnel electronics with regrouping them at surface with an extensive use of fibre optics.

## Slide 12: Challenges and expected Breakthroughs Beam Transfer Elements (1/2)
Requirements
  Facing 3+ TeV p+ extraction/injection and TLs, 50 TeV beam dump (8GJ beams) and dump kicker protection systems,… are much higher than ever reached.
Challenges
  Scaling from the existing technology will require an improvement in reliability / availability by more than an order of magnitude… a real challenge!
Breakthroughs
  Injection / Extraction insertions
    Special injection/extraction insertion magnet concepts with split quadrupole/dipole, coil/yoke beam passages, superconducting (massless?) septa, very slim quadrupole cold-mass and cryostats, very large aperture quadrupoles, opposite-field septa, ….
  High current semiconductor switches
    Design and construction of very fast high-current semiconductor switches: sub-us turn on, >20 kA, x15 voltage range, reliability, radiation resistance, …
  Beam absorbers
    Shall go for sacrificial beam absorbers with optimised materials, failure modes, exchange methodology, vacuum, absorption, diagnostics, …

## Slide 13: Challenges and expected Breakthroughs Beam Transfer Elements (2/2)
Less “breakthrough” but still appearing as showstoppers…
  Kickers
    Impedance shielding: thin films, wires, active current elements, geometry, …
    Ferrite cooling technologies: solid-state, thermal design, surface emissivity, …
    Electron cloud (SEY) and UFOs
  High saturation, high temperature ferrite materials
  Ultra-high reliability system design: redundancy, failsafe modes, diagnostics, testing, QC, …
  Thermomechanical design and fatigue mitigation for fast-repetition rate, high field pulsed magnets.
  Burst-mode bunch-to-bucket transfer systems: CLIC inductive adder concept.
  Diluter materials and designs for dumps and transfer line collimators: low density, high robustness, magnetised, optics insertions, …
  Thermal, mechanical, electrical design for high-strength in-vacuum pulsed magnets: impedance, e-cloud suppression, heating mitigation, beam losses, …

## Slide 14: Challenges and expected Breakthroughs Vacuum – for Beams (1/2)
Challenges
  Vacuum compatibility of beam equipment: collimators, beam instrumentation, kickers, beam absorbers,…
  UFOs at design stage and during installation in the tunnel: cleanroom” type installation ?!
  Definition of the Operating temperature of the beam screen
    Hydrogen pumping, beam lifetime, HOM, Impedance, dB/dt,…
Breakthroughs
  New beam screen approach compatible with:
    Beam-induced dynamic effects: electron and ion clouds, pressure bursts, …
    Beam screen shielding and heat load evacuation…
    Temperature transients during the ramp in energy…
  Alternative materials (or alloys) with a better radiation activation “signature” and similar mechanical / thermal / electrical performances… including Beryllium beampipes ad windows.

## Slide 15: Challenges and expected Breakthroughs Vacuum – for thermal insulation (2/2)
Challenges
  Leak tightness: reliability issues since about 4 times more sealing and welding “length”…for the same reliability!
    500 km of welds!
    100 km of elastomer seals!
  Mechanical design and compatibility with superfluid helium
    Interconnection bellows, flexible links and bellows
      Multiplies technology to be optimised!
Breakthroughs
  Sealing technologies, reliable and compatible with radiation…
  Helium pumping (trapping) to mitigate leaks appearing during operation?
  Pressure sensors with radiation hard converters and fibre optics…
    Multiplexing of signal?

## Slide 16: Technical Challenges and Breakthroughs for the FCC-hh Radiation to Electronics (R2E)
Challenges
  Radiation levels will roughly scale with energy
    Shielding issues in particular integration
      To reduce by a factor ten one needs approximately 80 cm of concrete plus 40 cm of iron
  Finding the right balance between number of alcoves for controls and power electronics, and massive development of rad hard electronics.
Breakthroughs
  Electronics to remain in the tunnel improved by at least a couple of order of magnitudes.
  Radiation hardness of miniaturized electronics, which normally would have an increased sensitivity.

## Slide 17: Technical Challenges and Breakthroughs for the FCC-hh Collimation Systems (1/3)
Challenges
  New optics concepts and IR layouts to be developed in order to achieve at least 20x better cleaning with larger collimator gaps
    Reduced impedance and operational tolerances… might need more than 2 collimation IRs…!
  Inter-alignment
    If the hierarchy of different collimators depend on micrometer or submicrometer alignment from collimator to collimator is necessary, it will be necessary to further develop position measurement and control solutions based on new technologies (piezo, optical, etc…)
  Assuming that one can clean the primary halo stopping the secondary halo will be a challenge.
    Optics and collimation shall have to check that one can safely clean the beam from secondaries, or invent a new strategy.

## Slide 18: Technical Challenges and Breakthroughs for the FCC-hh Collimation Systems (2/3)
Challenges (cont.)
  Operational aspects
    How often will we have to change the collimators?
    Radiation issues? Remote handling?
    Disposable collimators should be developed: quick and fully automated collimator replacement?
  FLUKA models are already reliable for most purposes related to the design of the machine. Will need some scaling and integration of new models derived from data published by LHC experiments
    This work actually already started…

## Slide 19: Technical Challenges and Breakthroughs for the FCC-hh Collimation Systems (3/3)
Breakthroughs
  New collimator design to withstand much larger energy loads with reasonable transient deformation and no permanent damage.
  Associated to that, some breakthrough is most likely needed in collimator material science
    Compatible with Impedance and Vacuum requirements
    Explore new collimation concepts like crystal collimation. Crystal collimation will however push even further the material challenge.
  Manufacturing tolerances
    Micrometer or submicrometer planarity will be required. Knowing that the present 20 micron planarity is already at the edge of what is available in industry, it will probably be necessary to develop a special temperature and vibration controlled machine for flattening all the surfaces facing the beams and provide it to the companies that will build collimators?!

## Slide 20: Setting Collaborations…
Range of technologies to be covered is wide
and
We need be on time within 3 years with the CDR…
Thus, we would like to focus on:
  Identified showstoppers.
  Required technological breakthroughs.
…an evaluation will quickly be made to address and assess the required R&D levels.
We need you on-board!

## Slide 21: Willing to take part to the FCC Conceptual Design Report…
Interested by Technologies, please send an email with details or questions to…
FCC-technologies-hh for the FCC hh
FCC-technologies-ee for the FCC ee
FCC-technologies-he for the FCC he
…we’ll then come back to you with answers / clarifications

## Slide 23: Challenges and expected Breakthroughs Major issues not necessarily expected: Survey
Requirements
  Determination of a new reference system which will be used to transfer the coordinates calculated by the physicists in a Cartesian XYZ system into an XYH coordinates system taking into account the shape of the earth
    Is the actual ellipsoid chosen to represent the shape of the earth accurate enough ?
    And the deviation of the vertical generated by the lake and the mountains (Jura, Salève, Vuache)…
Challenges
  Geodesy and Survey in a 100 km ring passing under a lake and/or mountains needs to be worked out… where is our reference?!
Breakthroughs
  Learn from major civil engineering projects… and integrate accelerator specificities:
    Operational aspects : regular realignments, accessibility of components, time constraints, radiation issues and associated shielding, …