Muon Cooling for a Neutrino Factory and Muon Collider
Impact of Magnet Performance on the Physics Program of MICE
Chris Rogers,
ASTeC,
Rutherford Appleton Laboratory

---
High Energy Muon Facilities
Overview
- Focus Coil 1 has not reached specified currents
  - Non-flip mode → specified currents reached
  - Flip mode → stuck at around 200 MeV/c required current
    - Even here, need an operating overhead of order 10%
- If FC can't be fixed; how does this limit the performance of Step IV?
- What about Step VI?
- Caveat:
  - All of this is linear optics
  - Great for getting an idea of the parameter space
  - Not sufficient for redefining MICE baseline

---
Step IV
- Step IV has just FC, no coupling coil and no lattice
  - What beta function can be achieved with reduced FC current?
- Coils
  - End coils and Centre coil is fixed for 4 T field on tracker
  - Optimise for matching using Match 2 and Match 1
  - Vary focus coil and look at response

---
Beta function matching
- Standard setting at Step IV is that beta should be symmetric about absorber (z=0)
  - Require dbeta/dz = 0 at the absorber centre
  - Choose dbeta/dz = 0 in the constant solenoid field (analytic solution here)
- Example for 200 MeV/c
  - E2, Centre, E1 set for 4 T
  - M2 set to max current 148.09 A/mm2
  - M1 varied for matching
  - FC current at nominal 113.95 A/mm2

---
Solutions to Match Condition
- In some cases, there is more than one solution to the match condition for a given M2 current
  - e.g. at 140 MeV/c case to right
  - Means we need to be careful about applying optimisation routines
  - Want to find all the possible match conditions...

---
Scaling M2
- Fix M2 and let M1 vary freely to find a match
  - As before, scan to find all possible solutions
  - Then optimise to get the best match
- See two families of solutions for p = 140 MeV/c

---
Matching vs Momentum
- Range of available optics for a given focus coil strength
  - Nominal + 20% (“Best”)
  - Nominal – 10% (“Actual”)

---
Step IV - Conclusions
- Reduced FC current limits accessible range of beta functions
  - Assume FC performance as FC 1
    - e.g. J < 102 A/mm2 with 10 % operating margin
  - Minimum beta function 32 mm → 104 mm at 140 MeV/c
  - Minimum beta function 136 mm → 224 mm at 200 MeV/c
  - Minimum beta function 215 mm → 356 mm at 240 MeV/c
  - Can still achieve “nominal” beta function (420 mm)
  - Some exotic options are ruled out in flip mode
  - Maximum beta function is unaffected
    - Prefer low FC current for large beta functions

---
Step VI
- Consider now Step VI SFoFo lattice only
  - Assume we can match (but see discussion above)
  - Look at how optics scales with Coupling Coil and Focus Coil currents
- Repeat over 5500 mm cell length in flip mode

---
Nominal magnets, 200 MeV/c
- By way of example
  - Bz as a function of z
  - Beta function for a half cell
- What is momentum dependence of beta function?
  - At focus (absorber)
  - At anti-focus (scraping aperture)

---
Response to FC – 200 MeV/c
- MICE operates in 2 pi → 4 pi phase advance region
  - Fills the momentum acceptance
  - Interested in beta and stop bands
- Assume FC performance as FC 1
  - e.g. J < 102 A/mm2 with 10 % operating margin
  - Stop bands unmoved
  - Beta function 420 -> 500 mm
  - Equilibrium emittance increases by ~ 20% (proportional to beta)

---
Response to FC – 240 MeV/c
- Scale lattice by increasing currents by 20 %
- Assume FC performance as FC 1
  - Beta function ~ 50-100% higher
  - Equilibrium emittance ~ 50-100 % higher
  - Bigger chromatic aberations
  - Weaker (2pi) resonance
  - Possibly slightly better acceptance
    - Beta at midpoint is lower
- How do these optics scale with CC current?

---
Response to FC current
- Overview
  - Something
    - Something else
      - And more

---
Response to FC current
- Overview
  - Something
    - Something else
      - And more

---
Response to FC current
- Overview
  - Something
    - Something else
      - And more

---
Conclusions
- MICE is still operable with reduced FC
  - Quite robust to poor performing magnets
- But physics performance is slightly reduced
  - Lose low beta function options at Step IV
  - Poor 240 MeV/c performance at Step VI
- Caveat:
  - All of this is linear optics
  - Great for getting an idea of the parameter space
  - Not sufficient for redefining MICE baseline
- Further details in MICE Note 434
- http://mice.iit.edu/micenotes/public/pdf/MICE0434/MICE0434.pdf