## Slide 1: Linear Collider R & D Status in Cooperation between CERN and KEK, focusing on ILC
Akira Yamamoto (KEK/LCC)
CERN-KEK Committee, 30 December, 2013

## Slide 2: ILC Time Line
ILC-GDE
2005
2006
2007
2008
2012
2009
2010
2011
2013
Tech. Design：TDP1
Higgs
discovered
126 GeV
Selection of SC Technology
TDP 2
Ref. Design (RDR)
LCC
LHC
2004
TDR
1980’ ~ Basic Study
completion
2013.6.12
2012.12.15

## Slide 3: RDR (2007) to TDR (2012)
Cost Containing Effort
Single acc. Tunnel
Reducing # bunches
  w/ smaller damping rings
Allowing gradient spread
  31.5 MV/m +/- 20 %,
Site-dependent RF system:
  Clustered on surface (KCS),
  Distributed in tunnl (DKS)
RDR’07 
(Reference Design Rep.)
TDR’12
(Technical Design Rep.)
Flat-land or Mountainous Tunnel Design
5 m

## Slide 4: ILC TDR Design
Damping Rings
Polarised electron source
E+ source
Ring to Main Linac (RTML)
(including
bunch compressors)
e- Main Linac
e+ Main Linac
Parameters | Value
C.M. Energy | 500 GeV
Peak luminosity | 1.8 x1034 cm-2s-1
Beam Rep. rate | 5 Hz
Pulse duration | 0.73 ms
Average current | 5.8 mA (in pulse)
E gradient in SCRF acc. cavity | 31.5 MV/m +/-20% Q0 = 1E10

## Slide 5: ILC Time Line: Progress and Prospect
Expecting: 3+2 year

## Slide 6: ILC Timeline Proposed by LCC
2013 - 2016
  Negotiations among governments
  Accelerator detailed design, R&Ds for cost-effective production, site study, CFS designs etc.
  Prepare for the international lab.
2016 – 2018
  ‘Green-sign’ for the ILC construction to be given (in early 2016 )
  International agreement reached to go ahead with the ILC
  Formation of the ILC lab.
  Preparation for biddings etc.
2018
  Construction start (9 yrs)
2027
  Construction (500 GeV) complete, (and commissioning start)
  (250 GeV is slightly shorter)

## Slide 7: Cooperation of ILC host- and hub-laboratories with worldwide industry (proposed)
Regional hub-laboratories responsible to regional procurements to be open for any world-wide industry participation
Regional Hub-Lab:
E, & …
Regional Hub-Lab:
A
Regional Hub-Lab:
B
Regional Hub-Lab:
D
World-wide
Industry responsible to
‘Build-to-Print’ manufacturing
ILC Host-Lab
Regional Hub-Lab:
C: responsible to
Hosting System Test and Gradient Performance
Technical Coordination
for Lab-Consortium
: Technical
coordination link
: Procurement link

## Slide 8: Further Works in Preparation Phase
Accelerator Engineering Design
Positron Source: Conventional source development as backup
Damping Ring: Ultra low emmittance beam, and the stability, Undulators, 650 MHz SCRF
RTML: residual magnetic field effect in long beam transport-line
ML: Cavity integration, CM engineering for cost-effective industrialization, Cryogenic Eng.
BDS: Final focusing with nano-beam, alignment w/ tighter tolerance, and design update
Beam Dynamics: Accurate lattice design based on the specific site
CFS: Site specific work including Detector hall and Central Campus design and others
EDMS: engineering based on the EDMS

## Slide 9: Cooperation Anticipated between KEK-CERN-European Laboratories
Nano-beam handling technology
  Nano-beam and the stability as a common subject for both ILC and CLIC, through ATF collaboration
  Final focusing including magnet and the mechanical stability, as well as commissioning technology, still to be investigated
SCRF cavity integration technology,
  Specially on input-power couplers and tuners, as a common subject for both ILC and SPL for LHC injector upgrade,
Cryogenic engineering
  Specially on handling of large amount of helium inventory, as a specially crucial issue in mountain region,
Civil engineering study
  specially for the detector-hall design,

## Slide 10: Cooperation Anticipated between KEK-CERN-European Laboratories
Nano-beam handling technology
  Nano-beam and the stability as a common subject for both ILC and CLIC, through ATF collaboration
  Final focusing including magnet and the mechanical stability, as well as commissioning technology, still to be investigated
SCRF cavity integration technology,
  Specially on input-power couplers and tuners, as a common subject for both ILC and SPL for LHC injector upgrade,
Cryogenic engineering
  Specially on handling of large amount of helium inventory, as a specially crucial issue in mountain region,
Civil engineering study
  specially for the detector-hall design,

## Slide 11: KEK-ATF：Progress
Ultra-small beam
Low emittance : KEK-ATF
  Achieved the ILC goal (2004).
Small vertical beam size : KEK ATF2
  Goal = 37 nm,
    160 nm (spring?, 2012)
    ~65 nm (April. 2013) at low beam current

## Slide 12: ATF Future Plan
CY
2011
2012
2013
2014
2015
2016
2017
2018
ATF長期計画(案)
Gamma-gamma laser system R&D
High Field Physics
Nano beam orbit control (FONT extension)
Develop.(2nmBPM, Fast FB)
2nm stab. R&D
Beam study
2nm steady op.
Nano beam orbit control
Beam study
Challenging R&D of the Very high chromaticity optics
Ultra small beam ~ 20 nm
Small beam
37nm
Steady op.
Develop. / beam study
4-mirror optical cavity (LAL/KEK)
Gamma-gamma collider R&D
General R&D
Ex) for KEKB; CSR, RF gun,
Instrument develop.,
Low emittance,…
Test beamline for detector?
Delay by fire and earthquake
Application
Next KEK Roadmap
GDE
ILC
others

## Slide 13: Cooperation Anticipated between KEK-CERN-European Laboratories
Nano-beam handling technology
  Nano-beam and the stability as a common subject for both ILC and CLIC, through ATF collaboration
  Final focusing including magnet and the mechanical stability, as well as commissioning technology, still to be investigated
SCRF cavity integration technology,
  Specially on input-power couplers and tuners, as a common subject for both ILC and SPL for LHC injector upgrade,
Cryogenic engineering
  Specially on handling of large amount of helium inventory, as a specially crucial issue in mountain region,
Civil engineering study
  specially for the detector-hall design,

## Slide 14: SCRF Linac Technology
1.3 GHz Nb 9-cellCavities | 16,024
Cryomodules | 1,855
SC quadrupole pkg | 673
10 MW MB Klystrons & modulators | 436 / 471 *
Approximately 20 years of R&D worldwide
 Mature technology, overall design and cost
* site dependent

## Slide 15: Plug-compatible Conditions
Plug-compatible interface established
Item | Varieties | Baseline
Cavity shape | TESLA / LL | TESLA
Length |  | Fixed
Beam pipe flange |  | Fixed
Suspension pitch |  | Fixed
Tuner | Blade/ Slide-Jack | Blade
Coupler flange (cold end) | 40 or 60 | 40 mm
Coupler pitch |  | Fixed
He –in-line joint |  | Fixed

## Slide 16: Demonstrations and Evaluation of Various Couplers and Tuners in S1-Global
Every coupler and tuner demonstrated, as expected, and be applicable for ILC cavities
Finding various subjects to be further investigated and settled

## Slide 17
TTF3/XFEL coupler
STF-2 coupler
TDR coupler
(1) Deep Technical Review of Input Couplers
Cu-plating is a key-issue

## Slide 18: EXFEL Cavity and Tuner

## Slide 19: Inter-Cavity Spacing
292
105
105
82
353
105
140
108
Reduction in inter-cavity spacing = 61 mm
Bellows: = 10882 = 26 mm
“Long” cavity end = 140105 = 35 mm
ILC Type-IV
XFEL

## Slide 20: CERN - CEA-Saclay Collaboration for CERN-SPL SCRF cavity and tuner development
Seeking for the best space-effective and cost-effective tuner, as a common subjects

## Slide 21: Cooperation Anticipated between KEK-CERN-European Laboratories
Nano-beam handling technology
  Nano-beam and the stability as a common subject for both ILC and CLIC, through ATF collaboration
  Final focusing including magnet and the mechanical stability, as well as commissioning technology, still to be investigated
SCRF cavity integration technology,
  Specially on input-power couplers and tuners, as a common subject for both ILC and SPL for LHC injector upgrade,
Cryogenic engineering
  Specially on handling of large amount of helium inventory, as a specially crucial issue in mountain region,
Civil engineering study
  specially for the detector-hall design,

## Slide 22: CERN’s Experience for He/N2 Storage to be reflected to the ILC Cryogenics design

## Slide 23: Cooperation Anticipated between KEK-CERN-European Laboratories
Nano-beam handling technology
  Nano-beam and the stability as a common subject for both ILC and CLIC, through ATF collaboration
  Final focusing including magnet and the mechanical stability, as well as commissioning technology, still to be investigated
SCRF cavity integration technology,
  Specially on input-power couplers and tuners, as a common subject for both ILC and SPL for LHC injector upgrade,
Cryogenic engineering
  Specially on handling of large amount of helium inventory, as a specially crucial issue in mountain region,
Civil engineering study
  specially for the detector-hall design,

## Slide 24: Site Specific Design to be carried out
Access Tunnel
Access Hall
(Slope <10%)
Damping Ring
Detector Hall
Ring To Main Linac (RTML)
e- Main Linac (ML)
e+ ML
RTML turn-around
e- Source
e+ Source
(Slope <7%)
Existing surface road
Existing road
(The background photo shows a similar site image, but not the real site.)
Surface Structures
PM-13
PM-12
PM-10
PM-8
PM-ab
PM+8
PM+10
PM+12
PM+13
(Center Campus)
PX
Kitakami-site cross section
Need to establish the IP and linac orientation
Then. the access points and IR infrastructure
Then. linac length and timing
Kitakami
Candidate
Site

## Slide 25: Summary
ILC design has reached the Technical Design Report including the technology demonstration,
“Design to Realization” is the next step, the design and techonology need to be further matured with cost-effective production technology to prepare for the construction stage,
CERN and KEK cooperation is expected, specially on
  Ultra-low emittance and nano-beam handling technology, including final focusing magnet technolgy,
  SCRF cavity integration technology, focusing on power-coupler and tuner technology to be matured for the best cost-effective mass-production, (to be discussed later by SS).
  Cryogenics engineering with a similar scale as that of the LHC, specially focusing on safe and stable helium resource handling,
  Civil engineering, focusing on a large detector hall based on the LHC experience (to be discussed later by SS)
The cooperative works are anticipated to be encouraged and supported by CERN and KEK

## Slide 26: backup

## Slide 27: ILC Time Scale required
 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
ILC TDP/TDR |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ATF-II | Beam test |  |  |  |  |  |  |  |  |  |  |  |  | 
ATF-future |  |  | Extended program |  |  |  |  |  |  |  |  |  |  | 
STF |  |  |  |  |  |  |  |  |  |  |  |  |  | 
QB | Beam test |  |  |  |  |  |  |  |  |  |  |  |  | 
STF2- CM1+CM2a |  |  | Beam test |  |  |  |  |  |  |  |  |  |  | 
STF-Future |  |  |  | Extended program |  |  |  |  |  |  |  |  |  | 
CFS |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Civil eng. |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Site-survey |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 14 19 |  | 16 21 |  |  | 19 24 |  |  |  |  |  | 25 30
ILC constr. |  |  |  |  |  |  |  |  |  |  |  |  |  | Commissioning
Fabrication |  |  | Preparation for the project |  | Preparation for industrialization |  | Fabrication and tests, preparation for installation |  |  |  |  |  |  | 
Inst/commission. |  |  |  |  |  |  |  |  |  |  | Installation |  |  | 
After getting Green Sign、
・Preparation for contract： ~ 2 years
・Construction period： ~ 10 years
・If the green sign given in 5 years、
ILC to be realized by 2030

## Slide 28: Cavity Integration
9-cell resonator
Input-coupler
  TTF-III coupler
Frequency tuners
  Blade tuner
He tank
Magnetic shield
  Inside He tank

## Slide 29: S1-Global hosted at KEK: Global cooperation to demonstrate SCRF system
DESY, FNAL, Jan., 2010
INFN
and
FNAL
Feb.
2010
FNAL & INFN, July, 2010
DESY, May, 2010
March, 2010
June, 2010 ~
DESY, Sept. 2010

## Slide 30
TTF-III Coupler: various support jigs are required.
coupler assembly
KEK STF Coupler:self standing

## Slide 31
Legend
Toward coupler side
Toward pick-up side
coupler side
motor side
top
bottom
Driving unit support elements are already installed on the tuner halves.
Preassembled parts