## Slide 1: My Works Review
Hamed Shaker

## Slide 2: Timeline-2011
2011
Dec
Oct
Sep
Aug
July
June
April
March
Feb
Jan
May
Nov
CTF3 TW Buncher
study
Estimation of
Input power
CTF3 SHBs study
SHBs design – Comparison between FTW,BTW and SW structures
Finding relation between phase switiching and bandwidth
First idea to use a backward traveling wave structure for the CLIC SHBs

## Slide 3: Powering – CTF3 vs. CLIC DB
PB
Buncher
Accelerating cavity
SHB-I
SHB-II
SHB-III
Gun
PB - II
15 MW
15 MW
?
?
?
15 MW
CTF3 | Field (MV/m) / Normalized | Length (cm) | Voltage (KV) | Input Power
Gun |  |  | 140 | 
SHB - I | 0.128/0.043 | 15.6 | 20 | 40 KW
SHB - II | 0.128/0.043 | 15.6 | 20 | 40 KW
SHB - III | 0.128/0.043 | 15.6 | 20 | 40 KW
PB | 1.375/0.458 | 2 | 27.5 | 100 KW
Buncher | 10.7(ave.) / 3.57 | 53.7 |  | 35 MW
CLIC DB Injector (CDR) | Field (MV/m) | Length (cm) | Voltage (KV) | Input Power (CTF3 rescaling)
Gun |  |  | 140 | 
SHB - I | 0.224 | 15.6 | 35 | 1.1 MW
SHB - II | 0.234 | 15.6 | 36.5 | 1.2 MW
SHB - III | 0.249 | 15.6 | 38.8 | 1.4 MW
PB | 1.2 | 6 | 72 | 686 KW
Buncher | 4.2 | 168.1 |  | 26.7 MW

## Slide 4: Fundamental Equation
Standing Wave Structure
Travelling Wave Structure
P
Load
V , τ
P
Load
V , τ
Forward Travelling Wave structure
Backward Travelling Wave structure
For the known gap voltage and filling time our goal is to increase R/Q to reduce the input power.
τ=10ns
V=36.5 KV
Pd : Power disappears on surface.
β : Coupling coefficient
Qe = ωτ : External quality factor
τ : Filling time
R : Effective shunt impedance
R’: Effective shunt impedance per length
Q : Unloaded quality factor
P: Source power
V : Gap voltage
W’ : Stored energy per length
L: Structure length
vg : Group velocity
n : Cell numbers
…
P
P/n V/n , τ
P/n V/n , τ
P/n V/n , τ
Load

## Slide 5: Pill Box Model – TM010 mode
a
g
Chart: Phase advance per cell (deg)
Chart: Phase advance per cell (deg)
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180
 | 0 | 0.0871 | 0.17321 | 0.25734 | 0.33856 | 0.41596 | 0.48868 | 0.55596 | 0.6171 | 0.6715 | 0.71865 | 0.75815 | 0.78972 | 0.81318 | 0.82847 | 0.83564 | 0.83486 | 0.82638 | 0.81057 | 0.78789 | 0.75887 | 0.72411 | 0.68428 | 0.64009 | 0.59229 | 0.54164 | 0.48891 | 0.43487 | 0.38027 | 0.32584 | 0.27226 | 0.22017 | 0.17015 | 0.12271 | 0.078302 | 0.0373 | 1.0755e-06
Maximum at 133.5°
Maximum at 77°

## Slide 6: CTF3 case – Forward TW structure
It means the minimum input power needs using the fundamental equation is around 1.11MW for CLIC DB injector.
Related to pill-box model and by attention to the disk thickness, the maximum R/Q is at 85° phase advance but 75.5° was chosen for CTF3 SHBs before detuning for beam loading compensation.
The best thing was done for the CTF3 SHBs with Forward TW structure and it can not be reduced so much then we should look for another structure type.
Chart: R/Q per cell for 75.5° phase advance per cell
| 0.13 | 0.78 | 2.09 | 2.94 | 3.8 | 4.9000000000000004 | 5.95 | 6.74 | 7.99 | 8.9500000000000028 | 9.9
HFSS simulation | 73.28 | 55.45 | 38.64 | 31.53 | 26 | 20.33 | 16.02 | 13.47 | 9.99 | 7.79 | 6.08
Pill Box model | 88.7
Chart: Total R/Q for 75.5° phase advance per cell
| 0.13 | 0.78 | 2.09 | 2.94 | 3.8 | 4.9000000000000004 | 5.95 | 6.74 | 7.99 | 8.9500000000000028 | 9.9
HFSS simulation | 3.6615 | 16.6235 | 31.0391 | 35.6285 | 37.9737 | 38.2877 | 36.6358 | 34.8942 | 30.6788 | 26.797 | 23.1348
Pill Box model | 0
Maximum is around 4.8% that was chosen for CTF3 SHBs.
From L. Thorndahl presentation (2) for 4 cells model. Finally 6 cells structure was chosen.
The group velocity is increased by increasing the iris radius. The iris radius is about 10cm for 4.8% group velocity.

## Slide 7: Optimization - II
number of cells | phase(deg) | vg/c(%) | R/Q - cell (Ω) | R'/Q (Ω/m) | R/Q (Ω) | Input power (KW) | r1(mm) | r2(mm) | rc(mm) | θc(deg) | lc(mm) | rn(mm) | t(mm) | g/l | phase velocity/c
3 | 105 | 10.86 | 142.76 | 1337.61 | 428.28 | 100.79 | 169.8 | 186.35 | 164.9 | 75 | 49.04 | 6.13 | 12.26 | 0.45 | 0.61
3 | 120 | 12.2 | 163 | 1336.35 | 489 | 86.81 | 152.9 | 167.8 | 148.49 | 89 | 44.16 | 5.52 | 11.04 | 0.44 | 0.61
4 | 105 | 14.34 | 142.16 | 1331.96 | 568.64 | 75.04 | 159.55 | 175.1 | 154.94 | 87 | 46.08 | 5.76 | 11.52 | 0.46 | 0.61
5 | 105 | 16.14 | 126.89 | 1314.05 | 634.45 | 67.07 | 162.88 | 178.75 | 158.17 | 95 | 47.04 | 5.88 | 11.76 | 0.54 | 0.61
another HFSS models with a little better R/Q
It is possible to reduce the power a little. For example to 75 KW from 80 KW in last slide.
After choosing the structure we can work to optimize cells depend on all parameters affect the design like beam loading, HOMs, minimum wall thickness for cooling water pipe holes and ...
It is the definition of drain time as was introduce by L. Thorndahl et al.(2) . This time is used to find the number of bunches passages during phase switching. For FTW case it is about 8% less (τ’≈9ns) and for BTW case it is about 20 % more than filling time(τ’≈12ns).

## Slide 8: Phase Switching Model and the Power Source Bandwidth
C
B
A
At f0fs (499.75  50 MHz) frequencies the amplitude is half of f0 frequency. By this fact that the bandwidth is measured from the frequencies that power consumption is half , the BW is about 57.7 MHz or 11.5%.
The BW of CTF3 SHBs sources - that are TWT structures -are about 160 MHz (10.7 %) then they have capability of phase switching at less than 4 ns.

## Slide 9: 180° Phase flipping test
Borrowed from Steffen
This measurement was done for a 800 MHz IOT with about 6MHz band-width.
About 100ns is needed for switching for 6 MHz band-width then about 60 MHz band-width is needed for 10ns switching as was shown in the previous slide.
Done at the end of 2012 that confirmed the analytical result

## Slide 10: Timeline-2012
2012
Dec
Oct
Sep
Aug
July
June
April
March
Feb
Jan
May
Nov
SHBs Design ; Coupler design and comfirmation of phase switching by CST particle studio
Finding analytical solution for the beam loading compensation
for a TW structure
Shahin joined to the group – Starting of the beam dynamic study
Mechanic’s group joined- Luca Dassa and Raphael Leuxe
Mohsen joined to the group for the Pre-Buncher Design

## Slide 11: Four cells structure with waveguide couplers
In this design for the first SHB about 73 MW peak power is needed for 10ns filling time and 36.5 KV gap voltage.

## Slide 12: Phase flipping simulation with beam – 10 ns
port 1
port 2
Beam Entrance
Continues beam with 6A current
Excitation signal from port 1 with 80 KW peak power.

## Slide 13: Phase flipping simulation with beam – 10 ns
Excitation signal – port 1
Output signal – port 2
Output signal – port 1
≈ 12 ns
≈ 44 ns

## Slide 14: Phase flipping simulation with beam – 10 ns
Chart: Maximum energy gain vs. Time
| 44.5 | 46.4 | 48.5 | 50.4 | 52.4 | 54.4 | 56.4 | 59.2 | 61.4 | 63.4 | 65.400000000000006 | 67.400000000000006 | 69.400000000000006 | 71.400000000000006
 | 35.784 | 35.273 | 35.273 | 32.718 | 27.097 | 18.41 | 7.679 | 7.679 | 16.366 | 24.031 | 31.185 | 34.762 | 36.806 | 38.85
About 5 bunches will be missed in comparison with about 120 bunches in each sub-pulse.

## Slide 15: Detuning definition in a TW structure
Usually a bunch should sees a fixed amplitude and phase in a TW structure then phase velocity(vp) and bunch velocity(ve) should be equal but as we will see this difference help us to compensate beam loading.
We can define detuning (Δω) by defining ω0 as the related angular frequency of bunch velocity (ve) in the TW structure dispersion function. This definition is velocity dependent.

## Slide 16: Fundamental mode beam-induced field
0
1
2
i
n-1
L
Δz
z
We can divide the structure length to n sections that each one is equal to energy transferring length (Δz) between two bunches passage.
Eb0 shows the fundamental mode induced field of a single bunch passages thorough the structure in each point.
Eb,p represents the previous bunches fundamental mode induced fields and Ei,b represents the total fundamental mode electric field seen by the reference bunch from its induced field and previous bunches induced fields.

## Slide 17: Bunching phase
The bunching phase is the best phase for bunching mechanism uses in prebunchers and our sub harmonic bunchers.
As you can see Δω>0. For backward TW it means |ve|>|vp| and for forward TW if vg>ve it means |ve|<|vp|.

## Slide 18: Timeline-2013
2013
Dec
Oct
Sep
Aug
July
June
April
March
Feb
Jan
May
Nov
SHB Design; The design of first SHB finished
Preliminary TW Buncher Design
Second and third SHBs are waiting for the finalized parameters
from the beam dynamic study
Analytical method for the efficinecy for the accelerating structures
Progress in the mechanic’s group
Thermal and Structural analysis was done
by the mechanic’s group

## Slide 19: First SHB

## Slide 21: Results from Beam Dynamics study done by Shahin
Chart: Beta per cell
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
 | 0.60134 | 0.60933 | 0.62505 | 0.64793 | 0.67707 | 0.71116 | 0.74851 | 0.78717 | 0.82504 | 0.86021 | 0.89123 | 0.91732 | 0.93896 | 0.95983 | 0.98117 | 1.003 | 1.0253 | 1.0481
Chart: Electric field amplitude per cell
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
 | 1.7061 | 1.7204 | 1.75 | 1.7962 | 1.8612 | 1.9479 | 2.0596 | 2.1996 | 2.3717 | 2.5788 | 2.8238 | 3.1083 | 3.4339 | 3.802 | 4.215 | 4.6755 | 5.1863 | 5.7503
Chart: Energy gain per cell
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
 | -25.3 | 32.2 | 58.4 | 55.5 | 41.1 | 24.1 | 11.8 | 11 | 29 | 60.3 | 96.1 | 131.9 | 170.1 | 211.7 | 261.2 | 324.8 | 403.9 | 501.4

## Slide 22: Normalized field
Chart: Power Consumption by beam per cell
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
 | -0.1265 | 0.161 | 0.292 | 0.2775 | 0.2055 | 0.1205 | 0.059 | 0.055 | 0.145 | 0.3015 | 0.4805 | 0.6595 | 0.8505 | 1.0585 | 1.306 | 1.624 | 2.0195 | 2.507
Power consumption/cell=
Energy gain/cell * Current (5A)
Chart: E (MV/m)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
Normalized field | 1.7004 | 1.722 | 1.7652 | 1.8254 | 1.9022 | 1.9974 | 2.1154 | 2.2626 | 2.4496 | 2.6863 | 2.9827 | 3.3487 | 3.7996 | 4.3581 | 5.0657 | 6.0018 | 7.3303 | 9.471
Non normalized field | 1.7061 | 1.7204 | 1.75 | 1.7962 | 1.8612 | 1.9479 | 2.0596 | 2.1996 | 2.3717 | 2.5788 | 2.8238 | 3.1083 | 3.4339 | 3.802 | 4.215 | 4.6755 | 5.1863 | 5.7503
Normalized field= sqrt(P0/P)*non normalized field. P0=19MW
Chart: Incident power in each cell
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
 | 19.1265 | 18.9655 | 18.6735 | 18.396 | 18.1905 | 18.07 | 18.011 | 17.956 | 17.811 | 17.5095 | 17.029 | 16.3695 | 15.519 | 14.4605 | 13.1545 | 11.5305 | 9.511 | 7.004

## Slide 23: Cells design
cell no. | beta | norm_field | vg/c(percent) | R/Q (Ohm) | a0 | a-1 | a1 | a-2 | Q | E_field | R(Mohm) | l(cm) | r(Mohm/m) | a(cm) | b(cm) | r/Q(Ohm) | alfa | dP/P(%)
1 | 0.6 | 1.70 | 6.7 | 28.88 | 0.8789 | 0.1298 | 0.00637 | 0.01123 | 16610.44 | 1.69 | 0.47971 | 5.998849 | 7.99669304 | 53 | 129.73 | 481.42572 | 0.009411 | -0.11285
5 | 0.68 | 1.90 | 7.81 | 48.31 | 0.857 | 0.15 | 0.00535 | 0.00876 | 18466.8 | 1.9 | 0.892131 | 6.798695 | 13.12209328 | 52.7 | 128.25 | 710.57754 | 0.007262 | -0.0987
9 | 0.83 | 2.45 | 8.2 | 102.45 | 0.818 | 0.195 | 0.00967 | 0.00378 | 21554.42 | 2.45 | 2.20825 | 8.298407 | 26.61053228 | 49.8 | 124.77 | 1234.5743 | 0.005926 | -0.0983
13 | 0.94 | 3.80 | 4.67 | 158.55 | 0.782 | 0.256 | 0.02466 | 0.014265 | 23409.13 | 3.79 | 3.711518 | 9.398196 | 39.49180796 | 40.9 | 120.24 | 1687.0259 | 0.009581 | -0.17993
17 | 1.03 | 7.33 | 1.48 | 205.23 | 0.767 | 0.328 | 0.0552 | 0.0397 | 24687.44 | 7.31 | 5.066603 | 10.29802 | 49.19976497 | 29.55 | 116.9 | 1992.9067 | 0.028666 | -0.58868
5 cells was designed and the rest was interpolated
5 cells was designed and the rest was interpolated
ai
ai+1
bi
bi+1
dt=10mm

## Slide 24: Cells design-2
Chart: Group velocity per cell
| 1 | 5 | 9 | 13 | 17
 | 6.7 | 7.81 | 8.2 | 4.67 | 1.48
Chart: Q0 per cell
| 1 | 5 | 9 | 13 | 17
 | 16610.44 | 18466.8 | 21554.42 | 23409.13 | 24687.44
Chart: Shunt Impedance
| 1 | 5 | 9 | 13 | 17
 | 7.9967 | 13.1221 | 26.6105 | 39.4918 | 49.1998

## Slide 25: Cells design-3
cell no | beta | l | energy gain(KV) | power consumption | power left | power loss on surface | power left-total | E | norm_E | norm_E_tot | r/Q | Eb0 | F | Eb0/E | dw/w | df(MHz) | vg/c(%) | dv | vp
1 | 0.601335 | 6.0122 | -25.3 | -0.1265 | 19.1265 | -0.021584594 | 19.10491541 | 1.71 | 1.700449 | 1.701408993 | 481.4257 | 6049.769 | 0.8 | 0.003546 | 0.000547 | 0.546649 | 6.7 | 0.003138 | 0.623138
2 | 0.609327 | 6.0921 | 32.2 | 0.161 | 18.9655 | -0.020731838 | 18.94476816 | 1.72 | 1.721964 | 1.722906014 | 538.7137 | 6769.67 | 0.8 | 0.003935 | 0.000596 | 0.595679 | 6.9775 | 0.003283 | 0.623283
3 | 0.62505 | 6.2493 | 58.4 | 0.292 | 18.6735 | -0.01975191 | 18.65374809 | 1.75 | 1.765233 | 1.76616712 | 596.0016 | 7489.571 | 0.8 | 0.00428 | 0.000576 | 0.575608 | 7.255 | 0.003051 | 0.623051
4 | 0.647934 | 6.4781 | 55.5 | 0.2775 | 18.396 | -0.01880747 | 18.37719253 | 1.80 | 1.825449 | 1.826383226 | 653.2896 | 8209.472 | 0.8 | 0.00457 | 0.000639 | 0.639018 | 7.5325 | 0.003263 | 0.623263
5 | 0.67707 | 6.7694 | 41.1 | 0.2055 | 18.1905 | -0.017953731 | 18.17254627 | 1.86 | 1.902162 | 1.903101505 | 710.5775 | 8929.373 | 0.8 | 0.004798 | 0.000722 | 0.721439 | 7.81 | 0.003553 | 0.623553
6 | 0.711156 | 7.1102 | 24.1 | 0.1205 | 18.07 | -0.017816997 | 18.052183 | 1.95 | 1.997397 | 1.998382392 | 841.5767 | 10575.56 | 0.8 | 0.005429 | 0.000851 | 0.850478 | 7.9075 | 0.004136 | 0.624136
7 | 0.748514 | 7.4837 | 11.8 | 0.059 | 18.011 | -0.017741079 | 17.99325892 | 2.06 | 2.115392 | 2.116434191 | 972.5759 | 12221.74 | 0.8 | 0.005934 | 0.000942 | 0.941189 | 8.005 | 0.004522 | 0.624522
8 | 0.787171 | 7.8702 | 11 | 0.055 | 17.956 | -0.017669213 | 17.93833079 | 2.20 | 2.262641 | 2.26375539 | 1103.575 | 13867.92 | 0.8 | 0.006305 | 0.001001 | 1.000904 | 8.1025 | 0.004751 | 0.624751
9 | 0.825038 | 8.2488 | 29 | 0.145 | 17.811 | -0.017508982 | 17.79349102 | 2.37 | 2.449584 | 2.450789282 | 1234.574 | 15514.1 | 0.8 | 0.006541 | 0.00103 | 1.029072 | 8.2 | 0.004827 | 0.624827
10 | 0.860205 | 8.6004 | 60.3 | 0.3015 | 17.5095 | -0.020785464 | 17.48871454 | 2.58 | 2.686319 | 2.687914917 | 1347.687 | 16935.52 | 0.8 | 0.006567 | 0.001006 | 1.00533 | 7.3175 | 0.005284 | 0.625284
11 | 0.891231 | 8.9106 | 96.1 | 0.4805 | 17.029 | -0.023689886 | 17.00531011 | 2.82 | 2.982745 | 2.984822132 | 1460.8 | 18356.94 | 0.8 | 0.006501 | 0.000956 | 0.955722 | 6.435 | 0.005712 | 0.625712
12 | 0.917316 | 9.1714 | 131.9 | 0.6595 | 16.3695 | -0.026112672 | 16.34338733 | 3.11 | 3.348745 | 3.351418728 | 1573.913 | 19778.36 | 0.8 | 0.006363 | 0.000898 | 0.897347 | 5.5525 | 0.006215 | 0.626215
13 | 0.93896 | 9.3878 | 170.1 | 0.8505 | 15.519 | -0.027922653 | 15.49107735 | 3.43 | 3.799554 | 3.802976424 | 1687.026 | 21199.77 | 0.8 | 0.006174 | 0.000835 | 0.834234 | 4.67 | 0.00687 | 0.62687
14 | 0.959834 | 9.5965 | 211.7 | 1.0585 | 14.4605 | -0.040794975 | 14.41970502 | 3.80 | 4.358101 | 4.364261097 | 1763.496 | 22160.73 | 0.8 | 0.005829 | 0.000756 | 0.755167 | 3.8725 | 0.0075 | 0.6275
15 | 0.981168 | 9.8098 | 261.2 | 1.306 | 13.1545 | -0.050552842 | 13.10394716 | 4.22 | 5.065674 | 5.075435498 | 1839.966 | 23121.68 | 0.8 | 0.005486 | 0.000677 | 0.676461 | 3.075 | 0.008461 | 0.628461
16 | 1.002972 | 10.0278 | 324.8 | 1.624 | 11.5305 | -0.056094536 | 11.47440546 | 4.68 | 6.00179 | 6.016442434 | 1916.437 | 24082.63 | 0.8 | 0.005151 | 0.000591 | 0.590903 | 2.2775 | 0.009978 | 0.629978
17 | 1.025267 | 10.2507 | 403.9 | 2.0195 | 9.511 | -0.055988965 | 9.455011035 | 5.19 | 7.330293 | 7.351964736 | 1992.907 | 25043.58 | 0.8 | 0.004829 | 0.0005 | 0.499471 | 1.48 | 0.012979 | 0.632979
18 | 1.048061 | 10.4786 | 501.4 | 2.507 | 7.004 | -0.048388078 | 6.955611922 | 5.75 | 9.470965 | 9.503851283 | 2069.377 | 26004.54 | 0.8 | 0.004522 | 0.000399 | 0.398959 | 0.6825 | 0.022482 | 0.642482
By interpolation
Total power loss on the surface is about 0.52 MW (≈ 2.7%)

## Slide 26: optimisations
ηRF ≥ 97.5 %
|tfill – 245 ns| ≤ 5 ns
Pin = 15 MW
Beam dynamic (Avni Aksoy): RB = 49 mm, N = 19 cells
Borrowed from Rolf

## Slide 27: Accelerating structure efficiency
For constant-impedance structure
It shows that for higher efficiency we need increase “r*Q0*vg”. For the electric coupling when you increase r, the vg will decrease. But with the magnetic coupling we can increase both together. Alexej reached the same equation and his structure efficiency is about 1% more than Rolf’s structure.

## Slide 28: Full beam loading in Constant impedance TWS
Efficiency in steady-state:
Full beam loading condition:
In order to maximum efficiency means maximum relative beam loading parameter at the full beam loading condition: => Maximum R’*vg*Q0
Borrowed from Alexej

## Slide 29: Future plans
Construction of the first SHB
Finishing the beam dynamic study
Design and construction of the second and third SHBs
Design and construction of the TW Buncher
Finishing the design of accelerating structures like HOM dampers and a prototype construction.
Prebuncher : Shahin showed the prebuncher decreases the satellite population.
RF photocathode gun : Next subject by Mohsen

## Slide 30: RF Source for SHBs
L3 Electronics: IOT
PSI: Solid-state amplifier
India : Solid-state amplifier