## Slide 1: Proposal for LHC BLM Disabling Rules after LS1
Pre-LS1:
A maximum of one IC per beam and quadrupole magnet allowed to be disabled. If one arc IC is disabled in the half cell n, the corresponding monitor of the same family in the half cells n-2, n+2 and n+4 (counted in beam direction) shall remain operational.
After LS1:
A maximum of one IC per beam and quadrupole magnet allowed to be disabled. If one arc IC is disabled in the half cell n, the corresponding monitor of the same family in the half cells n-2, n+2 and n+4 (counted in beam direction) shall remain operational.
In addition, one dipole-dipole interconnect IC per half-cell can be disabled, but only if no neighboring quadrupole monitor is disabled.
Re-location of 2nd position quadrupole BLM to the close-by dipole-dipole interconnection

## Slide 2
Pre-LS1:
In the LHC dispersion suppressor no monitor shall be disabled.
In the LHC LSS all monitors shall remain operational on the triplet magnets (Q1, Q2 and Q3).
All monitors at collimators and absorbers, and all monitors in IR3 and IR7 shall remain operational.
At least 2 monitors per beam shall remain operational on each LSS quadrupole.
Disabling of any other LSS monitor or another special monitor will have to be decided by the MPP representative and the BLM representative on a case-by-case basis.
After LS1:
All stays the same with the exception of:
 At least one monitor per beam shall remain operational on each quadrupole.

## Slide 3: Text Changes to the Document LHC-OP-MPS-0012