## Slide 1: Accelerators for Medical and Industrial Applications JUAS Archamps, March 4th 2014 Wiel Kleeven
MID 42328

## Slide 2: Organization of the lecture
Intro: About IBA
Part 1: Radioisotopes for medical applications
  Diagnosis and molecular imaging
  Radioisotopes for cancer therapy
Part 2: Cyclotrons for Isotope production
Part 3: Particle therapy of cancer
Part 4: The ProteusOne and S2C2 project
Part 5: Industrial applications of electron beam technology

## Slide 3: Foreword
In this lecture, I cannot present an exhaustive overview of all possible applications of accelerators
I will mainly limit myself to subjects where IBA has first hand experience

## Slide 4: Belgium has a tradition and important know how in civil nuclear applications
Belgium is one of the first European countries to install a cyclotron in 1947
SCK/CEN Research centre for nuclear energy (MOL), founded in 1952
Cyclotron Centre at LLN was started in 1970
Yoke of first cyclotron in Belgium
CRC CYCLONE-110
Thomson-CSF
p 65 MeV, d 50 MeV, a 110 MeV

## Slide 5: Foundation of IBA
1986 => spinoff from the CRC at UCL (Catholic University of LLN)
Start of IBA => Cyclone 30: a revolutionary cyclotron for medical isotopes => 5 x more output and 3 x less power consumption
Founder Yves Jongen currently IBA Chief Research Officer and recognized global leading accelerator expert

## Slide 6: The origins of IBA
The initial company ambitions in 1986 were modest:
  Build one cyclotron per year
  Maximum 15 employees
  Business of 1.5 to 2 M€ per year
  Getting rich was not part of the initial objectives, but having fun clearly was…
  …and in this respect, we were quite successful !
6

## Slide 7: The IBA Group in 2014
1200 employees worlwide
Turnover > 220 M€ and growing steadily every year
More than 300 systems (200 Cyclotrons) installed
Not anymore just a cyclotron company, but a company focused on medical technology for the fight against cancer:
  Cancer diagnostic: molecular imaging
  Cancer treatment: Particle therapy & dosimetry
More than 400 patents in use
Listed on Euronext Brussels
http://www.iba-worldwide.com
7

## Slide 8: IBA Today: Centering on the fight against cancer
Particle Therapy
Pharmaceuticals
Radiopharmaceuticals
Molecular Imaging
Nuclear Medicine (diagnostics & therapy )
Proton Therapy is increasingly considered as the ultimate radiotherapy for cancer due to its superior dose distribution
Dosimetry
Dosimetry equipment to measure and calibrate radiation dose for
Radiotherapy
Radiodiagnostics
Accelerators
Cyclotrons
To produces Radioisotopes
E-beam / X-rays
To irradiate / treat many industrial products
8
Notes: 8

## Slide 9
PART I:
Radioisotopes for Medical Applications
9

## Slide 10: Part I-A: radio-isotopes for medical diagnosis
SPECT: Single Photon Emission Computed Tomography
PET: Positron Emission Tomography
Molecular Imaging

## Slide 11: How is imaging done with radio-tracers ?
2 photons of 511keV
( β+ annihilation )
β+ emitter
γ emitter
Single photon
11
SPECT
PET
A camera (Gamma or PET) detects the photons emitted from the body and computes 3D distributions of the radio-activity
Radio-isotope

## Slide 12: The use of Radio Isotopes for medical imaging
Radio tracers can be used to label a specific bio-chemical molecule.
They allow to see metabolism
  X-ray scan or MRI are better to see the anatomy (structure)
Nuclear medicine (imaging of metabolism using molecules labeled with an appropriate radioisotope) is therefore not in competition, but in complement of imaging techniques such as X-ray, X-ray CT-scan or MRI.
12

## Slide 13: Metabolic versus anatomic imaging
MRI
PET
Anatomic View
(Tissue-structure)
Metabolic imaging
(Biological-function)

## Slide 14: The three body planes
Coronal => frontal
Sagital => side
Transverse

## Slide 15: Metabolic and anatomic imaging combined: fusion of SPECT and CT to improve image quality
15
SPECT
fuzzy
CT
clear
SPECT/CT
Improved resolution
Coronal (front) view
Sagital (side) view
Transverse view

## Slide 16: How is imaging done with radio-tracers ?
Single photon isotopes (SPECT)
The imaging of single photons emitters requires:
  a collimator (causes a loss of efficiency !).
  a position-sensitive detector (with good detection efficiency): the Gamma (or Anger) camera.
The image obtained is a projection.
Multiple (perpendicular) projections can be mathematically correlated to produce a 3D representation.
SPECT (Single Photon Emission Computed Tomography).
16

## Slide 17: How is imaging done with radio-tracers ?
Positron emitting radio-isotopes (PET)
The emitted positron travels a few millimeters, then meets an electron and annihilates, emitting two anti-parallel photons of 511keV.
These two photons can be detected in coincidence by a ring of detectors surrounding the region of interest.
One knows then that the origin of the photons is on the line connecting the two detectors.
Several detections allow to locate the source.
By mathematical reconstruction, a 3D representation of the activity can be obtained.
PET (Positron Emission Tomography).
17

## Slide 18: How to select a good single-photon radio-tracer?
The energy of the emitted photon
  Low enough to keep a good detector efficiency
  Low enough in order to achieve good collimation
  High enough to cross the body tissue
  100 keV < E < 300 keV is generally the optimum

## Slide 19: How to select a good single-photon radio-tracer ?
The half-life:
  Short enough to minimize the patient’s exposure
  Long enough to allow industrial production and distribution to the hospitals
  Practically 10h < T1/2 < 100h is roughly best
  Generators are great too !
  99Mo (66 hours) = 99Tcm (6 hours)
  81Rb (4.6 hours) => 81Kr (13sec)

## Slide 20: How to select a good single-photon radio-tracer
The chemistry
  The radio-tracer should bind easily to organic bio-molecules of interest
  Essential bio-chemical behavior of the molecule should remain intact after labeling
    Halogens (Fluor, Iodine), Technetium good;
    Noble metals (Gold)  difficult

## Slide 21: Detecting the radiation
Scintillator with photomultiplier tube
The incoming gamma ray interacts with the scintillator to produce photons. These photons dislodge electrons from the photocathode in the photomultiplier tube. These electrons are accelerated to the first nearest dynode where they dislodge further electrons. This process continues down the tube, resulting in a cascade of electrons. Multiplication factor can be up to 108
21

## Slide 22: Detecting the radiation
Scintillator with photomultiplier tube
22

## Slide 23: The SPECT gamma camera (Anger camera)
Anger camera
The collimator prevents photons that are not approximately perpendicular to the collimator holes from interacting with the detector.
The field of view for the detector element behind each hole of the collimator is divergent, so that in a gamma camera, spatial resolution degrades as the distance to the distance to the object is increased. Collimators are usually made of lead.
Typical dimensions: holes 3mm, walls 1mm, depth 40mm.
23

## Slide 24: The SPECT gamma camera (Anger camera)
The total sum of the voltages from each photomultiplier is proportional to the energy of the gamma ray interaction, thus allowing discrimination between different isotopes or between scattered and direct photons.
The location of the interaction between the gamma ray and the crystal can be determined by processing the voltage signals from the photomultipliers; in simple terms, the location can be found by weighting the position of each photomultiplier tube by the strength of its signal, and then calculating a mean position from the weighted positions. between scattered and direct photons.

## Slide 25: The SPECT gamma camera (collimator removed)
Photomultiplier tubes
Scintillator
25

## Slide 26: The SPECT gamma camera
26
Projections from different angles are taken by rotating the camera around the patient

## Slide 27: The SPECT gamma camera
3D Reconstruction
27
Multiple perpendicular projections
=> mathematical deconvolution
=> 3D distribution

## Slide 28: Nuclear reactions used for the production of medical isotopes
Nuclear Reactors  neutrons
  Neutron capture, as well as fission is performed in nuclear reactors (famous example: Mo-Tc generator)
Accelerators (often cyclotrons)  charged particles
  To bring a positive charged particle into a nucleus requires to overcome the Coulomb barrier and requires therefore the use of accelerators
  The compound nucleus formed is unstable, and immediately cools off by emitting neutrons or alpha particles (more rarely protons)
  Typical reactions are: (p, xn) , (p, ) , (d, xn)….

## Slide 29: Nuclear reactions for Radio-Isotopes production
Radioisotope Half-life Reaction Energy
(MeV)
201Tl 73.1 h 203Tl (p,3n) => 201Pb => 201Tl 17~28
67Ga 78.3 h 68Zn (p,2n) => 67Ga 12~28
111In 67.4 h 112Cd (p,2n) => 111In 12~28
123I 13.2 h 124Te (p,2n) => 123I 20~25
124Xe (p,2n) => 123Cs => 123I 20~30
124Xe (p,pn) => 123I
127I (p,5n) => 123Xe => 123I 45~68
29
A 30 MeV cyclotron can often do the job

## Slide 30: “Traditional” nuclear medicine
Technetium 99m, the most commonly used radio-isotopes in nuclear medicine is produced in reactors.
  90% of diagnostic studies in hospitals is done with 99mTc !
But a number of other, very important nuclear medicine radio-isotopes are produced with cyclotrons of higher energy.
  201Tl (Cardiac studies).
  123I (Thyroid, Various examinations).
For these longer life isotopes, international distribution is possible.
Large, very powerful cyclotrons are owned by radiopharmaceutical companies.
30

## Slide 31: The Cyclone 30
The cyclotron used by all radiopharmaceutical producers
31

## Slide 32: The positron (anti-electron)
Proton rich nucleus decays: proton → positron + neutrino.
Positron cools off by Coulomb interaction with electrons.
At thermal energy: positron annihilates producing two anti-parallel 511keV photons. (within 4mrad due to momentum conservation)
The finite positron range and the non-collinearity of the annihilation photons give rise to positional inaccuracy (±5mm).
32

## Slide 33: Coincidence detection in a PET scanner
In a PET camera, each detector generates a timed pulse when it registers an incident photon. These pulses are then combined in coincidence circuitry, and if the pulses fall within a short time-window, they are deemed to be coincident. A coincidence event is assigned to a line of response joining the two relevant detectors. In this way, positional information is gained from the detected radiation without the need for a physical collimator.
33

## Slide 34: The PET scanner
34
Coincidents events are grouped into projected images (sinograms) and sorted by the angle of view
Analogous to the projections obtained with Computed Tomography (CT) scanners
3D image re-construction is similar
PET scanner in a hospital
Currently available are
PET scanners integrated with CT: PET-CT
PET scanners integrated with MRI: PET-MRI

## Slide 35: Common positron emitting radioisotopes for PET
Radioisotope Half-life Positron Reaction Energy
(min) energy (MeV)
(MeV)
11C 20.4 1.0 14N (p,a)=> 11C 5=>16
13N 9.96 1.2 16O (p,a)=> 13N 8=>16
12C (d,n)=> 13N 3=>8
15O 2.07 1.7 15N (p,n)=> 15O 5=>14
14N (d,n)=> 15O 3=>8
18F 109.8 0.6 18O (p,n)=> 18F 5=>14
35

## Slide 36: FDG = Fluoro-Deoxy-Glucose
Most commonly made PET scan (90% of cases) is done with 18F-FDG (Fluoro-Deoxy-Glucose)
Metabolic activity by virtue of glucose uptake in tissue
This tracer is mainly used to explore the possibility of cancer metastasis
In glucose one OH-group is replaced by a 18-F atom
Both atoms have about the same size =>
Bio-chemical behaviour almost not altered

## Slide 37: FDG was used to study brain function
PET also allowed for fundamental medical research

## Slide 38: Cancer imaging with PET
18F FDG
45 minute scan time
normal heart, bladder.
normal kidney, brain.
colon tumor.
metastatic liver lesions.
38

## Slide 39: PET Scan - Response to therapy => cancer staging
Post Chemotherapy
Staging PET Scan
31 yo female with newly diagnosed Non-Hodgkin‘s Lymphoma
39

## Slide 40: Production and Application of PET radio-isotopes
Cyclotron Beam
Target
Target materials
H218O enriched (  18F)
H216O natural (  13N)
14N natural (  11C)
14N natural (  15O)
Radioactive products
18F, 13N, 11C, 15O
Labeled compounds
18FDG, 13NH3 , 11CO2 , 15O2
Injection
PET Scan

## Slide 41: IBA Molecular
200 PET & SPECT Cyclotrons sold worldwide to Hospitals, R&D centers, Radiopharma companies
33 facilities Worldwide producing Radiopharmaceuticals…
… distributed daily to
hospitals
41

## Slide 42: 52 PET Radiopharmaceuticals Production Facilities
Operational
In construction
Asia: 9
8 operational
1 in construction
USA+Canada: 17
16 operational
1 in construction
IBA realized many facilities and made alliances to enlarge network for distribution of future new drugs.
These facilities were sold last year but presently IBA is still connected via share-holding
EUROPE – Mid-East: 26
23 operational
3 in construction
Partnership
42

## Slide 43: Part I-B: Cancer therapy with radio-isotopes
Systemic radio-isotope therapy
Brachytherapy

## Slide 44: Four different types of radiation therapy
External beam radiation therapy (teletherapy)
  Radiation source is external (like proton therapy)
Brachy therapy:
  Sealed radioactive sources placed precisely in the tumor
  Can use temporary or permanent placement of radioactive sources
Systemic radiation therapy
  Radioistopes are given by infusion or by oral ingestion
BNCT: Boron Neutron Capture Therapy
  mixture of 1 and 3.

## Slide 45: Systemic radiation therapy
When the cancer is not limited to a well defined, primary tumor, systemic therapies can be used.
A form of targeted therapy. Targeting can be obtained by:
  Isotope chemical property. Example: iodine => thyroid gland
  Attach isotope to molecule or antibody that finds the target
    Iodine labeled MIBG to treat neuroblastoma (brain tumor-children)
    Hormone-bound Lutetium-177 or Yttrium-90 for neuroendocrine tumors
Injection of Yttrium-90 radioactive glass microspheres
  Liver tumors or metastatis. Sphere diameter about 30 mm
Treatment of bone-metastasis with Strontium-89
Alpha-particles or Auger electron emitting radio-isotope are often preferred because of short range of dose delivery.

## Slide 46: Pairs of radioisotopes for systemic therapy
Diagnostic (PET) RI | Therapy RI
124I | 131I
86Y | 90Y
64Cu | 67Cu
Etc! | 
46
Biochemical properties of pairs are exactly the same
PET-study allows quantitative diagnostics of distribution and uptake of the labelled molecule
With this information the actual delivered dose of therapeutic treatment can be predicted
Problem of dosimetry and treatment planning: how to assess the radiation dose received by the tumor and by the healthy organs at risk.

## Slide 47: Brachy therapy
Dose is delivered by placing the radiation source directly inside the area requiring treatment
Commonly used for cervical (uterus), prostate, breast and skin cancer
Irradiation affects only a very localized area => healthy tissues are spared
Much higher doses can be delivered. For comparison:
  Proton therapy: about 40 Gray
  Prostate brachytherapy: about 100 to 150 Gray
Brachytherapy can often be completed in less time
  Reduce the possibility of recovery of cancer cells between treatment intervals

## Slide 48: Brachytherapy
Theragenics
IBt
Local irradication of tumors by sealed radioactive implants placed directly inside the cancerous tissue
48

## Slide 49: Prostate brachytherapy with Pd-103 or I-125
49
Seeds placed with 3D precission verified with ultrasound probe
Seeds are not harmfull and can stay in place after treatment

## Slide 50: Pd-103 vs. I-125
103Pd 125I
Half-life (days) 16.97 60
Photon energy (keV) 20~23 27~35
Half-value-layer (mm.Pb) 0.008 0.02
Total delivered dose (Gy) 115 160
Initial dose rate (cGy/hr) 20~24 6~10
50