## Slide 1: OTR Interference test in CTF3
BE-BI-PM

## Slide 2: Background
R&D on beam size measurements techniques: Optical Diffraction Radiation (ODR – non invasive) and high resolution OTR.
Since Dec. 2012: ODR installation at CESR (Cornell) to perform beam size measurements at 2 GeV (plus test for materials, alignment, experimental procedure etc. )
Plan to complement with high resolution ODR at ATF2 (KEK)

## Slide 3: ODR Interference
3
SR mask
target
Mask (FW) and target (BW interference
Actually an ODR Interference experiment
Cianchi et al, PRST 14 102803 (2011)
Fiorito and Rule, Nucl. Instr. and Meth. in Phys. Res. B 173, 67-82 (2001)

## Slide 4: ODR interference - continued
When ODR screen distance is << than coherence length : fields interfere coherently i. e. signal only when mask, target have different width.
Need for simulation tool of interference: Zemax, physical propagation (B. Bolzon, T. Aumeyr).
Need for an experimental benchmark

## Slide 5: OTR interference
Experimental results : Wartski (1975) for distances >> Lc
Califes: Lc ≅ 2.5 cm @ 200 MeV, l = 500 nm
Ideal to study the coherent regime

## Slide 6: OTR interference
Vertical position of OTR screen assembly determines distance
Same ODR geometrical configuration
Single screen OTR
Between 0.5 and 1 Lc fourfold increase of OTR signal

## Slide 7: Installation - 1
c

## Slide 8: Installation - 1
c
299 mm segment
Small beam size (down to 50 um)

## Slide 9: Installation - 1
Installation incompatible with new module
Install during winter shutdown, remove in summer 2014
Critical item: 9 weeks delivery for actuator

## Slide 10: Installation - 2
Modification of an existing MTV (390).
Feasibility to be studied

## Slide 11: Summary
An OTR interference test is proposed in Califes/TBTS line
As stand-alone: still possible (but critical) during winter shutdown. Not compatible with new module
As modified MTV chamber. No time constraints, feasibility to be studied.