## Slide 1: Diamond Detector Test Stand @ CALIFES
F. Burkart, O. Stein
TE-MPE-PE, LHC machine protection

## Slide 2: Diamond Detectors
5cm
4cm
Bias voltage, LEMO
Signal, SMA
Nanosecond time resolution.
Radiation hard.
Wide dynamic range (1e – 5E9e).
E

## Slide 3: Diamond Detectors
5cm
4cm
Bias voltage, LEMO
Signal, SMA
Nanosecond time resolution.
Radiation hard.
Wide dynamic range (1e – 5E9e).

## Slide 4: Diamond Detectors installed at LHC
14 dBLMs installed along the LHC.
Diamond type: pCVD (cividec) 10 mm x 10 mm, wire bonded (8@LHC).
Analysis of dBLM data lead to e.g. a better understanding of UFO-events.
BQM

## Slide 5: Application of Diamond Detectors
Installed in the LHC to resolve bunch-by-bunch losses
  IR 2, 3, 4, 6, 7, 8
  Abort gap monitoring.
  Detection of ultra-fast losses (< 3 LHC turns).
Used as beam instrumentation for accelerator equipment damage tests in the HiRadMat-facility.
  High radiation / high fluence environment.
  Used for alignment of equipment to the beam.
  Online monitoring of beam impacting on material.

## Slide 6: HiRadMat – damage experiment single bunch
Carbon target
1.5E11 protons
Bunch length: 0.5ns

## Slide 7: HiRadMat – damage experiment multi-bunch
50 ns
Copper target
1.5E11 protons
Bunch length: 0.5ns
Bunch spacing: 50ns

## Slide 8: LHC – UFO event
Event, ~1ms
Bunch train, ~10us
Single bunches

## Slide 9: Diamond Detectors of MPE
3x100 mm thick diamond detectors (used in HiRadMat damage experiments)
  (Prototyp; designed with CIVIDEC for high-fluence experiments).
2x500 mm thick diamond detectors
  Standard LHC-type detector

## Slide 10: What we want to do …
  Improve understanding of measurement data taken in HiRadMat.
  Detector characterization:
  Measure charge collection distance (CCD).
  Evaluate efficiency of detector.
  Linearity of diamond detectors.
  Sensitivity and saturation limits.
Diamond detector studies on polarization effects.
Influence of supply capacitance on signal decay.
Minimum time resolution for detection.

## Slide 11: Experimental equipment
Detector, PCB
Signal, SMA
HV, LEMO
Detectors,
Detector holders,
Stage system for alignment,
Beam screen with camera between Detector and Dump,
Scope.

## Slide 12: Technical drawings
BPM
Beam screen
Beam dump
detectors

## Slide 13
Beam screen
Dipole
magnet
BPM
Beam dump

## Slide 14: Installation scheme (1/2)
Screen station
Window
dBLM
Screen
Beam
Beam
Dump
X- stage
XY- stage system
Side
Top
Optical rail

## Slide 15: Installation scheme (2/2)

## Slide 16: Fluence [charged particles/cm2/pp]
Fluence [charged particles / cm2 / pp]
Assumptions:
200 MeV electrons
2 mm x 2 mm spot size
0.1 mm aluminum foil as beam window
PRELIMINARY

## Slide 17: Energy deposition in aluminum foil
Energy deposition [GeV / cm3 / pp]
Assumptions:
200 MeV electrons
2 mm x 2 mm spot size
0.1 mm aluminum foil as beam window
PRELIMINARY
Estimated damage limit 1000bunches à 1E10e.

## Slide 18: Collaboration with BE-BI
First step to medium - / long-term test stand.
Possibilities at CALIFES:
  dBLM tests.
  Test of electronics, DAQ.
  Test of high-intensity beam loss monitors.
  Radiation-hardness tests.
Collaboration: Bernd Dehning, Eduardo Nebot (BE-BI).

## Slide 19: To be specified:
Setup layout:
  Support construction, installation of rail.
  Cabling Patrick Lelong.
Beam pipe modification:
  Installation of beam window.  Esa Puja.
Schedule for installations.
Beam parameters at Detector (Intensity, Monitoring, Beam size)
Beam dump as Faraday cup.
Radiation issues / shielding.
Other protection issues?
  Interlocking for dipole magnet.

## Slide 20
Thank You for your attention!
Any Questions?

## Slide 21: Beam Parameters CALIFES
Electrons @ ~200MeV.
Intensities from (107 ?)- 1010 electrons per shot.
1-300bunches
Bunch length: 4ps
Adjustable beam sizes < 100mm sigma.
Beam profile measurements (beam screen, 50cm upstream of detector installation).
Beam current measurements (Faraday-Cup (beam dump block) / WCM / BCT).
BPMs.

## Slide 23: Beam profile in distance of beam window

## Slide 24: Charge collection distance

## Slide 25: Time schedule
Installation in January?