## Slide 1: AD-4 Status Report 2013
Biological Effects of Antiprotons
Are Antiprotons a Candidate for Cancer Therapy?
Additional ontributions to phase two:
University of Athens, Queen’s University Belfast
German Cancer Research Center Heidelberg
Universita d’Insubria Como, University of Umeå
Michael H. Holzscheiter
The ACE Collaboration

## Slide 2
Dose and tumor control are limited due to organs at risk.
Dose (arb. Gy)
Probability (%)
Tumor control
Therapeutic
window
Complications
Rationale for Conformal Radiotherapy

## Slide 3: The AD-4 Experiment at CERN
ANALYSIS:
Study cell survival in peak (tumor), plateau (skin), and along the entire beam path. Compare the results to protons (and carbon ions)
INGREDIENTS:
V-79 Chinese Hamster cells embedded in gelatin
Antiproton beam from AD (126 MeV)
METHOD:
Irradiate cells with dose levels to give survival in the peak is between 0 and 90 %
Slice samples, dissolve gel, incubate cells, and look for number of colonies
V79
Developed by Ford and Yerganian in 1958 from lung tissue of a young male Chinese Hamster (Cricetulus griseus)

## Slide 4
Final Analysis of Data
Biology
Physics
Cell Count:
cells plated
cells counted
PE from control
PE from fit
Potential Errors:
Fitting Algorithm
Stability of fit
Redo dose calculations
Refine geometries
New input files
Run all relevant years using same FLUKA release
Fluka issues
Benchmark Experiment
no longer in agreement?
Combine data set
Extract RBE vs. Depth

## Slide 5
The Gel-Tube Method

## Slide 6
Biological Analysis Method
RBEpeak/plateau = 1.52

## Slide 7
Final Analysis of Data
Biology
Cell Count: cells plated ✓ cells counted ✓ PE from control ✓
Response to X-rays ✓
Response to Reference Radiation
Combined data from 2008, 2010, and 2012
DSF=10% = 5.3 Gy
PE from fit
Potential Errors: Fitting Algorithm Stability of fit

## Slide 8
Final Analysis of Data
Biology
Physics
Cell Count: cells plated ✓ cells counted ✓ PE from control ✓
Response to X-rays ✓
PE from fit
Potential Errors: Fitting Algorithm Stability of fit
Redo dose calculations
Refine geometries ✓
New input files ✓
Re-Run all relevant years
Fluka issues
Benchmark Experiment no longer in agreement?
Which version to use???
Sensitivity towards diff. versions
Combine data set
Extract RBE vs. Depth

## Slide 9
Available Data Sets

## Slide 10
Physical dose calculations requires exact knowledge of beam parameters and geometrical settings as input to FLUKA
To compare different years all dose calculations have to be repeated using identical release of FLUKA package.
Different years had (slightly) different set-ups and geometric effects need to be corrected for.
Do changes in FLUKA necessitate new benchmark measurements to decide which version is best suited for the experiment?
RBE Analysis for Antiprotons

## Slide 11: Influence from Geometry
Uncertainties in placement of degraders:
2%

## Slide 12: Influence from Geometry
Simplification in material arrangement outside of direct beam
(Approximate beam monitor by simple plane)

## Slide 13: Influence from Geometry
Beam definition using EBT-2 GafChromic Film:
For lack of better knowledge we assume virtual source position, beam spot size, and beam divergence to produce spot on EBT film
Estimated beam divergence from mechanical beam line design is maximal 4 mrad
FLUKA simulations show that the effect is small
unless extreme (unrealistic) cases are used
< 4%

## Slide 14
21%
Influence from FLUKA Version
Effect of FLUKA Version on Depth Dose Profile (2)

## Slide 15
Influence from FLUKA Version
Effect of FLUKA Version on Depth Dose Profile
10%

## Slide 16
Change of shape
Influence from FLUKA Version
Effect of FLUKA Version on Spread-out Bragg Peak

## Slide 17: Influence from FLUKA Version Current Status
FLUKA versions available to us are (STD) current official release (FLUKA 2011.2b.2 6/2013) (DEV) beta release provided to us by FLUKA team 7/2013 (DEV LIM) beta release with modified physics cards to better describe low energy processes and specifically antiproton annihilation at rest

## Slide 18
Dev Lim version 16% higher
Dev version 4% higher

## Slide 19
Can Benchmark help?
Construct 9-tablet Alanine stack and insert into water phantom. Include this set-up and all other experimental details in FLUKA input file.

## Slide 20
Can Benchmark help?
  Use different FLUKA versions to calculate dose deposited in Alanine pellets
  Use Hansen and Olsen track structure model to translate calculated dose into expected response of Alanine
?
?
?

## Slide 22
The Final Steps
Recalculate dose values for all years
Combine data from different years before fitting (higher quality fits)
Analyze for RBE using reference data
Estimate realistic error bars
Compare functionality of RBE of antiprotons and carbon ions
Use RBE vs. depth function for virtual treatment planning

## Slide 23
Closing Remarks
After 7 years of running with 500 MeV/c antiprotons we have collected a statistical significant pool of data.
Some problems in combining and interpreting these data continue, but the collaboration has decided on a clear path towards the final analysis
All tools for this analysis are in place and after a final decision concerning the FLUKA version of choice is reached can be applied immediately
This will result in a final publication on the RBE Depth Profile of antiprotons which then can be used for dose planning exercises and will be made available to the community at large.
The AD-4 Collaboration has decided to terminate the active phase of AD-4/ACE and requests no further beam time from CERN………

## Slide 24
…….we strongly feel a dedicated and well executed benchmark experiment would benefit the quality of the data and the final ACE result, the FLUKA team, and the community interested in absolute dosimetry using alanine for general particle beam therapy.
Irradiate 2 or 3 full stacks of alanine pellets covering the entire depth dose curve
Needed:
36 hours of beam time, including beam set-up and tuning at 500 MeV/c and return to normal operation.
BUT………

## Slide 25
THANK YOU
CERN for your continued interest and support
The AD Users community for your patience and the many incidences of generous help from all experiments during our runs
The AD Operations team for your relentless efforts to provide us with the best beam possible

## Slide 26
Can Benchmark help?
Measure SOBP Dose Profile with Alanine Alanine response is directly related to the absolute dose via Hansen and Olson track structure model using detailed information on particle energy spectrum of all fragments
Successfully used in 2006 benchmark experiment. Bassler et al., Nucl. Instr. and Meth. in Phys. Res. B 266 (2008) 929–936