## Slide 1
DE-KIT / GridKa LHC[OPN / ONE] Proposal
Bruno Hoeft DE-KIT / GridKa -- Network Site Manager LHCOPN OPS-WG Manager

## Slide 2: LHCOPN operation
LHCOPN
  Is a well understood network setup
  Dedicated ownership
    for each T0 – T1 link (stated in MOU signed by each Tier-1 Site)
    As well as T1 – T1 backup link
  All responsibilities of each link are defined
  Tight controlling/observing of constant operation
  solid maintaining  LHCOPN operational model defined
  Collaborating partners are very responsive to faults/errors at LHCOPN
  A very restricted number of Sites
    manageable # of peers, relatively small BGP table The lhcopn bgp routes are manageable
  The setup is very robust and can stand even severe interruptions

## Slide 3: LHCOPN / LHCONE quality difference
High capacity throughput
raw data distributed from T0 to T1 for long time storage (tape archive) and first calculation ( mDST)
Defined bandwidth requirement T0  T1
  After LS1 ~600MB
Constant and continuous availability  as defined in MOU
High capacity throughput
mDST access of between T2 and T1 incl. T2 and T2 (mesh / no hierarchical structure anymore)
  Data volume smaller (no raw data / mDST only/manly)
  Data for batchjobs only
    No defined bandwidth requirements
Good availability
No objections of including T1-T1 traffic
  If backup capacity is secured

## Slide 4: Historic link usage
LHCOPN CERN – GridKa/DE-KIT
LHCONE GridKa/DE-KIT
IT-INFN-CNAF – GridKa/DE-KIT
Backup link
FR-CCIN2P3 – GridKa/DE-KIT
NL-T1 – GridKa/DE-KIT
Backup link
GPI GridKa – X-Win sum
GPI GridKa/DE-KIT
GPI GridKa – X-Win
Link filled
Upgrade will be inevitable
Even during LS1
This two interfaces needs to get combined
- GPI  connecting GridKa to the none LHCONE Tier-[23] centers
Link filled not as much as LHCOPN
First thought about Upgrade requiered
GridKa /
DE-KIT
CERN
FR-In2P3
IT-INFN-CNAF
NL-T1
10GE
10GE
10GE
10GE
FNAL
2GE
GSI
DESY
UNI Wupertal
UNI Aachen
DFN
Géant
…
LHCOPN

## Slide 5: GridKa / DE-KIT planned network upgrade in 2014/2015
- 100G interface
- Multiple dynamical seperated subinterfaces (VLANs)
- Protocol
- tcp - udp - icmp -…
- replacment of CBFs :
- link via Géant
- one CBF to FR-CCIN2P3 remains at least as long as the 100G deployed infrastructure does not includ redundancy
- Layer-2 P2P (VLAN separate)
  DE-KIT – CERN
  KIT – DFN - GÉANT – CERNlight/Switch – CERN BGP routing at DE-KIT (DFN Layer-2 VLAN only)
  NL-T1 --> KIT – DFN - GÉANT – SURFnet – SARA BGP routing at DE-KIT (DFN Layer-2 VLAN only)
  INFN-CNAF --> KIT – DFN - GÉANT – GARR – CNAF BGP routing at DE-KIT (DFN Layer-2 VLAN only)
  Layer-3 (HEPPI / LHCONE VRF)
  P2P – CBF – DE-KIT – FR-CCIN2P3  last resort
  ? upgrade to 100G  Triangel DE-KIT – IN2P3 – CERN ?

## Slide 6: Services to evolve
Information dashboard with several information layers
  From abstract information layer (red/green dashbord)
  Successive drill down to detailed “error” information
  e.g.: red/green dashboard  info about T1-T1: GridKa--IT-INFN-CNAF end2end link
    Splitting into DFN/Switch/GARR NREN Domains
    May be not as detailed as the e2emon of Géant showing red/green down to a single device
  Combine and consolidate information of different information systems
    Dashboard / waethermap / perfsonar / monalisa / … at one location/”web portal”