## Slide 1: Could we abandon the HW LLT option and save money (and allow possible further improvements to the upgraded muon system)?
Alessandro Cardini
of behalf of the Muon Upgrade Group

## Slide 2: The muon upgrade
Get ready for the 40 MHz readout
  Muon detector will not be modified, M1 will be removed
  nODE (with nSYNC ASIC) for an efficient detector readout by TELL40
  nPDM and nSB for an efficient chamber pulsing and control using GBT through GBT-SCA
  Ready @ LS2

## Slide 3: nODE architecture
nODE
DATA Path
Sync
nSYNC
Bunch cross synchr.
TDC
Hit format
Hist.
GBT interf.
Zero Supp.
GBT interf.
ECS/TFC
LVDS Receivers Translators
GBTx
Hit data serializer
VTTx Optical transmitter
GBT-SCA
Control
Monitor
VTRx Optical transceiver
GBTx
Data Ser/Des
VTTx Optical transmitter
GBTx
Hit data serializer
Sync
nSYNC
Bunch cross synchr.
TDC
Hit format
Hist.
GBT interf.
Zero Supp.
GBT interf.
Sync
nSYNC
Bunch cross synchr.
TDC
Hit format
Hist.
GBT interf.
Zero Supp.
GBT interf.
Sync
nSYNC
Bunch cross synchr.
TDC
Hit format
Hist.
GBT interf.
Zero Supp.
GBT interf.
LVDS Receivers Translators
LVDS Receivers Translators
LVDS Receivers Translators
LVDS Receivers Translators
LVDS Receivers Translators
Sync
nSYNC
Bunch cross synchr.
TDC
Hit format
Hist.
GBT interf.
Zero Supp.
GBT interf.
192 Input channels
Power section
Voltage regulators
DC/DC converter
Power up sequencer
Clock management
Clock driver
Phase adjust
Sync
nSYNC
Bunch cross synchr.
TDC
Hit format
Hist.
GBT interf.
Zero Supp.
GBT interf.
GBTx
TDC data serializer
GBTx
HIT data serializer
To TELL40
2 links simplex
To Trigger 2 links
simplex
To/from TFC 1 link
duplex

## Slide 4: Muon readout improvements
The reviewers of the muon upgrade electronics architecture suggested to include the “TDC info in the binary data stream”
We agreed on this. So in each nODE we are planning to have:
  4 links carrying full information (hit position and time) to DAQ
  2 links with only binary hit information for the HW LLT
By doing so:
  the number of Optical Links (and transmitter/receiver and readout boards) will increase roughly by 50%
  The nSYNC design complexity will increase

## Slide 5: Could we already discard the HW LLT option?
We are starting designing the nSYNC
We would like to define what we should include in it
We have to define the fibres we need and the amount of optical transmitter/transceiver to order (this order was already done, BTW)
And there is something more…

## Slide 6: The muon upgrade (revised)
Ongoing muon identification performance studies are suggesting that we could improve the situation with additional “small” changes to the upgraded muon system, although we have still to run detailed MC simulation to exactly quantify the improvements in performances at high luminosity
A further step currently under study, and ready for 2020:
  New pad detectors in most irradiated regions (M23R12)
  More IBs removed (in M2R3, for example)

## Slide 7: Possible new pad detectors
M2R1
  Rates as high as 600 kHz/cm2
  Currently mixed readout  384 logical pads but only 112 R/O channels
  We could envisage to readout 192 real pads (24 FEBs, like in M1R1, will fit) with current FEBs
M3R1
  Rates as high as 200 kHz/cm2
  Currently mixed readout  384 logical pads but only 112 R/O channels
  192 pads as above or even 96 pads (simplified installation, final performances to be studied)
M2R2
  Rates as high as 100 kHz/cm2
  Currently mixed readout  192 logical pads but only 112 R/O channels
  192 pad detector possible but many cables to be added  we should check if 96 pads are enough that would imply NO cables to be added  check muon performance
M3R2
  Not critical from the rate point of view
  Currently mixed readout  192 logical pads but only 112 R/O channels
  96 pads OK for dead-time, check muon performance

## Slide 8: Possible removal of additional IBs
We currently have 104 ODE in our system. According to PID Upgrade TDR, the removal of IBs in M5R4 will bring to 108 the number of needed nODEs
M2R3
  it’s already a pad detector  no important CARIOCA dead-time
  It seems however that there is a large contribution for dead-time coming from DIALOG due to the large number of channels OR-ed together to make the logical strips (to be carefully verified)
  If we remove all M3R2 IBs  + 16 nODEs
M3R3
  Not so critical, if we want to maintain it similar to M2R2 we need +16 nODEs
If we could afford it, we could also think of removing IBs in M2R4 (+16 nODEs) and in M3R4 (+16 nODEs)
The option of removing IBs is simple and not too expensive, and can improve the situation in regions where inefficiency is dominated by the DIALOG dead-time (where a lot of logical channels contribute to the creation of a logical strip)

## Slide 9: Conclusion
The design of part of the upgraded muon system electronics components depends on the still open options for the LLT
A software-only LLT will allow the simplification of some muon components and money savings
Further modification to the muon system, currently under study, will allow muon performance improvements at high luminosity, but they are likely to be incompatible with an hardware LLT