## Slide 1: GBTX: Tips for users
Pedro Leitão
On Behalf of the GBT Project Collaboration
12/06/2014
CERN, Switzerland

## Slide 2: Summary
GBTX: a brief review
  Mode/encoding
  Clock domains
  Configuration methods
  Power-up sequence
  Phase Adjustable Output Clocks
  E-links
    How to phase align the data of an e-link group
  Power consumption example
A simple case-study:
  GBTX transceiver (“master” GBTX) as clock source for multiple GBTXs transmitters

## Slide 3: GBTX: a brief review
Mode/encoding
  GBT Frame encoding
    Uplink and downlink
      80 data bits using 5 groups
      32 FEC bits
  Widebus mode encoding
    Uplink
      112 data bits using 7 groups
      No FEC correction
    Downlink uses GBT Frame encoding
  8B/10B encoding
    Uplink
      88 data bits using 5 ½ groups
      No FEC correction
    Downlink uses GBT Frame encoding
  Slow Control Information (IC and EC channels)
    Only works in transceiver mode and with GBT Frame or Widebus mode
    Both present in the uplink and downlink
      2 bits for the GBTX’s Internal Control (IC) channel
      2 bits for EC (SCA link)

## Slide 4: GBTX: a brief review
Clock Domains
  Receiver mode:
    The CDR locks to the backend’s clock
    This clock is used for the e-links transmitter and e-links clock
    The GBTX SERIALIZER can be turned off to save power
BACKEND
GBTX
FE
SER
E-RX
CDR
E-CLK
E-TX
REFCLK

## Slide 5: GBTX: a brief review
Clock Domains
  Receiver mode:
    The CDR locks to the backend’s clock
    This clock is used for the e-links transmitter and e-links clock
    The GBTX SERIALIZER can be turned off to save power
  Transmitter mode:
    The transmitter uses the REFCLK as a clock source; turning off the GBTX RECEIVER will save power
    The EPORT-RX uses the SER clock
BACKEND
GBTX
FE
SER
CDR
E-CLK
E-TX
E-RX
REFCLK

## Slide 6: GBTX: a brief review
Clock Domains
  Receiver mode:
    The CDR locks to the backend’s clock
    This clock is used for the e-links transmitter and e-links clock
    The GBTX SERIALIZER can be turned off to save power
  Transmitter mode:
    The transmitter uses the REFCLK as a clock source; turning off the GBTX RECEIVER will save power
    The EPORT-RX uses the SER clock
  Transceiver mode
    The CDR locks to the backend clock
    The SER uses the CDR clock and should only present a phase shift
  The GBTX mode is selected by input pins
BACKEND
GBTX
FE
SER
E-RX
REFCLK
CDR
E-CLK
E-TX

## Slide 7: GBTX: a brief review
Configuration methods
  There are two methods to communicate with the GBTX
    I2C
      Direct connection using a standard 7-bit addressing I2C (external pull-up resistors to 1.5V required)
      Can be connected to the SCA or to an external device for initial prototyping
      The GBTX is an I2C slave; the address 7’b000_0000 is used for general call
    Internal Control (IC) channel / External Control (EC) channel (SCA LINK)
      Requires an high-speed serial link with the GBTX in transceiver mode to work
      The high-speed serial link can be established using I2C or by a set of fused values which are loaded after a power-on reset
      An IC wrapper will be available for the GBT-FPGA for easy read/write access (RAM based)
    The two methods are mutually exclusive and are selected by one input pin
  The GBTX provides a two-wire link for the VTRX programming
  After the optimal configuration settings have been found, the GBTX can be fused in order to have the self-configuration feature enabled (3.3V power supply required for fuse programming)
  All GBTX in transceiver (“master” GBTX) mode should be fused so that they are operational on power-up

## Slide 8: GBTX: a brief review
Power-up sequence
Ready!
At this stage both the I2C and the IC channel are available
Power-on
isFused?
Load Fuses
Goes through the power-up SM, waits for ready signals
use IC channel? (input pin)
No high-speed link; GBTX is unreachable
Wait for config; write using I2C
YES
YES
Config Done?
Config is Done
NO
NO
Config Done?

## Slide 9: GBTX: a brief review
Phase Adjustable Output Clocks:
  8 programmable clocks
  40, 80, 160 and 320 MHz
  Phase shifts of 50 ps
  The clock source of the phase shifter’s PLL is mode dependent
    In Transmitter mode, the PLL locks to the REFCLK clock
    In Receiver mode, the PLL locks to the CDR clock
    In Transceiver mode, the PLL locks to the CDR clock
  In receiver/transceiver mode the phase shifter can be used as clock sources for others GBTXs in transmitter mode
  If phase adjustment of the clocks is not required, the e-link clocks can also provide a stable 40/80/160/320 MHz clock in phase with the source clock. This will help to reduce power

## Slide 10: GBTX: a brief review
E-links
  Consists of three differential signals
    dCLK (clock driven by GBTX)
    dOUT (data line driven by GBTX)
    dIN (data line from the front-end)
    Data rate input, output and clock rate can be set independently
      They can run at 40, 80, 160 and 320 (Mb/s and MHz)
    Programmable driving current
    Enable/disable on-chip 100Ω termination
  Due to the e-links serialization/deserialization architecture, data misalignment (between 40 MHz frame and e-links) can occur (e.g. bit-shifts)
  Programmable e-link transmitter (eportTX)
    The dOUT data is driven in anti-phase with the dCLK
    The front-end should sample the data in the rising edge; dual data rate is also possible
    Coarse phase adjustment (bit clock) has to be done either in the front-end or in the back-end
  Programmable e-link receivers (eportRX)
    Modes
      Static phase-aligner
      Automatic phase-aligner
      Trained phase-aligner
n+2
n
n+1
dOUT
dCLK

## Slide 11: GBTX: a brief review
  E-links receivers (eportRX)
    The phase aligner value will depend on the line length
    The data is delayed in order to have a fine-phase alignment (max. delay is 7/4Tbit)
    There are 15 taps available
dataRate
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
dIN
Data Rate Switch
sampleSelect [3:0]
samplingClock
Edge detection/phase aligner algorithm
SERdata

## Slide 12: GBTX: a brief review
  E-links receivers (eportRX)
    Only a fine-phase adjustment (max. 7/4Tbit) is available
    The automatic phase aligner mode is restricted between the [4; 11] tap
    After a fixed tap, it can vary ± 3 taps
    Coarse phase adjustment (bit clock) has to be done either in the front-end or in the back-end
  Automatic phase aligner process:
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
D[n]
0
1
2
3
4
5
6
7
8
9
10
11
12
D[n]
D[n]
D[n]
D[n]
D[n]
D[n]
D[n]
D[n-1]
D[n+1]
D[n-1]
D[n+1]
D[n-1]
D[n-1]
D[n-1]
D[n+1]
D[n-1]
D[n+1]
D[n-1]
D[n+1]
D[n-1]
D[n+1]
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
D[n+1]
D[n+1]
a)
b)
c)
d)
e)
f)
g)
h)

## Slide 13: GBTX: a brief review
  E-links receivers (eportRX) – How to data align a channel?
    Example:
      Group at 160 Mbit/s
      The automatic phase aligner mode is restricted between the [4; 11] tap
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
SER 40 MHz clock
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
Dn(3:0) = 0000
0000’h
SER 120bit frame

## Slide 14: GBTX: a brief review
  E-links receivers (eportRX) – How to data align a channel?
    Example:
      Group at 160 Mbit/s
      The automatic phase aligner mode is restricted between the [4; 11] tap
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
SER 40 MHz clock
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
Dn(3:0) = 1000
4848’h
1
0
0
0
Set the data to b‘1000’;
This will allow to identify the Dn(3) position
SER 120bit frame
0
1

## Slide 15: GBTX: a brief review
  E-links receivers (eportRX) – How to data align a channel?
    Example:
      Group at 160 Mbit/s
      The automatic phase aligner mode is restricted between the [4; 11] tap
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
SER 40 MHz clock
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
Provided enough transitions, the eportRX phase aligner locks
8181’h
Dn(3:0) = 1000
Set the data to b‘1000’;
This will allow to identify the Dn(3) position
SER 120bit frame

## Slide 16: GBTX: a brief review
  E-links receivers (eportRX) – How to data align a channel?
    Example:
      Group at 160 Mbit/s
      The automatic phase aligner mode is restricted between the [4; 11] tap
      Coarse phase adjustment (bit clock) is done in the front-end by pipelining the data
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
SER 40 MHz clock
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
Align the channels by bit-shifting the front-end output data
8888’h
Dn(3:0) = 1000
bitShift = 1
bitShift = 1
Provided enough transitions, the eportRX phase aligner locks
Set the data to b‘1000’;
This will allow to identify the Dn(3) position
SER 120bit frame

## Slide 17: GBTX: a brief review
  E-links receivers (eportRX) – How to data align a channel?
    Example:
      Group at 160 Mbit/s
      The automatic phase aligner mode is restricted between the [4; 11] tap
      Coarse phase adjustment (bit clock) is done in the front-end by pipelining the data
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
SER 40 MHz clock
D1(2)
D1(3)
D1(1)
D1(0)
D2(3)
D0(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
What if… it falls on the next bunch clock?
8888’h
Dn(3:0) = 1000
Provided enough transitions, the eportRX phase aligner locks
Set the data to b‘1000’;
This will allow to identify the Dn(3) position
SER 120bit frame
Align the channels by bit-shifting the front-end output data

## Slide 18: GBTX: a brief review
  E-links receivers (eportRX) – How to data align a group?
    Example:
      Implement a 4-bit LFSR pseudo-random pattern (overlaps every 16 words)
      Use the same pattern in the back-end and perform a bitwise XOR with the received frame
      Keep shifting the front-end output data until you have bitwise XOR = 4’b0000
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
D1(2)
D1(3)
D1(1)
D1(0)
D2(3)
D0(0)
SER 40 MHz clock
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
4-bit LFSR
Dn(3:0) = 4’LFSR
FE
4’LFSR
GBTX
BACKEND
(Internal [15:0] 4’LFSR)
bitwiseXOR
(received 4’LFSR)
What if… it falls on the next bunch clock?
SER 120bit frame

## Slide 19: GBTX: a brief review
  E-links receivers (eportRX) – How to data align a group?
    Example:
      Implement a 4-bit LFSR pseudo-random pattern (overlaps every 16 words)
      Use the same pattern in the back-end and perform a bitwise XOR with the received frame
      Keep shifting the front-end output data until you have bitwise XOR = 4’b0000
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
SER 40 MHz clock
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
What if… it falls on the next bunch clock?
4-bit LFSR
Dn(3:0) = 4’LFSR
bitShift = 4
FE
4’LFSR
GBTX
SER 120bit frame
BACKEND
(Internal [15:0] 4’LFSR)
bitwiseXOR
(received 4’LFSR)

## Slide 20: GBTX: a brief review
  E-links receivers (eportRX) – How to data align a group?
    Example:
      Implement a 4-bit LFSR pseudo-random pattern (overlaps every 16 words)
      Use the same pattern in the back-end and perform a bitwise XOR with the received frame
      Keep shifting the front-end output data until you have bitwise XOR = 4’b0000
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
SER 40 MHz clock
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
D0(2)
D0(3)
D0(1)
D0(0)
D1(3)
D-1(0)
What if… it falls on the next bunch clock?
4-bit LFSR
Dn(3:0) = 4’LFSR
bitShift = 4
FE
4’LFSR
GBTX
SER 120bit frame
BACKEND
(Internal [15:0] 4’LFSR)
bitwiseXOR
(received 4’LFSR)
  In order to use this method (data rate dependent):
  Add a unique pattern which enables you to identify the e-link MSB to your FE and BE
    e.g,
      10’b if 80 Mb/s
      1000’b if 160 Mb/s
      1000 0000’b if 320 Mb/s
  Add a 4-bit LFSR pattern for group/frame data alignment to your FE and BE
    e.g
      4LFSR[1:0] if 80 Mb/s
      4LFSR[3:0] if 160 Mb/s
      {4LFSR[3:0], 4LFSR[3:0]} if 320 Mb/s
  Perform the bitwise XOR using the whole group for group alignment
  The eportTX (e-link transmitter) can use the same method
  You only need to do this once – then you can save and reuse the same configuration
    e.g, use the eportRX trained phase aligner mode
  You can use the SCA to control the I2C channel of your FE

## Slide 21: GBTX: a brief review
Power consumption example
  Transciever mode
  GBT Frame
  All clocks enabled, multiple group data rates, I2C conn

## Slide 22: Study-case: GBTX transceiver as clock source
  GBTX transceiver as clock source for multiple GBTXs transmitters
BACKEND
“master” GBTX
(fused)
SER
xOSC
CDR
PhaseShifter Output
FE
dIN
dIN
dIN
CLK
SCA
eLink - SCA
SCOUT
SCCLK
SCIN
FE
Control
EPORTs
dIN
CLK
dOUT
I2C
Transmitter
GBTX
xPLL
Transmitter
GBTX
xPLL
Transmitter
GBTX
xPLL
Transmitter
GBTX
(opt. fusing)
xPLL
IC + EC channels
I2C
I2C

## Slide 23: Study-case: GBTX transceiver as clock source
  GBTX transceiver as clock source for multiple GBTXs transmitters
BACKEND
“master” GBTX
(fused)
SER
xOSC
CDR
FE
dIN
dIN
dIN
CLK
FE
Control
Transmitter
GBTX
xPLL
Transmitter
GBTX
xPLL
Transmitter
GBTX
xPLL
Transmitter
GBTX
(opt. fusing)
xPLL
IC + EC channels
PhaseShifter Output
SCA
eLink - SCA
SCOUT
SCCLK
SCIN
I2C
I2C
I2C
EPORTs
dIN
CLK
dOUT

## Slide 24: Study-case: GBTX transceiver as clock source
“master” GBTX
(fused)
FE
Control
EPORTs
dIN
CLK
dOUT
  GBTX transceiver as clock source for multiple GBTXs transmitters
BACKEND
SER
xOSC
CDR
FE
IC + EC channels
PhaseShifter Output
SCA
eLink - SCA
SCOUT
SCCLK
SCIN
I2C
I2C
I2C
Transmitter
GBTX
xPLL
Transmitter
GBTX
xPLL
Transmitter
GBTX
xPLL
Transmitter
GBTX
(opt. fusing)
xPLL
dIN
dIN
dIN
CLK

## Slide 25: Study-case: GBTX transceiver as clock source
  GBTX transceiver as clock source for multiple GBTXs transmitters
BACKEND
“master” GBTX
(fused)
SER
xOSC
CDR
PhaseShifter Output
FE
dIN
dIN
dIN
CLK
SCA
eLink - SCA
SCOUT
SCCLK
SCIN
FE
Control
EPORTs
dIN
CLK
dOUT
I2C
Transmitter
GBTX
xPLL
Transmitter
GBTX
xPLL
Transmitter
GBTX
xPLL
Transmitter
GBTX
(opt. fusing)
xPLL
IC + EC channels
I2C
I2C

## Slide 26: BACKUP SLIDES

## Slide 27: BACKUP SLIDES
  Align eportRX: find the correct position with the 4’LFSR
4-bit LFSR buffer
4’LFSR[0]
4’LFSR[1]
4’LFSR[2]
4’LFSR[3]
4’LFSR[4]
4’LFSR[5]
4’LFSR[6]
4’LFSR[7]
4’LFSR[8]
4’LFSR[9]
4’LFSR[10]
4’LFSR[11]
4’LFSR[12]
4’LFSR[13]
4’LFSR[14]
4’LFSR[15]
FE 4’LFSR
4’bitwiseXOR result
PositionArray
Pos[0]
Pos[1]
Pos[2]
Pos[3]
Pos[4]
Pos[5]
Pos[6]
Pos[7]
Pos[8]
Pos[9]
Pos[10]
Pos[11]
Pos[12]
Pos[13]
Pos[14]
Pos[15]
4’bitwiseXOR result
FE
BACKEND
GBTX
FE