## Slide 2
Is Pb54+ in LEIR limitted by space charge?
Michael Bodendorfer
May 20h, 2014
With the help of Django Manglunki, Maria-Elena Angoletta, Alan Findlay, Giovanni Rumolo, Simone Gilardoni, Elias Metral, Christian Carli, Sergio Pasinelli, Gerard Tranquille, Jerome Axensalva

## Slide 3
LEIR – Low Energy Ion Ring
From LINAC3 & to PS
Ecooler
Beam
Injection
Extr.
Septum
Extr.
Kicker
RF

## Slide 4
Why upgrade LEIR Pb54+ performance?
Parameter | Unit | LEIR 2013 run | LEIR Baseline upgrade | LEIR Full upgrade
Pb charge state | [-] | 54+ |  | 
Output Energy | [GeV/u] | 0.0722 |  | 
In/Out Bρ | [Tm] | 1.138 / 4.8 |  | 
Inject. to next machine | [-] | 1 |  | 
Bunches/ring | [-] | 2 |  | 
Charge at flat bottom | Charges | ~6.0x1010 | 6.0x1010 | 1.1x1011
Total extracted charge | Charges | ~5.4x1010 | 5.4x1010 | 8.6x1010
From: Performance of the injectors with ions after LS1
D. Manglunki for the LIU-Ions team, CERN, Geneva, Switzerland, 2013
All HI LHC experiments want by 2035: 10nb-1

## Slide 5: Machine specifications
Machine | Output Energy | Charge state
ECR ion source | 2.5 keV/n | …,29+,…
LINAC3 | 4.2 MeV/n | 29+/54+
LEIR | 72.2 MeV/n | 54+
PS | 5.9 GeV/n | 54+/82+
SPS | 176.5 GeV/n | 82+
LEIR Design Parameter | Value Injection Extraction | 
Length | 78m | 
brel.(Inj. ¦ Ej.) | 0.095 | 0.392
grel. (Inj. ¦ Ej.) | 1.0045 | 1.087
gtransition | 2.84 | 
ε*transv. (Hor.¦Vert.) | 6μm¦4μm | 0.65¦0.7μm
εlong. (Inj. ¦ Extr.) | 0.015eVs/u | 0.1eVs/u
Tune (Hor. ¦ Vert.) | 1.82¦2.72 | 1.82¦2.72
LEIR

## Slide 6: Optics
E-Cooling
Extraction
D=10m
D≅0
Ejection
Kicker 1
Quadrupole doublet
RF
D≅0
Injection
Bρ=1.14Tm
4.2MeV
Quadrupole triplet
Ejection
Kicker 2
D=10m
Bρ=4.8Tm
72.2MeV
Symmetry
Sextupoles

## Slide 7
6 injections. First at 215ms, then spaced 200ms. 200μs long.
Extraction
@ 2880ms
capture in H2, H4 @ 1780ms
Up to 50% beam loss
(Coasting beam)
B-field
Start of
Beam loss
BHN current [100A]
Standard LEIR nominal cycle: low energy beam loss.

## Slide 8
Finding a solution for LEIR
What we have found so far:
  Working point on 4th order resonance
  Transverse instability at RF capture
  Positive chromaticity in the vertical plane
  Beam loss associated to RF-capture rather than magnetic Ramp.

## Slide 9
1. Design tune: QH=1.82, QV=2.72
Qx - Qy = -1
2Qx - Qy = 1
4Qy = 11
Qx + 3Qy = 10
3Qy = 8
2Qx + 2Qy = 9

## Slide 10
2. LEIR Instability at RF capture and magnetic ramp
Before: -20ms
After: +20ms
Beam loss continues
1815ms
Beam loss starts here
Pickups output:

## Slide 11
3. LEIR chromaticity

## Slide 12: Elliminated working hypothesis “B-ramp”:
Start mag. ramp
Beam loss with advanced RF-capture
Beam dump
Start of
Beam loss
Advanced by 300ms
BHN current [100A]

## Slide 13
What can we do with this?
We can study the phenomenon without a magnetic ramp:
Flat bottom cycle
RF-capture with different beam parameters (emitt.)
Use of ionization pressure gages during beam loss
Elliminated working hypothesis “B-ramp”:

## Slide 14
Remaining working hypotheses for the LEIR low energy beam loss
Space charge
Direct / indirect
Tr. damper RF-capt.
Vert.
chromat. > 0
Electron cloud
Incoherent tune shift
Coherent
tune shift
Transverse instability
Head-Tail instability
Instability, outgassing
Cooling time sensitive?
H3/H6, H4/H8 -> beam loss?
Damper off:
Still loss?
Neg chrom. Still loss?
Pressure rise?
Can we eliminate further working hypotheses?
We are interested in refuting tests.

## Slide 15
Space charge limitation in LEIR?
During cooling?
At RF-capture?
Coasting beam

## Slide 16
Findings:
Clues from measurements:
  Working point on 4th order resonance
  Transverse instability at RF capture
  Positive chromaticity in the vertical plane
  Beam loss associated to RF-capture rather than mag. ramp
BHN current [100A]
4.
2.
3.
1.

## Slide 17
MD roadmap excerpt:
MD series with flat bottom cycle:
  Beam loss associated to RF-capture rather than magnetic ramp
    Try RF-capture with different beam parameters (bunch length and transverse emittances) to check the impact of space-charge.
    Capture at different harmonics than H2/H4
    Study the interaction of electron cooling and RF-capture.

## Slide 18
Summary and outlook
List of working hypotheses established
Working hypothesis of B-ramp eliminated
Flat bottom analysis ahead on MD roadmap
LEIR optical model with and without electron-cooler
PTC-Orbit simulation of:
  Flat bottom
  Multiturn injection
  RF-capture

## Slide 19
Thank you for your attention!

## Slide 20
3. Tune and chromaticity measurement after RF-capture
✗
Bad fit
Bad fit
RF capture
RF capture
Displayed
Displayed
✗
Coasting beam & Ecooling
Coasting beam & Ecooling
Beam
loss
Beam
loss

## Slide 21
3. Tune and chromaticity measurement after RF-capture
Good fit
RF capture
RF capture
Displayed
✓
Displayed
Good fit
(LSQR quadratic)
✓
Beam
loss
Beam
loss
Coasting beam & Ecooling
Coasting beam & Ecooling

## Slide 22
Good fit
Fit slop
(Linear chromaticity)
Residual of fit
Intensity
3. Horizontal chromaticity < 0 (after RF capt.) (Horizontal design chromaticy = -1)

## Slide 23
Good fit
Fit slope
(Linear chromaticity)
Residual of fits
Intensity
3. Vertical chromaticity > 0 (after RF capt.) (Vertical design chromaticy = -1)

## Slide 24: Overview
LINAC3 & LEIR

## Slide 25: Current scheme (“intermediate” in 2011, with 2013 performance)
PS (NO splitting) bunch spacing = 200ns
SPS at extraction, after 12 transfers from PS,
Batch spacing = 200 ns as well
LHC at injection, after 15 transfers from SPS
Pb ions / (future) LHC bunch
2.2 108
1.6 108
b* = 1 m -> L = 5.1026 cm-2 s-1
Harmonic number / Frequency
2
16–14-12-24 / 24-21-169
200 MHz
400 MHz
7 injections
2
Nb of bunches
2
24
358
3 108
5.5 108
LHC in collision
1.4 108
360
LEIR:(1.1 109 Pb ions / 3.6 s)

## Slide 26
TWISS parameters (MADX)
From: Low Energy Ion Ring LEIR, C. Carli, 14th March 2012

## Slide 27
Electron cooling: Cooling rate
Less hot ions
Hot electrons
Cold electrons
Hot ions
Uc
Uground
Electron cooling
Ue
Ui
Uc = Cathode potential
Ue = Space charge potential of electron beam
Ui = Space charge potential of ion beam
Δveli
Toroidal magnet
Ie >> Ii
Cooling rate:
How quick?

## Slide 28
Less hot ions
Hot electrons
Cold electrons
Hot ions
Ekin_e=qe-(Uc+Ue+Ui)
vele
Δveli
Uc
Uground
Electron cooling
Cooling
RF adjust
Frevcorr
necessary
Ue
Ui
Uc = Cathode potential
Ue = Space charge potential of electron beam
Ui = Space charge potential of ion beam
Δveli
Toroidal magnet
Ie >> Ii
Electron cooling: beam potential

## Slide 29
Tomoscope @ RF capture
before
Tomoscope @ RF capture after
Higher accumulated intensity (before RF-capture)
beam is lost at RF-capture
Adjusting Frevcorr -> RF-capture successful
Trev.
Measurements from Nov. 29th, 2012
55ms

## Slide 30: LEIR multi-turn injection (proposed by D.Möhl and S.Maury)
1st turn of incoming beam
Mechanism:
Bumper moves orbit inwards
Momentum ramping moves orbit outwards
Betatron amplitude for incoming beam remains constant
Stack “parked” with negative momentum offset
CO remains fixed
Closed orbit of injected beam
Range:
Δp/p=4x10-3
x
Towards machine centre()
time
D=10m
Linac3 beam
Septum
DxΔp/p
Bump
Low momentum
High momentum
Bump+DxΔp/p
200μs (71turns)
After 3 turns
End of injection (71 turns)
After bump collapse
LEIR beam

## Slide 31
BIPM measurement

## Slide 32
BIPM measurement

## Slide 33
εlong = 10.8eVs
Pb54+/bunch = 5.1E8
εlong = 8.1eVs
Pb54+/bunch = 5.0E8
S. Hancock, 21.2.2013

## Slide 34
Electron cooling: beam loss rate
From: Experimental Investigation of Electron Cooling and Stacking of Lead Ions in a Low Energy Accumulation Ring,
J. Bosser, C. Carli, M. Chanel et. al., CERN, 1999, p.22
Similar phenoma observed at TSR-Heidelberg with Au50+ (iso-electric to Pb53+) in 1997.

## Slide 35
Electron cooler loss rates for different Pb charge states
Loss-rate coefficients measured for lead ions of different charge states and different machine settings.
Experimental Investigation of Electron Cooling and Stacking of Lead Ions in a Low Energy Accumulation Ring
J. Bosser, C. Carli, M. Chanel, CERN, CH{1211 Geneva 23, Switzerland
April 27, 1999

## Slide 38: Restricted maxima search
LEIR horizontal tune NOMINAL (6 injections)
Fractional tune
Cycle time [ms]

## Slide 39
ΔQ for programmed radial offset from -20mm to +20mm
-20mm
-15mm
-10mm
-5mm
5mm
10mm
15mm
20mm
1 time step: 20ms
Difference of Horizontal tune to reference tune (@ 0mm beam offset)
Cycle time [ms]

## Slide 40: YASP output

## Slide 41: Linear extrapolation of Δp/p
Linear extrapolation:
-20mm to +20mm
radial offset
Measurement from +10mm programmed radial offset
Measurement from -10mm programmed radial offset
Δp/p
Cycle time [ms]