## Slide 1: Space charge in the SPS
H. Bartosik, A. Oeftiger, Y. Papaphilippou, G. Rumolo, F. Schmidt
and all members of LIU-SPS and OP crew

## Slide 2: Outline
Introduction
Achieved beam parameters in 2012
LIU target beam parameters
Experimental studies with high brightness beams
Space charge and machine modeling aspects
Summary and conclusions

## Slide 3: Introduction - SPS optics
Q20 optics with low gamma transition developed to increase instability thresholds
  Lowering SPS working point by 6 units: from “Q26”  “Q20” (γt=22.8  γt=18)
  Q20 is the default optics configuration for LHC beams since September 2012
Implications for space charge
  Higher synchrotron tune (almost factor 3 higher at injection)
  Larger dispersion  smaller space charge tune spread
Qx=26.13
Qy=26.18
“Q26” normal optics
Qx=20.13
Qy=20.18
“Q20” low γt optics

## Slide 4: Introduction - SPS cycle for LHC beam
Long injection plateau (10.8s)
  4 injections, 26 GeV/c
  Maybe even longer in case of BCMS beam
Budget for total losses: 10%
  Losses at start of acceleration ~3-5%
  Scraping at flat top ~3%
Budget for emittance growth: 10%
  Small optics mismatch at injection
  Avoid different emittance per batch
Need to preserve high brightness for >10s with ΔQ>0.2 with “practically no degradation”

## Slide 5: 2012 beam parameters – 50 ns beam
50ns standard scheme
  Regularly used to fill LHC at 2012 PS intensity limit
50ns Batch-Compression-Merging-and-Splitting (BCMS) high brightness scheme
  Beam sent to the LHC once to check emittance preservation and luminosity gain in LHC
Expected lines derived from the measured brightness curve of the PSB translated into SPS flat top values (with emittance and loss budgets in the PS – 5% – and in the SPS – 10%)
ΔQx/ΔQy ~ 0.10/0.18
ΔQx/ΔQy ~ 0.08/0.14

## Slide 6: LIU target beam parameters
Main LIU upgrades
  Double the PSB brightness thanks to injection at 160 MeV using H- from Linac4
  Raise the PS injection energy to 2 GeV for higher brightness in the PS
  SPS RF upgrade for higher intensity, electron cloud mitigation
Baseline scenario: 25 ns
Fallback scenario in case of problems with electron cloud in the LHC: 50 ns
SPS, 25 ns |  | N (1011 p/b) | εx,y (μm) | ΔQx,y
LIU | standard | 2.22 | 1.71 | (0.09, 0.16)
 | BCMS | 2.22 | 1.25 | (0.12, 0.21)
HL-HLC |  | 2.57 | 1.89 | (0.10, 0.17)
present SPS record
SPS, 50 ns |  | N (1011 p/b) | εx,y (μm) | ΔQx,y
LIU | standard | 3.00 | 1.77 | (0.13, 0.21)
 | BCMS | 3.00 | 1.77 | (0.13, 0.21)
HL-HLC |  | 4.09 | 2.27 | (0.14, 0.24)
to be studied …

## Slide 7: Experimental tune scan - horizontal
High brightness 50ns BCMS beam
  N = 1.95x1011 p/b (at injection)
  ε ~ 1.15μm
  Transmission up to flat top around 94% without scraping (very small losses on flat bottom)
  Emittance measurement at the end of flat bottom
  ΔQx/ΔQy ~ 0.10/0.18
“no blow-up”

## Slide 8: Experimental tune scan - vertical
High brightness 50ns BCMS beam
  N = 1.95x1011 p/b (at injection)
  ε ~ 1.15μm
  Transmission up to flat top around 94% without scraping (very small losses on flat bottom)
  Emittance measurement at the end of flat bottom
  ΔQx/ΔQy ~ 0.10/0.18
”no blow-up”
sum emittance

## Slide 9: Future experimental studies
Further explore the tune diagram
  Optimize working point for beams with very high brightness (“pure batch compression scheme”)
  Study effect of resonances in strong space charge regime
  Determine maximum tune shift acceptable in the SPS within emittance growth and loss budgets
Interplay with resonances excited in a controlled way for code benchmarking
  Further development of machine model (nonlinearities)
Interplay of space charge with other collective effects
  Impedance  transverse mode coupling instability
  Electron cloud
Q20/26 split tune optics
  Slight reduction of space charge tune shift compared to Q20 optics

## Slide 10: Modeling aspects and challenges
High energy (26 GeV) and short bunch length
  Complete 3D field calculation not necessary  slice approach should be ok
Slice-by-slice approach is needed
  To handle cases with intra-bunch motion
  Large dispersion in the SPS results in significant horizontal beam size variation along the bunch
  Approach of projecting the transverse bunch distribution to one slice and weighting the kicks with the longitudinal density can lead to numerical artifacts
Beam size is small compared to vacuum chambers
  Computationally heavy to include boundary conditions in the field calculations as large number of bins needed  presently only direct space charge considered
  Furthermore, many different types of vacuum chamber geometries in the SPS …
No measurements of magnetic field errors of SPS main magnets available
  Modeling will largely rely on beam based measurements

## Slide 11: Strategy for SPS simulation studies
Use PTC-pyOrbit for studying fast phenomena (<= 10k turns)
  SPS simulations with PTC-pyOrbit presently being setup  Many thanks to J. Holmes and S. Cousineau for their support and quick reactions to questions!
  Slice-by-slice space charge calculation (as needed to deal with intra-bunch motion and beam size variation along the bunch)  first version developed and presently being tested
  Effect of beam surroundings (indirect space charge and impedance) to be treated at a single lumped location in the ring  to be developed
Use (MADX) frozen space charge model for long term direct space charge effects
  SPS frozen space charge simulations presently being prepared
  Code needs to be extended to take into account the dispersion function in the initialization of the space charge kicks
  Slice-by-slice calculation will probably be difficult, but let’s see …
Use PyHEADTAIL to study interplay with other collective effects
  Impedance (TMCI instability) and electron cloud
  Need to implement space charge module

## Slide 12: Summary
Regime of strong space charge for future LHC beams in the SPS
  Long storage time at injection energy for multiple injections from PS
  Tight budgets for losses and emittance blow-up
  Space charge tune shift of ΔQy= –0.21 for baseline 25 ns scenario already demonstrated feasible
  Expected space charge tune shift of ΔQy= –0.24 for alternative 50 ns scenario to be studied
Experimental studies
  Tune scans performed in 2012 (BCMS beam)  achieved SPS record space charge tune shift
  Main goal of studies in 2014/15: determine maximum tune shift acceptable in the SPS within emittance growth and loss budgets
  Interplay of space charge and other collective effects
Space charge and machine modeling strategy
  Short term space charge effects with PTC-pyOrbit (slice-by-slice)
  Long term effects with MADX frozen space charge
  Rely on beam based measurements for modeling of machine nonlinearities
  Interplay with other collective effects using PyHEADTAIL

## Slide 13
Thank you for your attention!