## Slide 1
Studies into beam loss studies at European Spallation Source
Michał Jarosz
oPAC Topical Workshop on Beam Diagnostics
Wien, 2014-05-09

## Slide 2
I. Building an accelerator

## Slide 3
I. Building an accelerator model

## Slide 4: I. Building an Accelerator (Model)
A low-level model in a simulation code:
Very useful in the design phase
Could remain useful during the operation
Can be started early as rough estimation and then updated regularly as more detailed information about the machine parts become available
Coherence – one model utilizing the whole machine; whith strict rules and common depository; modular build

## Slide 5: I. Building an Accelerator (Model)
heltankm 2 0 2 0. 0. 19.6 20.9 21.4 92.6 !middle part of helium tank
helcovl 2 0 2 0. 0. 19.6 9.1 21.4 0.5 !helium tank left cover
helcovr 2 0 2 0. 0. 111.7 9.1 21.4 0.5 !helium tank right cover
magshld 2 0 8 0. 0. 19.45 24.25 24.4 92.9 !magnetic shield over cavities
magshll 2 0 8 0. 0. 19.45 9.1 24.25 0.15 !magnetic shield left cover
magshlr 2 0 8 0. 0. 112.2 9.1 24.25 0.15 !magnetic shield right cover
termshld 2 0 9 0. 0. 0. 47.25 47.4 131.8 !thermal shield around

## Slide 6: I. Building an Accelerator (Model)
SPOKES
ELLIPTICALS
QUADS

## Slide 7: I. Building an Accelerator (Model)
Automated Generation (small python script)

## Slide 8: I. Building an Accelerator (Model)
Automated Generation (small python script) – as for now semi-automatic
Planned integration with BLED (Beam Line Elements Database)
Biggest dificulty – MARS representation of the elements

## Slide 9
II. Using the accelerator model

## Slide 10: II. Using the accelerator model
A. Studies on the power deposition in the cold parts
Three different loss paterns (uniform, smeared over the gap between cavities, located in the quadrupoles), all obeying 1 W/m rule
Verifying the 0.5 W/m limit for the power deposition in the cryocavities

## Slide 11: II. Using the accelerator model
A. Studies on the power deposition in the cold parts
Three different loss paterns (uniform, smeared over the gap between cavities, located in the quadrupoles), all obeying 1 W/m rule
Verifying the 0.5 W/m limit for the power deposition in the cryocavities

## Slide 12: II. Using the accelerator model
B. Determining the cryovalves life
Providing information about the dose absorbed by the element during normal, long operation of the accelerator

## Slide 13: II. Using the accelerator model
Results:

## Slide 14: II. Using the accelerator model
Results:
Chart: Approximation of real power in cav / loss in quads
| 90 | 125 | 150 | 220 | 220 | 500 | 750 | 1000 | 2000
Approximation of real power in cav [W/m] | 0.49923 | 0.51029 | 0.49807 | 0.41327 | 0.19501 | 0.094632 | 0.061914 | 0.047933 | 0.032209

## Slide 15: II. Using the accelerator model
Results:
Chart: Approximation of real power in cav / loss in quads
| 90 | 125 | 150 | 220 | 220 | 500 | 750 | 1000 | 2000
Approximation of real power in cav [W/m] | 0.49923 | 0.51029 | 0.49807 | 0.41327 | 0.19501 | 0.094632 | 0.061914 | 0.047933 | 0.032209
Chart: Approximation of real power in cav / uniform loss
| 90 | 125 | 150 | 220 | 220 | 500 | 750 | 1000 | 2000
Approximation of real power in cav [W/m] | 0.98185 | 0.82589 | 0.81692 | 0.64875 | 0.4933 | 0.27178 | 0.20324 | 0.1752 | 0.12678

## Slide 16: II. Using the accelerator model
Results:
Chart: Approximation of real power in cav / loss in quads
| 90 | 125 | 150 | 220 | 220 | 500 | 750 | 1000 | 2000
Approximation of real power in cav [W/m] | 0.49923 | 0.51029 | 0.49807 | 0.41327 | 0.19501 | 0.094632 | 0.061914 | 0.047933 | 0.032209
Chart: Approximation of real power in cav / uniform loss
| 90 | 125 | 150 | 220 | 220 | 500 | 750 | 1000 | 2000
Approximation of real power in cav [W/m] | 0.98185 | 0.82589 | 0.81692 | 0.64875 | 0.4933 | 0.27178 | 0.20324 | 0.1752 | 0.12678

## Slide 17: II. Using the accelerator model
Results:
Chart: Approximation of real power in cav / loss in quads
| 90 | 125 | 150 | 220 | 220 | 500 | 750 | 1000 | 2000
Approximation of real power in cav [W/m] | 0.49923 | 0.51029 | 0.49807 | 0.41327 | 0.19501 | 0.094632 | 0.061914 | 0.047933 | 0.032209
Chart: Approximation of real power in cav / uniform loss
| 90 | 125 | 150 | 220 | 220 | 500 | 750 | 1000 | 2000
Approximation of real power in cav [W/m] | 0.98185 | 0.82589 | 0.81692 | 0.64875 | 0.4933 | 0.27178 | 0.20324 | 0.1752 | 0.12678
Reminder to self: even being too conservative is sometimes possible !

## Slide 18: III. Beam Loss Monitoring

## Slide 19: III. Beam Loss Monitoring
Beam loss monitoring at ESS:
LHC-type ionization chambers in cold sections up to the target (well tested; known response functions; ordered)

## Slide 20: III. Beam Loss Monitoring
Beam loss monitoring at ESS:
LHC-type ionization chambers in cold sections up to the target (well tested; known response functions; ordered)

## Slide 21: III. Beam Loss Monitoring
Beam loss monitoring at ESS:
LHC-type ionization chambers in cold sections up to the target (well tested; known response functions; ordered)
Ionisation chambers + additional lower energy detector in warm sections

## Slide 22: III. Beam Loss Monitoring
Beam loss monitoring at ESS:
LHC-type ionization chambers in cold sections up to the target (well tested; known response functions; ordered)
Ionisation chambers + additional lower energy detector in warm sections

## Slide 23: III. Beam Loss Monitoring
Beam loss monitors positioning
?
?
?
?

## Slide 24: III. Beam Loss Monitoring
Plans:
Research on the front end, warm part to inspect BLM needs
Fully automated accelerator model generation using BLED data
Investigation on influence of x-rays from cavities on the detectors performance

## Slide 25: Thank you for attention