## Slide 1: A Time-Multiplexed Track-Trigger architecture for CMS
G Hall, M Pesaresi, A Rose
Imperial College London
D Newbold
University of Bristol
Thanks also to the many who have helped make these ideas a reality, especially Greg Iles, John Jones,…

## Slide 2: Outline
The problem to be solved
Introduction to TMT
Status of CMS calorimeter TMT
Application to CMS Track-Trigger
Demonstrator system and readiness
Possible algorithm implementation
Open issues

## Slide 3: CMS Phase II Outer Tracker design
~15000 modules transmitting
  pT-stubs to L1 trigger @ 40 MHz
  full hit data to HLT @ 0.5-1 MHz
~8400 2S-modules
~7100 PS-modules
(D Braga talk)
(D Ceresa talk)

## Slide 4: What Is A Time Multiplexed Trigger?
Multiple sources send to single destination for complete event processing
  as used, eg, in CMS High Level Trigger
Requires two layers with passive switching network between them
  can be “simple” optical fibre network
  could involve data processing at both layers
  could also be data organisation and formatting at Layer 1, followed by data transmission to Layer 2, with event processing at Layer 2
  illustration on next slide

## Slide 5: Time-multiplexing
5
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
3
3
3
3
3
3
3
3
3
3
3
3
3
3
3
3
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
All data for 1bx from all regions in a single card!
Everything you need!
5
5
5
5
5
5
5
5
5
5
5
5
5
5
5
5
1
2
6
6
6
6
6
6
6
6
6
6
6
6
6
6
6
6
7
7
7
7
7
7
7
7
7
7
7
7
7
7
7
7
All data for 1bx from all regions in a single card!
Everything you need!
All data for 1bx from all regions in a single card!
Everything you need!
BX:1
BX:2
BX:3
BX:4
BX:5
BX:6
BX:7

## Slide 6: What are advantages of TMT?
“All” the data arrive at a single place for processing
  in ideal case avoids boundaries and sharing between processors
  however, does not preclude sub-division of detector into regions
    which may be essential for a large data source like a tracker
Architecture is naturally matched to FPGA processing
  parallel streams with pipelined steps at data link speed
Single type of processor, possibly for both layers
  L1= PP: Pre-Processor L2 = MP: Main Processor
One or two nodes can validate an entire trigger
  spare nodes can be used for redundancy, or algorithm development
Many conventional algorithms explode in a large FPGA
  timing constraints or routing congestion for 2D algorithms
Synchronisation is required only in a single node
  not across entire trigger

## Slide 7: Conventional versus TM Trigger Architecture
Options:
CT
TMT

## Slide 8: A simple example of Routing Congestion: 1
(G Iles) Created simple design to find routing limit
  30x36 2x2 tower clusters (“electrons”) with 10bit energy
  432 Gb/s (without 8B/10B)
    Approximately ¾ of CMS
  Sum 16 clusters to create “pseudojets”
  No other firmware (e.g. no sort, no transceivers, no DAQ, etc)
  XC7VX485T – Place & Route fails even though LUT usage only at 29%
but number of LUTs is not the whole story…
A bigger FPGA may not solve all the problems…
Bare minimum “physics” algorithm

## Slide 9: Routing Congestion 2 : A nasty example..
(G Iles) Implemented a proposed circular isolation algorithm
  using pipelined design
Searches every tower location in 56 x 72 region
  4032 sites
Counts the number of objects above threshold within a circular ring of diameter 9 towers or clusters
  Result passed into LUT with the energy to determine object status
f
72 towers
h
56 towers
Operates up to 400MHz
Compact: < 1% of the FPGA
Low latency - 9 clks (no overlap)
1.5 BX @ 240 MHz
* Only synthesised 36 towers in eta, rather than 56, but in the small FPGA
……
……

## Slide 10: Why was Time Multiplexed Trigger not already used?
Mainly technology limitations
  It is reliant on high performance hardware
    large & powerful FPGAs
    many high speed (optical) links
More recent objections to latency penalty in L1-L2 transmission
  but this is mostly a myth!
  If properly organised, data processing does not need to wait for entire event data.
  It can begin as soon as first cycle’s worth of data arrive

## Slide 11
Today’s hardware
MP7 (Virtex-7 XC7VX690T)
future generations will improve, but don’t yet know precisely how
purpose-built µTCA card for CMS upgraded L1 calorimeter trigger
TM performance & calo algorithms demonstrated in recent integration tests
- 72 input/72 output optical links
-all links operate at 12.5 Gbps
(10 Gbps in CMS)
- total bandwidth > 0.9 Tbps
tested, currently in production

## Slide 12
MP7-XE
First card of production order

## Slide 13: CMS Calo TMT demonstrator (Sep 2013)
MP7 used as PP & MP
PP-B
PP-T
MP
Demux
Simulating half of the PP cards with a single MP7
Simulating half of the PP cards with a single MP7
oSLB
uHTR
TPG input to PP not part of test
Test set-up @ 904

## Slide 14: Current status of TMT jet algorithms
Jets
  9×9 sum of trigger towers at every site
  Fully asymmetric jet veto calculation
  Local (“Donut”) or Global pile-up estimation
  Full overlap filtering
  Pile-up subtraction
  Pipelined sort of candidates in φ
  Accumulating pipelined sort of candidates in η
Ring sums
  Scalar and Vector (“Missing”) ET
  Scalar and Vector (“Missing”) HT
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
<
<
<
<
<
<
<
<
≤
<
<
<
<
<
<
<
≤
≤
<
<
<
<
<
<
≤
≤
≤
<
<
<
<
<
≤
≤
≤
≤
C
<
<
<
≤
≤
≤
≤
≤
≤
<
<
≤
≤
≤
≤
≤
≤
≤
<
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
<
<
<
<
<
<
<
<
≤
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
9×9 jet at tower-level resolution
50% LUT utilization INCLUDING links , buffers, control, DAQ, etc.
Runs at 240 MHz

## Slide 15: Results (from September test)
Random data passed through an emulator was used in the testing of the algorithms
Data injected into PP
Time-multiplexed
Optical Fibre
Circle jet algorithm (8x8)
Sort
Capture
Compared emulated results (solid line) with those from the MP7 (markers)
C++ emulator and hardware match precisely

## Slide 16: Results – Latency Measurement
36

## Slide 17: Possible layout of CMS TM Track-Trigger

## Slide 18
model elements
two stages of trigger processor
PP/FED
FE links
3.2Gbps per link
bidirectional DAQ links
10Gbps per link
TRG links
>10Gbps per link
MP
TRG links from PPs
>10Gbps per link
undefined
Pre-Processor (or FED)
- GBT links as input
- formats event fragment for DAQ
- formats, orders and time-multiplexes trigger data
- possible first stage trigger processing
Main Processor
takes links from all PPs as input
event is assembled over TM period
algorithms process pipelined data
output is still to be defined
  tracks, processed data,…?

## Slide 19
trigger regions
tracker has 15,508 modules => ~230 PP/FEDs
maximum number of input links to the MP7 = 72
limits the number of pre-processor cards to be connected
(without resorting to an intermediate stage and data compression)
assume 10 Gbps for conceptual design
define suitable trigger regions…
MP
TRG links from PPs
10Gbps per link
output

## Slide 20
trigger regions
split tracker into phi regions
constrained problem by looking at minimum number of trigger regions (TRs) required, and imposed constraint that one module cannot be shared across more than two TRs
- 5 TRs in phi only
- 1 GeV/c boundary region assumed
- e.g. could allow for better reco @ 2GeV/c in case of e+/e-, brem, low pT, multiple scattering etc.
1 GeV/c

## Slide 21
time multiplex period
the time multiplex period is not a completely free parameter
small TM period | large TM period
full event must be quickly assembled into one MP | could allow more efficient processing of pipelined data into MP
reduces data volume per event from PP to MP (or requires increased number of links) | increases data volume per event from PP to MP (or reduces number of links)
reduces latency | increases latency
reduces number of MPs | increases number of MPs
min ~15bx (PP output bandwidth without more Trigger Regions) | max ~34bx (68 links/2 Trigger Regions)
preferred direction
TM period of 24BX chosen for case study (could be optimised in future)

## Slide 22
PP/FEDs
PP/FED
68 FE links
3.2Gbps per link
4 bidirectional DAQ links
10Gbps per link
24 TRG links
10Gbps per link
to one TR
from non-shared modules
PP/FED
68 FE links
3.2Gbps per link
48 TRG links
10Gbps per link
to two TRs -
24 TRG links to each
from shared (boundary) modules
4 bidirectional DAQ links
10Gbps per link
4 DAQ links per PP/FED allows a maximum bandwidth of 40Gbps (~588Mbps available per tracker module)

## Slide 23
MPs
MP
MP
MP
MP
MP
MP
MP
MP
MP
MP
MP
MP
MP
each TM node takes up to 72 links
(reads in data from up to 72 PP/FEDs)
PP/FED
PP/FED
PP/FED
PP/FEDs
PP/FED
PP/FED
PP/FED
PP/FEDs
24 MPs per Trigger Region
up to 72 PP/FEDs per Trigger Region
24 links per PP/FED (1 to each TM node)
24BX TM period allows a maximum fixed TRG bandwidth of 240Gbps per PP/FED
(well below MP7 capacity)
=> ~3.5Gbps per tracker module max equivalent

## Slide 24
Organisation for 5 TRs in Phi & 24BX TM Period
28
18
29
17
29
17
29
18
28
20
66
64
63
64
66
24
24
24
24
24
1865
1194
1930
1156
1944
1102
1954
1170
1865
1328
672
696
696
696
672
432
432
408
408
408
408
432
432
480
1584
1536
1512
1536
1584
# FE links
# PP/FEDs
# PP->MP links
# PP links/ MP
# PP->MP links total
# TM nodes
480
φ1
φ2
φ3
φ4
φ5
(numbers from tkLayout…)

## Slide 25
Summary
full tracker L1 and trigger data can be read out with a total of 353 MP7s
after 24BX, all trigger data from tracker from first event are assembled into 5 MPs
each MP corresponds to a trigger region in phi
But processing should have started earlier than BX 25
subsequent events are available in next set of 5 MPs after one extra BX
no boundary sharing is required after duplication in PP;
no post-TM removal of duplicates necessary
What processing is possible in MPs?
track-finding? track fitting? data processing before an AM stage?
φ1
φ2
φ3
φ4
φ5

## Slide 26: Implementation of demonstrator
Only a fraction of the system is needed to fully demonstrate it
unlike many other architectures
The demonstrator is already available
but not yet used for this application

## Slide 27
demonstrator
5 MP7s emulate event data from full tracker, one out of every 24BX
46
46
46
47
48
66
64
63
64
66
1
1
1
1
1
46
46
46
47
48
66
64
63
64
66
# emulated PP/FEDs
# PP->MP links
# PP links/ MP
# PP->MP links total
# TM nodes
18
17
17
18
20
φ1
φ2
φ3
φ4
φ5
< 72 links out so 1 MP7 sufficient

## Slide 28
demonstrator
5 MP7s process event data from full tracker, one out of every 24BX
46
46
46
47
48
66
64
63
64
66
1
1
1
1
1
46
46
46
47
48
66
64
63
64
66
# emulated PP/FEDs
# PP->MP links
# PP links/ MP
# PP->MP links total
# TM nodes
18
17
17
18
20
φ1
φ2
φ3
φ4
φ5
<72 links in
so 1 MP7 sufficient

## Slide 29
even simpler demonstrator
2 MP7s emulate event data from 1 out of 5 regions, one out of every 24BX
46
46
64
1
46
64
# emulated PP/FEDs
# PP->MP links
# PP links/ MP
# PP->MP links total
# TM nodes
18
φ1
φ2
φ3
φ4
φ5
This demonstrator already exists
  just need to program source data to be ready to try algorithms

## Slide 30: Firmware design
Still to establish the best way of finding tracks at HL-LHC
  latency and efficiency, as well as (firmware) programming challenges
  we know from MP7 that large FPGAs present serious challenges, e.g.:
    exceeding RAM resources
    logic fails to synthesize within timing constraints after many hours
Possible approach based on Hough transform
  locate series of hits on a trajectory, for which y = mx + c
    For fixed (m,c): every “y” corresponds to single “x”
    For fixed (x,y): every “c” corresponds to single “m”
  point (m,c) -> line (x,y) point (x,y) -> line (m,c)
    All hits from a real track have same (m,c)
  For each data point (x,y), hypothesize “m” and calculate “c”
    When multiple hits have same (m,c), send for fitting
    identify by histogramming entries into array

## Slide 31
Data
C(M0)
Presort
Data
C(M0)
Data
C(M0)
Data
C(M0)
Data
C(M0)
Data
C(M0)
Data
C(M0)
Data
C(M0)
Data
C(M0)
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
Hist Cell
M
C
Fully pipelined!
No iteration!
All data-transfers local!
Realistic for implementation in an FPGA

## Slide 32: Histogramming local logic
Hist Cell
Arbitration buffer
Signal matches
C(MN) and MN
for this cell?
Yes
No
Histogram
Calculate C(MN+1)
No
Inup
Indown
Inleft
Outup
Outdown
Outright
Logic is defined for efficiency in populating array
  Step through each MN for each incoming data set
  Assign data to point in array
  Pass data values with sufficient entries in histogram location to track fitting step
Will high pile-up conditions generate too many matching combinations?

## Slide 33: Next steps
The TMT is now a proven architecture in CMS
  will operate in the CMS calorimeter trigger from 2016
The hardware is very flexible and can be deployed for a TMTT
  only a fraction of the system is required to validate the concept
  installing and building should only require replicating identical nodes
    a tracker implementation would have locally specific algorithm parameters
The next challenge is to prove suitable algorithms can be implemented
  or that alternative approaches can be shown to be required

## Slide 34: Backup

## Slide 35: Latency when performing data reduction
Imagine jet clustering @ double tower spacing
Need to sort 1440 jets (40 in eta x 36 in phi)
CT: 1440 => 4
One large sort potentially spread over several cards
TMT: 36+4 => 4
40 small sorts executed sequentially
Only the last sort contributes to latency
Latency of TMT sort is less than CT sort

## Slide 36: Routing congestion
FPGA internal interconnects are not unlimited
CT operates on areas of data
TMT operates on rows of data
2D design is really a 3D design when you consider sequence of tasks => Danger of routing congestion
1D design becomes 2D design when you add sequential tasks.

## Slide 37: Synchronisation & Structure
Synchronization is only required per-time-node, not across the whole trigger
  De-synchronization of a node only affects that node.
  A timing glitch in a CT disrupts the whole trigger.
The efficient pipelined logic should lead to lower latency, and the eventual clock speed can be as fast as the FPGA allows.
Firmware build times should be significantly shorter due to the pipelined, as opposed to combinatorial, nature of the architecture.