## Slide 1: CALICE Digital Hadron Calorimeter: Calibration and Response to Pions and Positrons
(S)DHCAL Meeting
January 15, 2014
Lyon, France
Burak Bilki
Argonne National Laboratory
University of Iowa

## Slide 2: Digital Hadron Calorimeter (DHCAL)
Concept of the DHCAL
Imaging hadron calorimeter optimized for use with PFA
1-bit (digital) readout
1 x 1 cm2 pads read out individually
(embedded into calorimeter!)
Resistive Plate Chambers (RPCs) as active elements, between steel/tungsten
Each layer with an area of ~ 1 x 1 m2 is read out by 96 x 96 pads.
The DHCAL prototype has up to 54 layers including the tail catcher (TCMT) ~ 0.5 M readout channels (world record in calorimetry!)

## Slide 3: DHCAL Data
x
y
z
Muon Trigger:
2 x (1 m x 1 m scintillator)
Secondary Beam Trigger:
2 x (20 cm x 20 cm scintillator)
Event
Particle ID: Čerenkov/μ tagger bits
Hit: x, y, z, time stamp
Nearest neighbor clustering in each layer
Cluster: x, y, z

## Slide 4
Calibration/Performance Parameters
Efficiency (ε) and pad multiplicity (μ)
Track Fits:
specifically for muon calibration runs
Identify a muon track that traverse the stack with no identified interaction
Measure all layers
Track Segment Fits:
for online calibration
Identify a track segment of four layers with aligned clusters within 3 cm
Measure only one layer (if possible)
Fit to the parametric line: x=x0+axt; y=y0+ayt; z=t
A cluster is found in the measurement layer
within 2 cm of the fit point?
Yes
No
ε=1
μ=size of the found cluster
ε=0
No μ measurement
muon
8 GeV secondary beam

## Slide 5
Calibration of the DHCAL
RPC performance
Efficiency to detect MIP ε ~ 96%
Average pad multiplicity μ~ 1.6
Calibration factors C = εμ
Equalize response to MIPS (muons)
Calibration for secondary beam (p, π±,e±)
If more than 1 particle contributes to signal of a given pad
→ Pad will fire, even if efficiency is low
→ Full calibration will overcorrect
Full calibration
Simulation
Hi … Number of hits in RPCi
More sophisticated schemes

## Slide 6
Calibration Procedures
1. Full Calibration
2. Density-weighted Calibration:
Developed due to the fact that a pad will fire if it gets contribution from multiple traversing particles regardless of the efficiency of this RPC. Hence, the full calibration will overcorrect. Classifies hits in density bins (number of neighbors in a 3 x 3 array).
3. Hybrid Calibration:
Density bins 0 and 1 receive full calibration.
Hi … Number of hits in RPCi

## Slide 7
Derived entirely based on Monte Carlo
Assumes correlation between
Density of hits ↔ Number of particles contributing to signal of a pad
Mimics different operating conditions with
Different thresholds T
Utilizes the fact that hits generated with the
Same GEANT4 file, but different operating conditions can be correlated
Defines density bin for each hit in a 3 x 3 array
Bin 0 – 0 neighbors, bin 1 – 1 neighbor …. Bin 8 – 8 neighbors
Weighs each hit
To restore desired density distribution of hits
Warning:
This is rather COMPLICATED
Density-weighted Calibration Overview

## Slide 8
Density-weighted Calibration Example:
10 GeV pions: Correction from T=400→ T=800
Mean response and the resolution reproduced.
Similar results for all energies.

## Slide 9
Density-weighted Calibration Expansion:
To large range of performance parameters
GEANT4 files
Positrons: 2, 4, 10, 16, 20, 25, 40, 80 GeV
Pions: 2, 4, 8, 10, 10, 25, 40, 80 GeV
Digitization with RPC_sim
Thresholds of 200, 400, 600, 800, 1000 (~ x 1fC)
Calculate correction factors (C)
for each density bin separately
as a function of εi, μi, ε0 and μ0 (i : RPC index)
Plot C as a function of R = (εiμi)/(ε0μ0)
→ Some scattering of the points, need a more sophisticated description of dependence of calibration factor on detector performance parameters
π: Density bin 3
R = (εiμi)/(ε0μ0)
25 GeV
Only very weak dependence on energy: Common calibration factors for all energies!

## Slide 10
π: Density bin 3
R = (εiμi)/(ε0μ0)
Density-weighted Calibration:
Empirical Function of εi, μi, ε0, μ0
Positrons
Pions
R = (εi0.3μi1.5) /(ε00.3μ01.5)
π: Density bin 3
Calibration factors
Calibration factors
25 GeV
Functional dependence of calibration factors depends on particle type!
(Due to different shower topologies: Different density distribution leads to different impact of performance)

## Slide 11
Density-weighted Calibration:
Fits of Correction Factors as a Function of R
Power law
Rπ+
Rπ+
Rπ+
Rπ+
Rπ+
Rπ+
Rπ+
Rπ+
Rπ+
Correction Factors
Correction Factors
Correction Factors
Fit results for p=pion, similar results for p=positron

## Slide 12
Calibrating Different Runs at Same Energy
4 GeV π+
8 GeV e+
Uncalibrated response (No offset in y)
Full calibration (+5 offset in y)
Density – weighted calibration (-5 offset in y)
Hybrid calibration (-10 offset in y)

## Slide 13
Comparison of Different Calibration Schemes
χ2/ndf of constant fits to the means for different runs at same energy
→ All three schemes reduce the spread of data points: Benefits of calibration!
No obvious “winner”: Similar performance of different techniques

## Slide 14
Linearity of Pion Response: Fit to N=aEm
Uncalibrated response
4% saturation
Full calibration
Perfectly linear up to 60 GeV (in contradiction to MC predictions)
Density- weighted calibration/Hybrid calibration
1 – 2% saturation (in agreement with predictions)

## Slide 15
Backup

## Slide 16
Particle Identification (PID)
0. Čerenkov counter based PID (good for 6, 8, 10, 12, 16, and 20 GeV)
1. Topological PID: Starts with the trajectory fit (used for 2, 4, 25 and 32 GeV)
Topological Variables
Visually inspect the positron events in the ~10% excess in the topological PID
They are positrons
10 % compatible with the inefficiency of the Čerenkov counter, which was ≥ 90% for most energies
Topological PID works nicely!
16 GeV