## Slide 1
A Straw Tracker in NA62
From idea to detector
Notes: 1

## Slide 2
Content
Introduction and first ideas Hans
Design and drawings Jordan
Construction and testing Jerome
On behalf of the NA62 straw team and PH-DT colleagues, in particular F. Perez Gomez, E. David and N. Dixon.
Notes: 2

## Slide 3: The NA62 experiment
NA62 is a fixed target experiment at CERN SPS
The main goal is to measure the branching ratio of the ultra rare kaon decay: with a precision better than 10% (BR ~10-10) i.e., ~1/10000000000
2012

## Slide 4: The study of Kaons

## Slide 5
First ideas and design considerations
What is really new is the straw…in vacuum (10-5mbar)!
Modular design (16 straws) for safe operation as the straws will be operated in direct contact with the decay vacuum at ~1 atmosphere above the surrounding vacuum! Leak: < 1.5 cm3/day
Minimum amount of material
  Apply pre-tension to the straws (1.5 kg) to get straight straw with minimum supporting material (spacer)

## Slide 6
Straw layout in one view
p+
2.1m
x
y
u,v
4 views: x,y,u,v
Each view (448 straws) gives one coordinate
The detector layout

## Slide 7: The straw
Straw construction
  2.1 m long tube with a diameter of 9.8 mm
  The base material is Poly Ethylene Terephthalate (PET) with thickness of 36 mm
  The foil is coated on the inside with 50 nm of Cu and 20 nm of Au by sputtering
The electrical properties and operation
  The anode wire is 30 m in diameter and made from gold-plated tungsten
  Resistivity of anode: 50 Ohm and resistivity of cathode: 70 Ohm
  HV 1750 V and gas mixture: Ar (70%)+ CO2 (30%)
36 mm PET
50 nm Cu
20 nm Au

## Slide 8: Ultrasonic welding of straws
Straw Quality Control:
  All straws are leak tested after a short (15 min) pressure test at 3 bar
  The strength of the weld is verified at both straw ends (traction test)
  The electrical conductivity between the two straw ends is measured
“Classical straw winding”
600 mm
Ultrasonic welding
Microscope pictures of a straw cross- section for quality control of the weld

## Slide 9
Strategy
Use the competence at CERN. Three examples:
PCB work shop! Since 1/1/2014 PH-DT !! 
Notes: 9

## Slide 10
Straw development – 3 years of studies!
EN-MME
Company SEFAR (CH)
16 km of welded
straws !!!!!!!
TE-VSC

## Slide 11: NA62 straw electronics and readout PH-DT + PH-ESE
30 Front-End “covers”/view
Straw
Readout (+control) Boards
2 SRB/view
2 Fibers
2 Gbit/s
PC farm
Serial link
Each “cover” has two 8-channel front–end chips, “CARIOCA”, developed for the LHCb muon tracker (MWPC).
On-detector TDC based on FPGA with a <1ns intrinsic resolution

## Slide 12
Simulations with Garfield
Cluster production
R-t dependence
Time spectra
FE electronics response

## Slide 13
The NA62 Straw Collaboration
CERN
  PH/DT: Design, development, prototyping, procurement, coordination, assembly…
  PH/ESE: development electronics, readout
Dubna: straw production , module assembly, software
Notes: 13

## Slide 14
Time line
Pre-study 2007-2008
Prototypes 2009-2010
Module 0 in 2011-2012
Construction & installation 2013-2014 (now!)

## Slide 15
The PH-DT involvement :
Detector layout and development
Mechanical design and FEM calculations
Prototyping and tooling
Gas system
Testing and QC
Simulations of detector performance
Aging studies
Test beam and performance studies (cosmics)
Detector cosntruction
Integration assembly commissioning…..

## Slide 16
Design and Drawings
Jordan

## Slide 17
Avant-Projet:
3 propositions en fin d’année.
4 modules Ronds
2 modules Carrés
4 modules Octogonaux
2007

## Slide 18
2008
Choix du module Carré.

## Slide 19
2008
Choix du module Carré.

## Slide 20
2009
Réalisation d’un prototype

## Slide 21
2009
Réalisation d’un prototype

## Slide 22
2009
Réalisation d’un prototype

## Slide 23
2009
Développement du circuit WEB:

## Slide 24
2009
Création Plug HV.

## Slide 25
2009
Réutilisation des Pins de
sertissage du TRT d’ATLAS
Création Plug HV.

## Slide 26
2010
Début de l’étude
Position des pailles sur le module:

## Slide 27
2010
Début de l’étude
Assemblage d’un module:
Notes: Un module est donc composé de 4 poutres support précisément positionnées et boulonnées entre deux flasques.
Des usinages dans ces deux flasques permettent d’assembler deux modules entre eux, et d’assurer l’étanchéité avec un o-ring de +ou- 7m de long.

## Slide 28
2010
Début de l’étude
Usinage partitions :

## Slide 29
2010
Pièces de connexion:
Etude réalisée par l’institut de DUBNA

## Slide 30
2010
Pièces de connexion:
Etude réalisée par l’institut de DUBNA

## Slide 31
2010
Pièces de connexion:
Etude réalisée par l’institut de DUBNA
Notes: Ces pièces permettent de fixer une chambre (2modules) sur les xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx

## Slide 32
2011
Recherche de partenaires pour la fabrication.
Suivi de la réalisation des premières pièces prototypes.
Contrôle qualité des pièces livrées
Suivi du premier montage.
Mise au point Modifications Améliorations
Suivi du lancement des pièces séries.
Reception 1:er module 03/2011
Notes: Durant l’année 2011, il a fallu rechercher des partenaires pour la fabrication des éléments composant un module.
Une fois les partenaires trouvés, il a fallu suivre le déroulement de la fabrication, contrôler les pièces livrées, commencer le montage du Module 0.
Une fois le module 0 monté, testé, il a été validé, puis il a été décidér de le passer en Module 1. Il est donc devenu le module U-V de la première chambre.
Il a ensuite fallu relancer la fabrication des 15 modules restant, et recommencer le même processus, suivi de fabrication, contrôle, et montage.

## Slide 33
2012
Outillage de «STACKING»:

## Slide 34
2012
Outillage de «STACKING»:

## Slide 35
2012
Outillage de «STACKING»:

## Slide 36
2012
Outillage de «STACKING»:
Notes: Le montage des modules se réalisant en partie dans le bâtiment 154, il a fallu concevoir et réaliser un outillage permettant de le montage de deux pièces de connexions, ainsi que 2 modules en position horizontal.
Grace à une rotation motorisé et deux contre-poids, il fut possible de repositionner cet assemblage de 5T (3.8T pour les deux pièces de con. + 1.4T pour la chambre) pour permettre l’élingage et le transport jusqu’à l’ECN3.

## Slide 37
2013
Service
Active Side
Notes: Pour la partie Service, il y a deux versions, le coté ACTIF, avec les patch panel HV et LV, les manifolds pour le retour GAZ, ainsi qu’un chemin de câble pour l’acheminement des câbles nécessaire.
Cet élément est non solidaire de la chambre, il est assemblé en 154, il permet le montage des pieds de renfort après sa mise en place .

## Slide 38
2013
Service
Passive Side
Notes: Et le coté PASSIF, avec l’assemblage des manifolds pour l’entrée de Gaz.
L’alimentation jusqu’aux manifolds est faite depuis les rack GAZ, et ensuite la distribution sur chaque cover est faite par un enroulement d’un capilaire formé pour chaque position (ils font tous 3m de long).

## Slide 39
2014
Notes: Voila donc un ensemble complètement équipé !

## Slide 40: Jérôme
Prototype 64 Straws
Gluing and Vacuum Test
Assembly and Testing
Quality control and testing during assembly
Leak Test and Repair
High Voltage measurement the Front End cover
Current status

## Slide 41
Prototype 64 Straws:
- 32 Straws Cern
- 32 Straws Dubna
Side Cern
Side Dubna
Web Prototype
Partition Prototype
with 1 cover
Straws
Spacers

## Slide 42
Gluing and Vacuum Test
1- Sealing Angles
. DP 490 Epoxy 3M
. ~ 160 m of gluing
2- Vacuum Test
. pressure 10-3 mbar
. ~3 days
3- Module on frame
. Rotation 360°
. Wight ~ 1,5t

## Slide 43
Assembly 1
. Spacers & Straws installation:
. 128 spacers (15360 rings)
. ~ 7200 straws for 8 modules
28 straws
1 Layer
Cutting End-Straws

## Slide 44
.Installation WEB:
. 480 pcs
Assembly 2
. Wiring Machine:
. ~ 16 km of wire
. Thickness 30µm ( W/Au)

## Slide 45: Module assembly at CERN (4pcs)
The straws are inserted straight in horizontal position and glued in vertical position
Dedicated tooling keep the straws under tension, during the gluing process (1,5kg)
Each straw is guided in two points along its length by light weight spacers anchored in the module frames.
The straws are floating with respect to the spacer and are positioned with a precision of ~ 20mm

## Slide 46: Module assembly at Dubna (4pcs)
The straws are inserted straight in vertical position and glued
Dedicated tooling keep the straws under tension, during the gluing process (1,5kg)
Each straw is guided in two points along its length by light weight spacers anchored in the module frames.
The straws are floating with respect to the spacer and are positioned with a precision of ~ 20mm
. The module rotate about Z axis

## Slide 47: Quality control and testing during assembly
Leak testing at different stages
  The Aluminum frames and the straws are leak tested before wire installation
  Specifications: 1mbar x cm3/min/straw (mainly diffusion of CO2)
Straw straightness measurement
Straw tension verification
  An infrared emitter/receiver measures the natural frequency of the straws and the straw tension is calculated
  A straw is replaced if tension is < 70% of its nominal value
Wire tension measurement
  A mechanical test of the wire tension is used by applying a fixed force (F) on the crimp tube (visual inspection)
High Voltage (HV) tests
  A first HV test is carried out once the web are installed and a second HV test after the wires are inserted. The current is measured. In a second test, the front-end cover board is read out in order to look for micro discharges.
F

## Slide 48
Quality Control
. HV Test
. Straw straightness and tension measurement
. Leak Test & HV Test

## Slide 49: Measurement of the straw straightness
A laser device measures the distance to the straws and the x-position of the center is found
A decoder measures the x-position in each straw layer (top, center and bottom position)
The nominal distance between two adjacent straws is 17.6 mm

## Slide 50: Leak Test and Repair
Test 4 Cells and more..
Test 1 Straw
Search leak
Leak Measurement

## Slide 51: High Voltage measurement the with FE cover
The final high voltage test is performed with the front-end cover installed
A threshold scan is performed to detect activity on individual channels. Noisy wires are replaced
Time: 1s/ch

## Slide 52
Modules in 154
Ch1, Ch3 ready to receive FE covers
Ch2 module UV (tested and validated) ready to receive FE covers
Installation 2014!!
Ch1 UV
Ch1 XY & Ch2 UV
Ch3 XY
Ch3 UV

## Slide 53
Stacking Bldg. 157
Chamber in vertical position
The Team who prepare the Stacking
2012

## Slide 54
Detector handling & transport
. Handling by GS Group
. Truck goes to ECN3
Technical Run

## Slide 55
Installation and integration
. Final installation services
. Integration between two sections (blue tubes)
ECN-3

## Slide 56
Education & Visit
Every year, many students come to visit us…
It’s with pleasure that we welcome you to visit our assembly area….
Building 154
EDIT school 2011

## Slide 57: Spares

## Slide 58
Technical Run in November 2012
A measurement of the beam profile was performed using the straw chamber
One module (896 straws) was successfully operated in vacuum for > 2 months
Beam center
Measured leak = 1.56x10-2 mbar x l/s

## Slide 59
Picture of straw layout hand drawing 2007-2009

## Slide 61
Stacking