## Slide 1
Future Accelerators
F. Zimmermann, CERN
oPAC School 2014
Royal Holloway, University of London
12 July 2014
Work supported by the European Commission under Capacities 7th Framework Programme, Grant Agreement 312453

## Slide 2
history & past improvements
limitations
user needs
plans to overcome limitations
advanced future schemes
international R&D efforts
contents

## Slide 3
general accelerator history

## Slide 4
linear accelerator - LINAC
circular accelerators: synchrotrons, storage rings
hybrid: recirculating linacs
rf cavities
rf cavity
particles are
accelerated
many times by
same rf cavity
basic types of accelerators

## Slide 5
S. Feher, U Melbourne
1924 Ising, 1928 Wideroe, 50 keV Na & K ions (1 drift tube)
1931 Sloan and Lawrence, 2.8 MeV Hg ions (2 m, 36 drift tubes)
acceleration occurs only in gap between electrodes
1946 Alvarez
used for protons and ions, for p energies 50-200 MeV
resonant behavior of cavity provides longitudinal electric field ;
became possible due to the development of ultrahigh frequency
technology (e.g. klystron) before and during World War II
linear accelerators

## Slide 6
cyclotron
synchrotron
strong focusing
colliding beams
acc. el. field
reverses each
half circle
rf frequency changes with magnetic field
so as to keep particles on a constant circle
“phase stability”
novel idea: combination of two lenses focuses in both planes simultaneously
(1929, 1930)
(1934, 1943, 1944, 1945)
(1950, 1952, 1959: PS)
(1943, 1956, 1961, 1971: ISR)
much higher c.m. energies than for fixed target
circular accelerators

## Slide 7
CERN ISR ~1971
the first hadron collider

## Slide 8
repeated jumps from saturating to emerging technologies
storage rings have been the frontrunner technology for the last ~50 years
P. Lebrun
colliders
Nb-Ti SC magnets
evolution of beam energy over 70 years
new technologies:

## Slide 9
accelerator applications

## Slide 10
Source: Accelerators and Beams (APS-DPP), ORNL

## Slide 11
accelerators operating in the world
3 main applications:
Scientific research
Medical applications
Industrial uses
M. Silari, ASP 2010;
adapted from “W. Maciszewski and W. Scharf,
“Particle accelerators for radiotherapy, Present status and future”, Physica Medica XX, 137 - 145 (2004)

## Slide 12
synchrotron radiation
sources

## Slide 13
curved orbit of e- in magnetic field
L. Rivkin

## Slide 14
L. Rivkin

## Slide 15
year | event
1946 | Blewett observed energy loss due to synchrotron radiation at 100 MeV betatron
1947 | First visual observation of SR at 70 MeV synchrotron, GE laboratory
1949 | Theoretical paper by Schwinger
1953 | First undulator installed at Stanford by Motz
1961 | Experimental SR program at National Bureau of Standards
1976 | First demonstration of Free Electron Laser by Madey
ascent of synchrotron radiation

## Slide 16
storage ring light source
R. Hettel, IPAC’14

## Slide 17
spatial & temporal coherence
Coherence is a fundamental property of a radiation source. Most light sources including synchrotron radiation and FELs posses a certain degree of coherence.
Spatial coherence describes the degree to which the phase of the wave is correlated at two distinct points in the transverse plane.
Temporal coherence speciﬁes the extent to which the radiation maintains a deﬁnite phase relationship at two different times.
Z. Huang, IPAC13

## Slide 18
spectral brightness & related quantities
spectral brightness
coherent fraction
for coherent Gaussian photon distribution
diffraction-limited photon-beam emittance
R. Hettel, IPAC’14

## Slide 19
total emittance is minimized when εx,y is minimized and photon and e- phase space orientations are matched:
for undulator of length L optimum: bx,y=L/p
X-ray emittance from electron source
R. Hettel, IPAC’14

## Slide 20
diffraction-limited emittance
R. Hettel, IPAC’14

## Slide 21
state of SR light sources
R. Hettel, IPAC’14

## Slide 22
Chart: emittance, nm
| 518 | 780 | 2300 | 477 | 495 | 518.4
emittance | 1.6 | 2.1 | 1 | 1.2 | 0.8 | 0.67 | 0.28
PETRA-III
2009
NSLS-II 2014-DW
TPS-2015
MAX-IV-2015-DW
SIRIUS-2016
ILSF - 2019 ?
TAC > 2020
recent trends in light source design
circumference [m]
H. Wiedemann

## Slide 23
now: ESRF - DBA
future: ESRF - 7BA
MBA lattice: smaller emittance
R. Hettel, IPAC’14
minimizing
H(s)
below what
was
previously
thought
to be
possible

## Slide 24
on-axis injection with small dyn. aperture
more cells, smaller dispersion → stronger & more sextupoles
→ low dynamic aperture
R. Hettel, IPAC’14

## Slide 25
how do we get hard x-rays from low-field bending magnets?
use high field inserts (1.8 to 2T)
produce radiation only where needed
ISLF
low-field bends & high-field inserts
H. Wiedemann
lower-energy rings with high-field inserts

## Slide 26
brightness and coherence of future rings
R. Hettel, IPAC’14
diffraction-limited rings now being designed with Nb3Sn SC insertion devices
Compiled by M. Borland, July 2013

## Slide 27
Free Electron Laser (FEL)
coherence
T. Shintake
ultrafast dynamics, damage free imaging of nanostructure,…

## Slide 28
Scientific instruments and instrumentation
Undulator systems
Electron injector
Superconducting electron accelerator
S.L. Molodtsov, European XFEL
Status of the European XFEL, TAC ISAC Meeting, Istanbul, 7-8 July, 2014
European XFEL in Hamburg
3.5 km

## Slide 29
Niobium Cavities
Module: 8x Cavities
100 8-Cavity modules, 1.4 km, 17.5 GeV Electron Energy
S.L. Molodtsov, European XFEL
SC linac technology
module
protoype
PXFEL 1

## Slide 30
Superconducting LINAC technology provides 27.000 light pulses/s in burst-
like structure. It makes XFEL.EU attractive for photon-hungry experiments.
S.L. Molodtsov, European XFEL
XFEL time structure

## Slide 31
200 eV
1 keV
10 keV
284 eV - C K
410 eV - N K
543 eV - O K
12.4 keV
Electron
energy sets
Soft x-ray undulator
SASE 3 (68 mm)
20 keV
7112 eV - Fe K
25 keV
water window
Diffraction
(DAC, etc.)
4992 eV - Ti K
4038 eV - Ca K
2470 eV - S K
2145 eV - P K
500-1300 eV
2p TM, 3d RE
500 -1300
6 -14 keV
18 - >25 keV
12.0 GeV
8.5 GeV
17.5 GeV
14.0 GeV
0.25 – ≥3 keV
Hard x-ray undulators
SASE 1 & 2 (40 mm)
3.0 – ~25 keV
S.L. Molodtsov, European XFEL
31
Photon energy ranges
Status of the European XFEL, TAC ISAC Meeting, Istanbul, 7-8 July, 2014
XFEL photon energy ranges
~1 Angstrom

## Slide 32
peak brightness comparison
Z. Huang, IPAC13

## Slide 33
FEL seeding techniques
Z.T. Zhao et al, Nature Photonics 6, 360–363 (2012)
. b,. c,
SASE FEL, with poor temporal coherence
HGHG FEL: full temporal coherence with limited harmonic number (N ≈ 10) for a single stage
EEHG FEL: full temporal coherence with very high harmonic number in single stage
M, modulator; DS, dispersive section; R, radiator

## Slide 34
high intensity proton beams
nuclear physics
radioactive ion beams
ADS
spallation sources
neutrino sources

## Slide 35
hadron-accelerator power frontier
J. Wei
IPAC’14

## Slide 36
beam power growth at major facilities
J. Wei
IPAC’14

## Slide 37
Rare Isotope Beams: FRIB

## Slide 38
ADS: MYRRHA
An accelerator driven system (ADS): neutron source created by coupling a proton accelerator, a spallation source and a sub-critical core.
2.1 MW proton beam (600 MeV - 3.5 mA)
50-100 MW thermal power

## Slide 39
SINQ at PSI
  Continuous beam, 570 MeV H+
SNS at the ORNL
  60 Hz, short-pulse, 1 GeV H+
JSNS at MLF / JPARC
  25 Hz, short-pulse, 3 GeV H+
MW class spallation neutron sources
B. Riemer
Notes: Three MW facilities at different levels of maturity.
These server neutron scattering science missions

## Slide 40
MW class spallation neutron targets
SINQ at PSI
  Pb in Zr tubes, D2O cooled
SNS at the ORNL
  Circulating Hg in SS vessel
JSNS at MLF / JPARC
  Circulating Hg in SS vessel
Pb / Zircaloy target
Mercury
Mercury
B. Riemer, ICHEP’14

## Slide 41
T2K/T2HK, LBNE(/F)
physics data since 2010
3x1020 p on target so far
1300 km

## Slide 42
medical accelerators

## Slide 43
X-rays vs. Protons
cancer treatment - X rays vs protons
M. Schippers, M. Seidel
IPAC’14

## Slide 44
X-ray beams (IMRT ) from 7 directions
Proton beams from 3 direction
pictures: Medaustron
M. Schippers, M. Seidel
IPAC’14
cancer treatment - X rays vs protons

## Slide 45
M. Schippers, M. Seidel
IPAC’14
the boost in particle therapy

## Slide 46
high-energy colliders

## Slide 47
R. Assmann, Chamonix 2001
1000 pb-1 from 1989 to 2000
LEP – largest circular e+e- collider so far

## Slide 48
Large Hadron Collider (LHC)
design:
c.m. energy 14 TeV (pp);
luminosity 1034 cm-2s-1; 1.15x1011 p/bunch;
2808 bunches/beam;
360 MJ / beam
1983 first LHC proposal, launch of design study
1994 CERN Council: LHC approval
2010 first collisions at 3.5 TeV beam energy
2015 collisions at design energy (plan)
now is the time to plan for 2040!

## Slide 49
Discovery 2012, Nobel Prize in Physics 2013
The Nobel Prize in Physics 2013 was awarded jointly to François Englert and Peter W. Higgs "for the theoretical discovery of a mechanism that contributes to our understanding of the origin of mass of subatomic particles, and which recently was confirmed through the discovery of the predicted fundamental particle, by the ATLAS and CMS experiments at CERN's Large Hadron Collider”.

## Slide 50
With the discovery of a Higgs boson in 2012, we have completed the Standard Model (almost 80 years of theoretical and experimental efforts !)
However: SM is not a complete theory of particle physics, as several outstanding questions remain (e.g. composition of dark matter, cause of universe’s accelerated expansion [dark energy / inflation], origin of matter-antimatter asymmetry, neutrino masses, why 3 families?, lightness of Higgs boson, weakness of gravity, … ) which cannot be explained within the SM.
These questions require NEW PHYSICS
2014 Prospects for Particle Physics
Present knowledge is insufficient to determine energy scale of new physics ; LHC will provide new information from pp collisions at higher cm energy (13 TeV) by 2017-18
F. Gianotti et al.

## Slide 51
main questions in particle physics and main approaches to address them
question | high-energy colliders | high-precision experiments | neutrino experiments | dedicated searches | cosmic surveys
Higgs, EWSB | X |  |  |  | 
neutrinos | X |  | X | X | X
dark matter | X |  |  | X | 
flavour, CP violation | X | X | X | X | 
new particles and forces | X | X | X | X | 
universe acceleration |  |  |  |  | X
most of these questions require high-energy and/or
high-intensity accelerators
F. Gianotti et al.

## Slide 52
with emphasis on proton-proton and electron-positron high-energy frontier machines.
These design studies should be coupled to a vigorous accelerator R&D programme, including high-field magnets and high-gradient accelerating structures,
in collaboration with national institutes, laboratories and universities worldwide.
http://cds.cern.ch/record/1567258/files/esc-e-106.pdf
….“to propose an ambitious post-LHC accelerator project at CERN by the time of the next Strategy update”:
d) CERN should undertake design studies for accelerator projects in a global context,
European Strategy Update 2013
Design studies and R&D at the energy frontier
strategy adopted at Brussels in May 2013, during exceptional session of the CERN Council in presence of the European Commission

## Slide 53
Future Circular Collider (FCC) study ; goals: CDR and cost review for the next European Strategy Update (2018)
International collaboration :
pp-collider (FCC-hh)  defining infrastructure requirements
including HE-LHC option: 16-20 T in LHC tunnel
e+e- collider (FCC-ee/TLEP) as potential intermediate step
p-e (FCC-he) option
100 km infrastructure in Geneva area
~16 T  100 TeV in 100 km
~20 T  100 TeV in 80 km
M. Benedikt

## Slide 54
Qinhuangdao (秦皇岛）
50 km
70 km
easy access
300 km from Beijing
3 h by car
1 h by train
Yifang Wang
CepC, SppC
CepC/SppC study (CAS-IHEP), CepC CDR end of 2014, e+e- collisions ~2028; pp collisions ~2042
“Chinese Toscana”

## Slide 55
Courtesy V. Shiltsev,
pp
e+e-
factor 10 every
20-30 years
factor 10 every
10 years
factor 105-107 in e+e-
luminosity
collider c.m. energy vs. year
Ecm=2ec Br
hadron-lepton
FCC-he
LHeC
ep

## Slide 56
FCC-hh: 100 TeV pp collider
LHC
27 km, 8.33 T
14 TeV (c.m.)
FCC-hh (alternative)
80 km, 20 T
100 TeV (c.m.)
FCC-hh (baseline)
100 km, 16 T
100 TeV (c.m.)
“HE-LHC”
27 km, 20 T
33 TeV (c.m.)
Geneva
PS
SPS
LHC
B. Strauss
Key technology: high-field SC magnets

## Slide 57
Cms energy |  |  | 
Luminosity |  |  | 
parameter | LHC | HL-LHC | FCC-hh
c.m. energy [TeV] | 14 |  | 100
dipole magnet field [T] | 8.33 |  | 16 (20)
circumference [km] | 36.7 |  | 100 (83)
luminosity [1034 cm-2s-1] | 1 | 5 | 5 [→20?]
bunch spacing [ns] | 25 |  | 25 (5)
events / bunch crossing | 27 | 135 | 170 (34)
bunch population [1011] | 1.15 | 2.2 | 1 (0.2)
norm. transverse emitt. [mm] | 3.75 | 2.5 | 2.2 (0.44)
IP beta-function [m] | 0.55 | 0.15 | 1.1
IP beam size [mm] | 16.7 | 7.1 | 6.8 (3)
synchrotron rad. [W/m/aperture] | 0.17 | 0.33 | 28 (44)
critical energy [keV] | 0.044 |  | 4.3 (5.5)
total syn. rad. power [MW] | 0.0072 | 0.0146 | 4.6 (5.8)
longitudinal damping time [h] | 12.9 |  | 0.54 (0.32)

## Slide 58
only a quarter is shown
15-16 T: Nb-Ti & Nb3Sn
20 T: Nb-Ti & Nb3Sn & HTS
L. Rossi, E. Todesco, P. McIntyre
“hybrid magnets”
example block-coil layout
cost-optimized high-field dipole magnets

## Slide 59
B. Strauss, data by courtesy of J. Parrell (US DOE OST)
US-CDP
ITER wires
HL-LHC wires
Nb3Sn vs Nb-Ti SC wire production

## Slide 60
Chart: 
SUPERCONDUCTING MAGNETS
g Demonstration Test Coils
g Commercial Magnet Systems
Nb-Ti
SC solenoid magnets (dipoles to follow)
Nb3-Sn
23.5 T (1GHz NMR) Nb3-Sn Superconducting Magnets
(Manufactured Commercially)
High
Tc
35 T Proof-of-Principle Demo
(4T HTS Test Coil in a
31T Background Magnetic Field)
f 39 mm
G. Boebinger, NHMFL
superconducting magnet technology
“contributing to a revolution in real time”

## Slide 61
magnet R&D - possible spin offs & synergies
„Pilotstrecke AmpaCity: zum ersten Mal wird mitten in einer Großstadt (Essen) ein Supraleiter (HTS: BSSCO) für den Stromtransport in ein existierendes Stromnetz eingebunden.“
example : electric power transmission
using HTS
cables

## Slide 62
Courtesy W. Fischer
hadron-collider peak luminosity vs. year
LHC run 1 (2012-13) accumulated more integrated luminosity than all previous hadron colliders together!

## Slide 63
circumference ≈100 km
FCC-ee: e+e- collider up to 350 (500) GeV
for top up injection
short beam lifetime (~tLEP2/40) due to high luminosity supported by top-up injection (used at KEKB, PEP-II, SLS,…);
top-up also avoids ramping & thermal transients, + eases tuning
A. Blondel
top-up injection is the key to extremely high luminosity;
requires full-energy injector

## Slide 64
parameter | LEP2 | FCC-ee |  |  |  |  | CepC
 |  | Z | Z (c.w.) | W | H | t | H
Ebeam [GeV] | 104 | 45 | 45 | 80 | 120 | 175 | 120
circumference [km] | 26.7 | 100 | 100 | 100 | 100 | 100 | 54
current [mA] | 3.0 | 1450 | 1431 | 152 | 30 | 6.6 | 16.6
PSR,tot [MW] | 22 | 100 | 100 | 100 | 100 | 100 | 100
no. bunches | 4 | 16700 | 29791 | 4490 | 1360 | 98 | 50
Nb [1011] | 4.2 | 1.8 | 1.0 | 0.7 | 0.46 | 1.4 | 3.7
ex [nm] | 22 | 29 | 0.14 | 3.3 | 0.94 | 2 | 6.8
ey [pm] | 250 | 60 | 1 | 1 | 2 | 2 | 20
b*x [m] | 1.2 | 0.5 | 0.5 | 0.5 | 0.5 | 1.0 | 0.8
b*y [mm] | 50 | 1 | 1 | 1 | 1 | 1 | 1.2
s*y [nm] | 3500 | 250 | 32 | 130 | 44 | 45 | 160
sz,SR [mm] | 11.5 | 1.64 | 2.7 | 1.01 | 0.81 | 1.16 | 2.3
sz,tot [mm] (w beamstr.) | 11.5 | 2.56 | 5.9 | 1.49 | 1.17 | 1.49 | 2.7
hourglass factor Fhg | 0.99 | 0.64 | 0.94 | 0.79 | 0.80 | 0.73 | 0.61
L/IP [1034 cm-2s-1] | 0.01 | 28 | 212 | 12 | 6 | 1.7 | 1.8
tbeam [min] | 300 | 287 | 39 | 72 | 30 | 23 | 40

## Slide 65
e+e- luminosity vs energy

## Slide 66
Precision Measurements
Springboard for sensitivity to new physics
Theoretical issues:
  Higher-order QCD
  Higher-order EW
  Mixed QCD + EW
Rare Decays
Direct searches for new physics
Many opportunities
Z: 1012
b, c, τ: 1011
W: 108
H: 106
t: 106
The Twin Frontiers of FCC-ee Physics
J. Ellis
P. Janot
M. Ruan
M. Bicer et al., “First Look at the Physics Case of TLEP,’’ JHEP 01, 164 (2014)
S. Dawson et al., arXiv:1310.8361v2
FCC-ee promises much higher precision & and many more rare decays than any competitors
Higgs coupling
measurements
HL-LHC
ILC500
FCC-ee 350
CepC, 4/ab

## Slide 67
neutrinos have mass...
and this very probably implies new degrees of freedom
 Right-Handed, Almost «Sterile» (very small couplings) Neutrinos
completely unknown masses (meV to ZeV), nearly impossinle to find.
.... but could perhaps explain all: DM, BAU,-masses
“at least 3 pieces are still missing”
A. Blondel, The Hunt for Heavy Neutrinos at the Z & H factory, ICHEP’14
These would lead to spectacular ‘detached vertex’ signatures in Z-> neutrino decays at a Tera-Z factory like FCC-ee

## Slide 68
SuperKEKB = FCC-ee demonstrator
beam commissioning will start in early 2015
top up injection at high current
by* =300 mm (FCC-ee: 1 mm)
lifetime 5 min (FCC-ee: ≥20 min)
ey/ex =0.25% (similar to FCC-ee)
off momentum acceptance (±1.5%, similar to FCC-ee)
e+ production rate (2.5x1012/s, FCC-ee: <1.5x1012/s (Z cr.waist)
SuperKEKB goes beyond FCC-ee,
testing all concepts

## Slide 69
year
b* [m]
PETRA
SPEAR
PEP, BEPC, LEP
CESR
DORIS
TRISTAN
DAFNE
CESR-c, PEP-II
KEKB
BEPC-II
SuperKEKB
FCC-ee
SLC
ILC
vertical b* history

## Slide 70
collider / test facility | [nm]
LEP2 | 3500
KEKB | 940
SLC | 700
ATF2, FFTB | 45 (37), 77
SuperKEKB | 50
FCC-ee-H | 44
ILC | 5 – 8
CLIC | 1 – 2
collider / test facility | 
LEP2 | 3500
KEKB | 940
SLC | 700
ATF2, FFTB | 45 (37), 77
SuperKEKB | 50
FCC-ee-H | 44
ILC | 5 – 8
CLIC | 1 – 2
in regular
font:
achieved
in italics:
design
values
by*:
5 cm→
1 mm
ey:
250 pm→
2 pm
vertical rms IP spot size

## Slide 71
FCC-he: high-energy lepton-hadron collider
RR LHeC:
new ring
in LHC tunnel,
with bypasses
around
experiments
LR LHeC:
recirculating
linac with
energy
recovery
similar two options for FCC:
(1) FCC-ee ring, (2) ERL – from LHeC or new
LHeC CDR , published in 2012

## Slide 72
FCC
FCC-he: – 1st option ring-ring collider
– 2nd option: based on LHeC
J. Osborne

## Slide 73
collider parameters | FCC ERL | FCC-ee ring |  | protons
species | e- (e+?) | e± | e± | p
beam energy [GeV] | 60 | 60 | 120 | 50000
bunches / beam | - | 10600 | 1360 | 10600
bunch intensity [1011] | 0.05 | 0.94 | 0.46 | 1.0
beam current [mA] | 25.6 | 480 | 30 | 500
rms bunch length [cm] | 0.02 | 0.15 | 0.12 | 8
rms emittance [nm] | 0.17 | 1.9 (x) | 0.94 (x) | 0.04 [0.02 y]
bx,y*[mm] | 94 | 8, 4 | 17, 8.5 | 400 [200 y]
sx,y* [mm] | 4.0 | 4.0, 2.0 |  | equal
beam-b. parameter x | (D=2) | 0.13 | 0.13 | 0.022 (0.0002)
hourglass reduction | 0.92 (HD=1.35) | ~0.21 | ~0.39 | 
CM energy [TeV] | 3.5 | 3.5 | 4.9 | 
luminosity[1034cm-2s-1] | 1.0 | 6.2 | 0.7 | 
preliminary

## Slide 74
M. Klein and H. Schopper CERN Courier June 2014
lepton-hadron scattering facilities till FCC-he
FCC-he

## Slide 75
h-e Higgs-boson production and decay; and precision measurements of the H–bb coupling in WW–H production; FCC-he also gives access to Higgs self-coupling H–HH (<10% precision!? - under study), to lepto-quarks up to ≈4TeV & to Bjorken x as low as 10-7 - 10-8 [of interest for ultra high energy n scattering]
Higgs physics at LHeC & FCC-he
M. Klein and H. Schopper, CERN Courier June2014

## Slide 76
2014 |  |  |  | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
Kick-off, collaboration forming,
study plan and organisation
Release CDR & Workshop on next steps
Workshop & Review
 contents of CDR
Workshop & Review identification of baseline
Ph 2: Conceptual study of baseline “strong interact.”
Workshop & Review, cost model, LHC results  study re-scoping?
Ph 3: Study
consolidation
Report
Prepare
4 large FCC Workshops distributed over participating regions
Ph 1: Explore options
“weak interaction”
FCC global design study – time line
  presently discussions with potential partners (MoUs)
  first international collaboration board meeting at CERN on 9 & 10 September 2014
M. Benedikt

## Slide 77
http://indico.cern.ch/e/fcc-kickoff
http://cern.ch/fcc
FCC Kick-off Meeting
University of Geneva
12-15 February 2014
>340 participants

## Slide 80
FCC Kick-Off Parallel Sessions
Session | # Participants
Technical infrastructure and civil engineering | 47
Hadron collider design (+ SC magnets + injectors) | 75
Lepton collider design (+ SC RF + injectors) | 62
Hadron Physics, Experiments, Detectors | 93
Lepton Physics, Experiments, Detectors | 54
e-p Option | 18
Overall physics and phenomenology | 63

## Slide 81
signing FCC MoUs with partners

## Slide 82
main questions in particle physics and main approaches to address them
question | high-energy colliders | high-precision experiments | neutrino experiments | dedicated searches | cosmic surveys
Higgs, EWSB | X |  |  |  | 
neutrinos | X |  | X | X | X
dark matter | X |  |  | X | 
flavour, CP violation | X | X | X | X | 
new particles and forces | X | X | X | X | 
universe acceleration |  |  |  |  | X
many questions require high-energy and/or
high-intensity accelerators
F. Gianotti et al.
within the scope of FCC

## Slide 83
PSB
PS (0.6 km)
SPS (6.9 km)
HL-LHC
FCC-ee (80-100 km,
e+e-, up to 350
or 500 GeV c.m.)
FCC-hh
(pp up to
100 TeV c.m.
& AA)
FCC-he: e± (60-250 GeV) – p(50 TeV)/A collisions
≥50 years e+e-, pp, e±p/A physics at highest energies
LHeC & SAPPHiRE (gg)
LHC (26.7 km)
LHeC as FCC-ee injector?
LHeC-based FCC-he collider?!
FCC-he as ring-ring
collider ?!
possible evolution of FCC complex

## Slide 84
1980
1990
2000
2010
2020
2030
LHC
Constr.
Physics
Proto.
Design,
R&D
HL-LHC
Constr.
Design,
R&D
FCC
ee
hh
he
2040
LHeC/SAPPHiRE?
Constr.
Physics
Design,
R&D
Physics
tentative time line
Design,
R&D
Constr.
Physics

## Slide 85
accelerator cost

## Slide 86: Phenomenological Cost Model: Conventional Technology
Cost = α L1/2 + β E1/2 + γ P1/2
where α,β,γ – technology dependent constants
  α≈ 2B$/sqrt(L/10 km)
  β≈ 10B$/sqrt(E/TeV) for RF
  β≈ 2B$/sqrt(E/ TeV) for SC magnets
  β≈ 1B$ /sqrt(E/TeV) for NC magnets
  γ≈ 2B$/sqrt(P/100 MW)
“Total Project Cost “
“Tunnel Length”
Civil Construction
“Energy” – Cost of
Accelerator
Components
“Site Power”
Infrastructure
Phenomenological Cost Model: Present Technology

## Slide 87
The model is good to +-30%
Total Cost vs Model (Log-Log)
V. Shiltsev

## Slide 88
cost ~ Ecm 0.28
P. Lebrun, RFTech 2013
1959
1971
2008
remarkable advance in accelerator cost/energy
thanks to new technologies

## Slide 89: energy consumption & cost (survey)
Chart: Electricity consumption (GWh)
| 1.PSI | 2.ESRF | 3.ISIS | 4.KVI | 5.INFN | 6.ALBA | 7.GSI | 8.CERN | 9.SOLEIL | 10.DESY | 11.ESS | 12.MAX IV
 | 125 | 64 | 70 | 4.175 | 25 | 20 | 60 | 1220 | 36.768 | 150 | 270 | 65.625
EuCARD-2 EnEfficient;
J. Torberntsson, ESS; M. Seidel, PSI
Chart: Electricity price (€/MWh)
| 1.PSI | 2.ESRF | 3.ISIS | 4.KVI | 5.INFN | 6.ALBA | 7.GSI | 8.CERN | 9.SOLEIL | 10.DESY | 11.ESS | 12.MAX IV
 | 0 | 57 | 96 | 80 | 149 | 128 | 120 | 49 | 71.82 | 138 | 50 | 50

## Slide 90
Renewable energies cause strong variations
impact on accelerators?
found on the internet
energy spot market prices
EuCARD-2 EnEfficient;
M. Seidel, PSI

## Slide 91
in the presence of more and more renewable energies, flexibility becomes more important
adapt operation to situation on Grid, e.g. through efficient standby modes
energy storage on site, e.g. utilizing cryogenic facility?
cost effective backup power station, gas turbine?
 workshop planned for 2015 (J.Stadlmann, GSI)
energy management or „virtual power plant“

## Slide 92
energy recovery linacs
6-pass 2x10-GeV recirculating linac with energy recovery
Example: LHeC

## Slide 93
far future schemes
dielectric wake field acceleration
driven by another beam or by laser
plasma wake field acceleration of electrons
driven by laser, e- beam or p beam
crystal acceleration
driven by x-ray lasers
dielectric laser acceleration
cystal bending

## Slide 94
total length (main linac) ~30 (500 GeV) - 50 km (1 TeV)
accelerating gradient ~30 MV/m
ILC: SC linear collider

## Slide 95
total length (main linac) ~11 (500 GeV) - 48 km (3 TeV)
accelerating gradient
~100 MV/m
CLIC: warm X-band linear collider

## Slide 96
limits to accelerating gradients
Gmax30 MV/m (Nb superconductor)
Gmax100 MV/m (normalconducting metal)
due to surface breakdown
Gmax1-3 GV/m (dielectrics)
Gmax100 GV/m (n0 [1018 cm-3])1/2 (plasma
with n0 ≈1017-1018 cm-3 plasma density)
Gmax10 TV/m (n0 [1022 cm-3])1/2 (crystal
with n0 ≈1022-1023 cm-3)
Gmax1018 V/m (Schwinger critical field,
vacuum breakdown)
today
tomorrow?

## Slide 97
The plasma acts as an energy transformer: energy is transferred from the driver to the witness bunch that is accelerated.
The maximum energy gain of the accelerated beam in a single plasma stage is limited by driver energy (e- bunch, laser pulse, etc.)
Current proton synchrotrons can produce high energy protons, reaching up to multi TeV (LHC)  p bunches are the most promising drivers of wakefields to accelerate e’s to TeV energy scale
proton-driven plasma acceleration

## Slide 98
PoP Experiment: Awake
C. BV
FC
E, DE
MS
BPR
Laser +Diagnostics
RF GUN
Emittance
Incident, Reflected Power and phase
Spectrometer
Corrector
MTV
VPI
FCT
Accelerator
MTV,
Emittance
Matching triplet
BPR
BPR
Incident, Reflected, transmitted Power
Klystron
OTR for SMI diagnostics
Laser dump
Laser
RF gun
e- spectrometer
Plasma cell
SPS p+ beam
p+ dump
e- beam
Approved in August 2013
First p+ and laser beam in 2016 (Phase 1)
First e- beam in 2017-2018 (Phase 2)
C. Bracco
accelerating gradient
>1 GV/m

## Slide 99
An e+ e- collider
An e-p collider
far future p-driven plasma collider designs
S. Chattopadhyay
accelerating gradient
>1 GV/m

## Slide 100
(r)evolutionary advancement: DLA
Semiconductor Manufacturing
Traditional Manufacturing
Fibers
Gratings
Crystals
Room temp.
Superconducting
10E-4
λ = 10 cm
Eacc = 30 MV/m
λ = 1 - 2 μm
Eacc = 2 GV/m *
* in theory
R. Byer

## Slide 101
T. Plettner, et al. PRST-AB 9, 111301 (2006).
dielectric laser-driven accelerator
Electron microscope image of the bonded structure

## Slide 102
experimental results from SLAC
measuring the gradient by observing the resultant energy broadening
R. Byer

## Slide 103
experimental results from SLAC
Cross correlation of electron and laser pulses in time
Measured acceleration gradient vs Peak Electric Field
R. Byer

## Slide 104
injector
(Demonstrated at MPQ)
speed of light accelerator
(Demonstrated at SLAC)
particle source
(Demonstrated at MPQ)
Image courtesy of P. Hommelhoff
chip accelerator w integrated injector
R. Byer

## Slide 105
SiO2 wafer
Z
X
y
Etched
Channel
Electron
Source
Laser Couplers
e-
30 keV
40 MeV
e-
multi-MeV (XFEL) device on wafer in 5-10 years

## Slide 106: with particles appropriately bunched, the laser to electron power transfer efficiencies approach 60%
power transfer efficiency
total wallplug to electron efficiency (12%) comparable to conventional accelerators
R. Byer

## Slide 107
1.5 TeV  1750 meters
Main Linac (one half)
x7700/TeV
E. R. Colby, R. J. England, R. J. Noble, "A Laser-Driven Linear Collider: Sample Machine
Parameters and Configuration", PAC 2011.
one 6’’ wafer with 120
accelerator “chips” in series
3-TeV particle collider based on DLA
R. Byer
total length of collider
~3.5 km
bunches of 104 electrons at 100 MHz

## Slide 108
circular colliders beyond FCC
circular crystal collider?
cryogenic?
crystal
bending
stage
cryogenic?
crystal
bending
stage
proton beam
tunnel mostly empty
energy ramp using induction acceleration?
a dream or our future ?

## Slide 109
conclusions
particle accelerators
have had a glorious history,
are serving a large number of goals
for society and humankind,
may see a revolutionary development
in the coming decades, and
will sure have a bright future !
with oPAC you are at the right place

## Slide 110
„A really good idea is easily recognizable. It’s one whose implementation seems doomed at the outset.”
Albert Einstein