## Slide 1
Technical Board on LHC Injector Start-up
    Tune Monitors in PSB, PS and AD
    TT2/TT10 BPMs

## Slide 2
Tune monitor in the PSB
Now:
  Four BBQ front-ends for each ring - One H+V BBQ acquisition with 16-bit ADCs.
  Signal selection though an analogue NIM multiplexer, the only NIM module in the system; Control with obsolete ICV196.
  Excitation: kick with one revolution pulse, strength adjusted manually on the high voltage power supply. Same excitation for each ring by design (kickers connected together).
PSB OP request for “after LS1”:
  Motivation: resonant beam excitation to high amplitudes for machine studies.
  Plan: Chirp excitation with the transverse damper, similar to the PS
  Excitation parameters can be common for each ring, with the possibility to turn the chirp on/off for particular rings.
  Status: Some “PSB specific” parts of the FESA to be done to handle 4 rings of the PSB
  Motivation: kick adjustment according to actual requirement
  Plan: Remote control for the high voltage power supply (existing PS can be controlled with an analogue signal)
  Status: Cleaning of old kicker hardware ongoing
  HW installed in the machine ready for the beam
  On the DAC mezzanines , slow DACs for controlling high voltage of the kicker; this DAC is not included in the FPGA (Andrea) and FESA yet (SW)
  Motivation: Individual Acquisitions per ring to measure four rings in parallel for ring matching and fine machine tuning
  Status: 4 DABs, one DAB per ring, with separate acquisition of each ring and its own revolution installed and under tests for SW developments for few months

## Slide 3
Tune monitor in the PS, AD
PS
  New long stripline has been built and installed (May 2013).
  The pick will be connected to the acquisition as soon as the PSB is done (HW ready)
  Foreseen two separate acquisitions for the start-up (2 DABs): To be implemented in Fesa
AD
  VME with DAB installed
  The BBQ permanent installation requires an access to electrode signals of one position pick-up with favorable beta functions; Preferably it should be active splitting of signals from the head amplifier, To be done in collaboration with the PI section
  Fesa and expert Gui to be followed up
Software and expert GUIs
  After FESA changes the TuneViewer does not work anymore.
  New tool in preparation by Stephane
  Need to check the status and the functionalities of the expert Gui

## Slide 4
TT2/TT10 pick-up
New monitor installed (FT16 UDC106): Cables pulled but not tested yet by EN/EL: Front-end and acquisition in place and software has been modified to take the new monitor into account
Radiation damaged monitors in TT2, still one monitor to debug..should be finalised within the next few weeks.
In TT10 BPM 3 and 4 back in position (civil engineering in the tunnel) - Beam line is not under vacuum and BPMs are not aligned yet - Electronic has been re-installed
The last two BPMs in TT10 not re-installed yet, cables to be pulled (finished by end of March): new chassis for the FE are in place
PS
SPS
TT2
TT10
BPCL100618
BPCL100509
FT16UDC151
FT16UDC211
FT16UDC251
FT16UDC311
FT16UDC346
FT16UDC368
BPCL100407
BPCL100208
BPCL101302
BPCL101502
BPCL101902
BPCL102073
BPCL102302
BPCL102402
BPCL102573
BPCL102739
BPCL102911
BPCL102963
CFV-269-BPMTFL
PS Timing
SPS Timing
CFV-BA1-BPMTFL
SPS Timing
BPCL | TT2 | TT10
2 planes 66,5mm | 6 | 14
Cables length | 90  430 m | 160  620 m
Control | SPS | 

## Slide 6
Tune monitor in the PS
What is the status?
The PS tune system is working very nicely.
The implementation of an operational application has solved different problems due to the complexity of the expert GUI.
The porting to Linux MENA20 has increased performances and it allows the user to acquire the maximum amount of data (4 times more than before). Plus, the acquisition is very stable.
The long pickup is needed for low intensity beams.
What is requested or missing?
The user should be able to select which pickup/DAB he would like to use for acquiring the tune. The choice should be done from the application through the FESA server and in PPM mode.
Different fitting algorithms used for the peak detection should be added in the FESA server. Same as for the FFT windows types, a list could be proposed in the application.
It would be nice to quantify the coupling between the 2 plans H and V. One proposition is to use the 2 frequency windows in both plans.
Other algorithms with better performances (cf. Simone) to obtain the frequency spectrum could be implemented as well in the FESA server.
Would it be possible to estimate chromaticity?
  The ring revolution frequencies are already in the tune rack.

## Slide 7
Acquisition System
- VME 64x Digital Acquisition Board
LHC DAB64x (TRIUMF, Canada)
Mezzanine Card
- performs Manchester decoding
- Xilinx FPGA treats data to give
correct input for DAB64x
Final Configuration
- 2 VME Crates
- 2x5 DABs with 2x10 Mezzanines
2 monitors per DAB
- processing data from 20 PUs

## Slide 8
BPM Front-end