## Slide 1: LumiDAQ testing plan
Keith Rose
27 Jan 2013
LumiDAQ Meeting

## Slide 2: Current testing resources
may.cern.ch – SLC6 machine with XDAQ12
  Dedicated machine for testing lumiDAQ prototype
  “sandbox setup”; sender, eventing, receiver on same node
Data Histograms written out every 4096 orbits
4 channels from real histo data
Publisher reads out on 4096-orbit timer
3564-bx histogram output with properties:
“Nibble”, “channel”, “orbit”
Subscriber reads data from eventing. Calculates total coincidences per channel per nibble
Zhen’s example sets up 2 versions of the publisher and one of the subscriber. Subscriber reads from both as though they were equally valid.
Dipbridge example not tested yet

## Slide 3: PLT clients
Error monitoring
  Very short term (immediate feedback)
  Short term (single run analysis – publish at end of run)
  Long term (data trends over at least 1 days’ worth)
BRM
  BRM previously pulsed at about 1 Hz
  DIP interface
  Previously single quantity – well suited for lumiDAQ
LumiData
  Already working minimally from Histograms
Event Data
  Read out from pixel data (~1 kHz preferably)
  Find dead pixels
  Save N_Clusters for alternate lumi measurement

## Slide 4: To Do (within 1 month)
2nd Development note – august.cern.ch
  Currently SLC5, needs to be upgraded to SLC6
  Can serve as testing grounds for pub/sub
Test dipbridge interface
  Publish BRM quantity once per second
Repeat Data Histogram lumiDAQ process with Slink data
  Publish dead pixels
  Publish clusters per luminibble
Add Error functionalities to Slink/Histogram publishers
  Publish dead pixels
  Publish clusters per luminibble
Publisher/subscriber – raw Lumi to processed Lumi
  Take in dead channels, etc, produced processed Lumi