## Slide 1: Hadron Injector Considerations
B.Goddard, W.Herr
With input from M.Benedikt, L.Bottura, P.Lebrun, G de Rijk, D.Schulte, F.Zimmermann

## Slide 2: Outline
Initial assumptions
  Requirements, pre-injector performance, constraints
HEB tunnel options and features
  SPS
  LHC
  FHC
Main directions for future investigation

## Slide 3: Basic assumptions
Maximise CERN facility reuse
  Add High Energy Booster (HEB) to present LHC injector complex
  Not considering (yet) an “SPL/PS2-like” option
Take HL-LHC injector chain output for granted
  2.5e11 p+/bunch in 2 mm exy at 25 ns
FHC: 100 km collider length, 50 TeV/beam
  1e11 p+ per bunch, 25 ns spacing, need to fill ~11’000 bunches
Evaluate all HEB designs with 2-in-1 magnets, for filling times
  May not be realistic for all options – important for transfer lines and layout, and eventually considerations like polarity reversal
Filling times calculated assuming present injector complex cycle times (but increased PS batches in SPS from 4 to 8)

## Slide 4: FHC injection considerations
Minimum filling time (on paper) should be of the order of 10 minutes
  Aim to keep this ‘in the shadow’ of the FHC cycle time
  To note: present LHC could fill both rings in under 10 minutes – on paper
Injection energy between 1.8 and 3.2 TeV
  3.2 TeV gives same field ratio (collision/injection) as present LHC – take this as ‘baseline’
  1.8 TeV gives same minimum field in T as present LHC

## Slide 5: An FHC injector chain
LINAC4
0-160 MeV (H-)
PSB
0.16 – 2 GeV (x13)
PS
2 – 26 GeV (x13)
SPS
26 – 450 GeV (x17)
HEB
0.450 – 3.2 TeV (x7)
To FHC
3.2 - 50 TeV (x16)

## Slide 6: HEB magnet technology options

## Slide 7: Tunnels and magnetic lengths

## Slide 8: HEB options – SPS tunnel
SPS tunnel: SC low-field can reach 1.1 TeV, but ~3 TeV is tough

## Slide 9: HEB in SPS tunnel specifics
Reaching 3.2 TeV requires 15.6 T Nb3Sn SC dipoles
  14 HEB cycles to fill FCC…(23 us SPS length)
  Slow dipole ramp means (min.) 4 hours to fill FCC
Fast-ramping NbTi SC dipoles possible (à la SIS300), at 5 T
  Can reach only 1.1 TeV at extraction
  Min. filling time ~8 minutes (as for present LHC), dominated by pre-injectors where improvements might be possible
High field (LHC) NbTi has both disadvantages
  Only 2 TeV extraction energy
  Min. filling time ~25 minutes, limited by HEB ramp
SPS tunnel fairly large (Ø4.1 m) but maybe non-negligible integration issues (ex. LSS3)
Beam transfer to study – might need long new (SC?) lines
Overall none of SPS tunnel options initially appear too promising
  But clear cost advantage of short ring with ~4.6 km dipole length
  Critical to get answer on minimum FHC injection field

## Slide 10: HEB options – LHC tunnel
LHC tunnel: wide range of possibilities – including reuse of LHC

## Slide 11: HEB in LHC tunnel specifics
Machine length ratio is good, in regards low number of cycles to fill FHC (8 or 4, for single or double aperture)
Reaching ~3-4 TeV is possible with low-field NbTi SC
  Reusing present LHC at 3.8 T – min. filling time ~70 minutes (ramp rate would clearly need to be increased by factor 5-10)
  Replacing present LHC by new fast ramping SC machine (but ~18 km of new SC dipoles)
SF or NC look less feasible (2.5 or 2.0 T)
  Can reach only 2.1 or 1.7 TeV at extraction
  Again feasibility depends on minimum injection FHC field
Reuse of present LHC needs careful evaluation
  Maximum ramp rate (see discussions with MSC)
  Simplified machine layout (no low-b insertions)
  Can suggest already some ‘hard’ study directions/testing for this option
For all versions in LHC tunnel, decommissioning feasibility (at least insertion regions) to be evaluated
Beam transfer faces similar difficulties as SPS option

## Slide 12: HEB options – Collider tunnel
FCC tunnel: 2.0/2.5 T NC/SF

## Slide 13: HEB in FHC tunnel specifics
6-8 TeV accessible with iron pole magnets
  SF or purely NC are equally possible
Minimum filling times ~10 minutes
  Again, dominated by injector chain – improvements might be possible
To minimise number of dipoles, at ~3 TeV can conceive a “sparse” HEB lattice, with approx. 1 of 2 possible dipole slots installed
  Operate dipoles at around 2 T
  Dipole length then around 30 km (i.e. 3000x 10 m dipoles) – which is 6.5x SPS
  Still requires at ~1000 quadrupoles…(for 100 m half-cell length) which is 5x SPS
Beam transfer is obviously simplified with this option – will maybe need to foresee some tunnel enlargements and technical galleries, but no long addition SC transfer lines
Tunnel integration of HEB with FCC easy at this stage (!) but eventual HEB design might depend on whether e-p option is required

## Slide 14: Conclusions
Plenty of options….work now to reduce the number
Starting point for injectors assumes re-use of existing LHC chain, up to and including SPS
  New HEB: should be ≥3 TeV and fill FHC in around 10 minutes
Interesting initial options:
  7 km SC machine in SPS – 2 TeV reach
    High-field 9 T NbTi
  27 km machine in LHC tunnel – 4-7 TeV reach
    LHC reuse
      Ramp rate to increase by as much as possible: x5 reasonable target?
      New 2-quadrant higher voltage powering, new QPS, remove low-b, …
      Decommissioning of highly activated zones to study
    New fast ramping design
  100 km NC/SF machine – 6-8 TeV reach
    30-60 km of 2-in-1 iron dipole magnets, at least 1000 quadrupoles

## Slide 15: Some specific topics for studies
Minimum injection energy (field) in FHC
  Key question
  2 TeV opens other options for HEB...
Maximum ‘flat-bottom’ time for FHC
  Need to know if target of ~10 minutes is adequate
Feasibility of LHC reuse for HEB
  Lattice design for simplified synchrotron
  Key question of ramping at ~50 A/s. Tests???
  Availability (how often were there 4 consecutive LHC ramps??)
  Decommissioning feasibility
Feasibility of HEB in 100 km tunnel
  Beam dynamics at 450 GeV injection energy (space charge, impedance, IBS, …)
  Basic lattice needed
Preliminary cost scaling for magnet systems for all options
Beam transfer, machine protection (these get difficult!) and layouts

## Slide 17: Comment on energy ranges
450 GeV to 3.2 TeV is actually modest compared to all other machines
No sensible reason to lower SPS extraction energy….
…what would an ‘ideal’ chain look like in this respect?
Chart: Addition of 3.2 TeV HEB to existing LHC injector chain
| 2 | 26 | 450 | 3200 | 50000
 | 12.5 | 13 | 17.3077 | 7.1111 | 15.625

## Slide 18: Comment on energy ranges
450 GeV to 3.2 TeV is actually modest compared to all other machines
No sensible reason to lower SPS extraction energy….
…what would an ‘ideal’ chain look like in this respect?
Chart: Addition of 3.2 TeV HEB to existing LHC injector chain
| 2 | 26 | 450 | 3200 | 50000
 | 12.5 | 13 | 17.3077 | 7.1111 | 15.625
Chart: New FHC injector chain based on SPL-MEB-HEB
| 5 | 125 | 3200 | 50000
 | 31.25 | 25 | 25.6 | 15.625
 | 28.5714
Reuse SPS and LHC tunnels?
5 GeV SPL
125 GeV Medium Energy Booster
3.2 TeV High Energy Booster
  x25 range for both machines
  NC/SF technology for both

## Slide 19: Another FHC injector chain…
LINAC4
0-160 MeV (H-)
7 km MEB
5-125 GeV (x25)
27 km HEB
125 – 3.2 TeV (x25)
To FHC
3.2 - 50 TeV (x16)
LP-SPS
0.16 – 5 GeV (H-)

## Slide 20: Direct space charge….
Chart: Injection energy GeV
| 0.16 | 2 | 26 | 450 | 3200
Injection energy | 157 | 628 | 6912 | 26659 | 100000
 | 6912 | 26659 | 1346
~7 km ring in SPS tunnel with 5 GeV injection energy will have ~5x large Dqy than PS2 (for same bunch intensity and length)
  PS2 was designed for Dqy of -0.2 for 4e11 p+ at 25 ns
  Will already be at/above limit for 0.8e11 p+, with no margin for clever filling schemes etc.

## Slide 22: LHC ramp-rate and cycling limits
Factors which could limit the ramp rate for the LHC main dipoles and quadrupoles, between 0.5 and 3.8 T:
Maximum voltage per magnet (and insulation to ground)?
  “900 V for dipoles” (presently ~150 V for ramp-up)
Ramp-induced quench?
  “LHC dipoles could probably work up to 100 A/s (10 times the nominal) from the dB/dt capacity”
Effects on field quality?
  “negligible at 10 A/s, the interstrand resistance is about 5 times larger than lower acceptable limit. I would expect visible effects (requiring compensation) at 5 times the present ramp-rate, say 50 A/s”
QPS sensitivity?
  “this would be a real bugger. At present thresholds are around 100 to 200 mV, but we have magnets for which aperture compensation does not work well, not really clear why. It may be possible to double the detection threshold, but not much more (i.e. ramps at 20 A/s). Doing better will require new detection architecture”

## Slide 23: LHC ramp-rate and cycling limits
Limitation on mechanical lifetime from cycling?
  “Not that I know, but I guess that it should be analysed”
Power loss into cryo system?
Power drawn from network?
Eddy currents in beamscreen?
Additional factors:
Two-quadrants power converters will be needed for all circuits
Compensation rate for the corrector circuits. Higher dB/dt will imply larger band for the correction controls, higher voltage power supplies. The QPS of the correctors is not compensated, and already at the limit
Electrical lifetime at higher dielectric stress, not known
No need for the complication of IR's, should be better to change the layout in those areas

## Slide 24: LHC ramp-rate and cycling limits
What improvement could be gained by realistic upgrades and what is the associated cost, for example:
Extra powering sectorisation of the arcs (plus SC links etc.)?
  “Additional components required (feedboxes, shuffling modules) will have to fit in the space”
Cryo power upgrade?
  “will be required, but some limits are "built-in" the system (e.g. pipe diameters and lengths, heat transfer surfaces, flow conditions)”
Replacement of beamscreen e.g. with additional cryo capacity;
  “means removing the complete LHC from its feet”
Additional correction circuits/capacity?
New QPS?

## Slide 25: LHC ramp-rate and cycling limits
What also limits the overall cycle time for LHC, between 0.5 and 3.8 T, and what could be done about these:
Minimum essential pre-cycle?
  “can be removed”
Persistent current decay times?
Limits on d/dt(dI/dt) or d/dt(dB/dt)?
Could we be limited by the dipole/quadrupole lifetime?
What is the design lifetime of the dipoles/quadrupole?
Can we extrapolate already from the first years' operation to validate or refine this?
How many 'healthy' dipoles/quadrupoles would we expect to have at the end of HL-LHC operation?
Could we conceive of a new 3.2 TeV lattice running at e.g. 4.2 T with 10% fewer dipoles, to be used as spares/replacements,?
Can a refurbishment be foreseen?