## Slide 2: LEIR model A plan for understanding/upgrading the LEIR performance limitations M.Bodendorfer BE/ABP & LEIR team

## Slide 3: LEIR performance, 2013 and LIU Ions Why upgrade? All HI LHC experiments want by 2035: 10nb-1
Parameter | Unit | LEIR 2013 run | LEIR Baseline upgrade | LEIR Full upgrade
Pb charge state | [-] | 54+ |  | 
Output Energy | [GeV/u] | 0.0722 |  | 
In/Out Bρ | [Tm] | 1.138 / 4.8 |  | 
Inject. to next machine | [-] | 1 |  | 
Bunches/ring | [-] | 2 |  | 
Charge at flat bottom | Charges | ~6.0x1010 | 6.0x1010 | 1.1x1011
Total extracted charge | Charges | ~5.4x1010 | 5.4x1010 | 8.6x1010
From: Performance of the injectors with ions after LS1
D. Manglunki for the LIU-Ions team, CERN, Geneva, Switzerland, 2013

## Slide 4: LEIR NOMINAL cycle
6 injections. First at 215ms, then spaced 200ms. 200μs long.
Extraction
@ 2880ms
capture in H2, H4 @ 1780ms
Up to 50% beam loss
(Coasting beam)
B-field
Start of
Beam loss
BHN current [100A]

## Slide 5: Finding a solution for LEIR
What we have found so far:
  Working point on 4th order resonance
  Transverse instability at RF capture
  Positive chromaticity in the vertical plane
  Beam loss associated to RF-capture rather than magnetic Ramp
Proposed MDs series dedicated to each of the above findings in 2014, 2015.

## Slide 6: 1. LEIR working point Design tune: QH=1.82, QV=2.72
Qx - Qy = -1
2Qx - Qy = 1
4Qy = 11
Qx + 3Qy = 10
3Qy = 8
2Qx + 2Qy = 9

## Slide 7: 2. LEIR Instability at RF capture and ramp
Before: -20ms
After: +20ms
Beam loss continues
1815ms
Beam loss starts here
Pickups output:

## Slide 8
✗
Bad fit
Bad fit
RF capture
RF capture
Displayed
Displayed
✗
Coasting beam & Ecooling
Coasting beam & Ecooling
Beam
loss
Beam
loss
3. Tune and chromaticity measurement after RF-capture

## Slide 9
Good fit
RF capture
RF capture
Displayed
✓
Displayed
Good fit
(LSQR quadratic)
✓
Beam
loss
Beam
loss
3. Tune and chromaticity measurement after RF-capture
Coasting beam & Ecooling
Coasting beam & Ecooling

## Slide 10: 3. Horizontal chromaticity < 0 (after RF capt.) (Horizontal design chromaticy = -1)
Good fit
Fit slop
(Linear chromaticity)
Residual of fit
Intensity

## Slide 11: 3. Vertical chromaticity > 0 (after RF capt.) (Vertical design chromaticy = -1)
Good fit
Fit slope
(Linear chromaticity)
Residual of fits
Intensity

## Slide 12: 4. Disentangling beam loss from magnetic ramp
Start mag. ramp
Beam loss with advanced RF-capture
Beam dump
Start of
Beam loss
Advanced by 300ms
BHN current [100A]
RF beam bunching

Higher peak density increases
space-charge

Individual particle tune shift

Individual particles cross resonance

Loss

## Slide 13: Summary of observations
Clues from measurements:
  Working point on 4th order resonance
  Transverse instability at RF capture
  Positive chromaticity in the vertical plane
  Beam loss associated to RF-capture rather than mag. ramp
BHN current [100A]
4.
2.
3.
1.

## Slide 14: MD suggestions
Measurement clue and suggested MD:
  Working point on 4th order resonance
    Explore other regions of the tune space (Qy > 2.75)
    Investigate chromaticity for new tune regions

## Slide 15: MD suggestions
Measuremene clue and suggested MD:
  Working point on 4th order resonance
  Transverse instability at RF capture
    Study effect of the transverse damper
    Investigate origin of instability with transv. damper off

## Slide 16: MD suggestions
Measuremene clue and suggested MD:
  Working point on 4th order resonance
  Transverse instability at RF capture
  Positive chromaticity in the vertical plane
    Chrom. < 0 for both planes
    Qmeter software from PS

## Slide 17: MD suggestions
Measuremene clue and suggested MD:
  Working point on 4th order resonance
  Transverse instability at RF capture
  Positive chromaticity in the vertical plane
  Beam loss associated to RF-capture rather than magnetic ramp
    Try RF-capture with different beam parameters (bunch length and transverse emittances) to check the impact of space-charge.
    Study the effect of electron cooling and acceleration.

## Slide 18: Conclusion & Summary
Further reading:
Plans for the upgrade of CERN’s Heavy Ion Complex, D. Manglunki et al., CERN-ACC-Note-2013-034
LINAC3 tank2 phase change and LEIR performance, M. Bodendorfer, R. Scrivens, CERN-ATS-Note-2013-035
Chromaticity in LEIR performance, M. Bodendorfer & LEIR team, CERN-ACC-Note-2013-0032
Longitudinal emittance reduction in LEIR of ion beams for LHC, M. E. Angoletta, M. Bodendorfer, A. Findlay. S. Hancock, D. Manglunki, upcoming
So far we have:
found working point on/close to resonance
found transverse instability
found wrong chromaticity
Pb54+ beam loss associated to RF-capture rather than the magnetic ramp
The Plan:
Dedicated MD series for each finding.
Further disentangling of space-charge, transverse instability and resonant beam loss.
Refine the optics model of LEIR.