## Slide 2: Beams after LS1
Giovanni Rumolo and Hannes Bartosik
Acknowledgments: G. Arduini, H. Damerau, J. Esteban-Müller, A. Findlay, R. Garoby, S. Gilardoni, B. Goddard, S. Hancock, G. Iadarola, B. Mikulec, Y. Papaphilippou, E. Shaposhnikova, R. Tomás, PS & SPS Operation crews
LIU Day, 11/04/2014
Notes: Keywords
e-cloud status in PS and SPS
scrubbing plans in SPS and LHC
BCMS for 25 ns in LHC
8b+4e option

## Slide 3: Outline
The LHC beams
  Single bunches (probe and indiv)
  50 and 25 ns beams (standard and BCMS)
  Doublet beam (scrubbing)
  8b+4e (low e-cloud)
Summary

## Slide 4
The LHC beams
  Single bunches (probe and indiv)
  Achieved performance in 2013
  50 and 25 ns beams (standard and BCMS)
  Doublet beam (scrubbing)
  8b+4e (low e-cloud)
Summary

## Slide 5: LHCPROBE & LHCINDIV – specs @LHC injection
 | LHCPROBE | LHCINDIV
Intensity [p/b] | 5 x 109 – 2 x 1010 | 2 x 1010 – 3 x 1011
Transverse emittance, 1s [mm] | 1 | < 2.5
Longitudinal emittance [eVs] | 0.35 | 0.35 – 0.5
LHCPROBE usually below or about 1010 p/b, transverse emittance not critical
LHCINDIV parameter range also extended in MDs to produce single bunches with up to 4.5 x 1011 p/b and/or with lower longitudinal emittances (down to 0.15 eVs) at SPS injection
  Accelerate and extract high intensity variants for possible impedance or beam-beam studies ?

## Slide 6: LHCPROBE & LHCINDIV – 2013 status
Since 2013, new production mechanism in the PSB to cover parameter range for both these beams (S. Hancock, CERN-ATS-Note-2013-040 MD)
Based on longitudinal blow up (C16 voltage) during the first part of the cycle for intensity setting
Excellent intensity shot-to-shot reproducibility preserving the 6D phase space unchanged for different intensity values
Baseline for post-LS1

## Slide 7
The LHC beams
  Single bunches (probe and indiv)
  50 and 25 ns beams (standard and BCMS)
  Achieved performance in 2012
  Expected performance after LS1
  Doublet beam (scrubbing)
  8b+4e (low e-cloud)
Summary

## Slide 8: LHC25 and LHC50 (std & BCMS) – pre-LS1 status
50 ns and 25 ns beam at the SPS extraction in 2012 (Q20)
Combined wire-scans at end of SPS flat bottom (values cross-checked with LHC) and intensity measured at SPS flat top after scraping
Transport through PS/SPS nearly within intensity loss and emittance blow up budgets (except for LHC25 std)
Budget | PS | SPS
Dex,y /ex0,y0 | 5% | 10%
-DN/N0 | 5% | 10%

## Slide 9: LHC25 and LHC50 Post-LS1: Expected performance
Recover 2012 performance
  Machines exposed to air, electron cloud
Potential for higher bunch intensity
  Possibly extended reach thanks to the upgraded longitudinal feedback in the PS
  25 ns up to 1.3 x 1011 p/b at the SPS extraction (limited by RF power and longitudinal instabilities)
Potential for higher brightness
  Move RF manipulations in the PS to 2.5 GeV (instead of 1.4 GeV)
    Larger longitudinal emittance from the PSB
      Possible thanks to PSB control of longitudinal parameters along the cycle and at extraction
    Space charge alleviated by both longer bunches and larger momentum spread
  Improve SPS space charge limit (for 50 ns BCMS)
    Working point optimization for high brightness beams

## Slide 10: SPS scrubbing in 2014/15
2014
2015
Sept.
Nov.
Mar.
Aug.
LIU-SPS Review
Scrubbing or coating?
SCRUBBING RUN II (2 weeks)
Beams  High intensity 25 ns, scrubbing beam (doublet)
Main goal:
Determine whether scrubbing also works for high intensity
SPS MDs
  Set up the doublet beam with acceleration (long cycle)
  Push the intensity to higher values for 25 ns beam
SCRUBBING RUN I (weeks 39 & 40)
Beam  Standard 25 ns
Main goals:
Qualify scrubbing after long shut-down (efficiency and duration)
Recover 2012 performance
Notes: Scrubbing run I: operational recovery
Scrubbing run II: for LIU

## Slide 11: Beam parameters at LHC injection after LS1
25 ns | Intensity (p/b) | Emittance (mm)
Standard | 1.3 x 1011 | 2.4
BCMS | 1.3 x 1011 | 1.3
50 ns | Intensity (p/b) | Emittance (mm)
Standard | 1.7 x 1011 | 1.6
BCMS | 1.7 x 1011 | 1.1
Assuming:
Transport in the PS and SPS within budgets
Benefits from reviewed longitudinal parameters in the PSB – PS transfer
Successful SPS scrubbing after exposure to air during LS1
Summary tables

## Slide 12
The LHC beams
  Single bunches (probe and indiv)
  50 and 25 ns beams (standard and BCMS)
  Doublet beam (scrubbing)
  Achieved performance in 2012/13
  Expected performance after LS1
  8b+4e (low e-cloud)
Summary

## Slide 13: Doublet beam
Machine tests in the SPS at the end of 2012-13 run
  Doublet production scheme at SPS injection validated
  E-cloud enhancement experimentally demonstrated
Production scheme
  Injection of trains of 72 x 10ns long bunches with 1.7e11 p/doublet on unstable phase and capture in two neighboring buckets in the SPS (done)
  Acceleration on slower ramp and extraction to LHC of 1.6e11 p/doublet (to be set up, possible beam quality degradation)
  Should be fine in LHC  only interlocked BPMs to be checked with doublets
4
2
8
6
0
1
2
3
Time [ms]
200 MHz RF Voltage [MV]
4
-2
0
1st inj.

## Slide 14: Doublet beam
Machine tests in the SPS at the end of 2012-13 run
  Doublet production scheme at SPS injection validated
  E-cloud enhancement experimentally demonstrated
Production scheme
  Injection of trains of 72 x 10ns long bunches with 1.7e11 p/doublet on unstable phase and capture in two neighboring buckets in the SPS (done)
  Acceleration on slower ramp and extraction to LHC of 1.6e11 p/doublet (to be set up, possible beam quality degradation)
  Should be fine in LHC  only interlocked BPMs to be checked with doublets
4
2
8
6
0
1
2
3
Time [ms]
200 MHz RF Voltage [MV]
4
-2
0
1st inj.
 | Intensity (p/doublet) | Emittance (mm)
Doublets | 1.6 x 1011 | > 3.0

## Slide 15
The LHC beams
  Single bunches (probe and indiv)
  50 and 25 ns beams (standard and BCMS)
  Doublet beam (scrubbing)
  8b+4e (low e-cloud)
  Expected performance after LS1
Summary

## Slide 16: 8b+4e scheme
Trains with 4 missing bunches every 8 bunches (H. Damerau, RLIUP)
  Allows for larger intensity per bunch
  Is expected to reduce e-cloud effects
Production
  Std scheme  Unbalance h = 7  21 triple split into a double split, leaving empty bucket – bunch pattern 6x(8b+4e) + 8b
  BCMS  merging and triple splitting suppressed – bunch pattern 3x(8b+4e) + 8b
  Simulation
Ekin = 2.5 GeV
  Simulation
Ekin = 2.5 GeV
Standard scheme
BCMS
  Simulation
Ekin = 2.5 GeV
  Simulation
Ekin = 2.5 GeV

## Slide 17: 8b+4e scheme
Standard scheme
Limited to 1.8 x 1011 p/b because of longitudinal instabilities in the SPS
Brightness limited by
  PSB brightness for standard scheme
  No outstanding bottleneck for BCMS
BCMS

## Slide 18: 8b+4e scheme
Standard scheme
Limited to 1.8 x 1011 p/b because of longitudinal instabilities in the SPS
Brightness limited by
  PSB brightness for standard scheme
  No outstanding bottleneck for BCMS
BCMS
25 ns (8b+4e) | Intensity (p/b) | Emittance (mm) | Bunch pattern
Standard | 1.8 x 1011 | 2.3 | 6 x (8b+4e) + 8b
BCMS | 1.8 x 1011 | 1.4 | 3 x (8b+4e) + 8b

## Slide 19
The LHC beams
  Single bunches (probe and indiv)
  50 and 25 ns beams (standard and BCMS)
  Doublet beam (scrubbing)
  8b+4e (low e-cloud)
Summary

## Slide 20: Summary
Lots of MD time needed to produce “old” beams with new schemes and “new” beams
LHC start up and scrubbing
  LHCPROBE and LHCINDIV with new production mechanism in the PSB
  LHC50 standard
    Up to 1.7 x 1011 p/b with ex,y=1.6 mm
  LHC25 standard
    Up to 1.3 x 1011 p/b with ex,y=2.4 mm
  LHC25 doublet
    Up to 1.6 x 1011 p/doublet with ex,y> 3.0 mm
Physics
  LHC50 (standard or BCMS)
    BCMS up to 1.7 x 1011 p/b with ex,y=1.1 mm
  LHC25 BCMS
    Up to 1.3 x 1011 p/b with ex,y=1.3 mm
  8b+4e as alternative if LHC scrubbing is not enough to run with LHC25 BCMS
    Up to 1.8 x 1011 p/b with ex,y=2.3/1.4 mm (std/BCMS)

## Slide 22: Post-LS1: PSB – PS transfer
Constraints on longitudinal emittance per bunch at PS injection
Bunches to the SPS with ez=0.35 eVs
Quality of RF manipulations at Ekin=2.5 GeV
Bunches crossing transition on h=21 with ez<1 eVs
PSB available voltage (h1+2) to obtain the above bunch lengths
Recombination kicker rise time:
 | Ekin | Bucket length | Max bunch length | Bunch length (pre-LS1)
h=7 (std) | 1.4 GeV | 327 ns | 220 ns | 180 ns
h=9 (BCMS) | 1.4 GeV | 255 ns | 150 ns | 150 ns
Kinetic energy, Ekin | Rise time
1.4 GeV | 105 ns

## Slide 23: Post-LS1: PSB – PS transfer
Constraints on longitudinal emittance per bunch at PS injection
Bunches to the SPS with ez=0.35 eVs
Quality of RF manipulations at Ekin=2.5 GeV
Bunches crossing transition on h=21 with ez<1 eVs
PSB available voltage (h1+2) to obtain the above bunch lengths
Recombination kicker rise time:
 | Ekin | Bucket length | Max bunch length | Bunch length (pre-LS1)
h=7 (std) | 1.4 GeV | 327 ns | 220 ns | 180 ns
h=9 (BCMS) | 1.4 GeV | 255 ns | 150 ns | 150 ns
Kinetic energy, Ekin | Rise time
1.4 GeV | 105 ns
RF Manipulation: | @1.4 GeV | @2.5 GeV
50 ns (Std/BCMS) | 1.2/0.9 eVs | 1.9/0.9 eVs
25 ns (Std/BCMS) | 1.2/0.9 eVs | 2.8/1.5 eVs