## Slide 1: LHC expectations on injectors (after LS1 and in the long term…)
R. De Maria
Thanks to G. Arduini, O. Brüning, H. Bartosik, R. Bruce, R. Calaga, F. Cerutti,
H. Damerau, L. Esposito, S. Fartoukh, M. Fitterer, R. Garoby, S. Gilardoni,
M. Giovannozzi, B. Goddard, B. Gorini, M. Lamont, E. Métral, N. Mounet,
T. Pieloni, S. Redaelli, L. Rossi, G. Rumolo, E. Todesco, R. Tomas,
HL-LHC and LIU teams.

## Slide 2: Introduction
  General remark:
  As the aim of the LHC is saturating the experiments with useful luminosity, the Injectors aims at saturating the LHC capabilities.
  Once this regime is achieved, machine availability and reliability becomes the only effective lever arm for performances.
  Tentative schedule before HL-LHC:
  Run II: Integrate luminosity at 13 TeV center of mass. Target 25 ns operations and only if necessary fall back to 50 ns or 8b+4e.
  Run III: Maximize LHC performance. Prepare for HL-LHC times.
  Target performance:
  LHC program: Integrate 300 fb-1 or more before LS3.
  HL-LHC program: Integrate 3000 fb-1 or more for the following decade.

## Slide 3: Injectors’ parameters as seen by the LHC
Bunch intensity: Will beams saturate the cooling capacity due to e-cloud or be unstable?

## Slide 4: Beam current limitations
  Baseline 2.2 1011 ppb, current ~1 A.
  Assuming e-cloud issues solved.
  Couple bunch instability stabilized by the damper.
  Single bunch instability threshold far in the present model (with metallic collimator) or stabilized by head-on tune spread.
Understanding intensity limitations in the LHC is constantly evolving.
O. Bruning, R. Assmann,
E. Métral and teams

## Slide 5: E-cloud
G. Rumolo, G. Iadarola
Arc quadrupole, 2808b, 1 beam
SEY=1.3
E-cloud solution currently relying on:
Scrubbing for dipoles for suppression of electron cloud (SEY 1.3-1.4). (e.g. doublet beams for 25 ns scrubbing)
Expected to be difficult to eliminate the electron cloud in the quadrupoles (SEY<1.2-1.3).
Effects on on beam only at injection if ecloud in the dipoles. Can be cured if dipoles are scrubbed.
Cryo power compatible with the electron cloud in the quadrupoles only.
Based on simulations

## Slide 6: Injectors’ parameters as seen by the LHC
Bunch intensity: Will beams saturate the cooling capacity due to e-cloud or be unstable?
Emittance: Will the emittance be preserved during cycle? Is sufficiently small? Can small emittance be traded with intensity or number of bunches?

## Slide 7: LHC Injection to Collisions
R. Tomas, O. Dominguez
5% intensity loss assumed: when and where do we loose? Transfer lines, septa, TDI, LHC (BLM sunglasses), injection, ramp and setup limits should be assessed.
20% emittance blow-up budget, implies:
  Control of the additive sources of blow-up.
  Control of the blow-up due to electron clouds.
  Impedance reduction with metallic collimators.
  10 cm bunch length during injection to stable beam.
  Lower limit on starting emittance.
ϵcol ≈ ϵinj + 0.2 Nb /ϵinj [1011/µm]
Assuming: 10% blowup on top of IBS

## Slide 8: Transmission of Beam parameters
 | Bunch Spacing | Bunch Population Inj. | Emit. Std/BCMS Inj. | Bunch Population Coll. | Emit. Std/BCMS Coll.
LHC | 25 ns | 1.3 · 1011 | 2.4 µm | 1.2 · 1011 | 2.8 µm
 |  |  | 1.3 µm |  | 1.7 µm
 | 50 ns | 1.7 · 1011 | 1.6 µm | 1.6 · 1011 | 2.0 µm
 |  |  | 1.1 µm |  | 1.6 µm
 | 8b+4e | 1.8 · 1011 | 2.3 µm | 1.7 · 1011 | 2.7 µm
 |  |  | 1.4 µm |  | 1.9 µm
LIU | 25 ns | 2.0 · 1011 | 1.4 µm | 1.9 · 1011 | 1.9 µm
 |  |  | 1.9 µm | 1.9 · 1011 | 2.3 µm
HL-LHC | 25 ns | 2.3 · 1011 | 2.3 µm | 2.2 · 1011 | 2.5 µm
 | 50 ns | 3.7 · 1011 | 2.7 µm | 3.5 · 1011 | 3.0 µm

## Slide 9: Injectors’ parameters as seen by the LHC
Bunch intensity: Will beams saturate the cooling capacity due to e-cloud or be unstable?
Emittance: Will the emittance be preserved during cycle? Is sufficiently small? Can small emittance be traded with intensity or number of bunches?
Bunch spacing: Will collisions saturate the experiments?

## Slide 10: Bunch Spacing and Filling Schemes
Luminosity is proportional to nbunches . If experiments limited by pile-up,
maximum luminosity and integrated luminosity is proportional to nbunches too.
Filling schemes with 12 SPS injections in the LHC.
25ns: 2592; 50 ns: 1296; 8b+4e: 1728.
B. Gorini
Filling scheme | Total | IP1-5 | IP2 | IP8
BCMS: 48b 6 Ps inj, 12 SPS inj | 2604 | 2592 | 2288 | 2396
Standard: 72b 4 Ps inj, 12 SPS inj | 2748 | 2736 | 2452 | 2524

## Slide 11: Assumptions on experimental conditions
Average pile-up limit in IP1, IP5:
  Maximum 50 event per crossing for after LS1;
  Maximum 140 events per crossing for HL-LHC with
  1.3 event/mm baseline but 0.7 event/mm stretched target;
Average pile-up limit in IP8: 4.5 events per crossing.
Max lumi leveled in IP2: 2 1031 cm-2s-1.
Burn-off and pile-up estimation based on:
  Assumed visible cross-section: 85 mb in IR1/5, 75 mb in IP8;
  Assumed total cross-section: 110 mb.
A. Ball, B. Di Girolamo, B. Gorini, R. Jacobsson

## Slide 12: Bunch spacing and pile-up
 | Bunch Spacing | Bunch Population | Emit. Std BCMS | Pile-up Max/Lev | Daily Lumi [fb-1] | Fill duration [h]
LHC 6.5 TeV β*=60cm | 25 ns | 1.2 · 1011 | 2.8 µm | 30/50 | 0.58 | 10.1
 |  |  | 1.7 µm | 50/50 | 0.78 | 7.5
 | 50 ns | 1.6 · 1011 | 2.0 µm | 76/50 | 0.53 | 8.1(5.6)
 |  |  | 1.6 µm | 95/50 | 0.52 | 7.8(4.4)
 | 8b+4e | 1.7 · 1011 | 2.7 µm | 75/50 | 0.72 | 8.5(4.7)
 |  |  | 1.9 µm | 90/50 | 0.70 | 8.3(5.9)
LIU 7 TeV β*=15cm | 25 ns | 1.9 · 1011 | 2.3 µm | 419/140 | 2.99 | 7.2(5.7)
 |  | 1.9 · 1011 | 1.9 µm | 510/140 | 2.93 | 7.8(6.7)
HL-LHC 7 TeV β*=15cm | 25 ns | 2.2 · 1011 | 2.5 µm | 517/140 | 3.17 | 8.6(7.3)
 | 50 ns | 3.5 · 1011 | 3.0 µm | 517/140 | 1.75 | 15(14.1)

## Slide 13: HL-LHC Performance reach
Assuming 80 days of successful fills limited by leveled luminosity and fill durations, how much luminosity may we integrate in one year?
Average fill
duration 2012
Simplest model that bounds integrated performance:
run at max allowed luminosity for half of the scheduled physics until a failure occurs.

## Slide 14: HL-LHC Performance reach
Assuming 80 days of successful fills and a given peak luminosity, available current, how much luminosity could we integrate in one year?
Average fill
duration 2012
Adding a simple model of peak machine luminosity and burn-off decay (F. Zimmerman).

## Slide 15: HL-LHC Performance reach
Assuming 80 days of successful fills and a given peak luminosity and available current, how much luminosity could we integrate in one year?
→ Maximize leveled luminosity by pile-up limit and number of bunches,
→ Maximize probability of long fills
→ Obtain long fills
Average fill
length 2012

## Slide 16: HL-LHC Performance reach
16
Assuming 80 days of successful fills and a given peak luminosity how much luminosity may we integrate in one year?
→ Maximize leveled luminosity by pile-up limit and number of bunches,
→ Maximize probability of long fills
→ Obtain long fills
Average fill
length 2012

## Slide 17: HL-LHC Performance reach
17
Assuming 80 days of successful fills and a given peak luminosity how much luminosity may we integrate in one year?
→ Maximize leveled luminosity by pile-up limit and number of bunches,
→ Maximize probability of long fills
→ Obtain long fills
Average fill
length 2012

## Slide 18: HL-LHC Performance reach
18
Assuming 80 days of successful fills and a given peak luminosity how much luminosity may we integrate in one year?
→ Maximize leveled luminosity by pile-up limit and number of bunches,
→ Maximize probability of long fills
→ Obtain long fills by bunch population
Average fill
length 2012

## Slide 19: Open questions for the LHC
200 MHz: If used as main RF in LHC, can it lift SPS bunch population limit?
Bunch-by-bunch variations: Does it affect performance (or how much the differences will limit the average)?

## Slide 20: Performance of different scenarios (7 TeV)
 | Nb coll [1011] | e*n coll [mm] | Min b* (xing / sep) [cm] | Xing angle [mrad] | # Coll. Bunches IP1,5 | Lpeak [1034 cm-2s-1] | Llev [1034 cm-2s-1] | Lev. time [h] | Opt. Fill length [h] | η6h [%] | ηopt [%] | Avg. Peak- pile-up density [ev./mm]
RLIUP2 | 1.5 | 1.36) | 15/15 | 341 | 2592 | 19.0 | 4.8 | 4.7 | 6.0 | 63.4 | 63.4 | 0.94
LIU-BCMS | 1.9 | 1.656) | 13.5/13.53) | 405 | 2592 | 23.4 | 4.8 | 6.7 | 7.8 | 61.0 | 57.5 | 0.98
LIU-STD | 1.9 | 2.26 | 14.5/14.53) | 457 | 2736 | 17.0 | 5.06 | 5.7 | 7.2 | 58.2 | 56.4 | 1.01
HL-Flat | 2.2 | 2.5 | 30/7.51) | 3352)/550 | 2736 | 18.6 | 5.06 | 7.0 | 8.4 | 57.8 | 53.5 | 1.12
HL-Round | 2.2 | 2.5 | 15/15 | 4762)/590 | 2736 | 20.1 | 5.06 | 7.3 | 8.6 | 57.8 | 53.1 | 1.03
LIU-BCMS | 1.9 | 1.65 | 13.5/13.53) | 579 | 2592 | 23.4 | 6.875) | 4.6 | 6.4 | 51.4 | 51.3 | 1.34
HL-Round | 2.2 | 2.5 | 15/15 | 473 | 2736 | 20.1 | 7.245) | 4.8 | 7.0 | 48.2 | 47.4 | 1.37
HL-SRound | 2.2 | 2.5 | 10/104) | 600 | 2736 | 26.8 | 7.245) | 5.8 | 7.6 | 47.6 | 45.7 | 1.55
1) compatible with crab kissing scheme (S. Fartoukh)
2) BBLR wire compensator assumed to allow 10σ
3) b* could be reduced to 14.5 and 13.5 cm at constant aperture
4) Ultimate collimation settings
5) Pile-up limit at 200 event/ crossing 6) 30% blow-up from IBS makes 1.85 um is more likely

## Slide 21: Conclusion
Injector beam parameters should aim at saturating the LHC and experiment capabilities.
When experiments are not limited by total pileup, BCMS beams are an effective tool for increasing performance.
For HL-LHC times, the LHC expects maximum injectable bunch population with the maximum number of bunches.
Present LIU offer is a close match, but increasing bunch population is a key to exploit large accepted luminosity or long fill durations.