## Slide 2
PS: longitudinal instabilities and damper
Acknowledgments: H. Damerau, G. Favia S. Gilardoni ,
M. Migliorati, M. Morvillo, M. Paoluzzi, G.Sterbini
Speaker: L. Ventura
LIU day
11 April 2014

## Slide 3
Outlook
The PS RF system
Beam loading & cures
  Wideband negative feedback
Coupled-bunch instabilities measurements & simulations
Feedback system and new longitudinal kicker
10 MHz system impedance model and simulations
Summary and discussion

## Slide 4
Outlook
The PS RF system
Beam loading & cures
  Wideband negative feedback
Coupled-bunch instabilities measurements & simulations
Feedback system and damper
10 MHz system impedance model and simulations
Summary and discussion

## Slide 5
The PS RF system
The PS machine contains cavities operating at different frequencies. The 10 MHz cavities are the most important because they accelerate the bunches to the desired energy and perform the triple splitting.
The 10 MHz cavities (10+1 double gap cavities tuneable from 2.8 to 10 MHz) are driven by amplifiers based on electron tubes (vs solid state ones), for reasons of radiation hardness and power dissipation.
The 10 MHz cavity with a power up to 20 kV, it is tuneable from 2.8 MHz to 10.1 MHz, h = [6...21].
Courtesy of Carlo Rossi –http://indico.cern.ch/event/160434/contribution/11/material/slides/0.pdf
Finemet © cavity

## Slide 6
Injection
STABLE
UNSTABLE
Beam Instabilities
After triple splitting and transition
Impedance interaction
Not a correct population of the bucket
Time during cycle [ns]
Time during cycle [ns]
Machine circumference [ns]
Machine circumference [ns]
Double splitting at high energy
New LHC beam planned for the LIU project -> Increased intensity ->
Increased voltage in the cavity
induced by the beam
Beam instabilities
ppb at extraction
The PS has a complex multi-harmonic system which determines the longitudinal structure of the bunch train for LHC. The 25 ns LHC beam is prepared in the PS.
In h=21, with 100 ns bunch spacing -> cross-talk of bunches which are coupled with the longitudinal impedance of the PS -> LONGITUDINAL INSTABILITY OF THE BEAM

## Slide 7
Beam instabilities & Feedback system
2) Coupled-bunch Feedback acts on the beam
1) Wideband Feedback acts on the voltage sent to the cavity
BEAM LOADING
Cures:
Wideband negative feedback
1-turn delay feedback (see D.Perrelet talk)
Action: Reduce the impedance seen by the beam
REDUCE
COUPLED-BUNCH INSTABILITY
Cures:
Coupled-bunch feedback
New longitudinal kicker -> Finemet © cavity
Action: damp unstable oscillation modes caused
by the 10 MHz cavities (as found in measurements
and simulations)
COMPENSATE

## Slide 8
Outlook
The PS RF system
Beam loading & cures
  Wideband negative feedback
Coupled-bunch instabilities measurements & simulations
Feedback system and damper
10 MHz system impedance model and simulations
Summary and discussion

## Slide 9
Beam loading &
wideband negative feedback
Any cavity close to its fundamental mode can be represented as a parallel RLC resonator.
The beam and the RF amplifier are modelled as ideal current generators.
R= final resistance of the amplifier and cavity losses
= provided by the power RF amplifier
= current due to the beam producing a voltage
in the cavity called Beam loading voltage
V = total voltage in the cavity ()
Maintain V constant, (in the limit of the input signal), minimizing the effect of -> minimize
Reduce the impedance seen by the beam
BEAM LOADING VOLTAGE

## Slide 10
f
A
Cavity
+
Reduce the impedance seen by the beam:
Increase the loop gain
Wideband negative feedback
in the 10MHz cavity
Actual situation in the 10 MHz cavity
OBJECTIVE: INCREASE OF
UP TO 29dB (in the limit of stability)
Why don’t increase just ?
Closed loop gain
Not able any more to give to the cavity the per gap
G.Favia, V. Desquiens,
M. Morvillo
= feedback factor
= forward gain

## Slide 11
STAGE | GAIN Old configuration | GAIN Change of tubes working point
Predriver | 11.1 dB | 12.76 dB
Driver | 27 dB @3MHz 24.35 dB @10MHz | 28.8 dB @3MHz 25.9 dB @10MHz
Final | 42.5 dB @3MHz 38.8 @10MHz | 44.6 dB @3MHz 42.17 dB @10MHz
TO DO NEXT -> verify that with the new working points the amplificator (in the limit of stability and respecting the phase and gain margin) give to the cavity 10 kV per gap.
Driver
Predriver
Final
Work in progress: change the working point
of the electron tubes
2014 preliminary results

## Slide 12
Outlook
The PS RF system
Beam loading & cures
  Wideband negative feedback
Coupled-bunch instabilities measurements & simulations
Feedback system and damper
10 MHz system impedance model and simulations
Summary and discussion

## Slide 13
Coupled-bunch instabilities
Transverse (betatron) and longitudinal (synchrotron )
oscillations normally damped by natural damping.
Since wakefields are proportional to the bunch charge, instabilities are current dependent.
If the growth rate is stronger than the natural damping the oscillation gets unstable.
Wake fields act back on the beam and produces growth
of oscillations.
‘Theory and performances of the longitudinal active damping system for the CERN PS Booster’ F.Pedersen and F.Sacherer
Example of an n = 12 mode
Interaction of the particles with cavity-> wakefields.
Beam in a synchrotron ring made of bunches of charged particles.

## Slide 14
Up to present intensities (achieved ppb at extraction) coupled-bunch instabilities are damped using a feedback system limited to the first two dominant oscillation modes, but it will become insufficient for the beam parameters planned within the LHC upgrade (ppb at extraction).
State of the art of coupled-bunch instabilities in the PS
Longitudinal coupled-bunch instabilities are observed in the CERN PS during acceleration (above transition energy) and on the flat-top.
For LHC-type of beam in the PS with bunch spacing below 100 ns only the motion of the centre of mass of the bunches has been observed.
New coupled-bunch feedback system based on the 1-turn delay scheme
FB OFF
FB ON

## Slide 15
Measured damping rate with feedback on
Corrected for natural damping
Zero damping at zero gain
Natural damping independent from gain
A large amount of measurements has been done to check the behaviour of the coupled bunch instabilities in the machine with the feedback system, studying the damping rate vs many parameters like gain, intensity, emittance and cycle time.
Spare 10MHz cavity
Finemet © cavity
Coupled-bunch feedback & measurements
H. Damerau

## Slide 16
New PS longitudinal kicker cavity
Feedback kicker requirements | 
Frequency range | 0.4-5.5 MHz
RF voltage per sideband, |  1kV
Maximum total RF voltage, | 5kV
Un-damped shunt impedance at | <200Ω
Feedback kicker requirements | 
Frequency range | 0.4-5.5 MHz
 |  1kV
 | 5kV
 | <200Ω
straight section 02
Finemet cavity used in LEIR but to accelerate
During the first long shutdown (LS1) in 2013-2014, a new digital feedback has been installed, covering all coupled-bunch modes with a new longitudinal cavity based on the wideband frequency characteristics of Finemet © magnetic alloy and driven by solid-state amplifiers.
M. Paoluzzi
Installed in 2014

## Slide 17
Outlook
The PS RF system
Beam loading & cures
  Wideband negative feedback
Coupled-bunch instabilities measurements & simulations
New feedback system and damper
10 MHz system impedance model and simulations
Summary and discussion

## Slide 18
  Measurements done in 2013 before LS1 : coupled-bunch feedback and the spare cavity have been used to excite and damp coupled-bunch oscillation.
Need of SIMULATIONS to:
Study and deeply understand these instabilities
Predict the beam behaviour with the new LIU parameters
Longitudinal Coupled-Bunch simulation code
Tracks the longitudinal centre of mass motion of all the bunches, by including wakefields effects.
The feedback system in the code has been implemented according with the PS installation.
‘A time domain simulation code of the longitudinal multibunch instabilities’, M.Bassetti, A.Ghigo, M.Migliorati, L.Palumbo, M.Serio
Coupled-Bunch Simulations

## Slide 19
Re[Z] [Ω]
Impedance model of the 10 MHz RF system
Real part of the total impedance of the 10 MHz cavities at the revolution harmonics @ 3.3MHz
Coupled-bunch growth rate obtained by theoretical approach
ω/ω0
Re(Z)
Fit
@ 3.3MHz
@ 10.1MHz
Re(Z)
Fit
ω/ω0
Re[Z] [Ω]

## Slide 20
We compare the rise time of the instability obtained with simulations with
the CB growth rate from the eigenvalues system (PAC07).
Simulations vs. stability data in h=7 (3.3MHz)
Simulations results |  |  | 
Mode Number | 1 | 2 | 3
Growth Rate | 544ms | 467ms | 1.91s
Paper results |  |  | 
Mode Number | 1 | 2 | 3
Growth Rate | 400ms | 333ms | 1s
Parameters | Value
Beam energy (GeV) | 13
RF voltage (kV) | 165
Synchrotron frequency (Hz) | 230
Total beam intensity (ppp) | 9x
Parameters | Value
Beam energy (GeV) | 13
RF voltage (kV) | 165
Synchrotron frequency (Hz) | 230
Total beam intensity (ppp) | 
Longitudinal coupled-bunch instabilities in the CERN PS H.Damerau,S.Hancock,C.Rossi,E.Shaposhnikova,J.Tuckmantel,J.-L. Vallet

## Slide 21
Simulations results |  |  | 
Mode Number | 1 | 2 | 3
Growth Rate | 544ms | 467ms | 1.91s
Paper results |  |  | 
Mode Number | 1 | 2 | 3
Growth Rate | 400ms | 333ms | 1s
Parameters | Value
Beam energy (GeV) | 13
RF voltage (kV) | 165
Synchrotron frequency (Hz) | 230
Total beam intensity (ppp) | 9x
Parameters | Value
Beam energy (GeV) | 13
RF voltage (kV) | 165
Synchrotron frequency (Hz) | 230
Total beam intensity (ppp) | 
The code is a good tool to simulate coupled-bunch instabilities
Good agreement!!
Longitudinal coupled-bunch instabilities in the CERN PS H.Damerau,S.Hancock,C.Rossi,E.Shaposhnikova,J.Tuckmantel,J.-L. Vallet
We compare the rise time of the instability obtained with simulations with
the CB growth rate from the eigenvalues system (PAC07).
Simulations vs. stability data in h=7 (3.3MHz)

## Slide 22
2) Measurement
1) Simulation
Mode amplitude
Simulations predict oscillation mode µ=2 as the stronger one before knowing the measurements results!!
2013 measurements vs. simulations
in h=21 (10.1MHz)
Number
of turns
Mode number
Pattern of the oscillation modes at 10 MHz compared with measurements done in 2013 which show the evolution of the mode spectra for LHC50ns beam during acceleration for a full machine (21 bunches). The ‘mode pattern’ depends on the initial conditions and the oscillation amplitude depends on the bunch number in the train.
µ=2
µ=2

## Slide 23
Simulations with LIU intensity
Preliminary results
Simulations performed with 21 bunches IN h=21 with an intensity of ppb at extraction.

## Slide 24
Outlook
The PS RF system
Beam loading & cures
  Wideband negative feedback
Coupled-bunch instabilities measurements & simulations
New feedback system and damper
10 MHz system impedance model and simulations
Summary and discussion

## Slide 25
10MHz RF system behaviour with new LIU parameters: beam loading and coupled-bunch instabilities.
Modified the working point of the tubes into the amplifier to increase the loop gain and so reduce the impedance seen by the beam.
  In measurements done in 2013 before LS1 coupled-bunch feedback and the 10MHz spare cavity have been used to damp coupled-bunch oscillation.
  Finemet © cavity as new longitudinal kicker in the coupled-bunch feedback.
New feedback also to operate in the frequency domain, similar signal processing as existing feedback, but digital and covering all harmonics simultaneously based on hardware developed for the 1-turn feedback.
First test with the beam after the startup in 2014
10 MHz cavities impedance model implemented in the simulation code and crosschecked either with theory and measurements
Simulations with PS-LIU beam parameters with longitudinal feedback to find the maximum required feedback voltage (preliminary results)
Summary

## Slide 26
THANK YOU FOR YOUR ATTENTION!