## Slide 2
Initial LHeC Coordination Group meeting
Test Facility
Stages and Optics
Alessandra Valloni
CERN, 5th February

## Slide 3
Test facility for SCRF cavities and modules
Test facility for multi-pass multiple cavity ERL
Test facility for controlled SC magnet quench tests
  Injector studies: DC gun or SRF gun
  Study reliability issues, operational issues!
  Could it be foreseen as the injector to LHeC ERL?
TARGET PARAMETER* | VALUE
Injection Energy [MeV] | 5
Final Beam Energy [MeV] | 900
Normalized emittance γεx,y [μm] | 50
Beam Current [mA] | 10
Bunch Spacing [ns] | 25 (50)
*in few stages
Goals of a CERN ERL Test Facility

## Slide 4
Outline
1. Stages of building design
- layouts
- baseline parameters
2. Arc optics architecture
3. Test facility for sc magnet tests

## Slide 5
Planning for each stage
STEP 1
SC RF cavities, modules and e- source tests
- Injection at 5 MeV
- 1 turn
- 75 MeV/linac
- Final energy 150 MeV
ARC | Energy
ARC 1 | 80 MeV
ARC 2 | 155 MeV
*4 SRF 5-cell cavities at 802 MHz
LINAC 1*
LINAC 2*

## Slide 6
Planning for each stage
STEP 2
Test the machine in Energy Recovery Mode
- Injection at 5 MeV
- 3 turns
- 75 MeV/linac
- Final energy 450 MeV
ARC | Energy
ARC 1 | 80 MeV
ARC 2 | 155 MeV
ARC 3 | 230 MeV
ARC 4 | 305 MeV
ARC 5 | 380 MeV
ARC 6 | 455 MeV
Recirculation realized with vertically stacked recirculation passes

## Slide 7
Planning for each stage
STEP 3
Additional SC RF modules test
Full energy test in Energy Recovery Mode
- Injection at 5 MeV
- 3 turns
- 150 MeV/linac
- Final energy 900 MeV
ARC | Energy
ARC 1 | 150 MeV
ARC 2 | 300 MeV
ARC 3 | 450 MeV
ARC 4 | 600 MeV
ARC 5 | 750 MeV
ARC 6 | 900 MeV

## Slide 8
Planning for each stage
Step 3
Step 2
Step 1

## Slide 9
Outline
1. Stages of building design
- layouts
- baseline parameters
2. Arc optics architecture for step 3
3. Test facility for sc magnet tests

## Slide 10
Layout
A. Valloni, A. Bogacz

## Slide 11
Linac 1 Multi-Pass Optics
5 MeV
155 MeV
305 MeV
455 MeV
605 MeV
755 MeV
905 MeV
A. Valloni, A. Bogacz
βx,y
Dx

## Slide 12
Linac 2 Multi-Pass Optics
905 MeV
755 MeV
605 MeV
455 MeV
305 MeV
155 MeV
5MeV
A. Valloni, A. Bogacz
βx,y
Dx

## Slide 13
Arc 1 optics
155 MeV
4×450 sector bends
2-step vert.
Spreader
2-step vert. Combiner
Arc dipoles :
Ldip = 71.8 cm
B = 5.67 kGauss
ρ = 91.45 cm
300 bends
(1 rec. + 3 sec.)
300 bends
(1 rec. + 3 sec.)
A. Valloni, A. Bogacz
βx βy
Dx Dy

## Slide 14
Arc 3 optics
155 MeV
8×22.50 sector bends
2-step vert.
Spreader
2-step vert. Combiner
Arc dipoles :
Ldip = 90.58 cm
B = 6.58 kGauss
ρ = 230.66 cm
9.80 bends
(1 rec. + 3 sec.)
9.80 bends
(1 rec. + 3 sec.)
455 MeV
A. Valloni, A. Bogacz
βx βy
Dx Dy

## Slide 15
Arc 5 optics
155 MeV
8×22.50 sector bends
Vertical chicane
Arc dipoles :
Ldip = 90.58 cm
B = 10.92 kGauss
ρ = 230.66 cm
755 MeV
Vertical chicane
A. Valloni, A. Bogacz
755 MeV
βx βy
Dx Dy

## Slide 16
Arc 1,3,5 layout
13.66 m
13.43 m
41.06 cm
92.6 cm
6 cm
Synchronous acceleration
Isochronous arcs
Achromatic arc
FMC optics
Total Arc length for Arc 1,2,3
34.5112 m
94 x λrf

## Slide 17
Footprint
Total length for Arc 1,2,3
34.5112 m
94 x λrf
(last cavity linac1 to first cavity linac 2)
Total length for Arc 2,4
34.2704 m
101 x λrf
(last cavity linac1 to first cavity linac 2)
Total length for Arc 6
3445.74 m
101.5 x λrf
(last cavity linac 1 to first cavity linac 2)
ARCS
LINAC
Total length ~ 13 m
Chicane inj/extr
Length ~ 1.75 m
TOTAL DIMENSIONS
42 m x 13.7 m

## Slide 18
Arc optics OPTION 2
Same optics layout for all the arcs 900/750/600/450/300/150 MeV
Arc dipoles :
822.50 bends
Ldip = 100.6 cm
ρ = 256.3 cm
 | 1GeV | 750MeV | 600MeV | 450MeV | 300MeV | 150MeV
B FIELD | 1.30 T | 0.97 T | 0.78 T | 0.58 T | 0.39 T | 0.19 T
Arc quadrupoles
Lquads = 30 cm
 | Q1 | Q2 | Q3 | Q4
Kq[m-2] | -1.01 | 2.91 | 2.09 | 1.19
3 dipoles
on top of
each other
*Attilio Milanese

## Slide 19
Incoherent Synchrotron radiation in return arcs
ARC | E [MeV] | E [keV] | E/E [%]
1 | 150 | 0.0087 | 0.00000387
2 | 300 | 0.139 | 0.00002199
3 | 450 | 0.708 | 0.0000621
4 | 600 | 2.239 | 0.000132
5 | 750 | 5.467 | 0.00024
6 | 900 | 11.337 | 0.00039
7 | 750 | 5.4667 | 0.00052
8 | 600 | 2.239 | 0.00066
9 | 450 | 0.708 | 0.00089
10 | 300 | 0.139 | 0.00135
11 | 150 | 0.0087 | 0.0027
Beam Energy loss
Beam Energy Spread

## Slide 20
Next steps
Complete Step 2 and Step 1 configuration and optics layout
Available
space
Step 2
Step 1

## Slide 21
Linac 1 - Step 2
5 MeV
85 MeV
155 MeV
235 MeV
305 MeV
380 MeV
455 MeV
βx,y
Dx

## Slide 22
Outline
1. Stages of building design
- layouts
- baseline parameters
2. Arc optics architecture
3. Test facility for sc magnet tests

## Slide 23
Controlled quench tests of SC magnets
We are investigating the possibility of using the test facility for SC magnet tests
Requirements in terms of:
Beam energy, intensity and pulse length (energy deposition)
Space for the magnets installation (possible tests of cable samples and
full cryo magnets)
Cryo requirements
Vacuum requirements
Powering needs

## Slide 24
Study beam induced quenches (quench thresholds, quenchino thresholds)
at different time scales for:
SC cables and cable stacks in an adjustable external magnetic field
Short sample magnets
Full length LHC type SC magnets
Quench limits of LHC dipole as expected from QP3 simulations for different pulse durations
Courtesy A. Verweij
Controlled quench tests of SC magnets

## Slide 25
Beam parameters to generate a given amount of energy deposition
Calculations and FLUKA Simulations
Beam parameters
Z, cm
R,cm
1 GeV
150 MeV
Energy deposition, GeV/cm3/e-
Beam
Results are given for half of bulky target because of symmetry
Binning: 1 mm3 bins
Cylinder of copper
Radius = 50cm
Length = 100cm
Copper target
(no magnetic field)

## Slide 26
Beam parameters to generate a given amount of energy deposition
Calculations and FLUKA Simulations
Beam parameters
Beam
Results are given for half of bulky target because of symmetry
Binning: 1 mm3 bins
Cylinder of copper
Radius = 50cm
Length = 100cm
Copper target
(no magnetic field)
Peak at z = 0.6 cm, r=0
Peak value = 0.2199 GeV/cm^3
Energy deposition, GeV/cm3/e-
Peak at z = 2.1 cm, r=0
Peak value = 1.0785 GeV/cm^3
150 MeV
1 GeV
Z, cm

## Slide 27
Energy Deposition, GeV/cm3/e-
Depth
of max dE/dx
Max energy deposition
Max energy deposition
Depth of max dE/dx
Beam parameters to generate a given amount of energy deposition

## Slide 28
# electrons needed to quench the magnet
Quench threshold
Maximum value for
the energy deposition
1 GeV = 1.602 x 10-7 mJ
MB quench limit 450 GeV is 140mJ/cm3 in 10ms:
~2.2 x 109 e- @ 1GeV necessary
MB quench limit 7 TeV is 16 mJ/cm3 in 10ms:
~2.6 x 108 e- @ 1GeV necessary
Number of particles
Beam parameters to generate a given amount of energy deposition
MB quench limit 3.5 TeV
Energy Deposition, GeV/cm3/e-

## Slide 29
Summary
The concept of the ERLTF is designed to allow for a staged construction with verifiable and useful stages for an ultimate beam energy in the order of 1 GeV
A sketch of the ERLTF optics configuration is provided and other options are under investigation
First analysis of having controlled quench tests of next generation superconducting magnets has been carried out. Beam parameters seem to match the requirements….further investigation is required!
Complete the optics layout for Steps 2 and 3 and make a second-order analysis
Thank you for your attention