## Slide 1: Tuning of the ultra slow muon beamline by utilizing ionized hydrogen
ADACHI, Taihei (KEK)
August 27, 2014
NuFACT2014

## Slide 2: Content
Overview of the ultra slow muon transport system
Commissioning by using thermal ionized Li+
Commissioning by using laser resonant ionized H+
Schedule

## Slide 3: Overview of the ultra slow muon transport system

## Slide 4: U-Line
Muon Production Target
↓
MIC Capture solenoid
↓
Superconducting curved solenoid
↓
Superconducting focusing solenoid
↓
Muonium Production Target
↓
Ultra Slow Muon Transport System
↓
μSR Spectrometer
or
Re-Acceleration
3 GeV Proton

## Slide 5: Schematics of the ultra slow muon beamline

## Slide 6: Overview of the Ultra slow muon transport system
Einzel lens
High Voltage Stage
Laser
Magnetical Bend
Electrical Bend
Spin rotator
(Not installed yet)
Electrical deflector
SOA Lens
Q
Q
Q
Q
Q
Q
Q
Q
Q
Q
Q
Q
Q
Q
Q
Q
Q
Re-accelerator
and microscope
will be installed
Sample position for μSR
Q: Electrical Quadruple
μ+

## Slide 7: Beam Detector: MCP (Micro channel Plate)
Laser
μ+
Single Anode
Delay-line Anode
MCP
MCP #1
(Single Anode)
MCP #2
(Single Anode)
MCP #3
(Single Anode)
MCP #4
(Delay-line Anode)
Count number of particle
Destructive
Put in beamline when use

## Slide 8: Commissioning by using thermal ionized Li+

## Slide 9: Mass Separation by Magnetic Bend
Current of Magnetic Bend [A]
Number of Event [events/4.8 s]
1H+
6Li+
7Li+
2H+
10B+
11B+
H2+
Laser
Detector (MCP)
Magnetic Bend

## Slide 10: Scanning with Slits
Position Resolution: 0.1 mm
Range: -5 mm ～ 30 mm from center
Picture of a set of slits
P1: Beam Center
P2: Half Width (1σ)
Fitting Function
Move & Measure
Move & Measure
Combine & Fit
Subtract & Fit

## Slide 11: Beam Profiles (L+ Tuning)
1
2
3
4
5
 | X mean | X sigma | Y mean | Y sigma
Slit 1 | -0.02 mm | 1.2 mm | -0.02 mm | 1.3 mm
Slit 2 | 0.02 mm | 3.8 mm | -0.10 mm | 4.1 mm
Slit 3 | 0.06 mm | 1.0 mm | -0.00 mm | 2.1 mm
Slit 4 | 0.18 mm | 3.8 mm | -0.36 mm | 4.0 mm
Slit 5 | 0.05 mm | 2.9 mm | 0.26 mm | 6.4 mm

## Slide 12: Measurement at Sample Position by using a MCP with delay-line anode
Sample Position
(MCP with Delay-line anode)
Horizontal Position [mm]
Vertical Position [mm]
Laser
MCP
Delay-line-anode
Preliminary

## Slide 13: Commissioning by using Laser resonant Ionized H+

## Slide 14: Measurement of Laser Ionized H+
Laser
Detector (MCP)
Laser Timing Signal
MCP signal
QDC gate
121.57 nm
355 nm
2p
1s
unbound
H atom
2.1 μs
Pulsed Lyman-α
Mu
122.09 nm
355 nm
2p
1s
unbound

## Slide 15: Beam Profiles (Laser Ionized H+)
1
2
3
Detector (MCP)
Laser
Rate ～ 1 @ middle of the beamline

## Slide 16: Schedule
August | September | October | November
H+ Tuning
Ultra slow muon
Now
Target
annealing
Laser
start-up
9/10
11/1

## Slide 17: Summary
A part of ultra slow muon beamline is installed.
Commissioning by utilizing laser ionized H+ is on going.
The first ultra slow muon beam at J-PARC will be created at next November!

## Slide 19
超低速ミュオン
低速ミュオン
[4 MeV]
ミュオニウム
生成標的
(hot W foil)
超低速ミュオン
[0.2 eV~]
レーザー
122 nm (Mu;1S→2P)
355 nm (Mu;2P→unbound)
→30keV (加速)
超低速ミュオン顕微鏡
物性実験に
使える強度へ
冷却 [エネルギーで7桁]
二光子共鳴
四波混合法
Pulsed Lyman-α
Mu
122.09 nm
355 nm
2p
1s
unbound
Kr
212.55 nm
212.55 nm
4p55p
4p6
820.65 nm
122.09 nm
ω1
ω2
ω1
Laser system
Superomega
beam line
Mu production chamber
Transport system of laser pulses
Transportation line for USM

## Slide 20: “H atom laser ionization” at MLF of J-PARC
Frontier of Materials, Life and Particle Science Explored by Ultra Slow Muon Microscope
July 2, 2014
All-solid-state laser system
as Lyman-α driving laser
Observed laser ionization of
hydrogen atom by MCP signal
W
dump
dump
Transportation line
H+
MCP
(Micro Cannel Plate)
355 nm
212 nm
840 nm
From laser cabin
Gas cell
(2.4kPa Kr-Ar mixture)
Sodium salicylate
painted plate
Mass Analyzing Magnet
J. Nakamura, T. Adachi (KEK)
Y. Oishi, K. Miyazaki, N. Saito (RIKEN)

## Slide 21
“H atom laser ionization” at MLF of J-PARC
Frontier of Materials, Life and Particle Science Explored by Ultra Slow Muon Microscope
July 2, 2014
Lyman-α on
ω1 (212.556 nm): Input to Kr Cell
ω2 (845.25 nm): Blocked
Kr Cell
ω1
ω2
Two-Photon Resonance
Four-Wave Mixing
Kr Cell
ω1
ω2
ωLy-α
Lyman-α off
121.57 nm
355 nm
2p
1s
unbound
H atom
ピーク高さ
レーザーに同期 (25Hz) して
水素がイオン化している様子
を確認
ピーク高さの
ω2 波長依存性を確認