## Slide 1: nuSTORM at CERN
Elena Wildner
CERN
NUFACT 2014 25-30 August 2014

## Slide 2: Material used
Slides from several recent workshops:
  26-27 March 2013, CERN
  14-15 April 2013, Virginia Tech
  21-22 November 2013, Fermilab
  ICFA, neutrinos, Paris January 2014
Material in recent
  Expression of interest to SPSC, CERN arXiv:1305.1419
    Proposal to Fermilab PAC arXiv: 1308.6822, plus updates
    Discussions at CERN around nuSTORM at CERN (K. Long, M.Nessi, E. Wildner )

## Slide 3: nuSTORM @ CERN
Concept and design study: Fermilab (A. Bross et al.)
Fit on CERN site (E. Wildner, Ken Long et al.)
Existing Infrastructures
  CERN SPS, North Area
Add a small storage ring (FODO/FFAG racetrack)
Several items can be developed independent of site
  Lattice, instrumentation, magnets, horn and target …
Some not
  Civil engineering, safety, controls system, target station…
Reuse/upgrade detectors
Develop generic detector concepts and technologies (Laguna, …)
9/1/14
p
p
n
FNAL

## Slide 4
CERN Neutrino Project
CERN Neutrino Platform
Neutrino detectors R&D
Logistics +
Test Beams Infrastructure (EHN1 ext)
Design and eventually implement a Neutrino Beam at CERN
EU participation in a High Intensity Facility
(detectors, beam, infrastr.)
PHYSICS
Investigate new programs (mu storage ring, betabeams ?, …)
It will happen
M. Nessi, Paris Jan. 2014

## Slide 5
CERN Neutrino Platform
proposed
80-90s
2006-2012

## Slide 7
LAGUNA-PROTO
NESSiE
ICARUS T150
~64 meters
MIND
New detectors?
n + charged beams for all experiments
Detectors

## Slide 8
Charged beam for the detectors
Target station can be developed for nuSTORM ?

## Slide 9: Primary Beam: Production & Extraction
Beam production scheme and beam structure similar to CNGS.
Successfully tested non-local fast extraction from LLS1 & LSS2.
Incompatible with simultaneous slow extraction  Time sharing.
Major upgrade/consolidation of machine protection system (BIS) required.
Magnetic septa (MST+MSE)
Inj. kicker (MKP)
1st Injection
from PS
2nd Injection
from PS
50 ms
1.2 s
100 GeV
10.5 μs
2100 bunches
1st Extraction
2nd Extraction
Cycle / Pulse 3.6 sec. (every 6 seconds)
14 GeV
Neutrino beam
North Area beam
EOI 2013

## Slide 10: Configurations
CERN SPS primary beam pulse: 10 msec.
FNAL MI primary beam pulse: 1.6 msec.
Best case is a pulse length = to the ring circumference. This gives best nu_mu from pion decay beam and most efficient use of the muon decays.

## Slide 11: Siting (from EOI)
CERN North Area
Neutrino platform (CENF), from EOI
FNAL
CERN
CERN

## Slide 12: Target&injection region
The target station would be for nuSTORM
CERN pion beam
From project definition report
arXiv:1309.1389.

## Slide 13
p-flux & n-flux
Alan Bross P5 Face-to-Face Meeting, Fermilab, Nov. 2013
CERN (EOI) 4.5 1020 100 GeV POT/10yr
  Assuming similar accelerator facility as FNAL (C target)
  Beam from SPS as proposed for the CENF primary beam
  Without any optimization
FNAL Proposal: 1021 120 GeV POT/10yr -> ~ 1.9 X 1018 useful m decays
  In PIP era, extract one Booster batch/cycle (1020 POT/yr 10 year run)
  Baseline FODO ring, C target, NUMI style 1 horn
  Inconel target + horn optimization + RFFAG  X5 ( 2 year run)
CERN EOI, Nov. 2013

## Slide 14
nuSTORM facility: parameters overview
Collect and transport pions from target: 5 GeV/c ± 10%
60% decay on the first straight section to muons
40%, up to 5 kW, go to pion dump or pion degrader for cooling experiments
Momentum of muons in ring 3.8 GeV/c ± 10%
p-beam: FNAL 120 GeV/c, CERN SPS 100 GeV/c (baseline)
  CERN SPS can deliver higher momentum, 450 GeV/c

## Slide 15
nuSTORM Ring Parameters
Courtesy A. Liu

## Slide 16
The Three Pillars of nuSTORM
  Can add significantly to our knowledge of n interactions, particularly for ne
Provides an accelerator & detector technology test bed for muons
Delivers on the physics for study of sterile n
  Worldwide collaborative efforts
  paves the way to a high precision neutrino/muon program
“European Strategy”: LBL program & collaboration

## Slide 17
Racetrack FFAG
Lattice options
FODO
Fermilab layout drawings are for FODO
Dynamic aperture, tunes etc. still to be optimized.

## Slide 18: Lattice option comparison
Paris, Jan. 2014

## Slide 19: Workpackages @ CERN: SPS
Preliminary

## Slide 20: Pion Production (FNAL)
120 GeV proton beam, beam radius – 1mm
5 GeV/c p+ yield optimization
  Inconel, Tungsten, Graphite
  Target length, radius, material and position inside horn. Horn current- 230 kA.
Yield rises very little with target length. Dependence on target position inside horn is weak. Dependence of yield on target radius is opposite for heavy and light targets.
Yields better for Inconel and Tungsten
Realistic horn model slightly decreases predicted yield, but changes distribution is not so marginal (interactions in the horn itself)
MARS model agrees well with exp. data on carbon in nuSTORM range of interest. MIPP and NA61/SHINE measurements for medium and heavy nuclei will be published in two years.
Development at CERN?

## Slide 21: WP2 @ CERN: Target and collection
Preliminary

## Slide 22: WP3 @ CERN: Collection and Transport
Preliminary

## Slide 23: WP4 @ CERN: Decay Ring Layout
Preliminary

## Slide 24: WP5 @ CERN: Pion Beam Dump
Preliminary

## Slide 25: Preliminary magnet considerations, FODO Lattice
Straights:
  Resistive quite standard technology.
  The apertures are quite large, prototyping needed
Arcs:
  Superconducting magnets. Most of them coil dominated, possibly a few quadrupoles in between could be iron dominated (superferric), also to avoid warm-to-cold transitions.
  Lattice to be optimized for quadrupole feasibility (even with Nb3Sn).
Space for sextupoles / orbit correctors (in the arcs): large apertures is a challenge (large stored energies per unit length, large forces and significant cross-talk between the magnetic elements)
Courtesy A. Milanese

## Slide 26: WP6 @ CERN: Magnets
Preliminary

## Slide 27
Determine the neutrino flux at the near and far end detectors with an absolute precision < 1%, which depends on the number of Neutrinos and their energy distribution.
If the circulating muon flux in the storage ring is known on a turn to turn basis together with the orbit and orbit uncertainties (uncertainty on the divergence), then the neutrino flux can be predicted:
Circulating muon intensity (on a turn by turn basis) to 0.1% absolute.
Mean momentum to 0.1% absolute
Width of momentum spread to 1% (FWHM)
Tune to 0.01
Accelerator commissioning and running: (turn by turn)
Trajectory
Tune
Beam loss
Profile
Instrumentation
Intensity, large chamber, challenging precision (0.1%)
L. Söby, CERN
Direct Diode Detection Base-Band Q (3D-BBQ) developed at CERN, by M. Gasior
Profile, low intensities, short lifetime (100ms), IPM not feasible, Sc. Screens or SEM strips to be foreseen, wire scanners not possible. Figure : 2m long tank, 60cm diameter, to be adapted.

## Slide 28: WP7 @ CERN: Instrumentation
Preliminary

## Slide 29: Including nuSTORM results
9/1/14
Pilar Coloma et al.
LBNF (40 kton detector, 1.2MW beam power)
Systematics is the same as before, only that including nuSTORM it is assumed that cross sections are determined at the 1% level of precision, removing the constraint between the cross sections for different flavors, they are all allowed to vary independently in the fit.

## Slide 30
Thank you for your attention !
Stay tuned:
a workshop will be held at CERN
Nov-Dec 2014

## Slide 31: Backup

## Slide 32
CERN Beams

## Slide 33: Beam parameters
Parameter | Value | Comments
Muon energy | 3.8GeV | 
Total intensity | 1 - 5E11? | Muon
Pulse length | 10.5µs | From SPS
Bunch frequency | 200MHz | Before injection
Nb of bunches | 233-2100? | Phase at injection?
Bunch length | 1-4ns? | Has to be simulated
Bunch intensity | 5E7-2E9? | More precise data needed
Rev. frequency | 851kHz | T = 1.17µs
Bunch current | 2-80mA ? | Injection scheme?
Average current | 14-68mA | At injection
Circumference | 350m | 
Beam size | 30cm | Diameter
Aperture | 40-60cm | 
Beam life time | 100 turns | 
Vacuum | 10E-7 | 
Continuous multi turn (~9 turns) injection.
No RF
Injecting on top of circulation bunches NOT foreseen yet, i.e. 200MHz plus any frequency above is possible.
Structure in beam unknown for the moment

## Slide 34: Sterile-neutrino search sensitivity
Global fit from: J. Kopp, P. A. N. Machado, M. Maltoni, and T. Schwetz (2013)
Notes: o the left, the appearence sensitivity is shown. The top pane shows the event yield for different energies together with the mis-id events. Below is shown the 5 and 10 sigma exclusion contuors also showing that the difference between 1 and 5% systematic uncertainties is not important. nuSTORM would cover the brown and yellow areas that correspond to the LSND appearance data at the 10 sigma level.

## Slide 35
Spectra X cross-section (3.8 GeV/c m+)
ne
nm-bar
Event rates /100T at ND hall 50m from straight with m+ stored for 1021 POT exposure
Event rates at Far detector
Notes: the two left figures show the spectra times cross section for the neutrinos coming from the decay of a 3.8 GeV muons
In the table top right are shown the number of events expected from 10^21 POT in a near detector at 50 m from the end of the ring straight section.
In the table bottom right, the events in the far detector are shown. The red line would be the appearance events from mue going to numu via a sterile neutrino.
The disappearance channels are shown in the remaining four line