## Slide 1
Electron cloud estimates in the HL-LHC triplets/D1
G. Iadarola and G. Rumolo
Technical meeting on Vacuum for HL-LHC
05/03/2014

## Slide 2
Outline
  Introduction: the HL-LHC triplets/D1 in IP1 (IP5)
  Electron cloud effects in the HL-LHC inner triplets for IP1 and IP5
    Simulation results
    Comparison with present triplets and mitigation
  IP2 and IP8 triplets: observations and scaling
  Conclusions

## Slide 3
Q1 (A/B)
Q2 (A/B)
Q3 (A/B)
D1
Q1
Q2 (A/B)
Q3
D1
Present
HL-LHC
  IP1, 4 TeV, β* = 0.6 m
  IP1, 7 TeV, β* = 0.15 m
Inner triplets for HL-LHC upgrade

## Slide 4
HL-LHC triplets in IP1 (IP5)
  Main differences between present and HL-LHC (with potential impact on integrated effect of e-cloud)
  Total length of triplets (IP1 and IP5): about 25% more quadrupole length
  D1 sharing the same cooling circuits

## Slide 5
HL-LHC triplets in IP1 (IP5)
  Main differences between present and HL-LHC (with potential impact on integrated effect of e-cloud)
  Total length of triplets (IP1 and IP5): about 25% more quadrupole length
  D1 sharing the same cooling circuits
   Shape and size of the beam screen

## Slide 6
HL-LHC triplets in IP1 (IP5)
  Main differences between present and HL-LHC (with potential impact on integrated effect of e-cloud)
  Total length of triplets (IP1 and IP5): about 25% more quadrupole length
  D1 sharing the same cooling circuits
  Shape and size of the beam screen
  Beta functions (up to a factor 50) and beam positions (up to a factor 2)
  Bunch population (HL-LHC: 2.2 x 1011 ppb, nominal LHC: 1.15 x 1011 ppb)

## Slide 7
A look to the EC buildup in the quads
  Few snapshots of the electron distribution  HL-LHC triplets develop thicker stripes along field lines farther from the center of the chamber
  HL-LHC (2.20 x 1011 ppb)
Present (1.15 x 1011 ppb)

## Slide 8
Distribution of heat load – HL-LHC triplets
  Heat load distribution along HL-LHC triplets + D1
  Build up more or less efficient at different locations mainly due to the different hybrid bunch spacings
  The least efficient build up, i.e. lower heat load, at the locations of the long-range encounters (vertical dashed lines)
   Values in D1 are comparable or higher than values in the quads

## Slide 9
Total heat load per element – HL-LHC triplets
  Total heat load per element in HL-LHC triplets + D1
  Similar thresholds for quads and D1
  Values in D1 higher than values in the quads for high SEY values

## Slide 10
  Effect of larger bunch population and chamber size. For the same SEY:
  - Similar energy, but significantly larger number, of impacting electrons
  Total heat load about x2-3 larger
  E-cloud suppression can be obtained using low SEY coatings (studies already ongoing  COLDEX) and/or clearing electrodes (low impedance design needed)
Total heat load on the triplet beam screen
Present triplets
  (1.15 x 1011 ppb)
  HL-LHC triplets
  (2.20 x 1011 ppb)
Cu beam scr.
SEY like 2012
Cu beam scr.
SEY like 2012
Aged SPS-like a-C coating
Full suppression
(SEY≈1 or clearing electrodes)

## Slide 11
Measured heat load (25ns) – IP2 and IP8

## Slide 12
Measured heat load (25ns) – IP2 and IP8

## Slide 13
Measured heat load (25ns) – IP2 and IP8

## Slide 14
Scaling with bunch population - IP2 and IP8
1.1e11 ppb
2.2e11 ppb
  Scaling heat load in present inner triplets with bunch population:
  Doubling bunch population leads to about x2-3 larger heat load
  e-cloud suppression strategies needed also in IP2 and IP8

## Slide 15
Summary
  HL-LHC Inner triplets IP1 and IP5 + D1:
    Expected values of heat load on the beam screens about a factor 3 larger than with present triplets
    Suppression measures (like low SEY coating or clearing electrodes) necessary to keep heat loads within cooling capacity
  Inner triplets IP2 and IP8 + D1
    Data from 2012 show similar behaviour to IP1 and 5
    Pure scaling with bunch population indicates that HL-LHC beams will lead to threefold heat load in the beam screen of IP2 and IP8 triplets