## Slide 1: Bandwidth-sharing in LHCONE
an analysis of the problem
Insert title here…

## Slide 2: Run-2 vs. Run-1
Relative reduction in CPU, disk, people
  Efficiency is becoming more important
Network now seen as more reliable
  Stable, performant, well-provisioned
  Now used as if free and infinite
Computing models: more relaxed data-placement
  T2 -> T2 transfers
  Xrootd data federations for WAN access (CMS: AAA)
  Significantly more fluid than originally planned

## Slide 3: Scheduling the network
Data-transfer needs are growing
  Cannot assume the network will remain free and infinite forever
Computing models are evolving
  Increasingly close interaction with h/w resources
  Broader range of resource-types (opportunistic, cloud, volunteer) with different storage & I/O characteristics
Can see the value of scheduling network use
  Just-in-time data-placement, deadline management
  Possibilities that come from deterministic behaviour, not necessarily just more speed

## Slide 5: Schedule, but how?
How to allocate bandwidth fairly & efficiently to users with different & time-dependent needs?
Candidate technologies, won’t discuss here
  Virtual circuits, multi-path flows
  Bandwidth guarantees can be hard or soft
  Networking groups are making progress towards a technical solution
Then you get a new problem: oversubscription
  Common to all successful middleware:
    phase 1: make it possible, phase 2: stop users abusing it!

## Slide 6: A good bandwidth-sharing system?
Automatic, lightweight
  Set up ‘circuits’ automatically, but only where needed
  Participation not mandatory (casual or low-load users)
Elastic, responsive
  Shares can grow and shrink over time
  Change on timescale of ~1 hour to follow needs
Efficient, fair
  Allows maximal use of bandwidth at all times
  Short-term & long-term: no starvation, no hogging
Fixed quotas

## Slide 7: High-level requirements: we want…
A way for users to tell LHCONE their needs
  At any time, across the whole of the LHCONE network
To resolve over-subscription, quickly & fairly
Technology to implement the shares
  (out of scope of this talk)
Candidate solution, the Progressive Second-price Auction (PSP)

## Slide 8: How does it work?
Network offers bandwidth Q on a given link
Bidders have fixed budget (varies per bidder)
Bidders specify quantity & unit-price: (qi,pi)
PSP calculates allocation & total cost: (ai,ci)
PSP sends all allocations/costs to all bidders
Bidders revise their bids, submit them again
Repeat until 3-6 until convergence
Convergence guaranteed for rational bidders

## Slide 9
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
Player with highest unit-price has their quantity subtracted from the total
Player with 2nd highest unit-price takes from what’s left
Bandwidth available for auction

## Slide 10
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
New bid ( qi, pi )

## Slide 11
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
New bid ( qi, pi )
How much does bidder i get?

## Slide 12
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
ai
How much does bidder i get?

## Slide 13
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
ai
How much does bidder i get?
How much does bidder i pay?

## Slide 14
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
ai
How much does bidder i get?
How much does bidder i pay?
ci =

## Slide 15: PSP on LHCONE?
PSP extends naturally to multiple links
  Decentralized, independent auction on each link
  Bidders have fixed global budget
  Best strategy is to bid for same bandwidth on each link
  Bidder offers a price per link dependent on the competition for that link
  Can show that it still converges if bidders are rational
Repeat auction whenever conditions change
  After some ‘lease-time’, to prevent chaos - ~1 hour?

## Slide 16: Practicalities: budgets…
Real world, real money
  Budgets set by bidders
  PSP guarantees the bidders converge on a solution
LHCONE, HEP experiments, fake budget
  Must ensure ‘fake money’ has real value in the auction
    Must have just enough to express needs coherently
  How to set the budgets?
    Budget spent ~every time you win a slice of an auction, need to reset/adjust periodically, to keep the bidders solvent
    Similar problem to allocating batch quota on shared farms?

## Slide 17: How, and how often, to update budgets?
Reset budget per-auction?
  No incentive not to spend entire budget every time
  Can lead to wasteful bidding, where not needed
Carry-over of unspent budget?
  Budget-hoarding => undesirable/‘unfair’ outcomes
Excess budget
  Blocking tactics, bidding for a link you don’t need
  Some way to penalize for under-used circuits?
Needs simulation, with various bidding strategies
  Budget adjustment must not destroy auction fairness

## Slide 18: Conclusion: principles
Bandwidth-allocation at LHCONE requires a mechanism which is fair, efficient, lightweight, responsive and automatic
The Progressive Second-Price auction offers this
  Users negotiate among themselves how much bandwidth they should get
    Repeat auction as needed, follow fluctuations automatically
  Network providers get clear statement of what users want at any point in time
    No negotiations between experiments & network providers

## Slide 19: Conclusion: practicalities
Fake budget complicates things
  Setting initial budgets, refreshing budgets periodically
  Similarities to batch quotas?
  (can we just charge real money instead?)
Bidding strategies
  Coupled to how budgets are managed
  Possible learning behaviour in repeat auctions
  Need to understand how budget allocation interacts with bidding strategy to keep the auction truthful