## Slide 2
Stefano Agosta
CERN IT/Communication Systems
High-Speed Mobile Communications
in Hostile Environments
CHEP 2015
Okinawa

## Slide 3: Introduction
Increasing demand for indoor wireless networks
Offices
Meeting points
Homes
Hostile environments
CERN underground
Trains

## Slide 4: CERN needs
Target
Gas release risk
Strict access constraints
Ionizing radiations

## Slide 5: CERN needs
Voice and data for :
Services
  Standard machines operation
  Remote experts consultancy
  Train Inspection Monorail (Radio Protection surveys)
  Temperature and humidity sensors

## Slide 6: WiFi technology
802.11ac wave 2 offers 3.5 Gbps
Access Points (AP) cover small areas (few meters)
Widely deployed in residential and office areas

## Slide 7: WiFi @CERN
Adopted for offices
Not suitable in the underground
  Ionizing radiations
  Tunnel lengths (27 Km for LHC, 7 Km for SPS)
  Temporary VDSL during LongShutdown1
    10 Mbps, 275 APs in LHC tunnel

## Slide 8: LTE technology
100% IP network
High spectral efficiency
MIMO (reliability and/or throughput enhancement)
Round Trip Time <10 ms
1 Gbps download, 500 Mbps upload

## Slide 9: CERN tunnels mobile infrastructure
Target: tunnels + LHC caverns
Services: GSM, UMTS, TETRA, TETRAPOL
Antenna cable
  resistant to radiations

## Slide 10: CERN tunnels mobile infrastructure
Inter-technology compatibility
  Passive Radio Frequency network optimized for bands:
    400 MHz
    800 MHz
    900 MHz

## Slide 11: CERN tunnels mobile infrastructure
Mobile operator
base station
Master Unit
Remote Units
Mobile operator
eNodeB
GSM + UMTS
LTE
Remote Units
LHC repeating system

## Slide 12: Measurements
  70 Mbps download, 15 Mbps upload
LTE-Advanced @ LHC8
  >100 Mbps download, >50 Mbps upload
LTE @ LHCb cavern
  Limited by measurements tools

## Slide 13: Conclusions
Voice + data services needs in CERN underground
WiFi: good performance, problematic feasibility
LTE: high throughputs in tunnels + caverns
RF infrastructure upgrade for inter-technology compatibility

## Slide 14: Questions?
Thank you!