## Slide 1: FCC kick-off meeting a summary for magnets
L. Bottura
http://indico.cern.ch/event/282344/timetable/#20140212

## Slide 2: FCC Kick-off
341 participants, large representation from 21 countries, very interesting program, very interested attendance
Interesting discussions on the physics case (Nima Arkani-Hamed)
A multitude of infrastructure questions
Very encouraging presentation on the challenges of tunneling in the area (Felix Amberg)
A number of critical items were identified were (I think) novel solutions are needed
  Cooling at 4.2 K ? Gain by a factor 3 on COP !
  Beam screen and SR power deposition vs. operating temperature and impedance
  Injection energy and allowable energy swing
Consult presentations at http://indico.cern.ch/event/282344/timetable/#20140212

## Slide 3: Superconductors
Material research: the FCC superconductors are not looking like anything we know from the past, nor HL-LHC. The present potential for improvement is in the range of 20 %... 50%, not enough
  5 years target: work on carrier density, pinning, grains to improve performance in present high-field materials
  10 years target: consider other materials (Fe-based, MgB2, round REBCO)
  Very large scale material requirements for LTS (10x ITER Nb3Sn production) and HTS (much above anything done so far)
Actions proposed:
  Launch a focussed 16 T Nb3Sn conductor program (factor 2 Jc at 18 T)
  Pursue work on HTS materials to make them suitable for accelerator magnets
  Consider other issues (protection, filaments/field quality, homogeneity and yield for low cost)
  The LTHFSM Workshop could be an incubation center for material R&D
Open questions:
  Are exotic materials (Fe-based SC) a realistic candidate for R&D ?

## Slide 4: Magnet technology
HL-LHC and companion HFM programs are exploring the 11...13 T operating field range, with ultimate field levels that are relevant to FCC (Fresca2), much experience can be drawn from these programs
Is there a “barrier” at 15 T, or is this only perceived as such ?
In the 16…20 T field range it is not clear what is the best geometry (block, cos-theta, CCT), examine them all
The present design margin, in the range of interest, is very large (20 %) – how to decrease it ?
Training, we cannot afford so many (> 10) quenches
Magnet protection is an issue both for LTS (energy density vs. JE) and HTS (propagation speed and detection)

## Slide 5: Matters of optima
Tunnel length, operating field and temperature, SC material selection, are parameters affecting greatly the location of the optimum (minimum cost, maximum performance)
Other constraints (e.g existing infrastructure), and benefits (e.g. the value of R&D at the field frontier) must be considered

## Slide 6: In practice
Define a direction for relevant R&D, set challenging (but realistic) targets, describe impact of this technology on other fields, and describe a development plan into a roadmap document to be contributed by the collaborators and edited within the scope of the FCC study
This roadmap document will become a reference for future accelerator magnets R&D proposals (e.g. US-DOE, Horizon 2020), and can be used as a basis of collaboration for FCC design and hardware R&D work
Time scale: 3 months (tough !)

## Slide 7: A skeleton of a 16 T model program
2014
  conceptual design of a 16 T dipole (choose coil cross section)
  Identify priority R&D
  performance targets for critical items (e.g. superconductor Jc)
2015
  Start wire and cable R&D
  Model magnet design
2016
  Model magnet components/tooling
  Start coil winding and processing (HT, impregnation, collaring,… )
2017
  Model assembly
2018
  Model test
  Wire and cable R&D results (next generation Nb3Sn)
Candidates for work
  Wire and cable: EU, US, China, Russia, Japan
  Model: EU, US

## Slide 8: A skeleton of a 20 T model program
Program aligned to EuCARD2 objectives (or the other way around)
2014
  conceptual design of a 5 T HTS dipole (two options)
  HTS cable R&D and material selection (EU: YBCO, US: BSCCO)
2015
  Cable production
  DEMO magnet components and tooling
2016
  DEMO magnet winding and assembly (EU, US ?)
2017
  DEMO magnet test (standalone, 5 T)
2018
  DEMO magnet test in FRESCA2 (insert, 20 T)(
Candidates for work
  Wire/Tape and cable: EU, US, Japan
  Model: EU, US

## Slide 9
Goals fo EU DS: conceptual design, prototypes, cost estimates, …
From FP7 HiLumi LHC DS  positive experience:
5-6 work packages as sub-set of FCC study
~10-15 beneficiaries (signatories of the contract with EC)
FCC EU Design Study (DS) Proposal
Horizon2020 call – design study, deadline 02.09.2014
Prepare proposal parallel to FCC collaboration setup
Non-EU partners can join as beneficiary – signatory with or w/o EC
contribution (contractual commitment) or as associated partner – non-signatory (in-kind contribution with own funding, no contractual commitment)
kick-off
event
input from
interested
partners,
end of May
submission
of EU FCC DS
proposal, 2 Sept.
discussions
iteration,
agreements,
signatures
March April May June July August September 2014
complete
draft
proposal,
end of June
Time line
M. Benedikt, February 15th, 2014

## Slide 10: H2020 opportunities (for discussion)
High-field low-temperature magnets for science
  focus on 16 T for FCC
  potential impact on high-field MRI, dry MRI, 2nd generation 1GHz NMR, high-field HT machines
Energy efficient and compact cycled magnets
  focus on injectors/booster and large swing magnets (from FCC-ee to FCC-hh)
  potential impact on overall accelerator installations (CERN), HT machines

## Slide 11
16 T dipole
40 mm
Accelerator features (2018)
20 T dipole (2018)
SMC/RMC/FReSCa2 (2015)
EuCARD2
5 T HTS dipole as insert
40 mm aperture
Accelerator features (2016)
HL-LHC (2023)
15
20
10
Field (T)
EuCARD
6 T HTS insert (2015 ?)
HFM in 2010
HFM in 2014