## Slide 1: Fundamental Limits of Timing Resolution for Scintillation Detectors
W. W. Moses, W. S. Choong, & S. E. Derenzo Lawrence Berkeley National Laboratory
March 13, 2013
Outline:
  Basic Theory
  Real World Effects
  Optical Photon Propagation
This work was supported in part by the U.S. DOE (contract No. DE-AC02-05CH11231) and in part by the NIH (NIBIB grant No. R01-EB006085).
1

## Slide 2: The Fundamentals…
Timing Determined by I0 (Initial PE Rate)
I0 = Eϒ  (Light Output / )  Collect_Eff  Quantum_Eff
Look at Arrivial Times of Individual Photoelectrons
Zoom In…
I(t) = I0 exp(-t/)
Light Output = I0 
2

## Slide 3: Time Jitter of nth Photoelectron
Jitter (fwhm) = 2.35  sqrt(n) / I0
First Photoelectron has Least Jitter
PE Rate = 100 PE/ns
LSO (40ns, 30k ph/MeV)
PMT (25% QE), 50% CE
50 PE/ns
“Poor” TOFPET
LaBr3 (15ns, 72k ph/MeV)
UBA PMT (50% QE), 75% CE
900 PE/ns
“Good” TOFPET
PE Rate = 1000 PE/ns
3

## Slide 4: Timing Pickoff
First PE Traditionally Favored
Described by Post & Schiff in 1960
Trig. Level
Trig. Level
Leading Edge Discriminator Often Used
If the trigger level is at n photoelectrons, timing resolution ≈ jitter of nth photoelectron
Valid if PD_Rise ≪ PE Jitter ≪ PPD_Fall (individual photoelectrons resolved)
4

## Slide 5: Problem: Predicts Incredible Timing
“Poor” TOFPET
LSO (40ns, 30k ph/MeV)
Standard PMT (25% QE)
50% CE
50 PE/ns
“Good” TOFPET
LaBr3 (15ns, 72k ph/MeV)
UBA PMT (50% QE)
75% CE
900 PE/ns
⇒ 66 ps fwhm PET Timing
⇒ 3.7 ps fwhm PET Timing
5

## Slide 6: Why? Real World Effects
Overlap of photoelectron pulses
Photodetector transit time jitter (Gaussian)
Photodetector rise & fall time (Bi-Exponential)
Intrinsic scintillator rise time (Exponential)
Optical transport in scintillator (Exponential)
Estimated Through Monte Carlo Simulation
Described by Hyman in 1964 & 1965
Our Contribution
6

## Slide 7: “Real World” Probability Density Function
“Abrupt” Rising Edge Disappears…
7

## Slide 8: “Real World” Jitter of nth Photoelectron
First PE No Longer Has Lowest Jitter
Broad Minimum – Many PEs Have Similar Jitter
PE Rate = 100 PE/ns
PE Rate = 1000 PE/ns
8

## Slide 9: Run Lots of Monte Carlo
Get Tables of Simulated Timing Resolution
Fit Tables to Analytic Formula
820 Combinations
Initial Photoelectron Rate I0: 10 – 10,000 PE/ns
Intrinsic Scintillator Rise Time: 0 – 1 ns (exponential)
Photodetector Transit Time Jitter: 0 – 0.5 ns fwhm (Gauss)
Optical Photon Propagation Time: 0 – 0.2 ns (exponential)
Convolve w/ Photodetector Response to Simulate Analog Out (results insensitive to PD response, including rise time)
Simulate Leading Edge Discriminator with Optimized Threshold for Each Combination
9

## Slide 10: Analytic Formula for Timing Resolution
Formula Obtained Using “Eureqa” Software
Timing Resolution (ns fwhm) = B / sqrt(I0)
B (r , d, J, I0) =
sqrt[ 5.545 I0-1 + 2.424 ( r + d ) + 2.291 J + 4.938 r d + 3.332 J2 + 8.969 J2 I0-1/2 + 9.821( r2 + d2 ) I0-1/2 − 0.6637( r + d ) I0-1/2 − 3.305 J ( r + d ) − 6.149 J I0-1/2 − 0.3232 ( r2 + d2 ) − 3.530 J3 − 5.361 J r d − 9.287 r d I0-1/2 − 5.814 J𝜏( r3 + d3 ) ]
I0 = Eϒ  (Light Output / )  Collect_Eff  Quantum_Eff (photons/MeV/ns)
r = Intrinsic Scintillator Rise Time (ns)
J = Photodetector Transit Time Jitter (ns)
d = Optical Photon Propagation “Decay Time” (ns)
10

## Slide 11: Fit vs. True Value for B
Excellent Fit (RMS Deviation ~ 2%)
For Virtually All Conditions, 0.5 < B < 2
11

## Slide 12: Other Observations
No Other Significant Dependencies
  Photodetector Rise Time
  Photodetector Fall Time
Timing Resolution Using “Optimal” Estimator that Uses All Detected Photoelectrons is ≤15% Better than Leading Edge Timing (for r = 0.5 ns, d = 0.1 ns, J = 0.2 ns)
Paper submitted to Phys. Med. Biol.
12

## Slide 13: Timing Resolution Predicted If You Know:
Initial Photoelectron Rate I0
  Gamma Ray Energy
  Scintillator Luminosity
  Scintillator Decay Time
  Collection Efficiency
  Quantum Efficiency
Intrinsic Scintillator Rise Time
Photodetector Transit Time Jitter
Optical Photon Propagation Time
✔
✔
✔
✔
✔
✔
✔
What Value to Use for Propagation Time???
✔
13

## Slide 14: Estimate Using GEANT / GATE / DETECT
Index of Refraction n = 1.82 (same as LSO)
Light Generated as a Delta Function in Time at Random Positions in the Scintillator
Three Surface Finishes Simulated
  Polished
  Chemically Etched
  Rough
Two Simulation Types for Each Surface
  “Unified Model” (σα = 0°, 6°, and 12°)
  “RealReflector” (measured values in LUT)
14

## Slide 15: Basic Pulse Shape
Well-Described By Exponential Decay
Delay
Amplitude
“Decay” Time
Photo- detector
Reflector
3x3x30 mm
Polished
Surfaces
15

## Slide 16: Simplifying the Simulation
Run Single Simulation w/ Infinitely Long Crystal
Superpose Signals from Positions x and 2L–x
Reflected Signal Less Important for Timing…
Photo- detector
Reflector
L
x
Photo- detector
∞
2L – x
3 x 3 x ∞ mm
16

## Slide 17: Simulation Results (Polished & Etched)
Delay =
Distance *
n c
17

## Slide 18: Simulation Results (Rough)
Unified “Rough” Very Similar to “Etched” and “Polished”
Lookup “Rough” is VERY Different
18

## Slide 19: Simulation Results (Rough Surface)
Lookup Table
Unified Model
Different Models Predict Very Different Behavior
19

## Slide 20: Scaling Crystal Dimensions
Simulations Run on 3 mm x 3 mm Crystal
Results for a W x W Crystal Can Be Found By Multiplying All Distances & Times on Graphs by W/3
Photo- detector
L
x
W
t
1.5 L
1.5 x
1.5 W
1.5 t
Photo- detector
20

## Slide 21: Conclusions
Simulation used to estimate timing resolution for many combinations of scintillation detector parameters
Includes virtually all known effects
Results encapsulated in “simple” formula that predicts timing resolution
All inputs to formula readily obtained (including optical dispersion in crystal)
Needs experimental validation!
21