## Slide 1: Mordicus-hw Framework for backend electronics control and configuration
Workshop on picosecond photon sensors
March 2014
G. Stelmakh
CEA Irfu Saclay

## Slide 2: What is Mordicus-hw?
Mordicus-hw is a C++ framework designed to optimize
collaborative development between electronics and software
engineers by providing them software tools that are adapted
to their respective activities.

## Slide 3
Workstation
Client
Embedded platform
Device
Server
MBus
I2C
AGET
device #1
device #2
device #3
device #4
ICE
Middleware
Network
TCP/IT
MBus
I2C
AGET
Memory-mapped register access
I2C register access
Proprietary register access
Device Server

## Slide 4
Client-Server Architecture
TCP Protocol
IP Networking
Switched Ethernet
Distributed processes
Middleware: Internet Communication Engine
Highly Distributed Application

## Slide 5
Client
Server
Contract:
Interface Defintion
Code:
Client Language
Code:
Server Language
Code:
Server Implementation
Generated
Implemented
Client-Server over ICE

## Slide 6
Network
Embedded
Target ECC Server
Electronics
Control & Config
Embedded
Target ECC Server
Mordicus-hw Framework
  Policy-based register access
  Dynamic Remote Registers
Communication
middleware (ICE)
Communication middleware (ICE)
Electronics Control & Configuration

## Slide 7
Mordicus-HW
  Policy-based register access
  Dynamic Remote Registers
ICE Interface & data definitions
Embedded C++ library (VxWorks & Linux)
Host C++ library (Linux, MacOS)
Node (network)
Device (Mem, ASIC…)
*
ECC
*
Register
*
Bit Field
*
(C++ templates)
(CConfig framework)
Optimal collaborative work between electronics and software engineers
Electronics Control & Config

## Slide 8
Every device is associated to a “register access policy” representing the protocol through which hardware registers are read from or written to.
The framework architecture confines the specification of the register access policy to a single Policy class that basically implements the 4 elements:
the type that represents a register reference: Policy::AddrType;
the data type that is read from / written to the register: Policy::DataType;
the register write function: void Policy:: poke(const AddrType& addr, const DataType& value);
the register read function: void Policy::peek(const AddrType& addr, DataType& value);
Register Access Policies

## Slide 9
Based on the described architecture, we can develop powerful clients running on general-purpose workstations capable with dynamic description of target hardware devices and then running any sequence of register accesses in the form of scripts.
Once firmware reaches a sufficient level of maturity, the scripts themselves can be either directly reused or ported to the final system.
Scripting tools for electronics design

## Slide 10
Bit-field access optimization was actually implemented in Mordicus-hw
resulting in significant acceleration of control sequences.
The caching mechanism uses C++ transient objects which accomplish
the single register read in their constructor and the final write-back in their
destructor, doing all the bit-field access operations in the form of chained
method calls such as (bit-fields are referenced here as strings):
myReg.poke("ctrl",2).poke("status",11).poke("cs",1);
In this example, myReg is a register object and the first call to the poke()
method returns the transient object on which, from then on, the subsequent
poke() calls are made.
Optimization Issues

## Slide 11
Configuration Framework
Electronics
Control & Config
Config ID
Config store
Database
    C++ framework (Std & embedded OS)
    XML File & Database persistence
    Graphical Editor (based on Qt4)
    Parameter default value mechanism
    Multilanguage server access (using ICE)
    …
Run Control

## Slide 12
Default value
Overriden value
#include "CCfg/CConfig.h"
#include "CCfg/Document.h"
Ccfg::Document doc("hardware_descr.xcfg");
CCfg::CConfig cfg(doc.getConfig());
CCfg::CConfig agetCfg = cfg("Setup","Hardware")("Device","aget");
int offset = agetCfg ("Register","reg3")("offset");;
Configuration Framework

## Slide 13
“Batch” objects
Series of remote register access instructions than would be transported in
a single network operation to their target node and then locally interpreted and
executed.
Advanced device parameterization
The possibility to instantiate register devices of any kind with an arbitrary
number of parameters.
Parameters in more than 64-bit values.
The possibility to transfer in a single network operation the whole configDB.
Further developments