## Slide 1
Development of fast frontend electronics for single-photon timing in RICH counters
M. Hoek
(hoek@uni-mainz.de)

## Slide 2
Fast Timing in DIRC detectors
TRBv3 FPGA TDC Development
Frontend Electronics Developments for PANDA Barrel DIRC
Characterisation of Frontend Cards
  Laser pulser
  Test experiment with DIRC prototype
Conclusions
Overview

## Slide 3
Fast single photon detection aids in
Pattern recognition
Improving angular resolution
Fast Timing in Cherenkov Detectors
FDIRC Prototype
D. Roberts, RICH 2013
dTOP/Lpath = (TOPmeasured - TOPexpected)/Lpath
Δθc [mrads]
Production
Chrom. smearing
Mult. scattering
Track bending
Transport
Scattering
Surfaces (DIRC)
Imaging & Detection
Optics
Pixel size
Stand-off distance
1 GeV/c p
1 GeV/c K
Planacon
MCP-PMT

## Slide 4
Developed at GSI (see http://trb.gsi.de/)
Readout for PANDA Barrel DIRC prototypes
TRBv3 Platform
Peripheral FPGAs
(Lattice ECP3-150EA)
Each with 64 TDC channels + Synchronisation
10ps RMS time precision (<20ps RMS on all channels)
Minimum pulse width <500ps
50 MHz max hit rate (burst, up to 63 events)
700 kHz max data readout trigger rate (empty frames)
Central FPGA
(Lattice ECP3-150EA)
Central Trigger System
4 TDC channels
GbE controller
Signal Inputs (LVDS)
Signal Inputs (LVDS)
Data transfer via optical links or GbE

## Slide 5
TRBv3 TDC Implementation

## Slide 6
TRBv3 TDC Implementation

## Slide 8
TRBv3 TDC Implementation

## Slide 9
Walk correction needed for best timing resolution
Measure charge
PANDA environment demands fast readout
Use Time-over-Threshold (ToT)
Non-linear correlation!
Analogue Signals (MCP-PMTs)
Single photon response

## Slide 10
Frontend Electronics Development
MCP-PMT
connector
NINO
PADIWA
Pre-amplifier
Card (16ch)
Discriminator
Card (16ch)
LVDS output+ slow control
Current feedback amplifier (THS3201)
NINO ASIC
(8 ch)
MCP-PMT
connector
Pre-amplifier
(MMIC)
FPGA
(Lattice MachXO2)
LVDS output
FPGA programming interface
Power supply
(+5V)
FEE Brief
Form factor set by MCP-PMT (5cm height)
16 channels per card (one connector row on Planacon MCP-PMT)
LVDS output to interface TRBv3
Low power consumption
Compare different technologies
  ASIC: NINO chip (ALICE TOF)
  FPGA: PADIWA (GSI)

## Slide 11
Frontend Electronics Development
NINO Card
  Adapt to single-ended signals
  Pre-amplifier (1.8 GHz) to avoid low-charge behaviour of NINO chip
PADIWA
  Input LVDS buffers in FPGAs (Lattice MachXO2) are used as discriminators
  Leading edge time and ToT are encoded in the output
  The thresholds are set by using the FPGA as DAC via PWM and low pass filter

## Slide 12
FEE Characterisation – Fast Laser
PiLas system with 633nm diode
Use ND filters to attenuate laser light
Avg photon yield ~0.3 (<4% multi photon events)
Illuminate one pixel only (laser spot ~1mm)

## Slide 13
Stable threshold achieved
Observed plateau for thresholds
Walk corrections effective
FEE Characterisation – NINO Cards
Plateau
136ps
84ps

## Slide 14
FEE Characterisation – PADIWA
Raw single photon timing resolution ~ 90ps
Walk correction implemented as 1st order polynomial based on ToT
Corrected timing resolution ~ 78ps
Rate capability tested up to 100kHz
Threshold setting very sensitive to noise
90ps
78ps

## Slide 15
Test Experiment at MAMI (Mainz)
2013 – MAMI B, 855 MeV electron beam
Test of frontend electronics
  Timing resolution
  Time walk correction
  Thresholds
MCP Tower

## Slide 16
Up to 384 channels readout with TRBv3
Different angles to check pattern shift
Different configuration of NINO & PADIWA cards
MCP-PMT gain ~1106
Test Experiment – Cherenkov Patterns
Simulation
NINO
PADIWA
Problems with threshold setting for PADIWA cards
No useful data from test experiment
Trigger signal
Cherenkov light

## Slide 17
Test Experiment – Timing Results
100ps from pixel acceptance
Electronics contribution

## Slide 18
Initially using walk parameters from laser characterisation
Different parameters during test experiment
  Optimise walk parameters using charge sharing
Improving resolution to ~40ps
  Works on different MCP-PMTs
Little impact on system timing (~5ps)
  Governed by path length variation
Optimisation of Timing
145ps

## Slide 19
Fast single photon timing (<100ps) in DIRC counters aids
  Pattern recognition
  Chromatic correction
TRBv3 FPGA TDC provides
  High-precision low cost TDC
  Up to 256 channels with <10ps RMS
Two types of Frontend Electronics developed
  NINO ASIC
  PADIWA based on FPGA
Successful characterisation with laser & test experiment
  Similar performance (<100ps SPE timing)
  Electronics contribution to timing resolution ~40ps
Conclusions