## Slide 1: AFP Technical Review ToF Electronics
Michael Rijssenbeek
for the AFP QToF Institutes:
U Texas at Arlington, Stony Brook U, U Alberta at Edmonton U New Mexico, Oklahoma SU

## Slide 2: AFP – ATLAS Forward Protons
7 TeV proton beam
6.5 TeV diffractive proton
Forward Proton Detectors (AFP):
  detect/measure protons going down the beam pipe
e.g. For pp→pXp:
where s=14 TeV, ξ fractional proton energy loss
Time of Flight:
Time difference between protons from same interaction arriving in the two AFP arms: zvtx= c(tL – tR)/2
σz=(c/√2)×σt ~2 mm σt ~10 ps
Use to reject pileup background
P
IP
p*
IP
IP
γ
γ
AFP 206m-214m Diffractive protons
X
IP
X
γ
γ
X
p*
IP
IP
IP

## Slide 3: Electronics – Goals & Constraints
preserve timing resolution of the detector: <20 ps/channel
  multiple measurements/proton  <10 ps/proton
  need multiplicity also for rejection of spurious background rejection!
  trade multiplicity for resolution: 4 measurements of 20 ps ≃ 10 ps
provide fast ξ-bin trigger; transverse deflection x ∝ ξ
  data rate up to 1 MHz/channel
radiation-hardness or tolerance
  fluence/dose estimate for 100 fb–1 (1 yr @ 1034 cm–2s–1)
  FLUKA, IP primary/secondary interactions only, NO beam-gas (2×)
estimates for 100 fb–1 | 5 cm from beam @214 m | Tunnel floor @214 m | RR13 @beam level
Electronics exposed: | PA-a | PA-b, Trigger | CFD, HPTDC, Clock
High-Energy hadrons | 5·1012/cm2 | 1010/cm2 | 5·109–108/cm2
1 MeV-equiv. neutrons | 5·1011/cm2 | 5·1010/cm2 | 109/cm2
Integrated dose | 5000 Gy | 50 – 10 Gy | 1 – 0.1 Gy
(1 Gy = 100 rad)

## Slide 4: Fast Timing Electronics
Two methods to deal with pulse-height variations:
  CFD + TDC …
  Sampling of the (leading edge of the) pulse and time-walk correction
  see slides by J-F Genat, and many others at this workshop!
AFP Baseline: CFD + HPTDC
  see Jim Pinfold ‘s talk
AFP Electronics R&D: SAMPIC

## Slide 5: Pulse Shape and Gain Requirements
Pulse shape from UTA Laser-Lab testing (25μm pore) :
  Gaussian, FWHM ~700 ps (trise~300 ps)
  Minimum pulse height at 2 pe, G=1E5: Vpeak~2 mV (~30 fC in 50 Ω)
Trigger: needs ~100 fC
CFD needs: 250 – 1500 mV
  2 mV  200 mV: 40 dB
  PMT pixel variation: ~6 dB
  PMT ageing: ~6 dB
Need ~50 dB gain
  2 or 4 (inverting) stages of ~20 dB each

## Slide 6: Irradiation of AFP Electronics
HiRad protocol:
  Neutrons or HE protons: 1012 – 1013 /cm2; γ: 1 – 10 kGy.
MedRad protocol:
  Neutrons or HE protons: 1011 – 1012 /cm2; γ: 10 – 1 kGy.
PA-a chips (PSA4-5043+): HiRad
PA-b boards & trigger: MedRad
NINO chips (trigger): MedRad
CFD daughter boards: MedRad
HPTDC chips: MedRad
estimates for 100 fb–1 (need update!) | 5 cm from beam @214 m | Tunnel floor @214 m | RR13 @beam level
Electronics exposed: | PA-a | PA-b, Trigger | CFD, HPTDC, Clock
High-Energy hadrons | 5·1012/cm2 | 1010/cm2 | 5·109–108/cm2
1 MeV-equiv. neutrons | 5·1011/cm2 | 5·1010/cm2 | 109/cm2
Integrated dose | 5000 Gy | 50 – 10 Gy | 1 – 0.1 Gy
Cfr. ALFA radiation dose LHC Run1 measured over 2010–2013 (~30 fb–1): ~20-30 Gy in each pot (≥10 cm from beam) See: K.Hiller, S.Jakobsen, S.Franz, ALFA General Meeting, Cracow, June 5-7, 201.

## Slide 7: Irradiation – Sep 2013
Irradiated at LANL Sept 2013; S. Seidel et al. (UNM), K. Gray (UTA):
800 MeV p, ~7 cm from direct beam; passive
  dose: 6.5-8.7×1012 p/cm2, 2.3-3.1 kGy
  for 100 fb–1: ~expected for PA-a; ~50× expected for PA-b and CFD
  devices are all operational after irradiation!
Quartic
Feed through
(32 ch REDEL-HV)
8× HV
64× Signal
8× Temp
2× Pressure
(SMA)
(uD)
AFP2 crate
Signals
Att
DCS
Trigger
RR13 ? crate
USA15 crates
Trigger (LMR600)
TDC ToT
Opto Board
DCS
DCS
BOC-ROD or RCE
CTF
DCS
iseg HV
LV +6V 5A
(50 Ω)
CFD ToT
LE
Data
LV +6V 20A
DCS
PA-a
PA-b
214 m
214 m
240 m
0 m

## Slide 8: Irradiation @ LANSCE – Jan 2014
4×
PA-b Att
Pulse LMR400
HPTDC (NIM)
NIM LV ±6V 3A
CFD
Data
PA-a
LANSCE Beam
30 m
4×
CFD-LV (NIM)
CTP (NIM)
+5V
+5V +3.3V +1.3V –5V
Safe Area
Ref CLK
Trigger
–20 dB
1→4 –6 dB
4 HPTDC chips
2 HPTDC chips: 1×1012 p/cm2
2 HPTDC chips: 1×1013 p/cm2

## Slide 9: 4-Channel Electronics Setup
Jan 31- Feb 2 irradiation at LANSCE
Protocol:
  Active irradiation
  up to 1.0×1013 p/cm2, in 10 steps of 1×1012 p/cm2
  i.e. 10 pulses of 1011 protons per step
PA-a
PA-b
CFD
Beam View

## Slide 10: January 31- Feb 2 Irradiation
People: Tim Hoffman (UTA); Sally Seidel, Martin Hoeferkamp (UNM)
Protocol: Active irradiation – keep voltages on!
  up to 1.0×1013 p/cm2, in 10 ‘steps’ of 1×1012 p/cm2; verify operation before & after each step.
  i.e. 1 ‘step’ equals ~10 pulses of 1011 protons/pulse, 1 Hz, ~1 cm Ø
Early results:
  HPTDC readout did not work (cable too short)  2 Channels were monitored on scope; all 4 channels were powered throughout the run.
  Irradiation up to 5.0×1013 p/cm2
  2 monitored channels were still operating at the end of the run
Next:
  Wait for cool-off and return of parts (<2 months)
  Pre-Amps, CFDs: Re-test performance and compare with non-irradiated parts
  HPTDC chips: mount on HPTDC board and check operation

## Slide 11: Fast ToF Electronics: we have …
Proven designs & prototype 8-ch modules for:
  Preamp on PMT (PA-a) (4×8 channels)
  2nd stage variable-gain amp on tunnel floor (PA-b) (2×8 channels)
  Constant Fraction Discriminator (CFD) (3×8 channels)
  High-Precision Time to Digital Converter (HPTDC) (3 12-ch modules)
Have design for:
  Trigger pick-off and Multiplicity Trigger board (based on NINO chip)
SMA pigtails
PA-b 1st Prototype
Alberta CFD Daughter Board
Alberta HPTDC Board
8-Channel Preamplifier (PA-a)

## Slide 12: Preamp/amp reflections
20 ns/div; need to reduce “ringing”, tail, and reflection @ 20 ns
  Reflection:
  Understood: caused by mismatch of PA-b traces …
  Re-do PA-b PCB
  1 ns ringing:
  unclear, not seen with test pulses …
  PMT?
20 GHz LeCroy Oscilloscope pictures from beam test

## Slide 13: To Do: Trigger – Stony Brook
on PA-b motherboard; uses signal pick-offs from PA-b
  to be simulated with final layout and prototyped
  Output driver: to be designed …
Trigger Schematic

## Slide 14: To Do: Modify CFD – U Alberta
  add “Latch Enable”
  add Time-over-Thres- hold functionality
  Design Almost complete
D/FF and Drivers from Micrel
8 GHz SiGe Comparators from Analog Devices: 10 ps deterministic jitter, 0.1 ps random jitter

## Slide 15: Status Fast ToF Electronics: To Do …
Fast, ultra-stable, long-distance reference clock (U Texas at Arlington)
  prototype working: ~5 ps jitter
  Clock fanout: to be designed & built: (U New Mexico)
Trigger (Stony Brook):
  build prototype (Design almost complete)
  Radiation testing
  AFP trigger interface with CTF
Modification of CFD (Alberta):
  add Time-over-Threshold functionality (Design almost complete)
  build prototype
Modification of HPTDC (Alberta):
  Rad-tolerant design
  add ToT functionality (Design almost complete)
  build prototype
  Radiation testing
Readout:
  Opto board (2 pc ordered)
  RCE Interface (SLAC/SBU) used for IBL tests
DCS (?)