## Slide 1: VSC group seminar Leak propagation dynamics: experiment and simulation M. Hermann, M. Ady, D. Ziemianski, G. Vandoni, R. Kersevan, 21st March 2014
The research project has been supported by a Marie Curie Early Initial Training Network Fellowship of the European Community’s Seventh Programme under contract number (PITN-GA-2010-264330-CATHI)
1

## Slide 2
Outline
2
Motivation
Gas dynamics
Simulations
Fast valve systems
Experimental test-bench
Experiments and results
Conclusions and outlook

## Slide 3
3
Motivation
What we do? Study behaviour of propagating gas within beam pipes theoretically and experimentally
Purpose ?
Accidental vacuum failure or leak may result in an inrush of ambient air which might propagate with supersonic velocity
Support safe and efficient operation of the HIE-ISOLDE and SPIRAL2 facilities
Benchmark Molflow+ simulation results
Such a propagating pressure wave could…
  carry contaminated particles through beamlines
  have mechanically destructive effects on components
  transport inrushing air to cold surfaces of cavities and worsen their performance due to condensation
  increase heat load to cavities
 Gained knowledge is necessary to dimension and operate suitable protective systems

## Slide 4
4
Shock tubes consist in most cases out of two volumes with different pressure levels. The volumes are separated by a destroyable membrane.
Shock tubes are mostly applied for the experimental observation of gas and plasma propagation behaviour and measurement of properties such as velocities, pressures, temperatures, etc. at different positions
The shock wave velocity is supersonic. It depends on the low pressure with a max. velocity ≥ 1000 m/s (air) for expansion into UHV. Acoustic wave follows at velocity of ca. 400 m/s.
Analytical model describes properties
Flow regimes:
  Viscous flow regime: gas-gas collisions predominant
  Molecular flow regime: gas-chamber collisions predominant
http://en.wikipedia.org/wiki/File:Shock_tube.png
Generic knowledge regarding shock waves

## Slide 5
5
Analytical model vs. COMSOL simulation
Lower pressure limit for COMSOL simulation: 10 mbar
 usable for viscous flow regime

## Slide 6
6
Shock wave simulations
1000 mbar vs. 10 mbar
Pressures at positions
1 and 2 vs. time
1 baffle and 2 pressure gauges
Example of viscous regime simulation

## Slide 7
7
Recent Molflow+ improvements
Recent improvement of the Molflow+ code by M. Ady
Molflow+ now determines speed distribution and flight times of particles
This enables transient (time dependant) simulations
Inventor model of test bench in b. 113 imported into Molflow+

## Slide 8
8
High pressure
Haute pression
Low pressure
Basse pression
Courtesy M. Ady
Exemplary dynamical Molflow+ simulation

## Slide 9
9
Measures to protect SC linac from contamination with ambient air
Anticipatory actions
  Robust vacuum design of experiments
  e.g. Minimize amount and aperture of valves to atmosphere
Actions during operation
  Raising awareness of experimentalists for problematic
Implementation of protective equipment
  Usage of slow-down devices such as acoustic delay devices
  Implementation of fast pressure detection and fast valve system

## Slide 10
10
Fast valve system for HIE-ISOLDE SC linac
1
2
3
4
5
Penning gauges
3m

## Slide 11
11
Collaboration with vacuum team of SPIRAL2
Since rated as nuclear facility: obligation to prove
functionality of fast valve system and
compliance of response times
on frequent basis (yearly intervals)
SPIRAL2 beam lines with foreseen fast valves and pressure gauges
Common problematics:
- delicate components upstream, - space constraints
Differences:
SPIRAL2: risk of propagating radioactive gases
HIE-ISOLDE: no safety risk but necessity of cryomodule regeneration

## Slide 12
12
ca. 15 ms
What is a fast valve system ?
Consists of fast valve, pressure gauge, controls and connecting cables
Enables leak tight closure of a vacuum sector within less than 20 ms for DN40 aperture
VAT fast valve system

## Slide 13
13
Signal processing
Acoustic delay lines,
even as short as 30 cm
can help to “gain time” for valve closure
Acoustic delay devices
v_in
v_out
direction of gas flow
Turbulent flow regime created
Efficiency of an ADL = v_out / v_in
Values down to 0.2 measured in lit.

## Slide 14
14
Experimental setup: schematic
Installed in building 113, usage of former LHC long straight section test bench
4 sections of 7m length
DN80 stainless steel tube
Pumped by 3 turbomolecular pumping groups at the extremities and in the center
A
B

## Slide 15
15
Experimental setup: schematic
Installed in building 113, usage of former LHC long straight section test bench
4 sections of 7m length
DN80 stainless steel tube
Pumped by 3 turbomolecular pumping groups at the extremities and in the center

## Slide 16
16
Experimental setup: schematic
Installed in building 113, usage of former LHC long straight section test bench
4 sections of 7m length
DN80 stainless steel tube
Pumped by 3 turbomolecular pumping groups at the extremities and in the center

## Slide 17
17
Experimental setup: schematic
Installed in building 113, usage of former LHC long straight section test bench
4 sections of 7m length
DN80 stainless steel tube
Pumped by 3 turbomolecular pumping groups at the extremities and in the center
A
B

## Slide 18
18
Requirements for window:
Leak tightness
Withstand dp between pa = 1000 mbar and pv = 1E-8 mbar on diameters up to DN100
Low outgassing and permeation
Experimental setup: window design
100 micron alu foil

## Slide 19
19
Penning gauges to measure pressure range below 1E-3 mbar
Strain gauges foreseen to measure from atmospheric pressure
Experimental setup: DAQ
Sampling rate of fast DAQ: 9kHz
VAT control crates for SC linac
DN40 CF blind flange with 100 micron thickness
Calibration pump stand
Collaboration with
Mechanical measurement lab of Dep. EN for fast DAQ
Collaboration with
company VAT for troubleshooting

## Slide 20
20
Experimental setup: pendulum design at SPIRAL2
Pendulum on DN100 CF flange designed at GANIL, one will be delivered to CERN
Used to enable repeatable triggering (using accelerometer) of DAQ and foil break
  Time stamp of breaking foil
Courtesy R. Levallois

## Slide 21
21
Preliminary results with setup A
First test using DN40 CF flange and polymer foil
Velocity 200 m/s
1E-3 mbar
1E-8 mbar
1
2
3
4
A

## Slide 22
22
Preliminary results with setup A
Second test using DN40 CF flange and 200 micron aluminum foil
Velocity 100 m/s
1E-8 mbar
1E-3 mbar
1
2
3
4
A

## Slide 23
23
Micro-leaks of 5, 10 and 20
micron diameter
Study of micro-leaks
Pressure ratio p1/p2 < 0.53
Bernoulli’s equation for choked velocity flow
Molflow+ simulation
Test bench measurements

## Slide 24
24
Study of micro-leaks
Chart: 20 micron micro-hole
| D=20µm - measured | D=20µm - simulated
t_gauge1 [s] | 2.24 | 2.25
t_gauge2 [s] | 4.35 | 4.3
t_gauge3 [s] | 6.58 | 6.15

## Slide 25
25
Study of micro-leaks
Chart: 10 micron micro-hole
| D=10µm - measured | D=10µm - simulated
t_gauge1 [s] | 3.18 | 3.55
t_gauge2 [s] | 6 | 6.65
t_gauge3 [s] | 8.51 | 8.8
Chart: 5 micron micro-hole
| D=5µm - measured | D=5µm - simulated
t_gauge1 [s] | 5.82 | 7.05
t_gauge2 [s] | 10.16 | 11.45
t_gauge3 [s] | 13.12 | 14.15

## Slide 26
26
Protection of SC linac from air inrush of high importance
Simulations allow better understanding of propagating pressure waves
Test-bench in b.113 enables us to examine these and delivers important and useful insights regarding:
  Gas propagation velocities (for various leak sizes)
  How to operate a fast valve system
  Validation of closing times
  Quantification of transferred gas
Conclusions and outlook
Publication about results
Study of fast valve system using adjustable time lag
Implementation of accelerometer on pendulum as trigger for DAQ

## Slide 27
27
Acknowledgements
Special thanks to
  My supervisor Giovanna Vandoni
  My colleagues from VSC, esp. Paul, Jan, Claude, Alice, Berthold, Ivo, Jose, Chiara, Anthony, Marina, Philippe, Andrew, Henrik, Sebastien, Krzysztof
  Section LBV, esp. Giuseppe
  Colleagues on ground floor of b.30 for nice atmosphere

## Slide 28
Thank you for your attention…
…and for your support during the last 3 years 
28