## Slide 1: HL-LHCV1.0 Tracking Tools
R. De Maria, S. Fartoukh, M. Giovannozzi

## Slide 2: Tracking tools changes (a.k.a. mask file)
Assign field quality imperfections and misalignments to magnets.
Add beam-beam lenses.
Compute corrector circuit strengths.
Prepared by Stephane for SLHCV3 variants, here adapted for HLLHCV1.0 due to:
  split of Q1 and Q3 and change of names
  issues for certain squeezed β* .

## Slide 3: Directory structure
Same structures and general principle as SLHCV3.1b
  HLLHCV1.0/errors: contains error assignment routines, error tables for HL magnets and correction scripts:
    Efcomp_MQXF.madx: split of Q1 and Q3 with opposite orientations, change of names MQXC/D to MQXFA/B
    corr_tripD1_v2: change of names of triplet (MQXC/D to MQXFA/B) and a2 corrector (l.MQSX3 to MCQSX3)
    corr_value.madx: change kmax_MQSX to kmax_MCQSX
    corr_MB_v2: change of logic to assign focusing and defocusing trim quadrupole families (before based on betx/bety, now based on quad name) because failing on certain beta* combinations.
  HLLHCV1.0/beambeam: copied verbatim from SLHCV3.1b no need of changes (not tested).
  HLLHCV1.0/toolkit/align_sepdip.madx: macros for correcting the position of the sep/rec dipoles (see example in the mask file).
  HLLHCV1.0/job_tracking.mask: adapted from 3.1b (notably disabled B2s and B2r for D2 because of potential failure of coupling correction).

## Slide 4: Mag. Orientation
name | orientation | name | orientation | B1/B2
MQXFA.A1R1/5 | norm | MBXA.4L1/5 | inv | n/a
MQXFA.B1R1/5 | inv | MBXA.4R1/5 | norm | n/a
MQXFA.A1L1/5 | inv | MBRD.4L1/5 | norm | V2/V1
MQXFA.B1R1/5 | norm | MBRD.4R1/5 | inv | V2/V1
MQXFB.A2R1/5 | norm | MQYY.4L1/5 | norm | V2/V1
MQXFB.B2R1/5 | inv | MQYY.4R1/5 | inv | V2/V1
MQXFB.A2L1/5 | inv | MQYL.5L1 | inv | V1/V2
MQXFB.B2L1/5 | norm | MQYL.5R1 | inv | V2/V1
MQXFA.A3R1/5 | norm | MQYL.5L5 | norm | V2/V1
MQXFA.B3R1/5 | inv | MQYL.5R5 | norm | V1/V2
MQXFA.A3L1/5 | inv | MQYL.5L6 | norm | V1/V2
MQXFA.B3R1/5 | norm | MQYL.5R6 | norm | V1/V2
IP =Q1a||Q1b= =Q2a||Q2b= =Q3a||Q3b=