## Slide 1: LHC longitudinal collective effects
J. F. Esteban Müller
T. Argyropoulos, E. Shaposhnikova
9th HiLumi WP2 Task 2.4 meeting – 9 April 2014

## Slide 2: Outline
Introduction
Review of measurements
Analytical estimation
Simulations
Next steps
Conclusions

## Slide 3: Introduction (1)
LHC impedance is very small: according to DR Im Z/n ≈ 0.1 Ω, compared to 4 Ω in the SPS or 20 Ω in the PS
  Difficult to measure with beam using existing methods
No longitudinal instability in the LHC for operational beam parameters (so far)

## Slide 4: Introduction (2)
Our plans:
Check LHC impedance model with:
  measurements
  analytical calculations
  simulations
Study the case of HL-LHC parameters
  Single RF system
  Double harmonic RF systems
Currently working on this

## Slide 5: Review of measurements (1) Resistive impedance
From synchronous phase shift (MD 2012)
Good relative measurements for the TDI
TDI out
TDI in
W:= bunch energy loss per turn
V := RF voltage
N := bunch intensity

## Slide 6: Review of measurements (2) Resistive impedance
From synchronous phase shift (MD 2012)
Factor 4-5 with respect to estimation using the impedance model
  Possibly due to errors in the phase module (very high accuracy needed, ̴0.01 deg at 400 MHz)

## Slide 7: Review of measurements (3) Peak detected Schottky spectrum at 2 fs
Synchrotron frequency shift smaller than 1 Hz/1011 at 2 fs  Im Z/n < 0.1 Ω
Similar results for frequency shift from excitation by RF phase modulation
Frequency [Hz]

## Slide 8: Review of measurements (4) Loss of Landau damping
Observations during the ramp:
  2010:
    acceleration with Phase Loop (PL) on
    bunch with 1x1011 and 0.38 eVs unstable at 1.5 TeV  F Im Z/n ≈ 0.06 Ω
  Two MDs in 2011:
    acceleration with PL on for one bunch only
    acceleration with PL on for all bunches
Difficult to compare with simulations (PL)
MD in 2012 w/o PL

## Slide 9: Review of measurements (5) Loss of Landau damping
MD #2 2012:
  Acceleration without Phase Loop
  Similar intensities and different emittances
  Qualitative agreement with the expected dependence on energy (Eth ~ ε2)
  Need to simulate the acceleration ramp

## Slide 10: Review of measurements (6) Loss of Landau damping
MD #3 2012:
  Acceleration with Phase Loop on
  Controlled emittance blow-up during ramp  Similar emittances (1 eVs) and different intensities
  4 TeV without PL
  Can be used for comparison with theory and simulations!
Beam 1
Beam 2

## Slide 11: Analytical estimation Loss of Landau damping
From LHC impedance model: Im Z/n ≈ 0.09 Ω
Using
In agreement with measurements for F=1
F depends on distribution!

## Slide 12: Simulations (1) Loss of Landau damping
Aim: to reproduce measurements
Distribution similar to measurements
Emittance 1 eVs
Different intensities
LHC impedance model + RF cavities + HOM
4 different codes used

## Slide 13: Simulations (2) Loss of Landau damping
Measured instability growth rate is slow (>10 min)
 Phase kick in simulations to excite oscillations
Considered as damped (?)
Considered as undamped

## Slide 14: Simulations (3) Loss of Landau damping
Criteria: 0.8 in ratio of initial to residual oscillation is based on previous work (comparison of simulations with analytical threshold from Van Kampen modes by T. Argyropoulos and A. Burov)
With criteria chosen: Nth ≈ 3 x 1011  About factor 3 difference with measured threshold for similar bunch shape:
  Different bunch lengths and distributions
  Factor 3 in impedance (?)
  Damped / Undamped criteria

## Slide 15: Different bunch lengths and distributions
  Very strong dependence on bunch length (τ5) and distribution
Effect of bunch length
Distribution

## Slide 16: Different bunch lengths and distributions
Bunch length is measured by BQM from FWHM
A correction for the system transfer function is made assuming Gaussian bunches
Different distributions might need a different correction
Correction of the FWHM measurement T. Bohl

## Slide 17: Factor 3 in impedance (?)
Total Z/n ≈ 0.27 Ω is needed to reproduce measurements:
  BB resonator: fr = 5 GHz, Rsh = 80 kΩ, Q = 1 (0.18 Ω)

## Slide 18: Damped / Undamped criteria
Criteria for damped oscillations should be reconsidered
Both are considered as damped with the current criteria

## Slide 19: Next steps
To be verified:
  Effect of distribution on bunch length measurements
  LHC longitudinal impedance model
  Criteria to distinguish between damped and undamped oscillations

## Slide 20: Conclusions
Agreement between measurements and simple theory
Simulations suggest:
  Bunches are shorter than measured
  Higher impedance (factor 3)
  Different criteria needed
More data to simulate:
  Flat top
  Ramp
HL-LHC can be studied after impedance model is consolidated
Simulations with high harmonic RF system will require to study the effect of beam loading (relative phase shift)