Beam profile showing the size (sigma) in X for the 2 trackers and the ToF Z position.
In the plots ahead, the detector distance from the beam is calculated as:
15(20) sigma * X RMS (as above) + 0.3 mm

---
- acceptance in a single arm requiring hits inside both detectors
(at Z_1=203.8 and Z_2=215.0m) for pp →pWWp
- this plot doesn't contain the protons from pileup
- all smearing (beam dispersion in angle and energy and detector resolution)
- crossing angle
- t is given relative to the CMS z axis.

---
The same as the previous plot for 20 sigmas from the beam

---
The t vs xi acceptance in one arm (z>0, Forward) when requiring the other proton
To be inside the acceptance of the other arm (z<0, Backward), for 15(20)sigmas
in the left(right)

---
ToF occupancy, including all protons
From pileup, again with smearing in the beam
(angle, energy and starting position)

---
Hitmap requiring single arm (39.4%)
and double arm (10.8%)

---
Particle GUN, no beam smearing

---
Particle GUN, no beam smearing

---
t generated between 0 and 4 at MC, ref. frame
changes to 0 up to 20 with Crossing angle and all smearing