## Slide 1: Design of Solenoid Field Benoit CURE, CERN CERN, 10 June 2014
CLIC Detector optimisation

## Slide 2
R
Z
Reference design layout : initial CLIC_SiD layout with detector half length L=6.2m
    End cap iron thickness is 2445mm.
    8 muon chamber stations in the yoke end cap.
Longitudinal section :
quarter view,
detector axis horizontal,
only end cap and one barrel shown.
CLIC Detector optimisation – Design of solenoid field

## Slide 3
New design layout : reduced detector half-length to L=5m
    End cap iron thickness reduced by 1160mm (2445mm to 1285mm).
    7 muon chamber stations in the yoke end cap.
Longitudinal section :
quarter view,
detector axis horizontal,
only end cap and one barrel shown.
R
Z
CLIC Detector optimisation – Design of solenoid field
Solenoid length kept at 6.23m,
External radius identical,
No modification of barrel yoke.

## Slide 4
Comparison of the two layouts (no ring coils): B field vector sum map
R
Z
L=5m no RC
B = 4.896 T at IP
R
Z
L=6.2m
B = 5.06 T at IP
CLIC Detector optimisation – Design of solenoid field
(Detector axis is vertical on the maps !)
B-field 2D map : Area most affected is around the detector axis and outside the yoke.
Far region : Less significant effect, Bmax=9mT at R=15m.

## Slide 5
Comparison of the two layouts (no ring coils):
Axial B-field component Bz(R=0) on coil axis:
0.46e-3
0.56e-3
CLIC Detector optimisation – Design of solenoid field
 Improve the design with reduced length by implementing ring coils to :
  lower the stray field,
  lower the field near the beam line outside the yoke end cap.

## Slide 6
Effect of ring coils on B-field with L=5m: 3 configurations: J=3A/mm2, same cross section.
B = 4.828 T at IP
1 RC on inner radius
2 RC on inner and outer radius
1 RC on outer radius
B = 4.874 T at IP
B = 4.85 T at IP
R
Z
R
Z
R
Z
CLIC Detector optimisation – Design of solenoid field
Axial B-field component
Bz(R=0) on coil axis:

## Slide 7
R
Z
Ring coils with L=5m: Configuration giving a lower field on Z-axis.
  Effect of iron in concrete cavern wall (B-H curve = 10% of iron),
  4 RCs with resistive conductor and Jrc=3A/mm2,
  Assumption to have the ring coils attached to the cavern wall (increased gap).
B-field magnetic flux density vector sum maps
CLIC Detector optimisation – Design of solenoid field
B = 4.869 T at IP
B = 5.06 T at IP
R
Z
L=6.2m
L=5m + RC
Field at IP is 3.8% lower wrt L=6.2m.

## Slide 8
B = 4.827 T at IP
B = 4.869 T at IP
0.93e-5
Ring coils with L=5m:
CLIC Detector optimisation – Design of solenoid field
Forces on end cap and yoke:
Attractive axial force on end cap : 100 MN (170 MN with L=6.2m),
Compressive axial force on main coil : 207 MN (164 MN with L=6.2m).
Axial B-field component on the detector axis
Bfield on detector axis at Z=5m: 150 mT

## Slide 9
Ring coils with L=5m:
Radial B-field component
B = 4.827 T at IP
L= 6.2m
L= 5m + ring coils
CLIC Detector optimisation – Design of solenoid field

## Slide 10
Ring coils with L=5m:
Axial B-field component
B = 4.827 T at IP
CLIC Detector optimisation – Design of solenoid field
L= 6.2m
L= 5m + ring coils

## Slide 11
Ring coils with L=5m:
Magnetic field distortion in barrel tracker volume :
Increase 23% wrt L=6.2m.
CLIC Detector optimisation – Design of solenoid field

## Slide 12
Ring coils with L=5m:
→ Stray field lower than 3.2mT at R=15m.
B = 4.827 T at IP
CLIC Detector optimisation – Design of solenoid field
B-field vector sum :
Transverse plane Z=0m
At radius R=15m , parallel to Z-axis

## Slide 13
Characteristics of the ring coils on the cavern wall with L=5m :
Arbitrary gap from RC to yoke end cap: 192mm (RC1, RC3 & RC4) and 244mm (RC2),
Space available for radiation chicane,
Same copper conductor for all RCs,
Total copper weight : 250 tons (for 2 end caps). Suppressed steel mass wrt. L=6.2m (2 end caps)≈ 2800 tons,
Total electrical power of RCs (2 end caps): 2 x 2260 kW.
Water cooling system characteristics:
Estimated temperature increase ≈ 45°C,
Total water flow (2 end caps): 2 x 57 m3/hour.
RC1
RC2
RC3
RC4
Coil | Nb. turns | Copper mass (ton) | Resistance (1e-3 ohm) | Voltage drop (V) | Power (kW)
RC1 | 4x12 | 5.6 | 2.7 | 16.5 | 101
RC2 | 3x20 | 13.3 | 6.4 | 39.1 | 240
RC3 | 4x24 | 54.4 | 26.2 | 160.4 | 984
RC4 | 4x18 | 51.7 | 24.8 | 152.2 | 934
R
Z
CLIC Detector optimisation – Design of solenoid field

## Slide 14
Characteristics of the ring coils on the cavern wall with L=5m :
Parameters obtained are (coincidentally) very similar to LHCb dipole ones (*) !
 | LHCb dipole (*) | CLIC (L=5m + RC)
Conductor | 50x50mm2 aluminum 99.7, 24mm | 50x50mm2 copper, 24mm
Excitation | 2 x 1.3 MA.turns | 2 x 1.7 MA.turns
Total power | 4.2 MW | 4.5 MW
Stored energy | 32 MJ | 2 x 16.8 MJ
Inductance | 2 H | 2 x 0.9 H
Current density | 2.9 A/mm2 | 3 A/mm2
Current in conductor | 5.8 kA | 6.1 kA
Total resistance | 125 m | 2 x 60m
Total water flow | 125 m3/hour | 115 m3/hour
(*) LHCb Magnet, TDR, CERN/LHCC/2000-007, 1999.
CLIC Detector optimisation – Design of solenoid field

## Slide 15
Other cases:
1- Reducing the iron thickness to 4 disks then L=5m to 4.205m,
2- No end cap iron yoke.
As a first approach, only the current density was increased. The RCs are identical and in same positions in both models.
With resistive ring coils, the ring coil sizes would have to be increased to keep a realistic conductor and current density. SC coils would be more appropriate.
Jrc= 6A/mm2
B = 4.608 T at IP
Axial force on coil = 260 MN
0.15e-3
R
Z
R
Z
B = 4.265 T at IP
Axial force on coil = 320 MN
Jrc= 9A/mm2
0.13e-3
Case 1
Case 2
CLIC Detector optimisation – Design of solenoid field

## Slide 16
Case 1: L=4.205m
Case 2: no end cap
CLIC Detector optimisation – Design of solenoid field
0.56e-3
R
Z
R
Z
R
Z
R
Z
Bz component
Br component

## Slide 17
Wrt the ring coils defined for L=5m:
Case 1- Resistive ring coils x2 in size, total power x2.
Case 2- Resistive ring coils x3 in size, total power x3.
The magnetic field at IP is reduced (resp. 8.9% and 15.7% wrt L=6.2m) and the field distortion in the inner detector volume increases.
The EC iron yoke helps to shape the field.
CLIC Detector optimisation – Design of solenoid field
Axial B-field component on the detector axis

## Slide 18
B = 4.827 T at IP
B = 4.838 T at IP
R
Z
Reduction of external diameter of both end cap and barrel yoke:
Modified parameter: External radius Rext = 6.35m.
All other parameters unchanged :
  RCs at same position, same current density,
  Detector half length L=5m.
Field at IP is 4.4% lower wrt {L=6.2m; Rext=7m}.
CLIC Detector optimisation – Design of solenoid field
Axial B-field component on the detector axis

## Slide 19
B = 4.838 T at IP
Reduction of external diameter of both end cap and barrel yoke:
CLIC Detector optimisation – Design of solenoid field
Total reduction on iron mass (reduced length + radius)≈ 4700 tons wrt CLIC_SiD L=6.2m.
With external radius of 6.35m and L=5m + RC:
barrel yoke iron saturation is more uniform (around 2T!).
B-field vector sum in central transverse plane:
Stray field lower than 4.5mT at R=15m.

## Slide 20
Conclusions:
Reduced end cap in length is feasible with ring coils, provided the field homogeneity in the central volume is acceptable for physics.
The end cap is still useful to provide support for muon stations, radiation shielding, and magnetic field shaping.
The yoke material + manufacturing budget can be considerably reduced with ring coils.
The cost estimate for manufacturing, infrastructure and operation of the ring coils should be compared to the saving on the yoke cost.
The barrel yoke could also be reduced in diameter:
the fringe field is reduced by the ring coils,
If there is only one detector in the experimental cavern (no access to cavern during beam run), then it can be compatible with radiation due to accidental beam loss.
CLIC Detector optimisation – Design of solenoid field