## Slide 1: Operational Beams for the LHC (in the injector complex)
H. Bartosik, D. Manglunki, Y. Papaphilippou and G. Rumolo
LHC Performance Workshop
Chamonix, September 22nd, 2014

## Slide 2: Acknowledgements
G. Arduini, T. Argyropoulos, M. Bodendorfer, T. Bohl, R. Bruce, C. Cornelis, H. Damerau, J. Esteban-Müller, A. Findlay, R. Garoby, S. Gilardoni, B. Goddard, S. Hancock, K. Hanke, G. Iadarola, B. Mikulec, E. Shaposhnikova, R. Steerenberg, PS complex & SPS Operation crews

## Slide 3: Outline
  LHC requirements for the injectors
  Single bunch beams
  25 ns and 50 ns physics beams
  Doublet scrubbing beam and 8b+4e beam
  LHC Ion beam
  LHC beams’ status and planning
  Conclusions
H. Bartosik and G. Rumolo, LBOC, 08/04/2014
H. Bartosik and G. Rumolo, Evian 2014
D. Manglunki, LIU-Ion LEIR review, 20/08/2014

## Slide 4: Outline
  LHC requirements for the injectors
  Single bunch beams
  25 ns and 50 ns physics beams
  Doublet scrubbing beam and 8b+4e beam
  LHC Ion beam
  LHC beams’ status and planning
  Conclusions

## Slide 5: (Proposed) LHC start up in 2015
Commissioning (low intensity/luminosity)
Vacuum conditioning (50ns/short trains 25ns)
(5-7 days)
50ns
(intensity ramp up + physics)
Scrubbing with 25ns
(2 days)
450GeV
6.5 TeV ?
Intensity ramp up & physics with 25ns
25ns scrubbing
(5 days)
25ns test ramps + commissioning (≈ 5 days)
Scrubbing with doublet beams (≈ 5 days)
450GeV
6.5 TeV ?
LHCPROBE
LHCINDIV
(Van der Meer)
LHC50 (std)
up to 1.5 x 1011 p/b *
LHC25 (std)
1.2 x 1011 p/b *
LHC50 (std/BCMS)
up to 1.7 x 1011 p/b *
LHC25 (std)
1.2 x 1011 p/b *
LHC25doublet
1.6 x 1011 p/doublet *
LHC25 (std/BCMS)
up to 1.3 x 1011 p/b *
LHC25 (std/BCMS)
up to 1.3 x 1011 p/b *
Use of low e-cloud filling patterns
Or, if scrubbing not sufficient
Possible alternative
LHC25 (8b+4e)
up to 1.8 x 1011 p/b *
M. Lamont, LMC, 10/09/2014
* At LHC injection

## Slide 6: Outline
  LHC requirements for the injectors
  Single bunch beams
  25 ns and 50 ns physics beams
  Doublet scrubbing beam and 8b+4e beam
  LHC Ion beam
  LHC beams’ status and planning
  Conclusions

## Slide 7: LHCPROBE & LHCINDIV – specs @LHC injection
 | LHCPROBE | LHCINDIV
Intensity [p/b] | 5 x 109 – 2 x 1010 | 2 x 1010 – 3 x 1011
Transverse emittance, 1s [mm] | 1 | < 2.5
Longitudinal emittance [eVs] | 0.35 | 0.35 – 0.5
  LHCPROBE (=LHCPILOT) usually with intensities ≤ 1010 p/b, transverse emittance not critical (but anyhow small)
  LHCINDIV parameter range also extended in MDs to produce single bunches with up to 4 x 1011 p/b and/or with lower longitudinal emittances (down to 0.15 eVs) at SPS injection
    High-intensity variants for possible impedance or beam-beam studies

## Slide 8: LHCPROBE & LHCINDIV
  Production mechanism improved in PSB since 2013, covering parameter range for both type of beams
    Reworking of controlled longitudinal blow up (C16 and C02 parameters) during first part of PSB cycle
    Unique knob (C16 voltage) for intensity control
    Preserving the 6D phase space volume for different intensity values
    Excellent shot-to-shot reproducibility and control of both intensity and longitudinal emittance
1x1011 p
2x1011 p
S. Hancock, CERN-ATS-Note-2013-040 MD

## Slide 9: LHCINDIV for Van der Meer scans
Procedure for producing Gaussian bunches for Van der Meer scans established in 2012
  Based on longitudinal AND transverse shaving in the PSB to obtain “large” emittance single bunches with under-populated tails
  Provides Gaussian bunches with the desired intensities in the SPS after scraping
To be reproduced in 2014/15 …
Single bunch beam parameters | 
Intensity [p/b] | 7 – 9 x 1010
Transverse emittance, 1σ [μm] | ≥ 2.5
Transverse distribution | Gaussian
H. Bartosik and G. Rumolo, CERN-ACC-NOTE-2013-0008 MD

## Slide 10: Outline
  LHC requirements for the injectors
  Single bunch beams
  25 ns and 50 ns physics beams
  Doublet scrubbing beam and 8b+4e beam
  LHC Ion beam
  LHC beams’ status and planning
  Conclusions

## Slide 11: LHC25 and LHC50 (standard & BCMS)
Standard scheme:
(maximum number of bunches in LHC)
50 ns
Triple splitting up to 2013 at 1.4 GeV
(moved to 2.5 GeV after LS1)
25 ns
PS batches with 72 (36) bunches for 25ns (50ns)
Evian workshop 2014
11
h = 21
h = 9 10  1112  13  14  7  21
h = 21  42  84
+4 bunches
4 bunches
S. Gilardoni – Space Charge 2013
h = 9
BCMS scheme:
(less bunches in LHC but higher brightness)
50 ns
25 ns
PS batches with 48 (24) bunches for 25ns (50ns)

## Slide 12: LHC50 (std & BCMS) – pre-LS1 status
50 ns beam at the SPS extraction in 2012/13 (Q20)
  Combined wire-scans at end of SPS flat bottom (values cross-checked @ LHC)
    Error bars include measurement spread, as well as systematic uncertainty (10%)
  Intensity measured at SPS flat top after scraping
  Transport through PS and SPS within intensity loss and emittance blow up budgets
Four trains of 36 bunches
Routinely used for physics in 2012
Three trains of 24 bunches
Sent to LHC only for test to prove luminosity gain
Budget | PS | SPS
Dex,y /ex0,y0 | 5% | 10%
-DN/N0 | 5% | 10%

## Slide 13: LHC25 (std & BCMS) – pre-LS1 status
25 ns beam at the SPS extraction in 2012/13 (Q20)
  Combined wire-scans at end of SPS flat bottom (values cross-checked @ LHC)
    Error bars include measurement spread, as well as systematic uncertainty (10%)
  Intensity measured at SPS flat top after scraping
  Transport through PS and SPS 15% above budget for standard beam
Budget | PS | SPS
Dex,y /ex0,y0 | 5% | 10%
-DN/N0 | 5% | 10%
Four trains of 72 bunches
Used for the LHC scrubbing run in 2012
Three trains of 48 bunches
Used for the LHC pilot physics run in 2012

## Slide 14: Pre-LS1 performance limits
Both standard production and BCMS beams already very close to the limits in injectors
50 ns beam
  Intensity/bunch: close to the limit of longitudinal instability in the PS
  Brightness: BCMS at the present space charge limit in the SPS
25 ns beam
  Intensity/bunch: close to the limit of RF power and longitudinal instability in the SPS
  Brightness: At the present space charge limit in the PS

## Slide 15: LHC50/25 beam production after LS1
Recover 2012 performance
  Machines exposed to air  electron cloud  SPS scrubbing run
  RF manipulations in the PS performed at 2.5 GeV instead of 1.4 GeV in all LHC cycles (regularly used with BCMS beams in 2012)
    increases available bucket area
    tuning groups of cavities have changed  allows for further increase of bucket area
Potential for higher bunch intensity
  Possible benefits in the PS from
    upgraded 1-turn delay feedback for 10 MHz cavities (available at start-up 2014)
    upgraded longitudinal coupled-bunch feedback (commissioning starting in 2014)
  25 ns up to 1.3 x 1011 p/b at SPS extraction as during 2012 MDs (limited by RF power and longitudinal instabilities in the SPS)
Potential for higher brightness (as from RLIUP workshop)
  PS: Alleviate space charge by longer bunches and larger momentum spread
    need longitudinal blow-up on the PSB ramp to produce required emittance
    use of h1+2 in phase at PSB extraction to keep these larger longitudinal emittance bunches within certain length (recombination kicker rise time constraint)
  SPS : further working point optimization for 50 ns BCMS beam

## Slide 16: Post-LS1: PSB – PS transfer
Longitudinal emittance per bunch at PS injection should not exceed
[Total Split Factor x 0.35 eVs]/1.1 (includes 10% margin for blow-up)
About 3 eVs (h=7) and 2 eVs (h=9) for RF manipulations at Ekin=2.5 GeV
[FB Split Factor x 1 eVs] for transition crossing in h=21
Matched value in the PSB (h1+2) to obtain the above bunch lengths
Recombination kicker rise time:
 | Ekin | Bucket length | Max bunch length
h=7 (std) | 1.4 GeV | 327 ns | 220 ns
h=9 (BCMS) | 1.4 GeV | 255 ns | 150 ns
Kinetic energy, Ekin | Rise time
1.4 GeV | 105 ns
Notes: 3 eVs (h=7)/2 eVs (h=9) due to the acceptance bottleneck at the start of acceleration from 1.4 to 2.5 GeV;
(Total Split Factor 0:35 eVs)/1.1, as bunches at the PS extraction must have longitudinal emittance of 0.35 eVs with 10% blow up allowed in the PS;
Flat Bottom Split Factor 1 eVs for transition crossing on h=21, as bunches go smoothly through transition if their longitudinal emittance is below 1 eVs;
The matched value in the PSB with h=1+2 with available voltage and desired bunch length at extraction.

## Slide 17: Post-LS1: PSB – PS transfer
Longitudinal emittance per bunch at PS injection should not exceed
[Total Split Factor x 0.35 eVs]/1.1 (includes 10% margin for blow-up)
About 3 eVs (h=7) and 2 eVs (h=9) for RF manipulations at Ekin=2.5 GeV
[FB Split Factor x 1 eVs] for transition crossing in h=21
Matched value in the PSB (h1+2) to obtain the above bunch lengths
Recombination kicker rise time:
 | Ekin | Bucket length | Max bunch length | Bunch length (pre-LS1)
h=7 (std) | 1.4 GeV | 327 ns | 220 ns | 180 ns
h=9 (BCMS) | 1.4 GeV | 255 ns | 150 ns | 150 ns
RF Manipulation: | @1.4 GeV | @2.5 GeV
50 ns (Std/BCMS) | 1.2/0.9 eVs | 1.9/0.9 eVs
25 ns (Std/BCMS) | 1.2/0.9 eVs | 2.8/1.5 eVs
Kinetic energy, Ekin | Rise time
1.4 GeV | 105 ns

## Slide 18: Post-LS1: LHC25 (std & BCMS)
Std with new longitudinal parameters
BCMS with new longitudinal parameters
2012
2012

## Slide 19: Beam parameters at LHC injection after LS1
50 ns | Intensity (p/b) | Emittance (μm)
Standard | 1.7 x 1011 | 1.7
BCMS | 1.7 x 1011 | 1.1
25 ns | Intensity (p/b) | Emittance (μm)
Standard | 1.2 x 1011 | 2.6
BCMS | 1.15 x 1011 | 1.4
2012 performance
Assuming transport in the PS and SPS within budgets like in 2012
Requires successful SPS scrubbing !
All beams to be prepared in 2014!

## Slide 20: Beam parameters at LHC injection after LS1
50 ns | Intensity (p/b) | Emittance (μm) | Intensity (p/b) | Emittance (μm)
Standard | 1.7 x 1011 | 1.7 | 1.7 x 1011 | 1.6
BCMS | 1.7 x 1011 | 1.1 | 1.7 x 1011 | 1.1
25 ns | Intensity (p/b) | Emittance (μm) | Intensity (p/b) | Emittance (μm)
Standard | 1.2 x 1011 | 2.6 | 1.3 x 1011 | 2.4
BCMS | 1.15 x 1011 | 1.4 | 1.3 x 1011 | 1.3
2012 performance
with potential improvements from optimized PSB-PS transfer and intensity increase in SPS
Assuming transport in the PS and SPS within budgets like in 2012
Requires successful SPS scrubbing !
All beams to be prepared in 2014!
Setup of longitudinal blow-up along PSB ramp and h1+2 transfer to the PS during commissioning and MDs
Push SPS to intensity limit for 25 ns beams

## Slide 21: Outline
  LHC requirements for the injectors
  Single bunch beams
  25 ns and 50 ns physics beams
  Doublet scrubbing beam and 8b+4e beam
  LHC Ion beam
  LHC beams’ status and planning
  Conclusions

## Slide 22: Doublet beam
Injection of trains of 72 x 10 ns long bunches with 1.7e11 p/b on unstable phase and capture in two neighboring buckets in the SPS  successfully tested (no acceleration to 450 GeV)  e-cloud enhancement observed in the SPS
4
2
8
6
0
1
2
3
Time [ms]
200 MHz RF Voltage [MV]
4
-2
0
1st inj.
measurement!
Need to gain experience in the SPS with dedicated MDs in 2014 for complete parameter list at flat top
For more info see H. Bartosik, Chamonix 2014

## Slide 23: 8b+4e scheme
Trains with 4 missing bunches every 8 bunches
  Allows for larger intensity per bunch and expected to reduce e-cloud effects
BCMS scheme
bunch pattern:
3x(8b+4e) + 8b
Standard scheme
bunch pattern:
6x(8b+4e) + 8b
Simulations shown.
Recent successful tests in the PS.
To be fully optimized in MDs during 2014-2015
For more info see G. Rumolo, Chamonix 2014
25 ns (8b+4e) | Intensity (p/b) | Emittance (μm) | Bunch pattern
Standard | 1.8 x 1011 | 2.3 | 6 x (8b+4e) + 8b
BCMS | 1.8 x 1011 | 1.4 | 3 x (8b+4e) + 8b
H. Damerau, RLIUP 2013

## Slide 24: Outline
  LHC requirements for the injectors
  Single bunch beams
  25 ns and 50 ns physics beams
  Doublet scrubbing beam and 8b+4e beam
  LHC Ion beam
  LHC beams’ status and planning
  Conclusions

## Slide 25: LHC ion performance in 2011
Pb-Pb goal in 2011: 30-50 mb-1 in 4 weeks, with Lpeak = 1.4x1026 Hz/cm2
Achieved @ 3.5ZTeV : 150 mb-1 with peak luminosity 5x1026 Hz/cm2 (half of the nominal)
  Increased LEIR brightness with nominal bunch population of 4.5x108 Pb54+ ions/bunch but smaller emittances
  Scaling with E2, Lpeak = 2x1027 Hz/cm2 @ 7ZTeV (twice the nominal)
    Good beam behaviour at low energy in PS due to excellent vacuum
    Modified production scheme: No splitting in PS, i.e. half as many bunches with twice the intensity/bunch
    Good behaviour of bunches on SPS flat bottom (RF Noise improved, IBS & space charge less critical than expected and with Q20 after 2013)

## Slide 26: LHC ion performance in 2013 projected to 2015
For p-Pb run in 2013, LEIR bunch intensity further increased to 5.5x108 Pb54+ ions/bunch (1.2 times the nominal)
With same scheme as 2011, and performance of 2013, Pb-Pb peak luminosity of 3x1027 Hz/cm2 @ 7ZTeV can be expected
A 20% increase in peak luminosity (3.6x1027 Hz/cm2 @ 7ZTeV) can be gained by squeezing 20% more bunches in LHC
  Batch compression to 100ns in PS
  Two-bunch batches separated by 225ns in SPS (12 injections, to be optimised)

## Slide 27: LHC ion scheme in 2011
LEIR
PS (NO splitting) bunch spacing = 200ns
SPS at extraction, after 12 transfers from PS,
Batch spacing = 200 ns
LHC at injection, after 15 transfers from SPS
(9 108 Pb ions / 3.6 s)
Pb ions / LHC bunch
2.2 108
1.4 108
b* = 1 m -> L = 5.1026 cm-2 s-1
Harmonic number / Frequency
2
24-21 -169
16–14-12-24
200 MHz
400 MHz
7 injections
2
Nb of bunches
2
24
358
3 108
4.5 108
LHC in collision
1.2 108
358
200ns
200ns
200ns

## Slide 28: LHC ion scheme in 2015
LEIR
PS batch compression bunch spacing = 100ns
SPS at extraction, after 12 transfers from PS,
Batch spacing = 225 ns
LHC at injection, after 18 transfers from SPS
1.1 109 Pb ions / 3.6 s)
Pb ions / LHC bunch
2.2 108
1.6 108
Harmonic number / Frequency
2
-169
16–18-21
200 MHz
400 MHz
7 injections
2
Nb of bunches
2
24
432
100ns
100ns
225ns
LHC in collision
1.4 108
432
100ns
225ns
b* = 0.5 m -> L = 3.6 1027 cm-2 s-1

## Slide 29: Outline
  LHC requirements
  Single bunch beams
  25 ns and 50 ns physics beams
  Doublet scrubbing beam and 8b+4e beam
  LHC Ion beam
  LHC beams’ status and planning
  Conclusions

## Slide 30: Revised Injector schedule 2014

## Slide 31: LHC beam status and planning
  Recover 2012 performance
    LHCPROBE (=LHCPILOT) and LHCINDIV
      In good shape in PSB and PS, 12-24 bunches taken in SPS for realignment campaign and RF setting-up (energy matching)
    LHC 25 and 50 ns standard
      Produced in PSB and PS (triple splitting achieved), fine tuning in progress
      Not taken yet in SPS (scrubbing in week 45)
    LHC 25 and 50 ns BCMS not taken yet
  Pushing intensity of 25ns beam and production of doublet beam
    To be established in (dedicated) MDs by the end of 2014 (scrubbing run II in 2015)
    Many other concurrent MD requests and setting up of Ar for NA ion physics
  8b+4e beam
    Recent successful tests in the PS
    Tests in the SPS probably not before 2015 due to limited MD time
  LHC ion beams not yet produced in LEIR but general problems solved
    To be optimized in 2014-2015
K. Hanke, Chamonix 2014

## Slide 32: Outline
  LHC requirements for the injectors
  Single bunch beams
  25 ns and 50 ns physics beams
  Doublet scrubbing beam and 8b+4e beam
  LHC Ion beam
  LHC beams’ status and planning
  Conclusions

## Slide 33: Conclusions
Single bunch beams
  New production scheme for better control of intensity and longitudinal emittance
25 ns and 50 ns beams
  Recovering the 2012 performance relies on successful scrubbing of the SPS
  Implementation of new beam production schemes for higher brightness in PSB and PS and higher intensity in SPS
  Second SPS scrubbing run in 2015
Doublet beam for LHC (and SPS) scrubbing
8b+4e beam as low e-cloud option
  Successful measurements in the PS
  Tests in SPS not before 2015 (limited MD time)
LHC ions
  Pb performance in 2013 and PS batch compression (100ns)
Injectors are already very busy: physics beams, LHC beams (old and new schemes!), ion beams in preparation for 2015, MDs …
lots of SPS MD time with very long cycle needed !!

## Slide 34
Thank you for your attention