## Slide 2: PS Low-level Electronics and Tests
H. Damerau
Finemet Review Meeting
09/09/2014
Many thanks to T. Bohl, M. Haase, M. Migliorati, M. Paoluzzi, D. Perrelet, C. Rossi

## Slide 3
Overview
Introduction and motivation
  Coupled-bunch feedback and beam-loading compensation
  Beam tests with existing feedback before LS1
Beam-loading compensation feedback
  Impedance of Finemet cavity, design constraints and choices
  Narrow-band tracking filters, delay compensation
Plans for coupled-bunch feedback
  Decoupling of coupled-bunch damping and beam-loading compensation
First measurements with beam
Conclusions and outlook

## Slide 4
Overview
Introduction and motivation
  Coupled-bunch feedback and beam-loading compensation
  Beam tests with existing feedback before LS1
Beam-loading compensation feedback
  Impedance of Finemet cavity, design constraints and choices
  Narrow-band tracking filters, delay compensation
Plans for coupled-bunch feedback
  Decoupling of coupled-bunch damping and beam-loading compensation
First measurements with beam
Conclusions and outlook

## Slide 5
Introduction and motivation
Longitudinal coupled-bunch oscillations with LHC-type beams during acceleration and on flat-top
Present feedback using 10 MHz cavities as kickers covers only two modes
Insufficient for LHC-type beams after LIU upgrades
New digital coupled-bunch feedback
Finemet cavity installed in SS02 during LS1 (M. Paoluzzi et al.)
LLRF feedback loop to reduce cavity impedance
Direct feedback around amplifiers, but moderate gain due to large bandwidth can be added

## Slide 6
Feedback loops around Finemet cavity
The LLRF for the wide-band kicker (will) comprise(s) two distinct loops:
  Coupled-bunch feedback
    Input: Wall current monitor signal
    Output: Drive signal to cavity
Compensate beam-loading
    Wide-band feedback around amplifier  limited reach due to bandwidth
    Feedback to reduce cavity impedance at revolution frequency harmonics
    Input: Gap return signal from cavity
    Output: Drive signal to cavity
Priority was with beam-loading compensation loop so far
Signal processing for coupled-bunch feedback part to be added

## Slide 7
Coupled-bunch oscillations, freq. domain
Synchrotron frequency sidebands of the frev harmonics:
F. Pedersen, F. Sacherer, PAC77, pp. 1397-1399
In the case of LHC-type beams in the PS (h = 21)
upper
lower

## Slide 8
Coupled-bunch oscillation damping
Bunches oscillate with different phases (and amplitudes)
Example of an n = 12 mode (Df ≈ 206)
Mode number n defined by phase advance from bunch-to-bunch:
Coupled-bunch oscillations show up as side-bands of nfrev or (h-n)frev
Df = 2p n/h
Finemet cavity for coupled-bunch damping: kick at 0.4...5 MHz
frf
Kick
Measure
Kicker baseband
Preferred detection

## Slide 9
Excitation and damping of coupled-bunch oscillations  cross-damping
Tested basic features in view of new feedback kicker
Damping on different harmonic than detection works
Detect at h = 13  damp with C10-11 at h = 8
Detect at h = 8  damp with C10-11 at h = 13

## Slide 10
Low-level and high-power RF for PS damper
-3 dB
6
Splitter + amp.
Coupled-bunch feedback
Comb. + att.
Beam-loading compensation
Wall current monitor
fclk = 256 frev
  Single LLRF driving all six cells
Cavity return sum
But: beam-loading reduction essential to reduce power from beam
Two feedbacks: 1. Beam  Finemet cavity, 2. Cavity return  cavity
No detrimental effect on beam stability expected

## Slide 11
Overview
Introduction and motivation
  Coupled-bunch feedback and beam-loading compensation
  Beam tests with existing feedback before LS1
Beam-loading compensation feedback
  Impedance of Finemet cavity, design constraints and choices
  Narrow-band tracking filters, delay compensation
Plans for coupled-bunch feedback
  Decoupling of coupled-bunch damping and beam-loading compensation
First measurements with beam
Conclusions and outlook

## Slide 12
Cavity impedance of PS Finemet cavity
No tuning, impedance unchanged during acceleration
Impedance quasi constant within 10% frequency range
With 20 dB reduction  ~10 W/cell (cf., e.g., wall current monitor: 6 W)
Harmonic dependent delay, especially for low harmonics
Damping needed at many harmonics: ~ frev to 40 frev
M. Paoluzzi
Frequency [MHz]
Delay [ms]
Impedance per cell with amplifier
Delay of cells 5+6
Network analyzer
From beam induced voltage (low intensity)

## Slide 13
Options for LLRF beam-loading feedback
Feed-forward | 1-turn delay feedback | Narrow-band filters
Successful tests at JPARC Main Ring (F. Tamura et al.) High reduction (> 26 dB) of beam induced voltage Difficult to measure without beam Little experience with digital feed-forward systems at CERN | New system successfully commissioned on 10 MHz cavities (D. Perrelet et al.) Few adjustment parameters  excellent for changing impedance of sweeping cavities Set-up without beam Same gain for different harmonics  compromise Phase compensation filter for high gain at large bandwidth needed | Same hardware as 10 MHz 1-turn delay feedbacks No need for physical delay Gain, delay and phase adjustable per harmonic Combinable with coupled-bunch feedback Set-up without beam Potential issues with reduction of transients  to be investigated Many parameters to be adjusted  only easy for cavity with fixed impedance
 Bank of narrow-band tracking filters seems good compromise
F. Tamura et al., IPAC14, p. 3385
D. Boussard et al., EPAC88, p. 985

## Slide 14
Narrow-band tracking filters
  Band pass filter with high gain at frev harmonic
    Flexible, adapts to delay/phase curve of cavity: gain, delay and phase adjustable for each harmonic
    Avoid need for programmable delay (single clock, no delay lines, etc.)
  Filter bank for multiple harmonics (firmware)
  Similar to coupled-bunch feedback  correction from coupled-bunch part can be injected after low-pass filters
Low-pass
Low-pass
ADC
DAC
Cavity return
Cavity drive
sin(hFB frevt + f)
sin(hFB frevt)
cos(hFB frevt + f)
cos(hFB frevt)

## Slide 15
Overview
Introduction and motivation
  Coupled-bunch feedback and beam-loading compensation
  Beam tests with existing feedback before LS1
Beam-loading compensation feedback
  Impedance of Finemet cavity, design constraints and choices
  Narrow-band tracking filters, delay compensation
Plans for coupled-bunch feedback
  Decoupling of coupled-bunch damping and beam-loading compensation
First measurements with beam
Conclusions and outlook

## Slide 16
New azimuth register numerical oscillators
  Signals at various harmonics again synchronous with h = 1, but:
    No need for a tagged clock
    Main phase accumulator on h = 1 only reset once (or once per cycle)
    Additional standard direct digital synthesizer (DDS) for non-integer h
h
f
Counter
fclk
sin
cos
Reset
  Clock frequency choice: 28 frev = 256 frev  111.7 MHz to 122.1 MHz
  ‘Multi-harmonic source system on chip’
  Prototype firmware already contains up to 36 azimuth register sources on a single

## Slide 17
Open loop transfer function
  180 phase advance at each filtered harmonic
  Filter group delay ~ 1.4 ms (below 1 turn)
Single h tracking filter
4 adjacent harmonics
Prototype firmware

## Slide 18
Delay compensation
A. Ozturk, PS/RF/Note 99-05
  The ~ 700 ns delay of the cavity must be compensated to keep the filter phases correct during acceleration
  At 10 MHz, 1% frequency change would introduce ~25 phase shift
    ‘Delay without delay’, positive and negative
    Virtual delay by de-phasing the RF sources for delay t
  sin (wt)  sin (w(t ± t)) = sin (wt + f) with f = ± wt
    Need to de-phase RF sources by f = ± 2p h frev t
    Trivial for delays t = n tclk: f = ± 2p h frev n tclk = ± 2p h/hclk n = const.
    frev is measured by counters on main clock at h = 256
    Multiplication in real time in programmable logic

## Slide 19
Set-up for first measurements
  Prototype firmware for beam-loading compensation
    4 tracking filters at programmable harmonics (h = 7, 8, 9, 10 by default)
    Single swept clock at 256 frev
    Automatic measurement of clock frequency for delay compensation
    Possibility to inject additional RF signal (coupled-bunch damping)
  Running on 1-turn delay feedback hardware (D. Perrelet)
  New front-end close to high power racks (short delay) installed
  Coupled-bunch filtering part to be added
  Coverage of more harmonics (copy-paste)

## Slide 20
Closed-loop transfer function with cavity
fclk = 100 MHz (frev = 391 kHz)
fclk = 125 MHz (frev = 488 kHz)
Delay compensation works fine, symmetric notches while clock changing by Dfrev/frev ≈ 25%
Maximum feedback gain achieved at h = 7, 8 , 9 , 10: ~20 dB
Prototype firmware
h = 10
h = 7
h = 10
h = 7

## Slide 21
Overview
Introduction and motivation
  Coupled-bunch feedback and beam-loading compensation
  Beam tests with existing feedback before LS1
Beam-loading compensation feedback
  Impedance of Finemet cavity, design constraints and choices
  Narrow-band tracking filters, delay compensation
Plans for coupled-bunch feedback
  Decoupling of coupled-bunch damping and beam-loading compensation
First measurements with beam
Conclusions and outlook

## Slide 22
Add coupled-bunch feedback?
  Narrow notches at frev harmonics well decoupled
  But they are wide with respect to synchrotron frequency
Single notch
Close to hfrev
Synchrotron frequency side-bands close to hfrev
Beam-loading compensation feedback appears as constant numeric factor to coupled-bunch signal processing
Df ≈ ±fs

## Slide 23
Both feedbacks together (1 harmonic)
Low-pass
Low-pass
ADC
DAC
Cavity return
Cavity drive
sin(hFB frevt + f)
sin(hFB frevt)
cos(hFB frevt + f)
cos(hFB frevt)
fs side-band filter
ADC
Wall current monitor
cos((hRF-hFB)frevt + f)
sin((hRF-hFB)frevt + f)
fs side-band filter
  Signal processing for single harmonic
  Required multiple times

## Slide 24
How many harmonics?
 | Couple-bunch feedback | Beam-loading compensation
Signal processing chains | 10 | ~40
Detection harmonic | hdet = 11…20 5 to 10 MHz | hdet = hkick = 1…~40 0.4 to ~20 MHz
Damping harmonic | hkick = 1…10 0.4 to 5 MHz | 
  Full configuration needed 10 times
  For any further harmonics, only beam-loading reduction, needed ~30 times
Measured cavity transfer function, 1…12 frev

## Slide 25
Overview
Introduction and motivation
  Coupled-bunch feedback and beam-loading compensation
  Beam tests with existing feedback before LS1
Beam-loading compensation feedback
  Impedance of Finemet cavity, design constraints and choices
  Narrow-band tracking filters, delay compensation
Plans for coupled-bunch feedback
  Decoupling of coupled-bunch damping and beam-loading compensation
First measurements with beam
Conclusions and outlook

## Slide 26
First measurements with beam
At injection
At transition
Gap relay open
Gap relay closed
  Spectrum of beam induced voltage (passive probe)
  Important signal from beam at passive probe around ~40 MHz
  No effect on beam stability observed (cf. 40 MHz cavities)
  Gap relay only efficient below ~10 MHz  need damping circuit

## Slide 27
First measurements with beam
Open/closed loop transfer function
500 kHz 6 MHz
  Moderate feedback gain (very first test!)
  Transfer function measurement: ~ 10…12 dB
  Spectrum of beam induced voltage in Finemet cavity
  26GeV-test cycle, single bunch accelerated on h = 8
  Impedance reduction observed with beam as expected

## Slide 28
Frequency range and feedback gain
  Test of maximum feedback gain and frequency range
h = 1
h = 8, 9
h = 42
  Beam induced spectrum (passive probe)
At injection
At transition
  Close to 20 dB reduction achievable from 0.45 MHz to 20 MHz

## Slide 29
Overview
Introduction and motivation
  Coupled-bunch feedback and beam-loading compensation
  Beam tests with existing feedback before LS1
Beam-loading compensation feedback
  Impedance of Finemet cavity, design constraints and choices
  Narrow-band tracking filters, delay compensation
Plans for coupled-bunch feedback
  Decoupling of coupled-bunch damping and beam-loading compensation
First measurements with beam
Conclusions and outlook

## Slide 30
Summary
Design of beam-loading reduction feedback for the Finemet cavity
  Bank of narrow-band feedbacks, one per harmonic
  Expected gain ~ 20 dB in addition to fast feedback around amplifier
  Based on feedback circuit  feed-forward may be added if needed
  ≥ 12 signal processing chains (harmonics) integrated on one board
First tests without and with beam successful
  ‘Delay compensation without delay’ validated
  Beam induced voltage reduction consistent with gain from transfer function measurement
  Close to 20 dB reduction of beam induced voltage from 0.45 to 20 MHz
Beam induced voltage at passive gap voltage probe with relay closed
  Damping circuit being investigated, no effect on beam stability

## Slide 31
Outlook
Measurements with beam:
  Spectrum of beam induced voltage with and without wide-band feedback around amplifiers
  Beam induced voltage with gap relay closed during intensity increase
  Excitation with coupled-bunch feedback part
Firmware development to be continued:
  Improve resolution of numerical oscillators (12 bit  16 bit)
  Improve handling of numerical overflow
  Increase number of harmonics treated simultaneously
  Implement coupled-bunch damping part of feedback
Integration to control system

## Slide 32
THANK YOU FOR YOUR ATTENTION!

## Slide 33
Operational PS coupled-bunch feedback
Analogue signal processing, two channels
Two accelerating cavities as feedback kickers  limits to modes h – 1 and h - 2
New wide-band Finemet cavity as kicker
Digital feedback electronics
J.-L. Vallet, https://ab-div.web.cern.ch/ab-div/Meetings/APC/2005/apc050609/JL_Vallet_slides.pdf
Cover all modes

## Slide 34
New cavity (#25) in the PS ring
M. Paoluzzi
Wide-band (0.4 – >5.5 MHz, VRF = 5 kV) cavity based on Finemet material
No acceleration, but damping of coupled-bunch oscillations
SS02
6-cell cavity unit
Accelerating gap
Power amplifiers (solid state)
Cavity installed in SS02, amplifiers on 2 gaps
First installation of transistor power amplifiers close to beam in PS

## Slide 35
Beam induced voltage in Finemet cavity
Beam induced voltage in Finemet cavity observed
Amplitude higher than expected for present intensities
No effect of cavity observed on the beam
40 MHz ringing following each bunch passage
Verified:
  Closure of gap relay
  Attenuation of gap voltage divider

## Slide 36
Ringing at around 40 MHz
26GeV test cycle, single bunch, h = 8, close to transition
Resonance frequency ~ 39 MHz, quality factor ~ 12
Measurements correct? Probe attenuation at 40 MHz?

## Slide 37
Check probe attenuation around 40 MHz
Lab measurement
Chart: Monitors transfer functions
-21 dB
In-situ gap 3
(07/07/2014)
Lab and (both) in-situ measurements similar
Low probe attenuation (resonance?) around 38 MHz
M. Paoluzzi
50 W in parallel to gap
High impedance (~1 kW)

## Slide 38
Full bandwidth, gap relay open/closed
500 mV/div
100 mV/div
200 mV/div
200 mV/div
200 mV/div
200 mV/div
Gap 3
Gap 6
Gap 5
Open
Closed
Higher voltage with gap relay closed?  40 MHz resonance?
Passive probe + 10 dB

## Slide 39
10.7 MHz low pass, gap relay open/closed
500 mV/div
50 mV/div
Gap 3
Gap 6
Gap 5
50 mV/div
200 mV/div
20 mV/div
200 mV/div
Open
Closed
Gap relay reduces beam induced voltage in low frequency range by almost one order of magnitude
Passive probe + 10.7 MHz low-pass

## Slide 40
Local short circuit test below gaps
Gap 1, wire
Gap 4, copper strip
Gap 2, screw
10.7 MHz low-pass
Full band-witch
20 mV/div
100 mV/div
50 mV/div
10 mV/div
50 mV/div
5 mV/div
10 dB add. att
Copper strip directly below the cavity closes gap most efficiently
Temporarily implemented on four gaps

## Slide 41
Spectrum of beam induced voltage, gap 6
Amplifier inactive
Amplifier active
Gap relay open and closed
Passive probe + 20 dB, 26 GeVTest cycle
  Gap relay above ~20 MHz less efficient than expected

## Slide 42
Low pass filtering and transposition
  Two stage low pass filter:
  Cascaded integrator-comb (CIC) filter
  Leaky integrator filter
    1st order low-pass to reduce higher pass bands of CIC filter
Low-pass (transposed to 4 MHz)
  Attenuation at adjacent harmonic (500 kHz): > 45 dB
  Good decoupling between narrow-band feedback loops

## Slide 43
Numerical oscillators for down/up conversion
  Starting point: multi-harmonic source (MHS) of beam control
  Signals at various harmonics, synchronous with respect to h = 1, but:
    Needs clock tagging
    Main phase accumulator synchronously reset when changing h
R. Garoby, PS/RF/Note 97-10
Latch
fclk
f
sin
cos
h
Reset (using tag)
Simplified overview of existing multi-harmonic sources

## Slide 44
Excitation (feedback at hFB = 14, 18b)
Single side-band  single mode

## Slide 45
Mode scan with 18 bunches in h = 21
Excite each mode individually and measure mode spectrum
Some modes can be excited very cleanly, others as a mixture; artefact?

## Slide 46
Mode scan with 21 bunches in h = 21
Excite each mode individually and measure mode spectrum
Clean observation of all possible modes

## Slide 47
Damping rate versus gain and intensity
Measured damping rate with feedback on
Corrected for natural damping
Versus gain
Versus intensity
Zero damping at zero gain
Natural damping in-dependent from gain
Damping increases with intensity, more signal for given CB oscillation amplitude
Saturation leads to non-zero damping with zero Np?

## Slide 48
Damping rate versus el and cycle time
Versus el (RMS)
During cycle
Uncorrected: damping efficiency increases for larger el
Reduced natural stability for smaller el
Corrected damping independent from el
Damping efficiency reduces at higher energy
To be checked with simulations
~9 GeV
~26 GeV
~9 GeV
~26 GeV

## Slide 49
Kick voltage measurement
Time resolved spectrum of C10-11 cavity return
Time
19
20
18
h = 17
21
22
23
24
h = 25
Excitation
Extract an normalize relevant harmonic
Excitation
Damping
Amplitude modulation from carrier (at hf0) and fs side-band (hf0 ± fs)
Fit gives initial damping amplitude and time (+ fs and phase)

## Slide 50
Kick voltage versus oscillation amplitude
Excite a coupled-bunch oscillation and measure its amplitude
Observe maximum damping voltage required
Only order of magnitude for kick voltage
Overestimate expected as feedback normally started before oscillations are well developed
Frequency range | 0.4 to 5.5 MHz
RF voltage per sideband, Vmode | ~ 1 kV
Maximum total RF voltage, Vmax | ~ 5 kV
Un-damped shunt impedance at n·frev | < 200 W
M. Paoluzzi, H.D., CERN-ACC-NOTE-2013-0019
Basic specifications of kicker cavity: