## Slide 2: Radiation protection study for the HIE-ISOLDE project
S. Giron*, A.-P. Bernardes, A. Dorsival, D. Voulot and J. Vollaire**
* Marie-Curie Fellow now at EDF (France)
** Presenting

## Slide 3: Outline
Radiation Protection challenges of HIE-ISOLDE
Shielding design for the post-accelerator
  X-ray measurements
  FLUKA calculations for the post-accelerator
Ion interactions after post-acceleration
  Operational parameters for HIE-ISOLDE
  Activation calculations
Radiation Monitoring System upgrade
Conclusions

## Slide 4: RP challenges of HIE-ISOLDE
Field emission in RF cavities lead to X-rays
  Accelerating structures within a shielded enclosure
  BUT many feed-trough for services
  Keep the current radiological classification of the hall
Beam accelerated above the Coulomb barrier
  Possibility to have nuclear reactions
  Strong wish to keep the current working practices (access to experimental setup during operation)
RIB implantation (risk increases with intensity)
  Hot-spot for gamma emitters
  Contamination risks when opening the vacuum chamber or working on vacuum related equipment

## Slide 5: Outline
Radiation Protection challenges of HIE-ISOLDE
Shielding design for the post-accelerator
  X-ray measurements
  FLUKA calculations for the post-accelerator
Ion interactions after post-acceleration
  Operational parameters for HIE-ISOLDE
  Activation calculations
Radiation Monitoring System upgrade
Conclusions

## Slide 6: X-ray measurements
Measurements in SM18
Measurements in Orsay
Time dependent measurements + passive dosimeters

## Slide 7: X-ray measurement results
Dose Rate (mGy/h)
Measurements in SM18
Measurements in Orsay
Measurements in different phases (conditioning, Q…)
Implementation of the SM18 setup in FLUKA
  Emission of electrons at the beam axis level
  Electron emission rate derived from the measured dose rate
FLUKA simulation

## Slide 8: FLUKA calculations
Detailed model of the accelerator implemented in FLUKA
Source term based on X-ray measurements (900 keV e-)
Considering the most penalizing case (conditioning of all cavities at the same time)
3D model
FLUKA geometry

## Slide 9: Some results
105 dose reduction factor
Exclusion area on the roof (RF on)
Simulations for Phase 1 and 2
Conservative scenario…
RF interlocked with access

## Slide 10: Outline
Radiation Protection challenges of HIE-ISOLDE
Shielding design for the post-accelerator
  X-ray measurements
  FLUKA calculations for the post-accelerator
Ion interactions after post-acceleration
  Operational parameters for HIE-ISOLDE
  Activation calculations
Radiation Monitoring System upgrade
Conclusions

## Slide 11: Operational parameters
RIBs delivered at very low intensity (~ppA)
Stable beam (C, N, O, Ne or Ar) for setup from REXEBIS rest gas or gas injection
  20 e-pA (beam tuning on a weekly basis)
  Exceptionally (typically once a year) up to 500 e-pA for commissioning and for machine development
Gas injection is done by experts only and can be destructive (in case of gas leaked in EBIS)
1 p-e pA = 6.25x106 particle-charge /s

## Slide 12: Prompt dose rate
Analytical approach for different combinations of beam/target
Neutron dose rate @ 1 m and 90 degree
Verified with FLUKA
(approach described in ISAC-II safety file)
Area Classification | Ambient Dose Rate (permanent workplaces) | Ambient Dose Rate (Low occupancy)
Supervised Radiation Area | <3 μSv/h | <15 μSv/h
Simple Controlled Radiation Area | <10 μSv/h | <50 μSv/h

## Slide 13: Ion interactions (FLUKA)
Helium
19.8 MeV/amu
Helium
12 MeV/amu
Example full beam loss of 1 ppA
Generic geometries
(dipole, flange or FC)
Very good agreement with the analytical approach
used in the ISAC-II safety file
Example full beam loss of 1 ppA

## Slide 14: Classification / mitigations
Optimization (posting)
for beam tuning with 20 epA
Special measure for emittance measurements (beam permit, exclusion areas ….)
Experimental setups remain accessible during operation and standard tuning periods
Dose rate @ 1 m / 90 degree in Sv/h

## Slide 15: Beam induced activation
Demonstrate that bulk activation of intercepting devices is not an issue (still contamination from RIBs !)
  Criteria : (LE = exemption limit)
 | Nuclide | T1/2 | LEi (Bq) | Ai (Bq) | Ai/LEi
Copper target | 73As 68Ga 68Ge 65Zn 63Ni 60Co 57Co 56Co 55Fe 54Mn 3H | 80.3 d 67.7 m 270.8 d 244.2 d 100.1 y 5.3 y 272.0 d 77.3 d 2.7 y 312.5 d 12.3 y | 4E+04 1E+05 8E+03 1E+02 7E+04 1E+02 1E+03 1E+02 3E+04 1E+02 1E+05 | 4.5E+00  0.96 % 3.1E+01  1.53 % 3.1E+01  1.53 % 2.5E+01  1.02 % 8.6E+00  1.43 % 1.2E+01  3.25 % 3.5E+01  1.37% 1.2E+00  2.37% 5.5E+01  1.36% 1.6E+01  2.20% 1.3E+02  0.99% | 1.1E-04 3.1E-04 3.9E-03 2.5E-01 1.2E-04 1.2E-01 3.5E-02 1.2E-02 1.8E-03 1.6E-01 1.3E-03
 |  |  |  |  | Sum = 0.00141
No activation of the water in the dipole cooling circuit

## Slide 16: Outline
Radiation Protection challenges of HIE-ISOLDE
Shielding design for the post-accelerator
  X-ray measurements
  FLUKA calculations for the post-accelerator
Ion interactions after post-acceleration
  Operational parameters for HIE-ISOLDE
  Activation calculations
Radiation Monitoring System upgrade
Conclusions

## Slide 17: Monitoring upgrade
Additional radiation monitors needed to ensure the proper area classification
  Unsufficient number of monitor in some areas
  New projects
Old monitoring system not scalable (ARCON)
New architectural options
  gamma monitoring (GRAMS)
  RAMSES (LHC standard)
Scheduling: LS1 was a good time window

## Slide 18: New RAMSES system
Ionisation chambers, induced activity / X-ray monitors, Hand foot monitors…..

## Slide 19: Environmental monitoring
Aerosols
Sampler
Gas monitor
Iodine Sampler
Radon/Thoron
Monitor
INEMIA project
Monitoring of facility releases

## Slide 20: GRAMS in the hall
PIMSM11=170PAGIS501
PADIS509
PIMSM05=170PAGIS407
PADIS405
PIMSM01=197PAGIS601
PADIS601
PAGIS602
PIMSM10=170PAGIS416
PADIS410
PIMSM01=170PAGIS401
PADIS401
PIMSM02=170PAGIS402
PADIS402
PIMSM03=170PAGIS403
PADIS403
PAGIS404
PIMSM04=170PAGIS405
PADIS404
PAGIS406
PIMSM06=170PAGIS408
PADIS406
PAGIS409
PAGIS410
PAGIS411
PAGIS415
PIMSM08=170PAGIS412
PADIS408
PAGIS413
PIMSM09=170PAGIS414
PADIS409

## Slide 21: Conclusions
Complete radiological analysis for the new post-accelerator
  Post-accelerator shielding (X-ray measurements and FLUKA calculations)
  Prompt dose due to ion beams interactions
New monitoring system will facilitate future upgrades of ISOLDE (MEDICIS, TSR….)
Thanks to partners visited in the frame of the CATHI program (INFN Legnaro, Triumf, GANIL, IPNO, CEA where Sandra made her secondment…)

## Slide 22: Questions ?

## Slide 23: Experimental benchmark
 | Interaction model | Evaporation model | Evolution model
PHITS 2011.2b-5 | BME | SDM | DCHAIN SPD2001
 |  | GEM | 
FLUKA 2.64 | QMD | New evap model (heavy fragments) | RADDECAY
Chart: Dose rate (µSv/h)
| 90 degrees
FLUKA | 3960.2843
PHITS | 2844
Maximum measurement | 3500
Mean measurement | 2431
Uncertainty on beam intensity prevent to be conclusive

## Slide 24: Experimental benchmark
Uncertainty on beam intensity
prevent to be conclusive