## Slide 1
Powerpoint Templates
High Resolution Separator
Mathieu Augustin (EN-RBS-STI) HIE-ISOLDE Workshop September 2014
Notes: The HRS is one of the two isotope separators, part of the ISOLDE facility located alongside CERN PS Booster. It is a mass spectrometer...etc. It has a significant role for experiments in which isobaric contamination from abundantly produced isotopes can be a major disturbance to measurements.

## Slide 2
Outline
The High Resolution Separator and its current situation
The new constraints
Design proposals
Magnet features
The technology: pole face winding coils
The testbench

## Slide 3
Layout view of the separator room (courtesy of V. Barozier
Beam
source
MG90
MG60
Optical layout of HRS (courtesy of T. Giles)
The High Resolution Separator
Current status
Layout view of the separator room
Beam
source
MG90
MG60
RFQBC
Notes: Include current separation of HRS (beam distrib)

## Slide 4
Layout view of the separator room (courtesy of V. Barozier
The High Resolution Separator
Current HRS optical performances
Attainable mass resolution R=5000
for beam source of emittance ε=20π.mm.mrad
OBJECTIVE :
  Resolution R=M/ΔM=20 000
Notes: Include current separation of HRS (beam distrib)

## Slide 5
The High Resolution Separator
How to reach high resolution ?
Beam emittance
Eliminate higher order terms (=aberrations)
Dispersion D
Mx magnif. Factor
x0 beam size at source
Notes: Dispersion : area occupied by the beam in the magnet

## Slide 6
RFQ
Layout view of the separator room
Beam emittance factor
 RFQ displacement
Ensuing constraints :
  Beamlines installations and positioning
  Separator room size
The High Resolution Separator
RFQ-CB displacement
OBJECTIVE :
  Resolution R=M/ΔM=20 000 for a beam source emittance ε=3π.mm.mrad
Moving of the RFQ-CB

## Slide 7
Design proposal #1
Schematic 3D view of the layout #1
Resolution at int.
focus = 20 000
Resolution at final.
focus = 1 000
Notes: Good dispersion but bad resolution of higher order effects
Overaall resolution low at fina lfocus
Basic principles of the design : quad doublet : their function (quick), advantage (higher order terms)
Multipoles element bracketing the 90deg magnet

## Slide 8
Design proposal #1bis
Schematic 3D view of the layout #1bis
Resolution at int.
focus = 20 000
Resolution at final
focus = 16 000
Notes: Good dispersion but bad resolution of higher order effects
Overaall resolution low at fina lfocus
Basic principles of the design : quad doublet : their function (quick), advantage (higher order terms)
Multipoles element bracketing the 90deg magnet
Neighbouring beam heavily distorted : hard to tune

## Slide 9
Design proposal #2
Schematic 3D view of the layout #2
Beam emittance ε=3π.mm.mrad R = 20 000 for more than 99% transmission of pure beam R ~ 23 000 for 90% transmission of pure beam
Resolution at final
focus = 20 000
Notes: For a beam source emittance ε=3 π.mm.mrad, numerical simulations performed with program COSY Infinity indicate that the resolution at first order amounts to R=23 500, and at third order to R= 23 000. Monte Carlo simulation results are shown hereunder, for a beam set of 100 000 particles, at neighbouring masses such that m/∆m=20 000. Results show a transmission of slightly more than 99% of pure beam out of 100 000 particles for mass M=100. If one is ready to lose some beam, numerical simulations show that the resolution can be pushed up to R ~ 23 000 for a transmission of 90% of pure beam.

## Slide 10
Magnet features Optical parameters
List of parameters for the mechanical design of the magnet
Notes: Considering the high bending angle, using a entrance/exit profile would lead to the use of at least 30 degrees (to check)
Complicated for the beamline (next elements such as quad)
Inhomogeneous field gives more flexibility in the choice of the quadrupole component
Easy tuning done with knob (to inject current in order to simulate the value of coefficientS)
Back up slide for effects of hexa and octopole on tails of beam distribution. Helps for reaching High Resolution (compare to HRS current casE)

## Slide 11
Magnet features : optical parameters
Beam enveloppe for design #2 in lab coordinates (x,z), featuring a magnet using entrance/exit profiles (producing a quadrupole component)
No entrance/exit angular profile
Radially Inhomogeneous Magnetic field :
(with α, β and γ respectively being the quadrupole, sextupole and octopole components)
Plane pole faces  easier to machine
Inhomogeneous field produced with pole face windings
Example of magnet design, producing a radial inhomogeneous field, using inclined pole faces.
Notes: Considering the high bending angle, using a entrance/exit profile would lead to the use of at least 30 degrees (to check)
Complicated for the beamline (next elements such as quad)
Inhomogeneous field gives more flexibility in the choice of the quadrupole component
Easy tuning done with knob (to inject current in order to simulate the value of coefficientS)
Back up slide for effects of hexa and octopole on tails of beam distribution. Helps for reaching High Resolution (compare to HRS current casE)

## Slide 12
H type magnet  mechanically more stable, possibility of better pole face machining
Magnet features
Yoke made of laminated steel  reduction of eddy currents, allowing an increase in cycling speed (~1min VS 15min)
Changing pole face width  saving of material (~8%)
Notes: Considering the high bending angle, using a entrance/exit profile would lead to the use of at least 30 degrees (to check)
Complicated for the beamline (next elements such as quad)
Inhomogeneous field gives more flexibility in the choice of the quadrupole component
Easy tuning done with knob (to inject current in order to simulate the value of coefficientS)
Laminated steel : more complicated to build,b ut nowadays handable
Reduces cycling speed : 15min
Back up slide for effects of hexa and octopole on tails of beam distribution. Helps for reaching High Resolution (compare to HRS current casE)

## Slide 13
The High Resolution Separator
Pole face windings
Optimize currents in the conductors to match the field composition
Effect of pole face winding for α and β component in the main field distribution. Dashed curves represent the additional field necessary to modify α and β
Schematid view in cross section of the new HRS magnet (H-type), featuring the pole face windings technology (picture credit to M. Breitenfeldt
Iron case
Higher order term coefficients are adjustable by changing current
High degree of freedom
Current density in the conductor : up to 1A/mm2 (with air cooling)
for the studied magnet : 0.2 A/mm2 were necessary

Notes: Space available due to the expected low height of the beam.
23mm at worst in height, the gap foreseen is 60mm.
Technology avoids tedious pole shimming to reach the correction coefficients.
Just rogowski profile is performed for adjusting magnetic length and avoiding field leaking (or fringe fields)
Calibration needed for the first time :
Once calibration is done, task should be easier
EXTRA:
Size of coils calculated including the cooling water ducts
With max magnetic field of 0.5T, ampere turns per coil calculated to be NI=N*h / 2 eta * mu0 = 12.3 kA
Pole gap as small as possible, but needs space for beam, vacuum chamber and pole face windings  h=60mm

## Slide 14
The High Resolution Separator
Pole face windings
Schematic view in cross section of the new HRS magnet (H-type), and partial view in 3D, featuring the pole face windings technology (picture credit to M. Breitenfeldt)
Iron case
Avoid field lines saturation  adapting the design

## Slide 15
The High Resolution Separator
3D view of the new HRS magnet (H-type), featuring the pole face windings technology (picture credit to M. Breitenfeldt)

## Slide 16
The High Resolution Separator
Poleface windings allow the adjustment of the magnetic field along the beam axis.
Rogovski profile at pole entrance and exit adjusts magnetic length.
Excitation of return yoke is not exceeding 0.9T for max field at beam axis (0.5T)  the excitation is in the linear regime.
3D magnetic field map of the new HRS magnet for a section of a magnet, computed with Opera software (picture credit to M. Breitenfeldt)

## Slide 17
The Offline Separator

## Slide 18
The Offline Separator
October 2013 : FE8 made its first beam : 30 nA at 40 kV with surface ion source !
March 2014 : First separation tests successful
Front End
Magnet 90
Diagnostics
RFQ-CB (soon)

## Slide 19
The Offline Separator
Objectives
Design of a new offline magnet ongoing, featuring pole face windings
Objective : validate the technology
Current magnet is of flat pole type, with entrance/exit profile (later used as pre-separator?)

## Slide 20
The Offline Separator
Objectives
ISOLDE FRONT END 8
Beam production
Tests and characterization of different ion sources
THE RFQ-CB
Investigation of functional parameters :
      injection/extraction system efficiency
      Emittance and beam parameters

## Slide 21
A workable layout, including all necessary items
Design choice for the magnet features
Functional test bench for validating the technology
Pole face winding
source parameters
Conclusion
ON THE ROAD TO A NEW HIGH RESOLUTION MAGNET…
Notes: Workable layout
Design choice for the layout
Design choice for the magnet construction
Offline as a testbench for validating thesep oints (source and pole face windings)

## Slide 22
Acknowledgements
My supervisor Tim Giles
All the Marie Curie Fellows, and CERN staff
The Marie Curie Actions
The research project has been supported by a Marie Curie Initial Training Network Fellowship of the European Community’s
Seventh Programme under contract number (PITN-GA-2010-264330-CATHI)

## Slide 23
Thank you for your attention

## Slide 24
The Offline Separator
0D characterization of dipole magnet
Pole shoe face
Geometrical bending start
Magnet symmetry line
Vacuum chamber flange edge

## Slide 25
The Offline Separator
Dipole magnet
Characterization of dipole magnet
  Magnetic characterization
  1D magnetic field map
Separation test
Stability of magnetic field
Notes: Plasma ion source was used (MK5, model of plasma ion source)
Reason why you see CO (carbon monoxyde) in the beam

## Slide 26
The Offline Separator
In the future…
Foreseen layout of ISOLDE offline #2 (courtesy of S. Marzari)

## Slide 27
The High Resolution Separator
Optical simulations
source of emittance ε=20π mm.mrad
Considered masses :
  M0=100
  M1=100.02
  M2=99.98
Computation performed at 3rd order
Dispersion D=2700mm
Resolving power : R=M/ΔM=5000
Octave computation of the current HRS
Optical layout of HRS (courtesy of T. Giles)

## Slide 28
The Offline Separator
Frame for characterization
Magnet case
Vacuum chamber
Magnet symmetry line
s
Magnet flange
Notes: There was the need to obtain a characterization of the magnet, as we had no data about this magnet.
NOw, having a precise magnetic field map takes long time and complicated devices : train matching the shape of vacuum chamber, long run of measurements with high precision etc…. We were told 1 year and a half to construct etc…

## Slide 29
The Offline Separator
0D characterization of dipole magnet
Use of a Hall (teslameter) probe and a polycarbonate frame
m
Notes: Conditions to remind :
2 ramps, each time up and down, for checking the measurements.

## Slide 30
In order to obtain high resolution, a large value of (x|δ) and small values of (x|x) and Δ are desirable
Resolving power (ideal case)
Aberrations decrease the resolving power
Δ total amount of aberrations Mx lateral magnification factor D dispersion
The High Resolution Separator
Resolution parameters
Factors limiting the attainable mass resolution :
  Ion source emittance
  Optical aberrations
  Beam instrumentation
Ion source emittance

## Slide 31
The High Resolution Separator
Reaching high resolution
Beam emittance
Eliminate higher order terms (=aberrations)
Dispersion
Q quality factor, Ao area occupied by the beam in the magnet increasing resolution R for given source (transmission) means increasing the term A0/po

## Slide 32
Design proposal #1 : details
Beam enveloppes in dispersive and the vertical plane

## Slide 33
Design proposal #2 : details

## Slide 34
Design proposal #1bis : details
Beam enveloppes in dispersive and the vertical plane

## Slide 35
Done for 133deg magnet, po=1m, alpha=0.58

## Slide 36
No entrance/exit angular profile
Magnet with a Radially Inhomogeneous Magnetic field :
(with α, β and γ respectively being the quadrupole, sextupole and octopole components)
Plane pole faces  easier to machine
Yoke made of laminated steel  reduction of eddy currents, allowing an increase in cycling speed (~1min)
H type magnet  mechanically more stable, possibility of better pole face machining
Changing pole face width  saving of material (~8%)
Magnet features
Notes: Considering the high bending angle, using a entrance/exit profile would lead to the use of at least 30 degrees (to check)
Complicated for the beamline (next elements such as quad)
Inhomogeneous field gives more flexibility in the choice of the quadrupole component
Easy tuning done with knob (to inject current in order to simulate the value of coefficientS)
Back up slide for effects of hexa and octopole on tails of beam distribution. Helps for reaching High Resolution (compare to HRS current casE)

## Slide 37
tracking in OPERA 3D
Preliminary