## Slide 1: Extending the scope of the ISOLDE Laser Ion Source

## Slide 2
2012
3060 h laser on time
24 runs
344 RILIS operator shifts (24/7)
13 elements
B.Marsh, Isolde Workshop and Users Meeting, CERN, 2013
The Resonance Ionization Laser Ion Source - RILIS
RILIS is the most requested ion source available at ISOLDE
RILIS is ultra selective while efficient

## Slide 3
Magnet set to A = 205
The Resonance Ionization Laser Ion Source - RILIS
ground State
excited states
Rydberg state
auto-ionizing state
ionization potential
Stepwise laser ionization scheme
At
Laser tuned to Z = 85
205At
Isotope of interest
Z selective
ion source
laser beams
extractor
experiments
mass separation
target
neutrals
ions
protons
target material
kV
Ionization and extraction

## Slide 4
RILIS
CABIN
The Resonance Ionization Laser Ion Source - RILIS

## Slide 5
Contents
History & Laser Upgrades
Technical improvements
Ongoing RILIS developments

## Slide 6
Laser ion source Proposal (1988)

## Slide 7
1993
Mishin, V., Fedoseyev, V. , Kluge, H., Letokhov, V., Ravn, H., Scheerer, F., Shirakabe, Y. et al. (1993).
Chemically selective laser ion-source for the CERN-ISOLDE on-line mass separator facility. NIM B: 73(4), 550–560.
Slava Mishin
Valentin Fedosseev
RILIS at PSB ISOLDE

## Slide 8: RILIS operation in 1994-2007
Chart: Year
| 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007
 | 490 | 348 | 486 | 1679 | 1267 | 547 | 1203 | 1429 | 1787 | 1820 | 2055 | 2075 | 2253 | 1763
1763 h
2250 h
Reduction of planned RILIS operation time for 2007 down to 1500 hours has been was recommended in the conclusions of the 2007 ATC/ABOC days.
No laser trouble happened during scheduled operation, all required service and repair work was performed between runs

## Slide 9: HIE-ISOLDE aims at increasing the energy of the RIB up to 10AMeV and their intensity by a factor 10
Energy Upgrade:
The HIE-ISOLDE project concentrates on the construction of the SC LINAC and associated infrastructure in order to upgrade the energy of the post-accelerated radioactive ion beams to 5.5 MeV/u in 2016 and 10 MeV/u by 2017-2018
Intensity Upgrade:
The design study for the intensity upgrade, also part of HIE-ISOLDE, started in 2012, and addresses the technical feasibility and cost estimate for operating the facility at 15 kW once LINAC4 and Upgraded PS Booster are online.
Beam Quality Upgrade:
RFQ cooler and buncher
Solid state lasers for RILIS Higher mass resolving
power HRS

## Slide 10
RILIS Requirements
Diversity of elements
tunable lasers
Rilisdb: Web 2.0, open to everybody
www.cern.ch/riliselements
Flux and fluence conditions
Laser pulse overlap
precise in ~ns range
Atom confinement
geometry
Pulse repetition rate:
34mm
3mm
10KHz
~10GHz line width covers HFS and Doppler broadening
10-50ns pulse width
Accuracy: 40 µeV
UV …VIS… NIR
Saturate resonant transitions
If hard to saturate apply the following
Power (w)
Ion signal (a.u.)
The more power the better
Ensure overlap with atoms
Focus at 20m distance
-> 0.7µrad angular resolution in RILIS
Consider drifts,
SPACE
POWER
TIME
ENERGY

## Slide 11
“The ISOLDE RILIS pump laser upgrade and the LARIS Laboratory”
B. Marsh et al: Hyperfine Interactions, Volume 196, Issue 1-3, pp. 129-141 (2010)
Green Beams
45 W @ 511 nm
Yellow Beams
35 W @ 578 nm
CVL
Green Beams
75 W (+28 W)
@ 532 nm
UV Beam
20 W @ 355 nm
Solid State Laser (Nd:YAG)
8 ns @ 10 kHz
30 min start up time
Reliable long term power output
Copper Vapour Laser upgrade
2007/2008
2 hr start time
Pulse-to-pulse instability (jitter)
Aging equipment
Procurement of consumables is difficult
Risky combination:
High tension ~ 16 kV
High temperature ~ 1500 C
Cooling water
Catches fire (sometimes)
15 ns @ 11 kHz

## Slide 12
The new RILIS dye lasers
dye lasers:
2 x broadband (6 GHz)
1 x narrow band (1 GHz)
> 10 different dyes used
Laser table Jan. 2011
2010/2011

## Slide 13
The RILIS Ti:Sa lasers
Wavelength tuning range:
Fundamental (w) 690 - 940 nm (5 W)
2nd harmonic (2w) 345 - 470 nm (1 W)
3rd harmonic (3w) 230 - 310 nm (150 mW)
4th harmonic (4w) 205 - 235 nm (50 mW)
Change of mirror sets in resonator
No amplifier yet available
No ageing
100 mm
Pump laser: Nd:YAG (532 nm), Photonics
Repetition rate: 10 kHz
Pulse length: 180 ns
Power: 60 W
Ti:Sa lasers:
Line width: 5 GHz
Pulse length: 30-50 ns
2010/2011
S Rothe et al, A complementary laser system for ISOLDE RILIS, 2011 J. Phys.: Conf. Ser. 312 052020

## Slide 14
 | Dye | Ti:Sa
Active Medium | > 10 different dyes | =1 Ti:sapphire crystal
condition of aggregation | liquid (org. solvents) | solid-state
Tuning range | 540 – 850 nm | 680 – 980 nm
Power | < 12 W | < 5 W
Pulse duration | ~8 ns | ~50 ns
Synchronization | optical delay lines | q-switch, pump power
# of schemes developed | 47 | 37
Maintenance | renew dye solutions | ~ none
Comparison dye vs. Ti:Sa system
Ti:Sa
Dye
2x Ti:Sa
2x Dye
3x Ti:Sa
4x Ti:Sa
3x Dye
Ti:Sa system is complementary

## Slide 15
RILIS Dye Laser System
GPS/HRS
Target &
Ion Source
RILIS Ti:Sa Laser System
pA – meter
Faraday cup
Experiments
SHG/THG/FHG
l – meter
Ti:Sa 2
l – meter
Dye 1
SHG
Dye 3 (narrowband)
THG
Dye 2
Ti:Sa 1
Ti:Sa 3 (narrowband)
Nd:YAG
Nd:YAG
10 kHz Master clock
Delay generator
LabVIEW based DAQ
Integration of Ti:Sa to the dye RILIS

## Slide 16
RILIS laser room
2012

## Slide 17
RILIS laser room
2012

## Slide 18: Independent laser for non resonant ionization
Blaze laser tested at RILIS in Dec 2012, purchased with 50% CATHI funds, installed 2014
40W at 10 kHz
17ns Pulse
Low Jitter
Gaussian beam
Much better transmission
efficiency to ion source
A similar efficiency improvement should be expected for the 18 RILIS elements that use non-resonant ionization for the final step!
Laser | Laser Power (on table) | Reference beam power in 3 mm aperture | Transport efficiency
Edgewave | 43 W | 370 mW | 33 %
Blaze | 15 W | 350 mW | 88%
Blaze | 40 W | 800 mW | 76%
Power dependent thermal lensing in the beam transport optics is to be eliminated
B. Marsh et al., Suitability test of a high quality Nd:YVO industrial laser for the ISOLDE RILIS installation.
CERN-ATS-Note-2013-007 TECH
Can be used for Dye and Ti:Sa pumping as a back-up laser
The Upgrade continues: The BLAZE!
2014

## Slide 19: RILIS room extension
Laser table
Existing laser room + SAS
DESK
REF
254 cm
320 cm
28 m2
6 m2
REX EBIS
RILIS
IS COOLER
HV cage
100 cm
Required for / facilitate:
Safety
Reference cell installation
Dye handling
Upgrade of beam observation system
Installation of extra YAG laser
Improved ventilation system
Comfort/ergonomics
LS1

## Slide 20
RELATED projects/tasks:
New reference beam area
New beam stabilization system
Reference cell installation
Benefits:
4 beams to GPS
Fewer power losses
Improved ergonomics
STATUS:
Installed and operational
New GPS laser beam launch & reference system (GLARE)
LS1

## Slide 21
RELATED projects/tasks:
New reference beam area
New beam stabilization system
Reference cell installation
Benefits:
4 beams to GPS
Fewer power losses
Improved ergonomics
STATUS:
Installed and operational
New GPS laser beam launch & reference system (GLARE)
LS1

## Slide 22
Mounted as first target on HRS after LS1. Lasers successfully aligned. Unit Functioning as expected.
facilitates laser alignment - normally only possible with ion beam
helps to clarify laser beam transport issues (thermal lensing)
enables remote check of status of magnet windows when in doubt, reducing interventions to separator areas
Thanks to:
Bernard, Ermanno & our 2013 summer student Sasha
Tungsten ionizer acts as light source for pre-alignment after shutdown
Laser power meter measures laser power delivered through ion source
readout via existing thermocouple infrastructure
RILIS lasers
Magnet window
HRS/GPS
Target Unit
The RILIS Powermeter target unit
LS1

## Slide 23
New features add safety and usability
ease of access for inspection
use of a standard CF mounted viewport (stocked item)
no special tools required for exchange
preserve thread in HRS Al vacuum tank
adding port aligner makes window useful as additional reference point for RILIS
Photo thanks to C.Seiffert
People involved: RILIS, Erwin, Stefano, Alexandre, Giovanna, Ermanno
HRS.MAG.90 laser window upgrade
LS1

## Slide 24
New HRS window tube, port aligner and prism mount
HRS.MAG.90 laser window upgrade
LS1

## Slide 25: Laser Ion Source Trap (LIST)
Suppression of surface ions by electrostatic repeller
Highly selective laser ionization inside the LIST
Ion guiding towards extraction by transverse rf-trapping field
Shielding of laser interaction region from high field gradient of extraction electrode
S.Richter, D.Fink; Laser 2013, Poznan
2006-2012

## Slide 26: Laser Ion Source Trap (LIST)
Suppression of surface ions by electrostatic repeller
Highly selective laser ionization inside the LIST
Ion guiding towards extraction by transverse rf-trapping field
Shielding of laser interaction region from high field gradient of extraction electrode
23Na
24Mg
27Al
25Mg
26Mg
ion current [A]
mass [u]
S.Richter, D.Fink; Laser 2013, Poznan
2006-2012

## Slide 27
target & ion source
The Reference chamber: An atomic beam unit for RILIS
4% reflected beams
~20 m
RILIS cabin
Reference chamber
quartz plate
Installation at RILIS in 2014
measure reference spectra for stable isotopes in In-Source laser spectroscopy
Reduces time for data taking
Increases precision
Application for on-line RILIS monitoring
Scheme development
designed at U Mainz
ultra portable & simple atomic beam unit
Tested at
Fibre of laser light to the RefCell
Demonstrated at the OFFLINE
Laser on
Laser off
T. Day Goodacre
T.Kron

## Slide 28: On-call operation (not yet)
3 requirements for On-Call operation:
3) Automation
2) Performance monitoring
1) Machine protection / safety
To avoid risk of equipment
damage or danger to personnel.
This must be a ROBUST system
(PC independent).
Remote monitoring of key
parameters with an alert system
to request operator intervention.
To maintain RILIS performance
therefore reducing the frequency
of operator interventions.
ESSENTIAL
NON ESSENTIAL
Slide by B.Marsh
Concept outline: R.E.Rossel, Implementation M.Butcher (EN-STI-ECE)

## Slide 29
RILIS Measurement & Control – The REACT framework
R.E. Rossel, et al, Data acquisition, remote control and equipment monitoring for ISOLDE RILIS
Nucl. Instr. and Meth. in Phys. Res. B

## Slide 30
Tom Day Goodacre Students’ Coffee 10/9/2014 46
RILIS@VADIS and VADLIS
VADIS aperture 1.5mm
178Hg Activity
More time required at OFFLINE !
LOI: I-153
In-source laser spectroscopy of mercury isotopes

## Slide 31
2+ Ba ionization at RILIS
Removes possible Caesium contamination
Laser ON
Laser OFF
Tom Day Goodacre Students’ Coffee 10/9/2014 46

## Slide 32
2+ Ba ionization at RILIS
Tested with RILIS at GPS
Laser ON
Laser OFF
Laser OFF
Tom Day Goodacre Students’ Coffee 10/9/2014 46

## Slide 33
Fast beam gating tests at ISOLDE OFFLINE
LS1
100µs
10µs
Increase Voltage spread using high resistive cavities
(suggested by S.Mishin)
Factor 10 selectivity improvement basically for free
To get higher improvement one requires shorter pulses
Use PWM to heat the source
Prototype of pulser (Thx to Pascal Fernier)
is ready to be tested OFFLINE
Pieces are machined by Ermanno, require tests at pump stand and OFFLINE
Ca
Ga

## Slide 34
Permanent Laser Installation at ISOLDE OFFLINE 2
Stefano
2015 ?
Test new RILIS cavities / ion source designs and modes of operation
Verify compatibility of RILIS with future target concepts and separator/pre separator/ISCOOL configurations
quality control of RILIS based ion sources (e.g LIST) before on-line use.
DAI and DR for purchasing a pump laser is ready

## Slide 35: Acknowledgements: CERN – KTH Collaboration
Lars-Erik Berg
Olli Launila
Fabian Österdahl
Marica Sjödin
Ulf Sassenberg
Thomas Pauchard
Göran Tranströmer
Johanna Vannesjö
KTH – Royal Institute of Technology
Stockholm, Sweden
KTH – Royal Institute of Technology &
Knuth and Alice Wallenberg Foundation
Stockholm, Sweden

## Slide 36
Acknowledgements
Current RILIS based core team at CERN (EN-STI-LP)
Valentin Fedosseev
Bruce Marsh
Thomas Day Goodacre
Ralf Erik Rossel
Sebastian Rothe
Former Members
Marica Sjödin
Daniel Fink
Nobuaki Imai
Maxim Seliverstov
Temporarily Supported by
Maxim Seliverstov
Pavel Molkanov
Anatoly Barzakh
Dmitry Fedorov
Yuri Volkov