## Slide 1
RIB at TRIUMF: From ISAC to ARIEL
Colin Morton | Beam Delivery Group Liaison/Coordinator | TRIUMF

## Slide 2: What is TRIUMF?
Canada’s national laboratory for particle and nuclear physics
Programs in nuclear medicine and materials science
Accelerators and accelerator-based research

## Slide 3
PET
520 MeV main cyclotron
Isotope production

## Slide 4
TRIUMF 520 MeV cyclotron:
18 m diameter
4000 t magnet
H- – multiple p+ beams

## Slide 5
Meson production
p+ irradiation
ISAC

## Slide 6
Targets:
  Ta, Nb foils
  SiC, TiC, ZrC
  NiO
  Actinides: UO2, UCx, ThO (this fall)
Ion sources:
  Surface
  FEBIAD
  RILIS
  IG-LIS (RILIS + RF ion guide)
480–520 MeV p+
Up to 100 µA
~50 kW beam power on target

## Slide 7: ISAC operating envelope, 2000–2010
Chart: Mass
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0 | 105.0 | 110.0 | 115.0 | 120.0 | 125.0 | 130.0 | 135.0 | 140.0 | 145.0 | 150.0 | 155.0
2013: CSB | 17.5 | 13.5 | 12.1667 | 9.5 | 9.5 | 8.1667 | 11.6768 | 11.2466 | 10.8578 | 10.505 | 10.1834 | 9.8893 | 9.6194 | 9.3709 | 9.1416 | 8.9294 | 8.7326 | 8.5497 | 8.3794 | 8.2204 | 8.0719 | 7.9329 | 7.8027 | 7.6805 | 7.5657 | 7.4577 | 7.3561 | 7.2604 | 7.1701 | 7.085 | 7.0047
2010: ISAC-II Phase 2 | 17.5 | 13.5 | 12.1667 | 9.5 | 9.5 | 8.1667
2009: Phase 1 full energy | 9.5 | 7.5 | 6.8333 | 5.5 | 5.5 | 4.8333
2006: ISAC-II Phase 1 | 5 | 5 | 5 | 5 | 5 | 4.8333
2000: ISAC-I | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5

## Slide 8: ISAC operating envelope, 2000–2010
Chart: Mass
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0 | 105.0 | 110.0 | 115.0 | 120.0 | 125.0 | 130.0 | 135.0 | 140.0 | 145.0 | 150.0 | 155.0
2013: CSB | 17.5 | 13.5 | 12.1667 | 9.5 | 9.5 | 8.1667 | 11.6768 | 11.2466 | 10.8578 | 10.505 | 10.1834 | 9.8893 | 9.6194 | 9.3709 | 9.1416 | 8.9294 | 8.7326 | 8.5497 | 8.3794 | 8.2204 | 8.0719 | 7.9329 | 7.8027 | 7.6805 | 7.5657 | 7.4577 | 7.3561 | 7.2604 | 7.1701 | 7.085 | 7.0047
2010: ISAC-II Phase 2 | 17.5 | 13.5 | 12.1667 | 9.5 | 9.5 | 8.1667
2009: Phase 1 full energy | 9.5 | 7.5 | 6.8333 | 5.5 | 5.5 | 4.8333
2006: ISAC-II Phase 1 | 5 | 5 | 5 | 5 | 5 | 4.8333
2000: ISAC-I | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5

## Slide 9: ISAC operating envelope, 2000–2010
Chart: Mass
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0 | 105.0 | 110.0 | 115.0 | 120.0 | 125.0 | 130.0 | 135.0 | 140.0 | 145.0 | 150.0 | 155.0
2013: CSB | 17.5 | 13.5 | 12.1667 | 9.5 | 9.5 | 8.1667 | 11.6768 | 11.2466 | 10.8578 | 10.505 | 10.1834 | 9.8893 | 9.6194 | 9.3709 | 9.1416 | 8.9294 | 8.7326 | 8.5497 | 8.3794 | 8.2204 | 8.0719 | 7.9329 | 7.8027 | 7.6805 | 7.5657 | 7.4577 | 7.3561 | 7.2604 | 7.1701 | 7.085 | 7.0047
2010: ISAC-II Phase 2 | 17.5 | 13.5 | 12.1667 | 9.5 | 9.5 | 8.1667
2009: Phase 1 full energy | 9.5 | 7.5 | 6.8333 | 5.5 | 5.5 | 4.8333
2006: ISAC-II Phase 1 | 5 | 5 | 5 | 5 | 5 | 4.8333
2000: ISAC-I | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5

## Slide 10: ISAC operating envelope, 2000–2010
Chart: Mass
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0 | 105.0 | 110.0 | 115.0 | 120.0 | 125.0 | 130.0 | 135.0 | 140.0 | 145.0 | 150.0 | 155.0
2013: CSB | 17.5 | 13.5 | 12.1667 | 9.5 | 9.5 | 8.1667 | 11.6768 | 11.2466 | 10.8578 | 10.505 | 10.1834 | 9.8893 | 9.6194 | 9.3709 | 9.1416 | 8.9294 | 8.7326 | 8.5497 | 8.3794 | 8.2204 | 8.0719 | 7.9329 | 7.8027 | 7.6805 | 7.5657 | 7.4577 | 7.3561 | 7.2604 | 7.1701 | 7.085 | 7.0047
2010: ISAC-II Phase 2 | 17.5 | 13.5 | 12.1667 | 9.5 | 9.5 | 8.1667
2009: Phase 1 full energy | 9.5 | 7.5 | 6.8333 | 5.5 | 5.5 | 4.8333
2006: ISAC-II Phase 1 | 5 | 5 | 5 | 5 | 5 | 4.8333
2000: ISAC-I | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5
RFQ limit: A/q<30
q=1, so A<30

## Slide 11: Beyond A=30…
Need to increase q, lower A/q before acceleration
Charge State Booster (CSB)
  Pantechnik PHOENIX ECRIS charge breeder
  Boosts RIB to high charge states, A/q < 7
  10s to 1000s of pA of stable-beam background
Notes: Modified Pantechnik Phoenix ECRIS held at source bias. Singly charged RIB are injected, come to a soft landing in the ionization region, are charge-bred to high charge states and are extracted to the initial beam energy.

## Slide 12: …to high-mass beam delivery
New equipment:
  Al liner for CSB plasma chamber
  Bragg detector for particle ID and beam setup
New techniques:
  Time-of-flight separation using the low-energy prebuncher and RFQ
  A/q separation using the beamline magnets between the DTL and ISAC-II
  Stripping at 1.5 MeV/u to select charge states with favourable signal/noise ratios
New tools:
  Tune scaling utilities
  Web-based tools for planning high-mass delivery
Notes: Note: The ISAC accelerator chain was not designed for separation. Can achieve resolving powers of several hundred with each technique.

## Slide 13: ISAC operating envelope, 2014
Chart: Mass
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0 | 105.0 | 110.0 | 115.0 | 120.0 | 125.0 | 130.0 | 135.0 | 140.0 | 145.0 | 150.0 | 155.0
2013: CSB | 17.5 | 13.5 | 12.1667 | 9.5 | 9.5 | 8.1667 | 11.6768 | 11.2466 | 10.8578 | 10.505 | 10.1834 | 9.8893 | 9.6194 | 9.3709 | 9.1416 | 8.9294 | 8.7326 | 8.5497 | 8.3794 | 8.2204 | 8.0719 | 7.9329 | 7.8027 | 7.6805 | 7.5657 | 7.4577 | 7.3561 | 7.2604 | 7.1701 | 7.085 | 7.0047
2010: ISAC-II Phase 2 | 17.5 | 13.5 | 12.1667 | 9.5 | 9.5 | 8.1667
2009: Phase 1 full energy | 9.5 | 7.5 | 6.8333 | 5.5 | 5.5 | 4.8333
2006: ISAC-II Phase 1 | 5 | 5 | 5 | 5 | 5 | 4.8333
2000: ISAC-I | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5
3 high-mass, high-energy exp’ts to date (2013/2014)
Several more approved
Notes: 94,95,96Sr to TIGRESS (two runs); 38K to DRAGON
User community given guidance re. preparing proposals for high-mass delivery

## Slide 14: ISAC to date
1996: ISAC construction begins
1998: first RIB at ISAC
2000: first accelerated RIB at ISAC-I
2007: first RIB with ISAC-II SC-LINAC
Now: 3000+ hours/year of RIB to users
  ~32–36 weeks, 8–10 targets, 15–20 experiments + development
  Broad range of isotopes
  Low-energy beams from ~10–60 keV; high-energy beams from 150 keV/u to >6.5 MeV/u (A/q=6)

## Slide 15: Top-notch science
Sn=0
Sp=0
2
8
20
28
50
82
126
82
50
28
8
2
20
r-process
N
Z
Unitarity test of CKM matrix: superallowed β emitter 74Rb
precision branching ratio from 8π – ×3 improvement
precision measurement of the 74Rb8+ mass with TITAN (PRL)
charge radius from collinear laser spectroscopy
Nuclear reactions in Sun, ancient stars & novae
DRAGON: 18F(p,γ)19Ne , 33S(p,γ)34Cl, 17O(p,γ)18F, 3He(α,γ)7Be
TUDA : 18F(p,α)15O, 18F(α,p)21Ne (PRL)
Actinide weak interaction program with UCx targets
laser ionization and spectroscopy of At – towards Rn EDM
Fr yield measurements for Fr PNC experiments
Fr PNC experiment relocated to TRIUMF
LoI for electron EDM experiment with Fr atomic fountain
Tests of ab initio nuclear theory
reaction studies of halo nuclei 11Li & 10,11Be with TUDA and TIGRESS
6He, 8He mass measurements with TITAN
Probing shell evolution and 3-body forces
masses in neutron-rich Na, Ca, K with TITAN
Towards the r-process with UCx targets
masses of 96,98Rb from TITAN
decay properties of 96,98,100,102Rb from 8π
Reiner Kruecken, TRIUMF Science Division
Nuclear structure
Nuclear astrophysics
Fundamental
symmetries
Shape coexistence and shape transition
Transfer reactions with 94,95,96Sr at TIGRESS

## Slide 16: The challenge? Meeting demand
Two-year backlog of experiments
Huge specific demand for 8Li (β-NMR)
Beam delivery improvements:
  Improved scheduling to minimize interruptions
  Better coordination with experimenters
  Finding overlooked sources of downtime
However:
  Efficiency gets you 30–50% more beamtime – not factors of two or three
  We need something more.

## Slide 17
New ISOL infrastructure to build on past success
TRIUMF’s flagship facility
Focus of both the 2010–2015 and 2015–2020 five-year plans
Goal: to more than triple the amount of RIB available at ISAC

## Slide 18: ARIEL: A facility in two acts
ARIEL-I (2010–2015)
  Civil construction for both ARIEL-I and ARIEL-II facilities
  Electron linac up to 25 MeV, 100 kW – centrepiece of the project
ARIEL-II (2015–2020)
  Completion and use of the entire facility

## Slide 19
ARIEL building
ISAC
Existing
ARIEL-I
ARIEL-II
ARIEL LEBT
e-linac
BL4N
Cyclotron
BL2A
3 drivers
3 target stations
3 independent ISAC experimental areas
  Two low-energy
  ISAC-I + ISAC-II HE
3 simultaneous RIB to experiments
Target stations

## Slide 20: ARIEL-I: Civil construction
Building finished Sept. 2013
Also:
  Cryogenics building
  Conversion of Proton Hall for e-linac (e-Hall)
Notes: Time-lapse video of ARIEL building construction is on Vimeo (http://vimeo.com/triumflab).

## Slide 21: ARIEL-I: e-linac
State-of-the art SC linac
  TESLA (ILC) technology
  25 MeV, 100 kW now
  50 MeV, 500 kW later
Why electrons?
  RIB production by photofission – high production of neutron-rich species with less isobaric contamination, no spallation products
10 µA, 500 MeV p+
25 g/cm2 UCx
10 mA, 50 MeV e-
Hg converter
15 g/cm2 UCx

## Slide 22: ARIEL-I: e-linac status
In the last year:
  Cryogenics acceptance testing completed
  e-gun and LEBT installed and commissioned
  MEBT installed
  2 klystrons and HV supplies installed and commissioned
  Injector and accelerator cryomodules assembled, installed, and commissioned
January, 2014
September, 2014

## Slide 23: ARIEL-I: e-linac status
Commissioning underway
e-gun operated up to 10 mA peak current
Beam accelerated to 10 MeV beam dump
20 MeV test planned for next week
L. Merminga (NS2014)
Energy (MeV)
Intensity (normalized)

## Slide 24: ARIEL-II: Overview
Overall goal:
  Delivery of three simultaneous RIB to users
Technical objectives:
  High-intensity photoconverter/target development
    Solid converter for beam power below ~100 kW
    Liquid converter for beam power above ~100 kW
  Expanded expertise in SRF, targets, etc.
Project structure:
  Five phases with timing determined by scientific priority, technical readiness, resource availability

## Slide 25: ARIEL-II scientific deliverables
Phase | Will deliver isotopes…
1 | …as probes of magnetism at interfaces and surfaces of new functional materials using β-NMR.
2 | …to elucidate our fundamental understanding of atomic nuclei by enabling studies of the evolution of structure and dynamics of very neutron-rich nuclei approaching the r-process path.
3 | …for molecular imaging of diseases and treatment of cancer in the ARIEL collection station and isotopes for developing a standard model for nuclear physics.
4 | …to search for new forces in nature. It will also mark the milestone of three simultaneous rare isotope beams delivered to users.
5 | …to determine how the heavy elements from iron to uranium were produced in the universe.
Notes: From the ARIEL-II CFI funding proposal

## Slide 26: Why a phased approach?
Phasing ARIEL-II allows construction and science to alternate during the project
  Fastest way to new science
  Extends TRIUMF’s scientific reach with each phase
  Delivers continuous stream of results, discoveries, and papers through the duration of the project
ARIEL-II has been planned to minimize disruption to ISAC operation and beam delivery

## Slide 27: ARIEL-II Phase 1: Materials science with β-NMR
Goal:
  Photo-production of 8Li in BeO using bremsstrahlung photons from stopping a 100 kW electron beam in a solid target, and delivery to β-NMR at ISAC
Requirements:
  ARIEL e-linac – 25 MeV, 100 kW
  Electron target station (ATE)
  Pre-separator and LEBT
Target station
Pre-separator
LEBT
Notes: Isotopes “as probes of magnetism at interfaces and surfaces of new functional materials using β-NMR.”
First multi-user capabilities.

## Slide 28: ARIEL-II Phase 1: Materials science with β-NMR
Collaboration with VECC (Kolkata)
  MoU signed August 2013
  $10.4M – includes two ARIEL target modules (to be tested at ARIEL) and front-end beamlines
Notes: Dr. Nigel Lockyer (former Director of TRIUMF) and Dr. Dinesh Srivastava (VECC)

## Slide 29: ARIEL-II Phase 2: Photofission for r-process studies
Goal:
  Production and delivery of neutron-rich fission fragments using actinide targets with a solid photoconverter
Requirements:
  Electron target station (ATE) with actinide target
  Actinide chemistry lab
  RILIS source
Phase 2 greatly extends the range of RIB available
Notes: Isotopes “to elucidate our fundamental understanding of atomic nuclei by enabling studies of the evolution of structure and dynamics of very neutron-rich nuclei approaching the r-process path.”

## Slide 30: ARIEL-II Phase 3: Purified high-mass, high-energy RIB
Goals:
  Transport of high-mass RIB from ISAC to ARIEL and purification and charge-breeding of ISAC and ATE beams for delivery to high-energy experimental areas
  A collection station for medical isotopes
Requirements:
  CANREB – CFI-funded project including EBIS, HRS, RFQ coolers, etc.
  Low-energy beam transport through ARIEL
Notes: Isotopes “for molecular imaging of diseases and treatment of cancer in the ARIEL collection station and isotopes for developing a standard model for nuclear physics.”
CANREB: CANadian Rare isotope facility with Electron Beam ion source”

## Slide 31: ARIEL-II Phase 4: Actinide production for fundamental symmetries
Goal:
  RIB production using a new proton beamline (BL4N) delivering up to 100 µA of ~500 MeV protons to a dedicated actinide target station
Requirements:
  Proton beamline
  Proton target station (ATP) and actinide target
  Low-energy beam transport from ATP
Three simultaneous RIB delivered to users
Notes: Isotopes “to search for new forces in nature.”

## Slide 32: ARIEL-II Phase 5: Full-power e-linac
Goal:
  The full e-linac design specification of 50 MeV and 500 kW beam power for RIB production by photofission – 2×1013 fissions/second
Requirements:
  Second accelerator cryomodule
Opens up research into r-process nucleosynthesis with very neutron-rich isotopes
Notes: Isotopes “to determine how the heavy elements from iron to uranium were produced in the universe. ”

## Slide 33: ARIEL-II schedule: Science at every phase
Phase 1: Materials science with β-NMR
Phase 2: Photofission
Phase 3: Medical imaging and treatment; high-mass beams
Phase 4: Fundamental symmetries
Phase 5: Full power of e-linac; r-process astrophysics
Notes: CFI decision: ~$13.5M requested; total project cost ~$34M
Milestones: 2018 – photofission; 2019 – 3 RIB simultaneously
Interruptions: 2019 – BL4N and construction of ATP; 2020 – high-power converter development

## Slide 34
CFI proposal submitted – decision in October
Notes: 19 collaborating institutions from across Canada

## Slide 35: ARIEL-II Collaborators: 19 Canadian universities + TRIUMF
(from the ARIEL-II CFI proposal)

## Slide 36: Summary
ISAC:
  3000+ hrs/year of RIB for users
  High-energy, high-mass program underway
  More demand than available beam time
ARIEL:
  Expanded ISOL capabilities – builds on ISAC success
  New drivers (electron and proton), targets, front ends; new EBIS (CANREB)
  Phased approach designed to maximize science output during construction
  2019: 3 simultaneous RIB to users

## Slide 37: Acknowledgements
ISAC:
  TRIUMF Operations and technical support groups
  TRIUMF’s Beam Delivery group (F. Ames, J. Lassen, P. Kunz, M. Marchetto, R.E. Laxdal)
  High Mass Task Force (F. Ames, M. Marchetto, R.E. Laxdal, A. Garnsworthy*, G. Hackman*, P. Bender*, B. Davids*) (* = Science Division)
  ISAC’s experimental community
ARIEL:
  ARIEL, CANREB, and associated collaborations
This talk:
  R. Kruecken, L. Merminga, R.E. Laxdal, J. Lassen, M. Marchetto, TRIUMF’s Communications group