## Slide 1: CERN Summer School 2014 Introduction to Accelerator Physics Part II
by
Verena Kain CERN BE-OP

## Slide 2: Contents of today’s lecture
In the next three lectures we will have a look at the different components of a synchrotron.
Today:
Controlling particle trajectories in the transverse plane
  Linear beam optics, strong focusing

## Slide 3: Which fields to influence particle trajectories?
Usually use only magnetic fields for transverse control
What is the equivalent E field of B = 1 T?
  Ultra-relativistic:
 To guide the particles we use magnetic fields from electro-magnets.
Lorentz Force
Equivalent electric field!!:

## Slide 4: Dipole magnets: guiding magnets
Vertical magnetic field to bend in the horizontal plane
Dipole electro-magnets:
h

## Slide 5: Dipole magnets: guiding magnets
Circular accelerator: Lorentz Force = Centrifugal Force
Useful formula:
Example for the LHC
  p+ @ 7 TeV/c
  8.3 T
Beam rigidity

## Slide 6: Define design trajectory (orbit)
Length of dipole magnet and field define total bending angle of magnet:
Circular accelerator: total bending angle:= 2p
How many dipole magnets do we need in the LHC?
  Dipole length = 15 m
  Field 8.3 T
a
r
ds

## Slide 7: Focusing is mandatory for stability
Define design trajectory with dipole magnets
Trajectories of particles in beam will deviate from design trajectory
 Focusing
  Particles should feel restoring force when deviating from design trajectory horizontally or vertically
Design trajectory

## Slide 8: Focusing with Quadrupole Magnets
Requirement: Lorentz force increases as a function of distance from design trajectory
E.g. in the horizontal plane
We want a magnetic field that
Quadrupole magnet
Gradient of quadrupole Normalized gradient, focusing strength

## Slide 9: Separate function magnets
Instead of adding a quadrupole field component to our dipoles
Separate function for increased flexibility
  Optimize magnets according to their job: bending, focusing
Add between the dipole magnets separate quadrupole magnets

## Slide 10: The LHC main quadrupole magnet
Length = 3.2 m
Gradient = 223 T/m
Peak field 6.83 T
Total number in LHC: 392

## Slide 11: Towards the Equation of Motion
And now a bit of theory to see how we can calculate trajectories through dipoles and quadrupoles.
Taylor series expansion of B field:
Normalize and keep only terms linear in x
✗
✗

## Slide 12: Towards Equation of Motion
Use different coordinate system: Frenet-Serret rotating frame
The ideal particle stays on “design” trajectory. (x=0, y=0)
And: x,y << r
The design particle has momentum p0 = m0gv.
…. relative momentum offset of a particle

## Slide 13: Towards Equation of Motion
A particle is described with 6 coordinates:

## Slide 14: The Equation of Motion
All we have to do now is to write
in the Frenet-Serret frame,
develop with x,y << r , and keeping only terms linear in x or y for magnetic field
after a bit of maths: the equations of motion
Assuming there are no vertical bends,
Quadrupole field changes sign between x and y

## Slide 15: Solution of Equation of Motion
Let’s write it slightly differently:
horizontal plane:
vertical plane:
Solution can be found with ansatz
Insert ansatz in equation 
For K > 0: focusing
Equation of the harmonic oscillator with spring constant K

## Slide 16: Solution of Equation of Motion
a1 and a2 through boundary conditions:
Horizontal focusing quadrupole, K > 0:
Use matrix formalism: TRANSFER MATRIX

## Slide 17: Solution of Equation for Defocusing Quadrupole
Solution of equation of motion with K < 0:
New ansatz is:
And the transfer matrix

## Slide 18: Summary of Transfer Matrices
Uncoupled motion in x and y
Focusing quadrupole, K >0:
Defocusing quadrupole, K< 0:
Drift space: length of drift space L
….horizontal plane
….vertical plane

## Slide 19: Step 1 – when designing a synchrotron
Design orbit with dipole magnets and alternating gradient lattice.

## Slide 20: A few important concepts

## Slide 21: The Hill’s Equation
We had…
Around the accelerator K will not be constant, but will depend on s
Where
restoring force ≠ const, K(s) depends on the position s
K(s+L) = K(s) periodic function, where L is the “lattice period”
General solution of Hill’s equation:
Hill’s equation

## Slide 22: The Beta Function & Co
Solution of Hill’s Equation is a quasi harmonic oscillation (betatron oscillation): amplitude and phase depend on the position s in the ring.
The beta function is a periodic function determined by the focusing properties of the lattice: i.e. quadrupoles
The “phase advance” of the oscillation between the point 0 and point s in the lattice.
integration constants: determined by initial conditions

## Slide 23: The transport matrix re-vistited
Definition:
Let’s assume for s(0) = s0, y(0) = 0.
Defines f from x0 and x’0, b0 and a0.
Can compute the single particle trajectories between two locations if we know a, b at these positions!

## Slide 24: The Tune
The number of oscillations per turn is called “tune”
The tune is an important parameter for the stability of motion over many turns.
It has to be chosen appropriately, measured and corrected.
Measure beam position at one location turn by turn
Beam position will change with
With FFT get frequency of oscillation: tune

## Slide 25: The Tune
The choice of phase advance per cell or tune and hence the focusing properties of the lattice have important implications.
Misalignment of quadrupoles or dipole field errors create orbit perturbations
The perturbation at one location has an effect around the whole machine
 diverges for Q = N, where N is integer.

## Slide 26: The Tune and Stability
Quadrupoles can have gradient errors  avoid half-integer tunes
Higher order field errors…
In the end avoid simple fractional tunes where Q = n/m with n,m small integers.
Choose a stable working area in the tune diagram.
Qx
Qy

## Slide 27: Phase-space ellipse
With:
One can solve for
is a constant of motion: Courant-Snyder invariant
is parametric representation of an ellipse in the xx’space: phase-space
Shape and orientation of ellipse are given by a, b and g: the Twiss parameters

## Slide 28: Phase-space ellipse
The area of the ellipse is constant (Liouville):
The area of the ellipse is an intrinsic property of the beam and cannot be changed by the focusing properties.

## Slide 29: Emittance of an ensemble of particles
Typically particles in accelerator have Gaussian particle distribution in position and angle.
Transverse profile measurement and Gauss fit
x'
x
Define beam emittance e as ellipse with area in phase-space that contains 68.3 % of all particles. Such that
x

## Slide 30: Liouville during Acceleration
Liouville’s Theorem from Hamiltonian Mechanics:
canonical variables q, p
e.g. q = position = x
p = momentum = gmv = mcgbx
The theorem:
We use x’:

The beam emittance shrinks during acceleration!!

## Slide 31: The FODO-Lattice
Alternating gradient focusing.
F=focusing O=nothing (or bend, RF structure,…) D=defocusing
A FoDo lattice consists of FoDo cells:
This is what the beta functions look like in a FoDo cell
Focal length of quadrupole:
Stability criterion for FoDo:
…don’t focus too strong!
Notes: Thin lens approximation… ((1,1),(1/f,1)) Trace of total M > 2

## Slide 32: The beta functions around the machine
An example…
bx, by

## Slide 33: Some numbers…
The LHC consists of 8 arcs. Each arc consists of 23(+2) FODO cells.
The regular FODO cell has the following characteristics:
Phase advance: 90°
Maximum beta: 180 m
FODO
The beam size changes along the cell!
Maximum horizontal beam size in the focusing quadrupoles
Maximum vertical beam size in the defocusing quadrupoles

## Slide 34: Some numbers…
The emittance at LHC injection energy 450 GeV: e = 7.3 nm
At 7 TeV: e = 0.5 nm
Normalized emittance: e* = 3.5 mm
Normalized emittance preserved during acceleration.
And for the beam sizes:
At the location with the maximum beta function (bmax = 180 m):
s450GeV = 1.1 mm
s7TeV = 300 mm
Aperture requirement: a > 10 s
Vertical plane: 19 mm ~ 16 s @ 450 GeV
~ 47 mm
~ 38 mm

## Slide 35: Some numbers…
Need aperture margin for imperfections: e.g. orbit
Horizontal and vertical trajectory around the ring during commissioning. Corrected orbit peak ~ 4 mm.
Notes: The bunch center is not going through the center of the vacuum chamber, but is offset. And around the offcenter trajectory one needs at leat +/- 3 sigma.
What can also see here is the number of oscillations around the ring…which corresponds to the tune.

## Slide 36: What’s next?
We will have a look at longitudinal motion
Imperfections
Injection, Extraction

## Slide 37: Annex

## Slide 38: Coordinate Transformations – Curvilinear-Cartesian