## Slide 1: LHC Upgrade
O. Brüning
CERN, Geneva, Switzerland

## Slide 2: Contents
Introduction
Main challenges for the LHC operation
HL-LHC Upgrade Ingredients
LHC layout overview and main parameters
LHC Performance Summary
Upgrade Performance Goals
Other, future upgrade plans (if time permits)

## Slide 3: Introduction: LHC Goals & Performance
Collision energy: SM exploration requires ECM > 1 TeV
p collisions Ebeam > 4 TeV strong magnetic fields
and/or large storage ring
Instantaneous luminosity: # events in detector
Integrated luminosity: L
depends on the beam lifetime, the LHC cycle and
‘turn around’ time and overall accelerator efficiency
rare events L > 1033cm-2sec-1 L > 1034cm-2sec-1

## Slide 4: Introduction: the LHC is a Synchrotron
R = constant:
v = c B 
LHC / LEP: 0 = 11.3 kHz
More details in the lecture on Accelerators by Verena Kain
in the first week

## Slide 5: Introduction: the LHC is a Synchrotron
uniform B field: R = constant
high beam energies require: -high magnetic bending field
-large circumference
-large packing factor
realistic synchrotron: B-field is not uniform
-drift space for installation
-different types of magnets
-space for experiments etc
for E >> E0

## Slide 6: Introduction: Magnet Technology
physics goal: E = 7 TeV
existing infrastructure: LEP tunnel: circ = 27 km
with 22 km arcs
assume 80% of arcs can be filled with dipole magnets: F = 0.8
required dipole field for the LHC:
B = 8.38 T
(earth: 0.3 10-4 T)

## Slide 7: Introduction: Magnet Technology
high beam energies require large rings and high fields
1) Iron joke magnet design 2) air coil magnet design
-field quality given by pole face geometry -field quality given by coil geometry
-field amplified by Ferromagnetic material -SC technology avoids Ohmic losses
-iron saturates at 2 T -risk of magnet quenches
-Ohmic losses for high magnet currents -field quality changes with time

## Slide 8: Introduction: Magnet Technology - Quench
Critical surface of NbTi:
-high ambient magnetic field
lowers the capability to sustain
large current densities
-low temperatures increase the
capability to sustain large
current densities
-LHC: B = 8.4 T;
existing machines: Tev: B=4.5T; HERA: B=5.5T; RHIC: B=3.5T
He is superfluid below 2K and has a large thermal conductivity!
 6MJoule / magnet (L = 100mH)  energy for melting 10kg Cu
T = 1.9 K
j = 1 - 2 kA / mm2  ca. 11kA
More details on superconductivity and superconducting magnets in the lecture by Paolo Ferracin on Thursday and Friday
Notes: Specific heat for Cu: 385 J/kg, melting point 1085 degrees Celsius, Latent heat fusion: 0.2MJ.kg -> 0.6MJ melts 1 kg Cu

## Slide 9: Introduction: 2-in-1 Magnet design
collider ring design requires 2 beams:
design with one aperture requires particles & anti-particles
Not efficient for a hadron collider! (Tevatron, Chicago USA)
2-ring design implies twice the hardware
LHC features novel 2-in-1 magnet design

## Slide 10: Introduction: 2-in-1 Magnet Design
2-in-1 dipole magnet design with common infrastructure:
-15 m long few interconnects (high filling factor)
but difficult transport (ca. 30 tons)
-compact 2-in-1 design allows p-p collisions in LEP tunnel
-corrector magnets at ends tight mechanical tolerances

## Slide 11: Introduction: Luminosity
colliding bunches:
with:
is determined by the magnet arrangement & powering
L = 1034 cm-2sec-1
n is determined by the injector chain
goal:
high bunch intensity and many bunches
small  at IP and high collision energy

## Slide 12
Beam dumps
RF
Collimation
Collimation
1720 Power converters
> 9000 magnetic elements
7568 Quench detection systems
1088 Beam position monitors
4000 Beam loss monitors
150 tonnes Helium, ~90 tonnes at 1.9 K
140 MJ stored beam energy in 2012
370 MJ design and > 500 MJ for HL-LHC!
450 MJ magnetic energy per sector at 4 TeV
 ≈ 10 GJ total @ 7 TeV
LHC: big, cold, high energy
Injection B2
Injection B1

## Slide 13: The LHC and its Injector Complex:
SPS: 26 -> 450 GeV
PS: 1.4 -> 26 GeV
PSB: 50 MeV -> 1.4 GeV
LINAC2: 50 MeV
LHC: 450 -> 7000 GeV

## Slide 14: The Nominal LHC Operation Cycle:
 Operational Turn around time of 2 - 3 hours  Efficiency = time in physics / scheduled time
Beam dump
Ramp down/precycle
Injection
Ramp
Squeeze
Collide
Stable beams
Ramp down | 35 mins
Injection | ~30 mins
Ramp | 12 mins
Squeeze | 15 mins
Collide | 5 mins
Stable beams | 0 – 30 hours

## Slide 15: Main Challenges for the Operation
Magnetic field perturbations & field quality
Beam power and machine protection
Collective effects and impedance
Triplet aperture and beam-beam
Unintentional beam aborts
Electron cloud effect

## Slide 16: LHC Challenges: Magnet Field Errors
time varying field errors in super conducting magnets
Luca Bottura CERN, AT-MAS
t
I
192.1 A
11743A
769.1A

## Slide 17: LHC Challenges: Magnet Field Errors
the LHC features 112 circuits / beam (+ orbit correctors)
all magnet circuits
are tested before and during
installation
adjustments during operation
 non-destructive beam instrumentation

## Slide 18: LHC Challenges: Beam Power
Unprecedented beam power:
potential equipment
damage in case
of failures
during
operation
In case of
failure the
beam must
never reach
sensitive
equipment!

## Slide 19: LHC Challenges: Quench Protection
Magnet Quench:
Quench level: Nlost < 7 108 m-1
requires collimation during all operation stages!
requires good optic and orbit control! feedback loops
 beam abort  several hours of recovery
LHC nominal beam intensity: I = 0.5A => 3 1014 p /beam
 2.2 10-6 Nbeam!
(compared to 20% to 30% in other superconducting rings)

## Slide 20: LHC Challenges: Collimation Efficiency
III
Primary
Secondary
Triplet
Dump Kicker
Dump Protection
Tertiary
5.7
6.7
10
Absorbers
7
15
I
II
IV
beam
2012
‘Tight’ =
Iberian
Peninsula
2.2mm
2011
‘Interm.’
Norway =
3.1mm
1 (450GeV) ≈ 1mm
1 (4TeV) ≈ 0.35mm
1 (6.5TeV) ≈ 0.25mm

## Slide 21: LHC Challenges: Machine Protection
Unprecedented beam power:
all absorbers and the collimation system
must be designed to survive an
asynchronous beam dump!
(total of up to 136 collimators & absorbers) Machine protection System!
Robust collimator jaw design
fiber reinforced graphite jaws
are more robust than Cu jaws
fiber reinforced graphite
has a higher impedance and
electrical resistivity

## Slide 22: LHC Challenges: Collective Effects
resistive wall impedance:
image charges trail behind due to
resistivity of surrounding materials
 Wake fields drive beam instabilities
effect increases with decreasing gap
opening of the collimator jaws
depends strongly on jaw opening (3rd power)
impedance of Graphite jaws either limits the minimum
collimator opening  limit for b* or the maximum beam current
phased collimation system for the LHC:
Phase 1: graphite jaws for robustness during commissioning
Phase 2: nominal performance (low impedance collimators & coating)

## Slide 23: LHC Challenges: Triplet Aperture
Insertion Layout:
Symmetric drift space:
bmax proportional to L*2/b*
 b* = 0.5m  s ≈ 16mm at IP and s ≈ 1.5mm inside triplet
ca.130m
ca.50m

## Slide 24: LHC Challenges: Parasitic Collisions
long range beam-beam:
Operation with ca. 2800 bunches  approximately 30 unwanted collision points per Interaction Region (IR).
non-linear fields and additional focusing due to beam-beam
 Operation requires crossing angle
efficient operation requires large beam separation at unwanted collision points  separation of 10 s is at the limit of the triplet aperture for nominal b* values!
smaller b* values  larger triplet apertures
 upgrade studies!!!

## Slide 25: LHC Challenges: Electron Cloud
synchrotron light removes electrons
electrons are accelerated by the beam
e- hit vacuum surface and generate secondary e-
electron cloud (shields beam field)
Effect disappears for large bunch spacing
p

## Slide 26
L. Tavian,
2005
H. Maury Cuna,
2009
“ultimate”
nominal
spare cooling capacity for
0.55 m b*
going above Nb=1.7x1011 & ultimate luminosity requires
dedicated IR cryo plants; limit then becomes Nb~2.2x1011
spare
cooling
capacity
at zero
luminosity
(=total-SR
-impedance)
e-cloud heat
load for
SEY=1.3
cooling & e- heat for 25 ns spacing
nominal

## Slide 27: LHC Challenges: Unforeseen Beam Aborts
UFOs
20 dumps in 2012
Timescale 50-200 µs
Al2O3 at MKI
Conditioning observed
Worry about 6.5 TeV
Al
O
A. Gerardin, N. Garrel
EDMS: 1162034
Radiation to electronics
Concerted program of mitigation measures (shielding, relocation…)
Premature dump rate down from 12/fb-1 in 2011 to 3/fb-1 in 2012

## Slide 28
2011: Decrease from ≈10 UFOs/hour to ≈2 UFOs/hour.
2012: Initially, about 2.5 times higher UFO rate than in October 2011. UFO rate decreases since then. Up to 10 times increased UFO rate with 25ns.
  Extrapolation to 7 TeV: 91 UFO related beam dumps (2011 data: 112 dumps)
LHC Challenges: ARC UFO rate

## Slide 29: Challenge of Reaching US2 Goals:
 corresponds to ca. 40% machine efficiency (time actually spend in physics divided by scheduled time for physics operation)
2011
2012
Fill lengths in 2011 and 2012  exponentials.
  ~30% of the fills are dumped by operation.

## Slide 30
2010: 0.04 fb-1
  7 TeV CoM
  Commissioning
2011: 6.1 fb-1
  7 TeV CoM
  Exploring the limits
2012: 23.3 fb-1
  8 TeV CoM
  Production
Integrated Luminosity 2010-2012

## Slide 31
Performance Projections:
HL-LHC goal:
10 x performance
Increase after LS3
(5 x annual)
ca. 23fb-1
prior
LS1
ca.
300fb-1
by
LS3
ca. 40fb-1 – 60fb-1
per year between
LS1 and LS3

## Slide 32: LHC Upgrade Goals:
Consolidation activity for assuring running of the LHC & injector complex up into late 2030ies
Prepare the LHC for a total luminosity of ≈ 3000 fb-1
 Radiation and R2E
#Shielding and removing equipment from the tunnel
 Radiation hardness of magnets (lifetime) & shielding
#e.g. triplet and cleaning insertions
 Cryogenic and Cooling
Devise beam parameters for ca. 250 fb-1 / year
System Upgrades for allowing a peak Luminosity of
L > 5 1034 cm-2 s-1

## Slide 33
Huge efforts over last months to prepare for high lumi and pile-up expected in 2012:
optimized trigger and offline algorithms (tracking, calo noise treatment, physics objects)
 mitigate impact of pile-up on CPU, rates, efficiency, identification, resolution
in spite of x2 larger CPU/event and event size  we do not request additional computing
resources (optimized computing model, increased fraction of fast simulation, etc.)
Z μμ
Z μμ event from 2012 data with 25 reconstructed vertices
2012: ~30 events/xing
at beginning of fill
with tails up to ~ 40.
2011: average
12 events/xing,
with tails up to ~20
Use leveling techniques for keeping average
Pileup around 140 events per bunch crossing
 level luminosity at 5 1034 cm-2 s-1

## Slide 34: LHC Upgrade Goals: Performance optimization
Luminosity (round beams):
1) maximize bunch brightness (Injector complex)  [Nb/en]
2) minimize beam size (constant beam power; aperture)
3) maximize number of bunches (beam power; e-cloud)
4) compensate for ‘R’
Operation at performance limit
choose parameters that allow higher than design performance
leveling mechanisms for controlling performance during run
Event pileup & e-cloud

## Slide 35: LHC Challenges: Crossing Angle
geometric luminosity
reduction factor:
large crossing angle:
 reduction of long range beam-beam interactions
 reduction of head-on beam-beam parameter
 reduction of the mechanical aperture
 reduction of luminous region
 reduction of instantaneous luminosity
 inefficient use of beam current
effective cross section

## Slide 36: HL-LHC Upgrade Ingredients: b*
R(b*)/b*
b*
1/b*
Geometric reduction factor: b* = 15cm  10 cm
ca. 40% for b* 0.5m -> 0.25m
ca. 15% for b* 0.3m -> 0.2m
ca. 10% for b* 0.2m -> 0.1m

## Slide 37: HL-LHC Upgrade Ingredients: Crab Cavities
Geometric Luminosity Loss
Factor:
effective cross section
Reduces the effect of geometrical reduction factor
Independent for each IP
Noise from cavities to beam?!?
Little experimental evidence that it can work effectively
Feasibility needs to be demonstrated in beam tests (SPS)
Underground Infrastructure requirements to be assessed!
Crab Cavities:
More details on the RF System for the LHC Upgrade in the lecture by Erk Jensen on Friday

## Slide 38: HL-LHC Upgrade Ingredients: Triplet Aperture
R(b*)/b*
b*
1/b*
Geometric reduction factor  b* ≥ 10 cm
Triplet aperture:
 ca. twice the nom. aperture  Large aperture magnets
 b* = 0.15m  s ≈ 3.5mm inside triplet!
ca. 40% for b* 0.5m -> 0.25m
ca. 15% for b* 0.3m -> 0.2m
ca. 10% for b* 0.2m -> 0.1m
Need Crab Cavities for full
Exploitation!!!

## Slide 39: HL-LHC Upgrade Ingredients: Triplet Magnets
LHC triplet: 210 T/m, 70 mm coil aperture
 ca. 8 T @ coil (limit of NbTi technology)
 1.8 K cooling with superfluid He (thermal conductivity)
 critical current density of 2.75 kA / mm2
At limit of NbTi technology (HERA & Tevatron ca. 5 T @ 2kA/mm2)!!!
LHC Production in collaboration with USA and KEK

## Slide 40: HL-LHC Magnets:
LHC triplet:
210 T/m, 70 mm bore aperture
 8 T @ coil (limit of NbTi tech.)
1.8K
???
US-LARP MQXF magnet design
Based on Nb3Sn
technology
  Requires Nb3Sn technology
   ceramic type material (fragile)
   ca. 25 year development of a
  new magnet technology!
  US-LARP – CERN collaboration
HL-LHC triplet:
140 T/m, 150 mm coil aperture
(b* and crossing angle)
 ca. 12 T @ coil
More details on superconducting magnet technology and the LHC dipole magnets in the lecture by Paolo Ferracin

## Slide 41: HL-LHC Upgrade Ingredients
Geometric reduction factor  b* ≥ 10 cm & Crab Cavities
Maximize the bunch intensity
Triplet aperture  New large aperture triplet magnets

## Slide 42: HL-LHC Bunch Intensity: e-Cloud
25 ns scrubbing run in December 2012 provided demonstration of beam scrubbing (reduction in secondary electron yield (SEY) with time due to e-bombardment)
But HL-LHC operation requires SEY < 1.3 for 2 1011ppb!
Feasibility and time required for ‘beam scrubbing’ needs to be validated in next LHC operation RunII

## Slide 43: HL-LHC Upgrade Ingredients
Geometric reduction factor  b* ≥ 10 cm & Crab Cavities
Bunch intensity  Nb = 2.2 1011 (limited in LHC by e-cloud)
 injector complex upgrade prerequisite for HL-LHC!!!
Event pile-up in detectors  luminosity leveling
Collective effects and impedance  Collimator Upgrade
Electron cloud effect  beam scrubbing & feedback
Triplet aperture  New large aperture triplet magnets
Beam Losses and Radiation  shielding, Cryo upgrade &
relocation of electronics and PC

## Slide 44: Time Table for HL-LHC Upgrade (approved early 2011)
0.75 1034 cm-2s-1
50 ns bunch high pile up 40
1.5 1034 cm-2s-1
25 ns bunch pile up 40
1.7-2.2 1034 cm-2s-1
25 ns bunch pile up 60
Technical limits (experiments, too) like :
EYETS
LS2
LS3
Plan modification approved Dec 2013

## Slide 45: Upgrade Project Options beyond the HL-LHC:
Medium Term Future:
  Neutrino Program
  LHeC ep collider & Higgs factory
  SAPPHiRE gg Higgs factory
Long Term Future:
  HE-LHC/VHE-LHC pp/AA collider
  Linear Collider (ILC & CLIC)
  FCC: 100TeV hadron collider and
  e+e- Higgs factory
  ep collider…
More details on Project Studies beyond the LHC Upgrade in the lecture by Daniel Schulte (28 & 29 July) and
Patrick Janot (4 & 5 August)

## Slide 46: HE-LHC and FCC Challenges
HE-LHC
Use of existing tunnel infrastructure!
Can perhaps bring a factor 2-3 increase in CM collision energy
Magnet technology (15 T – 20 T)?!?
Investment versus physics case?!?!
FCC
Still at early R&D and study stage (20 T magnets!!!)
(magnets, beam power and machine protection, injectors...)
New tunnel would provide synergies with other machines
(e.g. TLEP as a Higgs factory)

## Slide 47
Future Circular Collider (FCC) study ; goals: CDR and cost review for the next European Strategy Update (2018)
International collaboration :
pp-collider (FCC-hh)  defining infrastructure requirements
including HE-LHC option: 16-20 T in LHC tunnel
e+e- collider (FCC-ee/TLEP) as potential intermediate step
p-e (FCC-he) option
100 km infrastructure in Geneva area
~16 T  100 TeV in 100 km
~20 T  100 TeV in 80 km
M. Benedikt

## Slide 48: Reserve Transparencies

## Slide 49: HL-LHC Ingredients: Leveling
Transverse offsets of the beams at the IP.
  tested in 2011 with HL-LHC parameters single bunches and in 2012 with present LHC
  worry about beam-beam: instabilities, emittance growth
The use of crab cavities for manipulating the beam overlap of the two beams in the luminous region  constant density!
Manipulation of the external crossing angle of the two beams
  e.g. with the help of partial compensation of the long-range beam-beam interactions in the common vacuum system with the help of wires
Dynamic change of the beta*  full beam-beam effect for the beams!
Bunch length variation
Or combinations of the above

## Slide 50: HL-LHC Performance Estimates
Parameter | nominal | 25ns | 50ns
N | 1.15E+11 | 2.2E+11 | 3.5E+11
nb | 2808 | 2808 | 1404
beam current [A] | 0.58 | 1.12 | 0.89
x-ing angle [mrad] | 300 | 590 | 590
beam separation [s] | 9.9 | 12.5 | 11.4
b* [m] | 0.55 | 0.15 | 0.15
en [mm] | 3.75 | 2.5 | 3.0
eL [eVs] | 2.51 | 2.51 | 2.51
energy spread | 1.20E-04 | 1.20E-04 | 1.20E-04
bunch length [m] | 7.50E-02 | 7.50E-02 | 7.50E-02
IBS horizontal [h] | 80 -> 106 | 18.5 | 17.2
IBS longitudinal [h] | 61 -> 60 | 20.4 | 16.1
Piwinski parameter | 0.68 | 3.12 | 2.85
geom. reduction | 0.83 | 0.305 | 0.331
beam-beam / IP | 3.10E-03 | 3.3E-03 | 4.7E-03
Peak Luminosity | 1 1034 | 7.4 1034 | 8.5 1034
Virtual Luminosity | 1.2 1034 | 24 1034 | 26 1034
(Leveled to 5 1034 cm-2 s-1
and 2.5 1034 cm-2 s-1)
HL-LHC-LIU baseline parameters:
Events / crossing (peak & leveled L) | 19 -> 28 | 207 | 476 | 140 | 140
6.2 1014 and 4.9 1014
p/beam
sufficient room for leveling
(with Crab Cavities)
Virtual luminosity (25ns) of
L = 7.4 / 0.305 1034 cm-2 s-1
= 24 1034 cm-2 s-1 (‘k’ = 5)
Virtual luminosity (50ns) of
L = 8.5 / 0.331 1034 cm-2 s-1
= 26 1034 cm-2 s-1 (‘k’ = 10)
Notes: 50ns beam option provides HL-LHC performance levels at ultimate total beam currents; only the ‘large beta*’ option reaches beam-beam limit; IBS growth rates are a concern!; low beta option has 50% higher performance potential

## Slide 51: LHC Layout and Main Parameters
2-in-1 magnet design
p-p & Pb-Pb collisions
7 TeV p-beam energy
 > 1 TeV CM energy
 Higgs discovery
2 high L experiments with
L = 1034 cm-2 sec-1
 2808 bunches / beam
with 1.15 1011 ppb
2 low L experiments:
ALICE (Pb-Pb) & LHCb

## Slide 52: Main Challenges for the Operation
Mechanical aperture
Magnetic field perturbations & field quality
Beam power and machine protection
Collective effects and impedance
Triplet aperture and beam-beam
Electron cloud effect

## Slide 53: LHC Challenges: Aperture
all magnets are geometrically measured
classification & slot compatibility
for installation at critical locations
microwave reflectrometer:
detection of obstacles

## Slide 54: LHC Challenges: Field Quality & Resonances
linear beam-beam force:
additional focusing
for small amplitudes
perturbation is proportional to
bunch intensity!
bunch intensity limited by non-linear resonances
strong non-linear field:
tune & perturbation depends on oscillation amplitude

## Slide 55: LHC Challenges: Field Quality & Resonances
tune: Q = number of oscillations per revolution
limited accessible area; limit for field quality and Q tolerance
resonances: n Qx + m Qy + r Qs = p; “order” = n+m+r
Qy
Qy
Qx
Qx

## Slide 56: LHC Challenges: Field Quality & Resonances
LHC working point: n+m < 12
Qx = 64.31; Qy = 59.32
total tune spread must be
smaller than 0.015!
N < 1.5 1011
Bunch intensity limited by beam-beam force:
Qy
Qx
The LHC features 3 proton experiments with
nominal: N < 1.15 1011
ultimate: N < 1.7 1011

## Slide 57: LHC Challenges: Errors & Resonances
presistent current errors
change with time (30%)
-decay varies
between magnets
-control spread during
production
-average errors depend
on powering history
correction circuit powering must change during operation
-operation requires correction on % level
-> procedures; field error data base & beam instrumentation!

## Slide 58: LHC Challenges: Electron Cloud 3/3
During 25 ns scrubbing run last December the reduction in the secondary electron yield (SEY) flattened out
A concentrated scrubbing run will probably be insufficient to fully suppress the EC from the arcs for 25 ns beams in future operation.

## Slide 59: Summary of LHC Intensity Limits (7 TeV)
R. Assmann
R. Assman @ Chamonix 2010
HL-LHC
Single bunch stability limit

## Slide 60: Changing 300x2 m both ATLAS & CMS (recent requests from LHC-b & Alice to be examined)
In total > 1.2 km of LHC for all IRs!!
More details on superconducting triplet magnets and Crab Cavities in the lectures by Paolo Ferracin and Erk Jensen

## Slide 61: Cryogenic Upgrade
6.5 kW@4.5K cryoplant
2 x 18 kW @4.5K cryoplants for IRs

## Slide 62: LHC Challenges: Unforeseen Beam Aborts
Radiation to electronics
Concerted program of mitigation measures (shielding, relocation…)
Premature dump rate down from 12/fb-1 in 2011 to 3/fb-1 in 2012

## Slide 63: LHeC: Baseline Linac-Ring Option
Challenge 1: Super Conducting Linac with Energy Recovery
& high current (> 6mA)
Challenge 2: Relatively large return arcs
    ca. 9 km underground tunnel installation
    total of 19 km bending arcs
    same magnet design as for RR option: > 4500 magnets
Two 1 km long SC
linacs in CW operation (Q > 1010)
requires Cryogenic
system comparable
to LHC system!

## Slide 64: HE-LHC:
2-GeV Booster
Linac4
SPS+
HE-LHC
20-T dipole magnets
higher energy
transfer lines
CERN Summer School July 2013
Oliver Brüning/CERN AB-ABP 64

## Slide 65: FCC:
FCC-hh
20-T dipole magnets
FCC-ee

## Slide 66
80-100 km tunnel: Geneva option